| WORLD METEOROLOGICAL ORGANIZATION __________________ COMMISSION FOR INSTRUMENTS AND METHODS OF OBSERVATION CIMO EXPERT TEAM ON STANDARDIZATION First Session Geneva, Switzerland 26 – 29 November 2012 |  | CIMO/ET-Stand-1/Doc. 4.2(3) (23.XI.2012) _______ ITEM: 4.2 Original: ENGLISH |
| --- | --- | --- |

Siting Assessment Forms used in Canada

(Submitted by Brian Howe)

Summary and purpose of document This document provides as an example the siting assessment forms used in Canada to evaluate the class of each sensors on a specific site.

Action proposed

The Meeting is invited to note this information and use it, as appropriate in developing guidance documentation for Members on the use and application of the Siting Classification for Surface Observing Stations on Land.

________________

Appendix:	Siting Assessment Forms

Siting Assessment Forms

Sensor Siting Classification System

For Automatic Surface Observing Weather Stations – Land

(AUTO8: RCS, SWX)

Last Update: October 31, 2012

The attached pages are worksheets for the purpose of archiving the results of a sensor ‘Siting Classification’ assessment.  There is a separate  summarized check list form for each sensor and a results summary page at the end. These forms are primarily intended just for internal archive – there are further entries required in ALM. The pages are best viewed in the ‘Print Layout’ format under the ‘View’ tab of Word. These forms will provide:

- information to management regarding the reasoning for the sensor siting classification result (1 – 5).

- a worksheet that can be used on-site via laptop.

- an archive source for future classification assessments for consistency and evolution of results.

- a highlight or focus on specific sensor exposure elements that may be improved upon if it can result in a better future classification.

- a document to determine or justify whether a station meets its exposure standards for its network type (ie. RCS).

- a remarks section to provide details regarding the assessment.

These forms can also be utilized for new or ‘green field’ sensor siting surveys to determine the probable future classification level such as when there may be several location options or a specific classification level is required. If a specific siting criteria does not apply since the station has not yet been installed, the criteria level box is left blank and is noted in the remarks section. It will need to be completed once the station has been installed and before data is released. It will be that final assessment value that is entered into ALM.

All text within these assessment forms have been abbreviated or summarized and are intended to be utilized in conjunction with the full classification criteria listing for the complete definitions.

Filling Out the Forms:

The forms are ‘auto fill’. After filling out the initial tombstone data for date, full station name and technician name, the entries into the table are done by entering the appropriate criteria class number at the end of the row in the gray box. Once each row has received the best class number that the sensor qualifies for,  the final class level of the sensor is determined by the numerically ‘highest’ class number selected. This class number is auto entered into the sensor ‘Classification Result’ in place of the “0”. If a local item/object is causing a significant sensor bias and does not fit the listed criteria, use Classification Result = 5 and supply details in the Remarks.

Remarks Section:

The remarks section is used to provide background details on the class levels selected for anything that may be of assistance to justify the siting result. It should also include notes on anything else not covered by the criteria that may bias the sensor (even on a temporary basis) and any known future tentative changes to the siting. If it has been determined that a criteria class level has now changed from a past assessment, this should be noted along with the date of the change if known. From this remarks section, it may need to be abbreviated for entry into ALM. The remark in ALM should concentrate specifically on why the sensor classification is at that level.

Once the form has been filled out, it will be saved to a different name and location. It is recommended that the files are saved as an attachment in ALM and will be available for the next trip or technician that may be required to update the classifications. Anytime a siting criteria change is suspected and might result in a classification change, these forms should be consulted.

Timing of Full Sensor Suite Classification Assessment:

The intent is that a full assessment of the sensors take place on a 5 year cycle. This should be timed with the established maintenance routine where all site drawings are updated and standard updated exposure photos are taken. In addition to the classification regarding ‘siting’, the Maintained Performance classification would also be updated or confirmed.

Intermediate or Single Sensor Re-assessment:

If a change in sensor exposure or a relocation takes place that may result in an altered classification level result, unused sensor pages may be deleted from this file and only the applicable page(s) would be used/saved.  If the date is known when the exposure change took place, this is the date that should be archived. If unknown, utilize the date when the exposure alteration was first known. In remarks, note the date that the assessment took place.

Results Summary of Station Sensor Siting Classifications:

A page has been added at the end of this form document. It is a summary of the station’s siting classification results and is considered as ‘optional’ based on regional or supervisory requirements.

Siting Assessment Form Index:

Air Temperature...............................................		Page 4

Air Humidity……..............................................		Page 5

Precipitation AWG………………………………		Page 6

Surface Wind (10m)……………………………..		Page 7

Rainfall Intensity (TBRG)………………………		Page 8

Precipitation Wind ……………………………...		Page 9

Snow Depth - Single Configuration (SR50)....	Page 10

Solar Radiation (RF-1)…………………………...	Page 11

Station Result Summary of Classifications…….	Page 12

Date of Classification:

Station Name:

Technician Name:

Class 1                 Class 2             Class 3         Class 4     Class 5

| T1) Ground Cover | 10m radius <10cm | 5m radius <15cm | 5m radius <25cm | <50cm | >50cm |  |
| --- | --- | --- | --- | --- | --- | --- |
| T2) Area ground slope | Flat 10m, Area <19 deg | Flat 5m, Area <19 deg | <5m Flat, Area>19deg |  |  |  |
| T3) Nearby irrigation | >30m away | >10m away | >5m away | None immediate | Irrigation at sensor |  |
| T4) Significant heat sources | >100m away | >30m away | >10m away | Less than 10m away |  |  |
| T5) Nearby infrastructure | Subjective & 2:1 from objects | Subjective & 2:1 from objects | Subjective & 1:1 from objects | Subjective | Affected |  |
| T6) Aircraft and/or Highways | >100m away | >50m away | >30m away | Less than 30m away |  |  |
| T7) Radiation shield or enclosure | Yes |  |  |  | No |  |
| T8) Sensor height above ground | 1.2m – 2.0m | 1.2m – 2.5m | 1.2 – 3.0m | 1.0 – 3.5m | Beyond Class 4 |  |
| T9) Max anticipated snow depth | >1m below enclosure | >0.5m below enclosure | Below enclosure | Ventilation not obstructed | Ventilation may obstruct |  |
| T10) No significant shade | Horizon + 5 deg. (<10 deg shade) | Horizon + 7 deg. (<20 deg shade) | Horizon + 10 deg. (<30 deg shade) | Horizon + 20 deg. (<45 deg shade) | Beyond Class 4 |  |

Air Temperature Classification Result: 0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1               Class 2             Class 3          Class 4     Class 5

| H1) Ground Cover | 10m radius <10cm | 5m radius <15cm | 5m radius <25cm | <50cm | >50cm |  |
| --- | --- | --- | --- | --- | --- | --- |
| H2) Area ground slope | Flat 10m, Area <19 deg | Flat 5m, Area <19 deg | <5m Flat, Area>19deg |  |  |  |
| H3) Nearby irrigation | >30m away | >10m away | >5m away | None immediate | Irrigation at sensor |  |
| H4) Significant heat sources | >100m away | >30m away | >10m away | Less than 10m away |  |  |
| H5) Nearby infrastructure | Subjective & 2:1 from objects | Subjective & 2:1 from objects | Subjective & 1:1 from objects | Subjective | Affected |  |
| H6) Aircraft and/or Highways | >100m away | >50m away | >30m away | Less than 30m away |  |  |
| H7) Radiation shield or enclosure | Yes |  |  |  | No |  |
| H8) Sensor height above ground | 1.2m – 2.0m | 1.2m – 2.5m | 1.2 – 3.0m | 1.0 – 3.5m | Beyond Class 4 |  |
| H9) Max anticipated snow depth | >1m below enclosure | >0.5m below enclosure | Below enclosure | Ventilation not obstructed | Ventilation may obstruct |  |
| T10) No significant shade | Horizon + 5 deg. (<10 deg shade) | Horizon + 7 deg. (<20 deg shade) | Horizon + 10 deg. (<30 deg shade) | Horizon + 20 deg. (<45 deg shade) | Beyond Class 4 |  |

Air Humidity Classification Result: 0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1         Class 2          Class 3          Class 4           Class 5

| P1) Area ground slope | Flat 10m radius. Area <19 deg | Flat 5m radius. Area <19 deg | Area less than 30 deg | Area > 30 deg |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| P2) Wind Shielding | Tree surround >300 deg | Standard shield |  |  | none |  |
| P2.1) Double Wind Shielding (option for P2) | DFIR or Double Alter (to spec.) |  |  |  |  |  |
| P3) Sensor orifice height above ground | 1.5m – 2.5m (+snowdepth or DFIR allowance) | 1.5m – 3m (+snowdepth allowance) | 1.5m – 4m (+snowdepth allowance) | >1.0m | Less than 1.0m |  |
| P4) Max anticipated snow depth | >1m from sensor top | >1m from sensor top | >1m from sensor top | >0.5m from sensor top | Less than 0.5m |  |
| P5) Obstacles | >4x height away (2x-4x if ‘tree surround’) | >2x height away | >1x height away | >1/2x height away | Less than 1/2x |  |

Precipitation AWG Classification Result: 0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1            Class 2             Class 3             Class 4           Class 5

| W1) Sensor height above ground | 10m | 10m | 10m | >11m or less than 9m |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| W2) Aircraft movement | Beyond 100m | Beyond 50m | Less than 50m |  |  |  |
| W3) Obstacles | 30x height away | 10x height away | 5x height away | 2.5x height away | Less than 2.5x |  |
| W4) Can ignore individual obstacles (based on highest class in table) | <4m height | <4m height | <5m height | <6m height (if sensor height of 10m) |  |  |
| W5) Narrow objects higher than 8m | >15x width away (4 deg) |  | >10x width away (6 deg) | Max 60 deg width >10m high within 40m distance | Beyond class 4 |  |
| W6) Wind doming | No |  |  |  | Yes |  |
| W7) Ground | Index 4 or | Index 5 | Index 6 | Index 7 | Index 8 |  |
| Roughness | less |  |  |  |  |  |
| Index |  |  |  |  |  |  |

Surface Wind Classification Result:  0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1              Class 2            Class 3          Class 4         Class 5

| R1) Area ground slope | Flat 10m radius. Area <19 deg | Flat 5m radius. Area <19 deg | Area less than 30 deg | Area over 30 deg |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| R2) Nearby infrastructure | >2m radius, >0.5m below | >1m radius, >0.4m below | >0.5m radius, >0.3m below | Less than 0.5m radius, <0.3m below |  |  |
| R3) Routine irrigation | No |  |  |  | Yes |  |
| R4) Sensor orifice height | 0.5m – 1.0m | 0.4m – 1.5m | 0.4m – 2.0m | 0.3m – 3.0m | Beyond class 4 |  |
| R5) Obstacles | >4x height away | >2x height away | >1x height away | >1/2x height away | Less than 1/2x |  |

Rainfall Intensity Classification Result:  0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1         Class 2          Class 3          Class 4           Class 5

| PW1) Area ground slope | <19 deg (3:1) |  | <30 deg (2:1) | Area over 30 deg |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| PW2) Objects between | No |  | Yes |  |  |  |
| PW3) Same ground cover | Between and 10m radius | Between and 5m radius | Different ground covers |  |  |  |
| PW4) Sensors height difference | <0.1m | <0.2m | Wind 0.5m below to 1m above | Wind 0.5m below to 2m above | Beyond class 4 |  |
| PW5) Distance between sensors | 3m – 15m. | 2m – 20m. | 1m – 30m. | 0.5m – 50m. | Beyond class 4 |  |
| PW6) Sensor mast thickness | <0.1m | <0.2m | Over 0.2m wide |  |  |  |
| PW7) Pcpn Wind Shield distance | >3x shield width away | >2x shield width away | >1x shield width away | Less than 1x shield width |  |  |
| PW8) Obstacles | Same siting class as Pcpn sensor | Same siting class as Pcpn sensor | Up to single class difference | Up to 2 class differences | Over 2 classes |  |

Precipitation Wind Classification Result: 0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1                 Class 2             Class 3         Class 4     Class 5

| SD1) Area ground slope | Flat 10m, Area <19 deg | Flat 5m, Area <19 deg | Level pad, Area <30 deg | Generally level pad | Unlevel |  |
| --- | --- | --- | --- | --- | --- | --- |
| SD2) Sensor height above ground | 1.5m – 2.5m | 1.5m – 3.5m | 1.5m – 4.5m | 1.5m – 6m | Beyond class 4 |  |
| SD3) Max snow depth | >1.0m below |  | >0.5m below | Below sensor | Conflicts |  |
| SD4) Prepared measurement area/pad | Pad equal or greater than table ‘B’ | Pad equal or greater than table ‘B | >0.5m x 0.5m pad | Maintained area | Not maintained |  |
| SD5) Nearby snow removals | None within 50m | None within 25m | Within 25m |  |  |  |
| SD6) Horizontal mounting mast | Non-flexible, <0.1m wide | Non-flexible, <0.2m wide | Flexible or >0.2m wide |  |  |  |
| SD7) Conflict with mast/tower footing | >30 deg. Meets table ‘A’ separation | >20 deg. No sig. drifting conflict | No sig. drifting conflict | Drifting conflict |  |  |
| SD8) Nearby objects | >5m from all objects | >4m from all objects | >3m from all objects | >2m from all objects | Less than 2m away |  |
| SD9) Obstruction Siting Class of Pcpn AWG | Same pcpn obstruction classification | Within 1 Classification level | Within 2 Classification levels | Over 2 classes |  |  |
| SD10) Shade Siting Class of Temp enclosure | Same shade obstruction classification | Within 1 Classification level | Within 2 Classification levels | Over 2 classes |  |  |

Snow Depth Classification Result: 0

Remark:

Date of Classification:

Station Name:

Technician Name:

Class 1         Class 2          Class 3          Class 4           Class 5

| SR1) No shade above local horizon | Within 3 degrees | Within 5 degrees | Within 7 degrees | Less than 30% of daytime | More than 30% of daytime |  |
| --- | --- | --- | --- | --- | --- | --- |

Solar Radiation Classification Result:

Remark:

Result Summary of Station Sensor Siting Classifications:

(Optional Requirement)

Date of Classification:

Station Name:

Technician Name:

Sensor							      Class Result

| 1 | Air Temperature | 0 |
| --- | --- | --- |
| 2 | Air Humidity | 0 |
| 3 | Precipitation AWG | 0 |
| 4 | Surface Wind (10m) | 0 |
| 5 | Rainfall Intensity (TBRG) | 0 |
| 6 | Precipitation Wind | 0 |
| 7 | Snow Depth – Single Configuration (SR50) | 0 |
| 8 | Solar Radiation (RF-1) |  |

________________