## Slide 1: WMO SPICE Tapado (Chile)
Site Configuration Update
Oct 10th, 2012
Information from Shelley MacDonell
Prepared by Rodica Nitu

## Slide 2: Site Layout
Under development

## Slide 3: Data Flow and Archive
Instruments
Datalogger
Manual collection to laptop (monthly)
Transfer to server in office
Push to CARE ftp
Instruments
Datalogger
Radio/satellite link to server La Serena (hourly?)
Push to CARE ftp
We currently can only access the site during the summer months, and have no direct communication connection with the station (Figure 1). Our current process is therefore to manually collect the data (generally monthly) to a laptop, and then transfer this data to a more secure storage in the office. We are currently investigating the possibilities for using either a satellite or radio link to the station for more frequent downloading (Figure 2). We will install this system in the austral summer.
Figure 1: Current data transfer from Tapado station
Figure 2: Potential data delivery from Tapado station

## Slide 4: Site Commissioning
Anticipated date of commissioning: April 2013
Expected status on commissioning:
  References (where applicable):
    R3: It is hoped a full R3 site will be installed using two Geonor T-200b sensors. Otherwise, during the austral summer we will install one OTT Pluvio2 plus other standard equipment (i.e. possibility of missing one reference gauge)
  Instruments under test:
    Provided by the host:
    From Instrument Providers: PWS100
  Instruments for Ancillary Measurements:
    Currently:
      Air temperature/Relative humidity – Vaisala HMP45C (shielded)
      Wind speed and direction – Young 5103
      Snow depth – CS SR50
      Net radiation - CS300+, Middleton EQ16, CS CG3 [looking to replace with CS CNR4]
Expected status on Nov 15th: Current status operational, R3 requirements in preparation
Gaps for the winter 2012/2013:
  It is hoped that a full R3 site will be commissioned by austral winter 2013, the only mitigating factor is the acquisition of Geonor gauges. Assuming the gauges are installed, they will not be heated due to inadequate power supply, however due to conditions at the site, it is unlikely that this will impact results.
  We are also hoping to setup a satellite or radio link with the site to facilitate data transfer.
  reasons: Availability of equipment and logistics of installing a link
  activities postponed for 2013: TBC

## Slide 5: Additional Information
Data archive;
  Existing system is storage on a secure server
  Frequency of data transmission from the site to an archive: Monthly (manually)
Have you sent data to NCAR for pre-SPICE? No
  Which is the reasonable frequency of data transfer to NCAR/SPICE archive to be expected during the experiment: Monthly under present configuration