## Slide 1: WMO SPICE Volga (Russia)
Site Configuration Update
Oct 10th, 2012
Information from Arkadi Koldaev
Prepared by Rodica Nitu

## Slide 2: Site Layout

## Slide 3: Site References (information provided as part of the site submission in June 2012)
(Tretyakov) gauge and Tretyakov shield; Snow Water Equivalent measurements measured daily since 1957
D2: Reference for the measurement of snow depth
  Availability of manual snow depth measurements Every 3 hours
  Method of measurement: Visual
  Instrument/equipment used (provide description): Metric mast
  Availability of web cameras for snow depth monitoring; provide details: Yes

## Slide 4: Instruments under Test
Instruments proposed by the host:
  Snow Depth, Russian company “AQUA NUBIS”, “NAST” type;

## Slide 5: Ancillary Measurements (as submitted in June 2012)
Parameter | Instruments Used (model, make, configuration, height, number of instruments. | Data available (data format) | Reporting Interval | Status
Air Temperature | 2 mercury TM4-1 thermometers for psychrometer at a height of 2 m; in winter a TM-9-1 thermometer for low temperatures is used | .xls spreadsheets | 8 times a day every 3 hours | E
Relative Humidity | 2 M-19-1 hygrometers (at temperatures <-10°) | .xls spreadsheets | 8 times a day every 3 hours (at <-10°C) | E
DewPoint Temperature | Determined with psychrometric tables using data from TM4-1 thermometers | .xls spreadsheets |  | E
Atmospheric Pressure | 1 station cup-shaped SR-A barometer | .xls spreadsheets | 8 times a day every 3 hours | E
Wind Speed 10 m | 1 M-63-1 anemorumbometer at a height of 11 m | .xls spreadsheets | 8 times a day every 3 hours | E
Wind Direction 10 m | 1 M-63-1 anemorumbometer at a height of 11 m | .xls spreadsheets | 8 times a day every 3 hours | E
Wind Speed at the gauge orifice (specify height) | N/A |  |  | P
Precipitation Detector (Y/N output) | - |  |  | P
Precipitation type | Visually |  | 8 times a day every 3 hours | E
Ice detection sensor | - |  |  | P
Snow Depth | 3 Snow masts | .xls spreadsheets | Every 3 hours | E

## Slide 6: Data Flow and Archive

## Slide 7: Site Commissioning

## Slide 8: Additional Information (provided by Arkadi Koldaev, Oct 3rd, 2012)
have fulfilled pre-construction project, and the construction works were started in September. I hope we will get first 5 positions ready to the end of October.
In general, have used the idea of Vigna de Vale for organization of the individual instrument position, cable connection tunnels, power supply and data collection units and so on. (can send the construction drawings. )
The experimental site will be attached to the operating meteorological station from two sides: West and North, and will have 9 positions for the instruments.
Three corners of this site will be equipped with additional wind, humidity and temperature sensors at 2m height
As we have discussed, Tret'yakov double fence standard gage is constructed also on the South-East corner of the operating meteorological station.
All area ( operating and experimental) will be covered with 4 video cameras and lights for 24 hours security. Additional funding for Geonor and OTT gauges , are still promised, but not received yet.
will have a meeting with Head of Volga River HM Department on October 10, and hope he will provide me with the photos of the site construction - I will pass it to you immediately.