1.0	introduction	5

1.1	Purpose of this Document	5

1.2	Scope	5

1.3	Relationship of the Specification to Other Standards	5

1.4	System Description	5

1.4.1	ACARS System Description	5

1.4.2	ACARS Use of ICAO-Compliant Communication Services	5

1.4.2.1	ICAO Compliant Subnetworks	5

1.4.2.2	ICAO ATN Communications Services	5

1.4.2.3	ACARS Transition Aspects	5

2.0	data link system	5

2.1	Overview	5

2.2	Message Transport	5

2.2.1	Uplink Message Handling	5

2.2.2	Downlink Message Handling	5

2.2.3	Accountability	5

2.2.3.1	Internetworking	5

2.2.4	Prioritization	5

2.2.5	Intercept Message Handling	5

2.2.5.1	Untransmittable Uplink Messages	5

2.2.5.2	Undeliverable Uplink Messages	5

2.2.5.3	Unformattable Downlink Messages	5

2.3	Flight Following	5

2.3.1	Aircraft Tracking	5

2.3.2	Optional Geographic Locator (GL) or Airport Locator (AP)	5

2.3.3	Aircraft Identification	5

2.4	Network Management	5

2.4.1	Data Link Station Outage Status (AOS)	5

2.4.2	Data Link Station Restoral (ARA)	5

2.4.3	Data Link Station Addition (ASA)	5

2.4.4	Data Link Station Deletion (ASD)	5

2.5	DSP Connectivity Offering	5

2.5.1	Data Link Service Provider Exchanges	5

2.6	Function Summary	5

3.0	message handling	5

3.1	Introduction	5

3.1.1	Section Outline	5

3.1.2	Definitions	5

3.2	Ground-Ground Segment Specification (DSP to Ground User Interface)	5

3.2.1	General Ground-Ground Message Format	5

3.2.2	Downlink Conversion and Processing Function	5

3.2.2.1	Downlink Addressing	5

3.2.2.1.1	Downlink Addresses of Messages From an ACARS Peripheral	5

3.2.2.1.2	Downlink Supplementary Addresses	5

3.2.2.1.3	Supplementary Address Field	5

3.2.2.1.4	Downlink Address Conversion	5

3.2.3	Uplink Conversion and Processing Functions	5

3.2.3.1	TEI Processing of Uplink Ground-Ground Message	5

3.2.3.1.1	AN (Aircraft Tail Number) and FI (Flight Identifier) TEI Processing	5

3.2.3.1.2	GL (Ground Locator) / AP (Airport Locator) and TP (Transmission Path) 
	TEIs Processing	5

3.2.3.1.3	MA (Message Assurance) TEI Processing	5

3.2.3.2	Uplink Addressing	5

3.2.3.2.1	Uplink Addresses for Messages Delivered to an ACARS Peripheral	5

3.2.3.3	Uplink Supplementary Address(es)	5

3.3	Service Messages	5

3.3.1	Uplink Message Receipt Confirmation	5

3.3.2	Uplink Message Delivery Confirmation	5

3.3.3	Untransmittable Uplink Service Messages	5

3.3.3.1	Message Assurance Report - Untransmittable Uplink	5

3.3.4	Undeliverable Uplink Service Messages	5

3.3.4.1	Message Assurance Reports	5

3.3.5	Unformattable Downlink Service Messages	5

3.3.5.1	Incomplete Downlink Service Message Intercept	5

3.4	Network Advisory Messages	5

3.5	ACARS Messaging Function Primitives	5

3.6	Air-Ground Messages	5

4.0	uplink message text formats	5

4.1	Introduction	5

4.2	Uplink Message Formats, System Control	5

4.2.1	General Response – Label _DEL	5

4.2.2	General Response, Polled Mode – Label _j	5

4.2.3	ACARS Frequency Uplink – Label 54 or Voice Go-Ahead – Label 54	5

4.2.4	Voice Circuit Busy – Label Q4	5

4.2.5	Uplink Squitter – Label SQ	5

4.2.6	Data Transceiver Autotune – Label :;	5

4.2.7	Reserved Label::	5

4.2.8	POA to AOA Retune – Label :}	5

4.2.9	Loopback Request – Label KB	5

4.3	Uplink Message Formats, Service Related	5

4.3.1	Ground GMT Update – Label 51	5

4.3.2	Ground UTC Update – Label 52	5

4.3.3	Reserved Spare – Label 53	5

4.3.4	Cockpit/Cabin Printer Messages – Labels C0-C9	5

4.3.5	Command/Response Uplink – Label RA	5

4.3.6	Network Statistics Report Request – Label S1	5

4.3.7	VHF Network Performance Report Request – Label S2	5

4.3.8	LRU Configuration Profile Report Request – MFI or Label S3	5

4.3.9	Meteorological Report Command Uplink – MFI or Label H2	5

4.3.10	Meteorological Report Command Uplink – MFI or Label H4	5

4.3.10.1	Basic Configuration Data	5

4.3.10.2	Region Data	5

4.3.10.3	Airport Data (1)	5

4.3.10.4	Interval and Wind Reporting Status	5

4.3.10.5	Ascent Data	5

4.3.10.6	Airport Data (2)	5

4.3.10.7	Descent Data (1)	5

4.3.10.8	Descent Data (2)	5

4.3.10.9	Reporting Disabled Status	5

4.3.10.10	Preset Target Heights Based on Pressure Level Selection	5

4.3.11	Refuel – Administrative and General Purpose Refuel Uplinks – Label ‘RE’	5

4.3.12	CG Targeting Refuel Uplinks – Label ‘RF’	5

4.3.13	Reserved for Data Loading Uplinks – MFI or Label ‘DL’	5

4.3.14	Technical (Cockpit) E-Logbook Uplinks – MFI or Label ‘LT’	5

4.3.15	Reserved for Cabin E-Logbook Uplinks – MFI or Label ‘LC’	5

4.3.16	De-Icing uplinks – Label ‘DI’	5

4.3.17	Meteorological Report Command Uplink, Version 5 – MFI or Label H4	5

4.3.17.1	Basic Configuration Data	5

4.3.17.2	Region Data	5

4.3.17.3	Airport Data (1)	5

4.3.17.4	Interval and Wind Reporting Status	5

4.3.17.5	Ascent Data	5

4.3.17.6	Airport Data (2)	5

4.3.17.7	Descent Data (1)	5

4.3.17.8	Descent Data (2)	5

4.3.17.9	Reporting Disabled Status	5

4.3.17.10	Preset Target Heights Based on Pressure Level Selection	5

4.3.18	Potable Water Remote Pre-selection uplinks – Label ‘WP’	5

4.4	Uplink Message Formats, ACARS Peripherals - Label H1	5

4.4.1	OAT – Label H1	5

4.4.2	OAX – Label H1	5

4.4.3	Uplinks (with Headers) to Peripherals – Label H1	5

4.4.4	Uplinks (With No Header) to Peripherals – Label H1	5

4.5	Uplink Message Formats, ATS Messages – MFI or Label Ax	5

4.5.1	Oceanic Clearance – MFI or Label A1	5

4.5.2	Unassigned – MFI or Label A2	5

4.5.3	Departure Clearance – MFI or Label A3	5

4.5.4	Flight Systems Message – MFI or Label A4	5

4.5.5	Unassigned – MFI or Label A5	5

4.5.6	Request ADS Reports – MFI or Label A6	5

4.5.7	Free Text from ATC – MFI or Label A7	5

4.5.8	Deliver Departure Slot – MFI or Label A8	5

4.5.9	ATIS Report – MFI or Label A9	5

4.5.10	ATS Facilities Notification (AFN) – MFI or Label A0	5

4.5.11	ATCCommunications – MFI or Label AA	5

4.5.12	Terminal Weather Information for Pilots – MFI or Label AB	5

4.5.13	Pushback Clearance – MFI or Label AC	5

4.5.14	Expected Taxi Clearance – MFI or Label AD	5

4.5.15	Unassigned – MFI or Label AE	5

4.5.16	CPC Command/Response – MFI or Label AF	5

4.5.17	Unassigned – MFI or Label AG	5

4.6	Uplink Message Formats, User Defined	5

4.7	Uplink Message Formats, Supplier Defined	5

4.8	Uplink Message Formats, DSP Defined	5

4.9	Uplink Message Formats, AMS-Protected Messages	5

4.9.1	AMS-Protected Uplink ATS Message – MFI or Label P7	5

4.9.2	AMS-Protected Uplink AMS-Specific Message – MFI or Label P8	5

4.9.3	AMS-Protected Uplink AOC Message – MFI or Label P9	5

4.10	Uplink Message Formats, MIAM Messages – MFI or Label MA, MB to MZ	5

5.0	downlink message text formats	5

5.1	Introduction	5

5.2	Downlink Message Formats, System Control	5

5.2.1	General Response – Label _DEL	5

5.2.2	Voice Contact Request – Label 54	5

5.2.3	Reserved Characters	5

5.2.4	Temporary Suspension – Label 5P	5

5.2.5	Unable to Deliver Uplinked Message – Label Q5	5

5.2.6	Voice to Data Channel Changeover Advisory – Label Q6	5

5.2.7	Intercept/Unable to Process – Label QX	5

5.2.8	Dedicated Transceiver Advisory – Label F3	5

5.2.9	Cockpit Printer Status – Label CA-CF	5

5.2.10	VDL Switch Advisory – Label 5V	5

5.2.11	Autotune Reject – Label QV	5

5.2.12	Loopback Response – Label KB	5

5.3	Downlink Message Formats, Service-Related Messages	5

5.3.1	Emergency Situation Report (Aircraft Hijack) – Label 00	5

5.3.2	Ground GMT Request – Label 51	5

5.3.3	Ground UTC Request – Label 52	5

5.3.4	ATIS Request – Label 5D	5

5.3.5	Aircrew Initiated Position Report – Label 5R	5

5.3.6	Weather Request - Label 5U	5

5.3.7	Airline Designated Downlink - Label 5Z	5

5.3.8	Aircrew Revision to Previous ETA/Diversion – Label 5Y	5

5.3.9	Aircrew Initiated Engine Data/Takeoff Thrust Report – Label 7A	5

5.3.10	Aircrew Entered Miscellaneous Message – Label 7B	5

5.3.11	Aircrew-Addressed Downlink – Labels 80 through 8~	5

5.3.12	Unassigned	5

5.3.13	Meteorological Report – Label or MFI H2	5

5.3.13.1	Meteorological Report, Version 1 – MFI or Label H2	5

5.3.13.2	Meteorological Report, Version 2 – MFI or Label H2	5

5.3.13.3	Meteorological Report, Version 3 – MFI or Label H2	5

5.3.13.4	Meteorological Report, Version 4 – MFI or Label H2	5

5.3.13.4.1	Ascent Reports	5

5.3.13.4.1.1	Initial	5

5.3.13.4.1.2	Series #1	5

5.3.13.4.1.3	Series #2	5

5.3.13.4.2	Enroute Reports	5

5.3.13.4.2.1	Series #1	5

5.3.13.4.2.2	Maximum Wind Report	5

5.3.13.4.3	Descent Reports	5

5.3.13.4.3.1	Series #1	5

5.3.13.4.3.2	Series #2	5

5.3.13.4.4	Data Smoothing	5

5.3.13.4.5	Optimization	5

5.3.13.5	Meteorological Report, Version 5 – MFI or Label H2	5

5.3.13.5.1	Ascent Reports	5

5.3.13.5.2	Enroute Reports	5

5.3.13.5.3	Descent Reports	5

5.3.13.5.4	Data Smoothing	5

5.3.13.5.5	Ascent, Enroute and Descent Weather Report Formats	5

5.3.14	Command/Response Downlink – Label RB	5

5.3.15	Link Test – Label Q0	5

5.3.16	Departure/Arrival Reports (IATA Airport Code) – Label Q1	5

5.3.17	ETA Report – Label Q2	5

5.3.18	Clock Update Advisory – Label Q3	5

5.3.19	Unassigned	5

5.3.20	Unassigned	5

5.3.21	Delay Message – Label Q7	5

5.3.22	Reserved – Label Q8	5

5.3.23	Reserved – Label Q9	5

5.3.24	OUT/Fuel Report (IATA Airport Code) – Label QA	5

5.3.25	OFF Report (IATA Airport Code) – Label QB	5

5.3.26	ON Report (IATA Airport Code) – Label QC	5

5.3.27	IN/Fuel Report (IATA Airport Code) – Label QD	5

5.3.28	OUT/Fuel/Destination Report (IATA Airport Code) – Label QE	5

5.3.29	OFF/Destination Report (IATA Airport Code) – Label QF	5

5.3.30	OUT/Return IN Report (IATA Airport Code) – Label QG	5

5.3.31	OUT Report (IATA Airport Code) – Label QH	5

5.3.32	Landing Report (IATA Airport Code) – Label QK	5

5.3.33	Arrival Report (IATA Airport Code) – Label QL	5

5.3.34	Arrival Information Report (IATA Airport Code) – Label QM	5

5.3.35	Diversion Report (IATA Airport Code) – Label QN	5

5.3.36	Out Report (ICAO Airport Code) – Label QP	5

5.3.37	OFF Report (ICAO Airport Code) – Label QQ	5

5.3.38	ON Report (ICAO Airport Code) – Label QR	5

5.3.39	IN Report (ICAO Airport Code) – Label QS	5

5.3.40	OUT/Return IN Report (ICAO Airport Code) – Label QT	5

5.3.41	Unassigned – Label QU	5

5.3.42	Reserved	5

5.3.43	Unassigned – Label QW	5

5.3.44	Unassigned – Label QY	5

5.3.45	Unassigned – Label QZ	5

5.3.46	Undelivered Uplink Report – Label HX	5

5.3.47	Aircrew Initiated Position Report, Alternate Format – Label 57	5

5.3.48	VHF Network Statistics Report – Label S1	5

5.3.49	VHF Network Performance Report – Label S2	5

5.3.50	LRU Configuration Report – Label S3	5

5.3.51	Media Advisory – Label SA	5

5.3.52	Icing Report – MFI or Label H3	5

5.3.53	Internet E-Mail Message – MFI or Label E1	5

5.3.54	Meteorological Report Configuration Downlink – MFI or Label H4	5

5.3.55	Internet E-Mail Message - DSP Service – MFI or Label E2	5

5.3.56	Administrative and General Purpose Refuel Downlinks – Label ‘RE’	5

5.3.57	CG Targeting Refuel Downlinks – Label ‘RF’	5

5.3.58	Reserved for Data Loading Downlinks – MFI or Label ‘DL’	5

5.3.59	Reserved for Technical Logbook Downlinks – MFI or Label ‘LT’	5

5.3.60	Technical (Cockpit) E-Logbook Downlinks – MFI or label ‘LS’	5

5.3.61	Reserved for Cabin Logbook Downlinks – MFI or Label ‘LC’	5

5.3.62	Reserved for Cabin E-Logbook Downlinks – MFI or Label ‘LB’	5

5.3.63	De-Icing Downlinks – Label ‘DI’	5

5.3.64	Potable Water Remote Pre-selection Downlinks – Label ‘WP’	5

5.4	Downlink Message Formats, Messages from Avionics Subsystem – Label H1	5

5.4.1	Messages from Airborne Subsystems: ARINC 597 ACARS – Label H1	5

5.4.2	Messages from Airborne Subsystems: ARINC 724 or 724B 
	ACARS MU – Label H1	5

5.4.2.1	OAT – Simple H1 Message	5

5.4.2.2	OAT – H1 Message with Additional Addresses	5

5.4.2.3	CFDIU, DFDAU, FMC, or Cabin Terminal Messages without Additional 
	Addresses	5

5.4.2.4	CFDIU, DFDAU, FMC, or Cabin Terminal Messages with Additional 
	Addresses	5

5.5	Downlink Message Formats, ATS Messages – MFI or Label Bx	5

5.5.1	Request Oceanic Clearance – MFI or Label B1	5

5.5.2	Oceanic Clearance Readback – MFI or Label B2	5

5.5.3	Request Departure Clearance – MFI or Label B3	5

5.5.4	Departure Clearance Readback Downlink – MFI or Label B4	5

5.5.5	Waypoint Position Report – MFI or Label B5	5

5.5.6	Provide ADS Report – MFI or Label B6	5

5.5.7	Free Text to ATC – MFI or Label B7	5

5.5.8	Request Departure Slot – MFI or Label B8	5

5.5.9	Request ATIS Report – MFI or Label B9	5

5.5.10	ATS Facilities Notification (AFN) – MFI or Label B0	5

5.5.11	ATC Communications – MFI or Label BA	5

5.5.12	Terminal Weather Information for Pilots – MFI or Label BB	5

5.5.13	Pushback Clearance Request – MFI or Label BC	5

5.5.14	Expected Taxi Clearance Request – MFI or Label BD	5

5.5.15	CPC Aircraft Log-On/Log-Off Request – MFI or Label BE	5

5.5.16	CPC WILCO/UNABLE Response – MFI or Label BF	5

5.5.17	Unassigned – MFI or Label BG	5

5.6	Downlink Message Format, User-Defined	5

5.7	Downlink Message Formats, Supplier Defined	5

5.8	Downlink Message Formats, DSP Defined	5

5.9	Downlink Message Formats, AMS-Protected Messages	5

5.9.1	AMS-Protected Downlink Message, Test System Destination – Label P0	5

5.9.2	AMS-Protected Downlink Message, End System Destination – Labels P1 
	through P5	5

5.9.3	Unassigned – Label P6	5

5.9.4	AMS-Protected Downlink ATS Message, DSP Destination – Label PA	5

5.9.5	AMS-Protected Downlink AMS-specific Message, DSP Destination – Label PB	5

5.9.6	AMS-Protected Downlink AOC Message, DSP Destination – Label PC	5

5.10	Downlink Message Formats, MIAM Message – MFI or Label MA, MB-MZ	5

6.0	SERVICE LEVEL STANDARDS	5

6.1	Introduction	5

6.2	Transit Times	5

6.3	Availability	5

6.3.1	System	5

6.3.2	Ground Stations	5

6.3.3	Critical Airports	5

6.4	Clock Accuracy	5

7.0	REFERENCE DOCUMENTS	5

ATTACHMENTS

ATTACHMENT 1	ground syStems standards relationsips	5

ATTACHMENT 2	service messages – reason codes	5

ATTACHMENT 3	performance report generation state diagram	5

APPENDICES

APPENDIX A	glossary and acronyms	5

APPENDIX B	section b.1 tei codes	5

APPENDIX B	section b.2 rules for smi/tei application	5

APPENDIX C	message information	5

APPENDIX D	reserved	5

APPENDIX E	iso 5 characters	5

APPENDIX F	vhf acars network performance reporting	5

APPENDIX G	UPLINK CONTROL PROGRAMMING NOTES FOR VERSION 4 ONBOARD SOFTWARE	5

APPENDIX H	meteorological report compression	5

# introduction

## Purpose of this Document

This document sets forth the desired interface characteristics of the data link service provider to the data link user.The intent of this document is to provide data link users the information needed to develop applications and to encourage uniformity and standardization, to the extent possible, among the various data link service providers.This document contains general and specific guidance concerning the interfaces between the data link service providers and both the airborne and ground user.

## Scope

This document describes the data link service provider system inputs, outputs and functions from the perspective of the data link user.The functions are described in the detail necessary to provide a complete understanding of what the functions do while not restricting the data link service provider network internal implementation.Where there are differences in message formats or functions provided between the various service providers which affect the data link user interface, the differences are specifically described.

This document was originally addressing ACARS-related ground interface by re-using TypeB.

It is also now defininga new user-service provider ground interface that can support other aircraft-ground communication solutions (e.g., MIAM, defined in ARINCSpecification 841).

The Extensions of Data Link Ground System Standard and Interface Specification for aircraft MIAM messaging are defined in Section 7 of this document.

## Relationship of the Specification to OtherStandards

The documentation of the protocols to be exercised within the Aircraft Communications Addressing and Reporting System(ACARS) environment is shown pictorially in Figure 1.3-1, ACARS Documentation.

The protocols used onboard the aircraft by subsystems participating in ACARS are defined in ARINC Specification 619:ACARS Protocols for Avionic End Systems.

The protocols and procedures to be used for ACARS communications between the airborne user and the data link service provider network are described in ARINC Specification 618:Air/Ground Character-Oriented Protocol Specification.

The capabilities of the onboard equipment are defined in: ARINC Characteristic 716:Airborne VHF Communications Transceiver,ARINC Characteristic 724B:Aircraft Communications Addressing and Reporting System (ACARS),ARINC Characteristic 750:VHF Data Radio,ARINC Characteristic 758:Communications Management Unit (CMU) Mark 2 as applicable. Provisions defined within from these Specifications and Characteristics are not duplicated in this document except as necessary to clarify the data link service provider to data link user interface.

COMMENTARY

Legacy ACARS Management Units, defined by ARINC Characteristics 597 and 724 may still be in service.

The ACARS communications function may be provided by a Communications Management Unit (CMU) in lieu of an ACARS Management Unit (MU).The CMU is described in ARINC Characteristic 758.When acting as an ACARS MU, the CMU utilizes the protocols and procedures defined in ARINC Specification 618.

ARINC Specification 841 defines Media Independent Aircraft Messaging (MIAM) protocol, which permits the exchange of a large volume of data over Aircraft Communications Addressing and Reporting System (ACARS) subnetworks or broadband Internet Protocol (IP) subnetworks.

Figure 1.3-1 – ACARS Documentation

The CMU is designed to support bit-oriented message transfer utilizing the protocols and procedures for routing. The CMU will interact with onboard systems that supply mobile air-ground communications over Very High Frequency (VHF), satellite and High Frequency (HF) media.These subnetworks are described by AEEC standards:

| VHF Data Radio (VDR) | ARINC Characteristic 750 |
| --- | --- |
| Aviation Packet Communications | ARINC Specification 631 |
| Aviation Satellite System | ARINC Characteristics 761 and 741 Part 1 and Part 2 |
| HF Data Link System | ARINC Characteristic 753 |
| HF Data Link Protocols | ARINC Specification 635 |

The CMU provides routing and transport services for the aircraft per ARINC Characteristic 758.

The protocols and procedures to be administered by the data link service provider are contained herein.

The protocols used between the ground-based user and the data link service provider network are described in the Air Transport Association (ATA)/International Air Transport Association (IATA) Interline Communications Manual (ICM).

## System Description

The transport of ACARS Application data over the air-ground segment can be accomplished using services which are two-fold:

- The ACARS Communications Service defined in ARINC Specification 618, which specifies the use VHF, Aeronautical Mobile Satellite Service (AMSS) Data-2, and HF data links as candidate air-ground data links.

- The ICAO-compliant communications services described in ARINC Characteristic 758 for interfacing to the ICAO-compliant subnetworks.

This document specifies a common ACARS user interface to access both Communications Services over the air-ground segment.

### ACARS System Description

The character-oriented version of mobile communications is referred to as the Aircraft Communications Addressing and Reporting System (ACARS). This system enablesaircraft to function as mobile communications terminals. With ACARS, aircraft operate as integral parts of an airline’s command, control and management systems.

ACARS provides message transfer between airborne users and ACARS ground users via air-ground links andACARS ground networks.

Figure 1-1 of Attachment 1 shows a typical end-to-end communications environment and applicable Characteristics/manuals.

The protocols and formats used to transmit messages between the ACARS ground user and the data link service provider network (ground-ground segment) differs from the protocols and formats used to exchange messages between airborne user and the data link service processor (air-ground segment).It is the responsibility of the data link service provider to provide translation between these protocols and formats as well as to provide proper message routing.The formats of messages exchanged between the ACARS ground data link user and the data link service provider network are fully described in this document.The format for ACARS Application text to be exchanged between the airborne user and the data link service provider network is also defined in this document.

The format used to transmit messages between the ACARS ground user and the ACARS groundnetwork is referred to as Standard Message Text (SMT), which uses Standard Message Identifiers (SMI) and Text Element Identifiers (TEI).See Appendix B for SMI/TEI descriptions.The data link service provider is responsible for putting messages received from aircraft (downlink ACARS messages) into SMT format for consumption by the ground data link user, and sending them to their ultimate destination(s).Similarly, data link service providers reformat messages received in SMT from the data link ground based user into air-ground message formats having labels/sublabels/ACARS text and then pass the reformatted messages on to the airborne user.

### ACARS Use of ICAO-Compliant Communication Services

#### ICAO Compliant Subnetworks

The early ARINC 618-compliant subnetworks (VHF ACARS, HF ACARS, Aeronautical Mobile Satellite Service (AMSS) Data-2 ACARS) are being replaced by a new generation of air-ground communications.

These new air-ground subnetworks such as VDL (VHF Digital Link) and AMSS Data-3 offer bit-oriented air-ground data communication services based on the Open Systems Interconnection (OSI) architecture and provide the communication framework supporting the Aeronautical Telecommunication Network (ATN) over VHF and Satellite media.Other ICAO-compliant subnetworks are being specified such as High Frequency Data Link (HFDL) or Iridium systems which are also potential candidate for transfer of ACARS application data over the air-ground segment.

In particular, the VHF air-ground subnetwork is termed VDL (VHF Digital Link) by ICAO. The two primary standardization organizations that have developed the VDL subnetwork are ICAO Aeronautical Mobile Communication Panel (AMCP) and Airlines Electronic Engineering Committee (AEEC). The AMCP specified and validated VHF Digital Link (VDL) Standard and Recommended Practices (SARPs) for the Air Traffic Services (ATS) community. ARINC Specification 631:VHF Digital Link (VDL) Mode 2 Implementation Provisions,makes direct reference to the ICAO VDL Standards and Recommended Practices (SARPs) and is updated to accommodate ACARS use of this new air-ground protocol.

#### ICAO ATN Communications Services

A new architecture for the use in the Aeronautical Telecommunications Network (ATN) environment offers interoperability among various terrestrial, air-ground and avionics subnetworks through conformance with a single bit-oriented ATN Internetworking Protocol, ATN Addressing Plan, and ATN Routing Plan.

#### ACARS Transition Aspects

COMMENTARY

The means for ACARS Applications to benefit from the ICAO-compliant communications service have been implemented.

# a

# B

# C

## 1

## 2

## 3

### 4

### 5

### 6

### 7

### 8

### 9

### 10

### 11

### Meteorological Report Command Uplink – MFI or Label H2

The following uplink report specifies the command structure for altering the configuration of reporting for the Meteorological Report, Versions2 and 3 (see Sections 5.3.13.2 and 5.2.13.3).

Automatic Weather Report (AWR) algorithm (see Section 5.2.13.2 and 5.2.13.3) limits can be changed via an ACARS uplink command using the following format:

| Char | Data | Description | Units |
| --- | --- | --- | --- |
| 1 | A | IMI |  |
| 2 | W | IMI |  |
| 3 | R | IMI |  |
| 4-5 | 0-9 | Ascent Series 1 intervals | Number of seconds, 03 to 20 |
| 6-8 | 0-9 | Ascent Series 1 duration | Number of seconds, 030 to 200 |
| 9-10 | 0-9 | Ascent Series 2 intervals | Number of seconds, 20 to 60 |
| 11-13 | 0-9 | Top of Ascent | Hundreds of feet PALT, 180 to 300 or tens of seconds, 051 to 111 |
| 14-15 | 0-9 | Enroute intervals | Number of minutes, 01 to 60 |
| 16-18 | 0-9 | Top of a Descent | Hundreds of feet PALT, 180 to 300 |
| 19-21 | 0-9 | Descent intervals | Number of seconds, 020 to 300 |
| 22 | 0-1 | Ascent Enable(1) / Disable(0) |  |
| 23 | 0-1 | Enroute Enable(1) / Disable(0) |  |
| 24 | 0-1 | Descent Enable(1) / Disable(0) |  |

### Meteorological Report Command Uplink – MFI or Label H4

The following uplink report specifies the command structure for altering the configuration of reporting for the Meteorological Report, Version 4 (Section 5.3.13.4).

Additional information in the form of programming notes is attached as Appendix G.

Automatic Weather Report (AWR) algorithm (see Section 5.3.13.4) limits can be changed via an ACARS uplink command using the following format:

#### Basic Configuration Data

Table 4.3.10.1-1 – Basic Configuration Data

| Number of Characters | Data | Description | Default Value | Remarks |
| --- | --- | --- | --- | --- |
| 1 | A | IMI |  |  |
| 1 | W | IMI |  |  |
| 1 | R | IMI |  |  |
| 2 | 04 | Version number |  |  |
| 1 | 0, 1, 9 | Enable AMDAR | 1 | 0 = disable, 1 = enable, 9 = no change |
| 1 | 0, 1, 9 | Inhibit reporting in selected time interval See Note 2. | 0 | 0 = disable (report through 24hrs every day), 1 = enable, 9 = no change. If enabled see Table 4.3.10.9-1. |
| 1 | 0, 1, 9 | Report in designated region See Note 3. | 0 | 0 = disable, 1 = enable, 9 = no change, If enabled see Table 4.3.10.2-1. |
| 1 | 0, 1, 9 | Airport selection See Note 4. | 0 | 0 = disable, 1 = enable, 9 = no change. If enabled see Table 4.3.10.3-1. |
| 1 | 0, 1, 9 | Ascent selection See Note 5. | 1 | 0 = disable, 1 = enable. If enabled see Tables 4.3.10.5-1 and 4.3.10.3-1. If disabled and airport selection is disabled see Tables 4.3.10.6-1 and 4.3.10.4-1. 9 = no change |
| 1 | 0, 1, 9 | Enroute selection See Note 6. | 1 | 0 = disable, 1 = enable, 9 = no change. If enabled see Tables 4.3.10.4-1 and 4.3.10.3-1. |
| 1 | 0, 1, 9 | Descent selection See Note 7. | 1 | 0 = disable, 1 = enable. If enabled see Tables 4.3.10.7-1 and 4.3.10.3-1. If disabled see Tables 4.3.10.8-1 and 4.3.10.4-1. 9 = no change |
| 1 | 0-2 | Downlink configuration tables See Note 8. | 0 | 0 = do nothing, 1 = downlink Table1, 2 = downlink Tables 4.3.10.1-1, 4.3.10.2-1, 4.3.10.3-1, 4.3.10.4-1, 4.3.10.5-1, 4.3.10.6-1, 4.3.10.7-1, 4.3.10.8-1 and 4.3.10.9-1 (see downlink report Label H4) |
| 8 | E2 E3 E4 E5 E6 E7 E8 E9 | Extended message indicator See Note 9. | 00000000 | E2= 2 means Table 4.3.10.2-1 follows, 0 means not included (and unchanged). E.g., 03450700 means Tables 4.3.10.3-1, 4.3.10.4-1, 4.3.10.5-1 and 4.3.10.7-1 follow in that order. |
| 1 | / | Delimiter |  | End of Table 4.3.10.1-1 (this table) commands |

Notes:

- This table is the basic configuration table.  It is the smallest message that can be uplinked and the information content is stored on board as Table 4.3.10.1-1. The information actually stored is determined by the commands contained in characters 6 – 12.  Following a complete system reset and/or initialization, Table 4.3.10.1-1 contains the default characters (0 or 1) corresponding to characters 6 to 12. These can be changed by the uplinked message as necessary.  Uplinked commands can be made to enable or disable the appropriate functions or leave the previous command unchanged. Each character gives links to further on board data that affects the downlinked message required and, as necessary, updates to these data can be appended. Further explanation of each command follows.

- Inhibit reporting in selected time interval, if enabled, points to Table 4.3.10.9-1. This command allows reporting to be inhibited for a selected period in any consecutive 24-hour period. When disabled, reporting is continuous unless inhibited by subsequent commands.

- Report in designated region, if enabled, points to 
Table 4.3.10.2-1. Table 4.3.10.2-1 allows specific regions to be designated for enabling reporting or inhibiting reporting. When disabled, reports are to be made globally unless inhibited by subsequent commands.

- Airport selection, if enabled, points to Table 4.3.10.3-1 which allows specific airfields to be selected for enabling ascent and/or descent reports or inhibiting ascent and/or descent reporting from specific airfields. If disabled, ascent and descent reports are required in all regions where AMDAR is enabled.

- If Ascent selection is enabled, it points to Table 4.3.10.5-1 that specifies the ascent reporting scheme to be followed. If disabled, it overrides all previous commands and inhibits all ascent reporting. However, if Airport selection is disabled also, routine, timed reports can be enabled by reference to Table 4.3.10.6-1 using time intervals designated in Table 4.3.10.4-1. If Ascent selection is disabled and Airport selection is enabled it points to Table 4.3.10.3-1 to determine if routine reports are required during ascent from designated airfields.

- Enroute selection, if disabled, overrides all previous commands and disables all enroute reporting. If enabled, enroute reporting is determined according to the commands linked to characters 6,7,
and 8.

- If Descent selection is enabled, it points to Table 4.3.10.7-1 that specifies the descent reporting scheme to be followed. If disabled, it overrides all previous commands and inhibits all descent reporting. However, if Airport selection is disabled also, routine, timed reports can be enabled by reference to Table 4.3.10.8-1 using time intervals designated in Table 4.3.10.4-1. If Descent selection is disabled and Airport selection is enabled it points to Table 4.3.10.3-1 to determine if routine reports are required during descent from designated airfields.

- Downlink configuration tables, if set to 0 is ignored. If set to 1 the basic configuration (Table 4.3.10.1-1), as amended by the current message, is to be downlinked after the current uplink message has been processed. If set to 2 all configuration tables are to be downlinked after the current uplink message has been processed.

- The Extended message indicator indicates which updated configuration table data to be uplinked follows, as necessary.

#### Region Data

Table 4.3.10.2-1 – Region Data

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 2 | NRNR | Number boxes following | NN= 0-16 Default = 00 |
| 14 | L1L1 A1L2L2A2 L3 L3L3 B1L4L4 L4B2 | Report in Lat/Long box | Lat in degrees north (A = N) or south (A = S) Lon in degrees east (B = E) or west (B = W) Convention is L1L1 to L2L2 (N -S) And L3L3L3 to L4L4L4 (W-E). |
| Variable, multiples of 14 | As above | As above | As above, repeated (NRNR-1) times |
| 1 | : | Delimiter | End of report boxes, start of inhibit boxes |
| 2 | NINI | Number boxes following | NN= 00-16 Default = 00 |
| 14 | L1L1 A1L2L2A2 L3 L3L3 B1L4L4 L4B2 | Inhibit reporting in Lat/ Long box | Inhibit has priority over enable |
| Variable, multiples of 14 | As above | As above | As above, repeated (NINI-1) times |
| 1 | / | Delimiter | End of Table 4.3.10.2-1 data. |

Note:	This Table is used if Report in designated region 
(Table 4.3.10.1-1, Character 8) is enabled. It allows up to 16 latitude/longitude boxes’that define regions in which profile and enroute observations should be taken (modified as appropriate by Table 4.3.10.3-1) and up to 16 regions in which observations are to be inhibited. Inhibited areas take precedence over reporting areas. Following a complete system reset and/or installation, the default number is 00 for both selection types. This is to be interpreted as the function is not enabled (i.e., report globally). When enabled, then no reporting is performed outside the designated regions unless specified in Table 4.3.10.3-1.

#### Airport Data (1)

Table 4.3.10.3-1 – Airport Data (1)

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 2 | NANA | Number of airfields following | NANA = 00-20 Default = 00 |
| 4 | AAAA | Airfield selected for ascent | 4 character airfield code |
| Variable multiples of 4 | " | " | Repeated up to NANA -1 times |
| 1 | : | Delimiter | End of ascent list; start of descent list |
| 2 | NDND | Number of airfields following | NDND = 00-20Default = 00 |
| 4 | DDDD | Airfield selected for descent | 4 character airfield code |
| Variable multiples of 4 | '' | " | Repeated up to NDND -1 times |
| 1 | : | Delimiter | End of descent list, start of (inhibit) ascent list |
| 2 | NANA | Number of airfields following | NANA = 00-20 Default = 00 |
| 4 | AAAA | Airfield inhibited for ascent | 4 character airfield code |
| Variable multiples of 4 | " | " | Repeated up to NANA -1 times |
| 1 | : | Delimiter | End of ascent list; start of descent list |
| 2 | NDND | Number of airfields following | NDND = 00-20 Default = 00 |
| 4 | DDDD | Airfield inhibited for descent | 4 character airfield code |
| Variable multiples of 4 | '' | " | Repeated up to NDND -1 times |
| 1 | 0 - 1 | Enable (1) or disable (0) routine observations during ascent and descent for the above selected inhibited airfields. | Default = 0 1 = enable routine observations. Routine observations are made at set intervals as defined in Table 4.3.10.4-1. |
| 1 | / | Delimiter | End of Table 4.3.10.3-1 data |

Note:	This table is used if Airport selection is enabled in 
Table 4.3.10.1-1. If also Report in designated region is set in Table 4.3.10.1-1 then the following rules apply to airfields within and external to the regions designated in Table 4.3.10.2-1. If airfields are specified outside a designated region then ascent and/or descent (but no enroute) reporting will apply to these airfields in addition to any requirements specified within the region. It is possible, therefore, to establish regions where only ascents and/or descents are made at specific airfields or all ascents/descents are made except those at designated airfields. The report list takes precedence over the inhibit list. For example if NANA (number of airfields following (for ascent reporting)) is set to 00 all ascents in an enabled region will be reported unless any are inhibited in the inhibit list following. If NANA (number of airfields following for ascent reporting) in an enabled region is non-zero, then only the listed airfields following, designated for ascent reporting, will be used. Ascent reporting at all other airfields in the same enabled region will be inhibited and the appropriate inhibit list will be ignored. The same logic applies to descent reporting. If in Table 4.3.10.1-1 Report in designated region is set to 0 then defaults in this table are to be interpreted as report ascents and/or descents (as appropriate) everywhere.

#### Interval and Wind Reporting Status

Table 4.3.10.4-1 – Interval and Wind Reporting Status

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 2 | mm | Routine-level flight observing interval (min) | Default = 07 Range = 01 – 60 |
| 1 | w | Enable or disable maximum wind reporting | Default = 1 (enable) Disable = 0 |
| 1 | / | Delimiter | End of Table 4.3.10.4-1 data |

Note:	This table sets the routine/enroute reporting interval. The third character (w), if set to the default value 1 enables maximum wind reporting during the enroute phase. If set to 0, this function is disabled.

#### Ascent Data

Table 4.3.10.5-1 – Ascent Data

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Pressure level (0 or Time interval (1) selection | Ascent sampling mode Default = 1 |
| 2 | ss | Series 1 intervals (seconds) | Default = 06 (seconds) Range = 03 – 20 |
| 3 | sss | Series 1 duration (seconds) | Default = 090 Range = 030 – 200 |
| 2 | ss | Series 2 intervals (seconds) | Default = 20 Range = 20 – 60 |
| 3 | SSS | Total duration (secondsx10) | Default = 051 Range = 051 – 111 |
| 3 | hhh | Top of climb (ftx100) | Default = 200 Range = 150 – 250 |
| 1 | 1 or 2 | Pressure target list selection | 1 = List 1, 2 = List 2 (Table 4.3.10.10-1) Default = 2 |
| 1 | 0 or 1 | Additional level flight timer for pressure-based sampling: enabled = (1), disabled = (0) | Default = 1 (Routine timer interval as defined in Table 4.3.10.4-1) |
| 1 | / | Delimiter | End of Table 4.3.10.5-1 data |

Note:	This table is used when ascent reports are made. (This will be established by reference to Tables 4.3.10.1-1, 4.3.10.2-1 and 4.3.10.3-1). Following a complete system reset and/or initialization, the table holds the default values as given (all of which must be stored onboard). The first character indicates whether interval selection is by time or pressure intervals. The next 4 fields (Series 1 int. etc.). give the required time interval parameters. If pressure is used, sampling commences using Series 2 format immediately. The next 3 characters set the top of climb defining the end of the ascent phase. This is followed by a single character that defines which of the two pre-stored lists of pressure altitude target heights are to be used (Table G-10 in Appendix G, List 1 or 2) when pressure level is selected by the first field. The next character selects whether a default timer is used in conjunction with pressure level selection to ensure that samples are still obtained if there is a pause during the ascent phase for periods of level flight. The additional interval timer resets and commences following each observation. If no pressure level is encountered during the pre-set time interval, a sample is taken and the timer is reset. The pre-set time interval is the same as selected in field 1 of Table 4.3.10.4-1 for routine/level flight. This technique also automatically commences the enroute phase of level flight if the top of climb is not reached. The function is disabled if Ascent selection is disabled in Table 4.3.10.1-1.

#### Airport Data (2)

Table 4.3.10.6-1 – Airport Data (2)

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Routine observations enabled = (1), disabled = (0) | Enables or disables routine observations when both ascent and airport selection are disabled in Table 4.3.10.1-1. Default = 1 |
| 1 | / | Delimiter | End of Table 4.3.10.6-1 data |

Note:	This table is used only if Ascent selection and Airport selection are disabled through Table 4.3.10.1-1 commands. If the first character is set to 1 (default) then routine observations at the time intervals given in Table 4.3.10.4-1 will be made whenever AMDAR reporting is enabled through previous Table 
4.3.10.1-1 commands.  If set to 0, no routine reports will be made anywhere during the ascent phase. If Ascent selection is disabled and Airport selection enabled this table is ignored and routine reporting requirements are determined from Table 4.3.10.3-1. Table 4.3.10.2-1 has no influence on this function.

#### Descent Data (1)

Table 4.3.10.7-1 – Descent Data (1)

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Pressure interval (0) or Time interval (1) selection | Descent sampling mode selection Default = 1 |
| 3 | sss | Descent interval (seconds) | Default = 040 Range = 020 – 300 |
| 3 | hhh | Top of descent (PALT) (ft x 100) | Default = 200 Range = 150 – 250 |
| 1 | 1-2 | Pressure target list selection | 1 = list 1, 2 = list 2 (Table G-10 in Appendix G) Default = 2 |
| 1 | 0 or 1 | Additional level flight timer for pressure-based sampling: enabled = (1), disabled = (0) | Default = 1 (Routine timer interval as defined in Table 4.3.10.4-1) |
| 1 | / | Delimiter | End of Table 4.3.10.7-1 data |

Note:	This table is used if descent reports are made. (This will be established by reference to Tables 4.3.10.1-1, 4.3.10.2-1 and 4.3.10.3-1.) The first character indicates whether interval selection is by time or pressure intervals. The next 3 characters give the required time interval and must be included even if the pressure sampling mode is selected. The following 3 characters set the top of descent. The next character indicates which of two pre-stored pressure altitude target heights lists are to be used (Table G-10 in Appendix G, List 1 or List 2). The second last character determines whether a default timer is used in conjunction with pressure level selection to ensure that samples are still obtained if there is a pause during the descent phase for periods of level flight. The additional interval timer resets and commences following each observation. If no pressure level is encountered during the pre-set time interval, a sample is taken and the timer is reset. The pre-set time interval is the same as selected in field 1 of Table 4.3.10.4-1 for routine/level flight. The function is disabled if Descent selection is disabled through Table 4.3.10.1-1 command.

#### Descent Data (2)

Table 4.3.10.8-1 – Descent Data (2)

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Routine observations: enabled = (1) disabled = (0) | Enables or disables routine observations when both descent and airport selection are disabled in 4.3.10.1-1. Default = 1 |
| 1 | / | Delimiter | End of Table 4.3.10.8-1 data |

Note:	This Table is used only if Descent selection and Airport selection are disabled through Table 4.3.10.1-1 command. If the first character is set to 1 (default) then routine observations at the time intervals given in Table 4.3.10.4-1 will be made during descent whenever AMDAR reporting is enabled through previous Table 4.3.10.1-1 commands. If set to 0 no reports will be made anywhere during the descent phase. If Descent selection is disabled and Airport selection enabled this table is ignored and routine reporting requirements are determined from Table 4.3.10.3-1. Table 4.3.10.2-1 has no influence on this function.

#### Reporting Disabled Status

Table 4.3.10.9-1 – Reporting Disabled Status

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 4 | H1H1H2H2 | Disable observations between selected hours (00-23) UTC, every day | H1H1 = start of inhibit period H2H2 = end of inhibit period Default = 0000 |
| 1 | / | Delimiter | End of Table 4.3.10.9-1 data |

Note:	This table is used if Inhibit reporting in selected time interval (Table 4.3.10.1-1) is selected. It allows observations to be inhibited between selected hours UTC, each 24 hours it is enabled. The default value is interpreted as no interval selected. The inhibit period starts at the first designated hour in the day and ends when the next designated hour is reached the same or next day. Thus 2301 means inhibit between 2300 hours and 0100 hours the next day, every day. (two hours spanning midnight UTC). 0000 means report though all 24 hour periods.

Additional notes:

Default data for Tables 4.3.10.1-1 through to 4.3.10.9-1 are stored onboard as part of the basic software but can only be altered through software re-programming. Following a complete system reset and/or initialization, the default table variables from non-volatile memory are loaded and then retained in volatile memory until altered by uplink command.  Default values can only be altered through software re-programming. Any subsequent uplinked changes are retained in volatile memory until the next system reset and/or initialization.

The uplink command can be used to change any of the system control parameters or simply to downlink an existing configuration for data management purposes.

#### Preset Target Heights Based on Pressure Level Selection

Table G-10 within Appendix G provides the preset target heights based on pressure level selection. An explanation of its derivation and use in accordance with the definition of the ICAO Standard Atmosphere is also provided.

Example 1:

Interpretation of Observation Requirements

AMDAR data is required from this aircraft reporting according to the following requirements:

- An exclusion time window is needed using the current pre-set time values i.e. no change to Table 4.3.10.9-1.

- Data are to be collected in a single regional Lat-Long box (60N – 50N, 
30W - 30E) but not in a small box within this area (52N – 50N, 001W – 001E) as defined in the update to Table 4.3.10.2-1.

- There is no requirement for data to be collected or inhibited at any special airports.

- Ascent data is required using the existing pre-set values in Table 4.3.10.5-1.

- Enroute data is required using the existing pre-set reporting interval as defined in Table 4.3.10.4-1.

- No high density data is required during descent, but sampling during descent is required as specified in the updated Table information below and at the existing pre-set routine reporting interval in Table 4.3.10.4-1.

- At the end of saving all table updates, a downlinked configuration report for all tables is required.

Command String:

AWR041110110220000080/0160N50N030W030E:0152N50N001W001E/1/

Decode:

| Character | Data | Meaning |
| --- | --- | --- |
| 1 | A |  |
| 2 | W |  |
| 3 | R |  |
| 4 | 0 |  |
| 5 | 4 | Version no (04) |
| 6 | 1 | AMDAR enabled |
| 7 | 1 | Time interval in day selected, refer to Char 21 and Table 4.3.10.9-1 |
| 8 | 1 | Reporting regions selected, refer to Char 14 and Table 4.3.10.2-1 |
| 9 | 0 | Airport selection disabled |
| 10 | 1 | Ascents enabled, refer to Char 17 and Table 4.3.10.5-1 |
| 11 | 1 | Enroute selected, refer to Char 16 and Table 4.3.10.4-1 |
| 12 | 0 | Descent disabled, refer to Char 16, 20 and Tables 4.3.10.4-1 and 4.3.10.8-1 |
| 13 | 2 | Downlink all tables (after command action) |
| 14 | 2 | Update for Table 4.3.10.2-1 follows |
| 15 | 0 | No change to Table 4.3.10.3-1 |
| 16 | 0 | No change to Table 4.3.10.4-1 |
| 17 | 0 | No change to Table 4.3.10.5-1 |
| 18 | 0 | No change to Table 4.3.10.6-1 |
| 19 | 0 | No change to Table 4.3.10.7-1 |
| 20 | 8 | Update to Table 4.3.10.8-1 follows. |
| 21 | 0 | No change to Table 4.3.10.9-1 |
| 22 | / | End of Basic Configuration (Table 1) Commands. Store Table 4.3.10.1-1 update (Chars 4-12) |
| 23 | 0 | } |
| 24 | 1 | } One designated reporting region follows |
| 25 | 6 | } |
| 26 | 0 | } 60N to |
| 27 | N | } |
| 28 | 5 | } |
| 29 | 0 | } 50N |
| 30 | N | } |
| 31 | 0 | } |

| Character | Data | Meaning |
| --- | --- | --- |
| 32 | 3 | } 30W to |
| 33 | 0 | } |
| 34 | W | } |
| 35 | 0 | } |
| 36 | 3 | } 30 E |
| 37 | 0 | } |
| 38 | E | } |
| 39 | : | End of reporting region selection, start of inhibit region selection. |
| 40 | 0 | } |
| 41 | 1 | } One inhibit region selected (52N-50N), (01W-01E) |
| 42 | 5 | } |
| 43 | 2 | } 52N to |
| 44 | N | } |
| 45 | 5 | } |
| 46 | 0 | } 50N |
| 47 | N | } |
| 48 | 0 | } |
| 49 | 0 | } |
| 50 | 1 | } 001W |
| 51 | W | } |
| 52 | 0 | } |
| 53 | 0 | } |
| 54 | 1 | } 001E |
| 55 | E | } |
| 56 | / | End of Table 4.3.10.2-1 update data- update stored Table 4.3.10.2-1 |
| 57 | 1 | Routine observations enabled (Table 4.3.10.8-1) during descent (intervals from Table 4.3.10.4-1) |
| 58 | / | End of Table 4.3.10.8-1 data- update stored Table 4.3.10.8-1 |

Example 2

Requirement:

Change only routine/enroute observation interval to 10 minutes with enroute enabled. Downlink all configuration tables.

Message:

AWR049999919200400000/100/

Note:	Chars 6-10 are encoded 9 meaning no change to stored configuration. Char 11 is encoded 1 to ensure enroute reporting is enabled. Char 12 is encoded 9 indicating no change to descent selection. Char 13 is encoded 2 to request downlink of all configuration tables at termination of uplink message. Chars 14-15 are encoded 0 to indicate Tables 4.3.10.2-1 to 4.3.10.3-1 are not included in the message. Char 16 is coded 4 to indicate updated Table 4 follows. Chars 17-21 are coded 0 to indicate Tables 4.3.10.5-1 through 4.3.10.9-1 are not included in the message. Chars 23 and 24 give new value of 10 minutes in Table 4.3.10.4-1 for routine/enroute observing interval. Char 25 is set to 0 to indicate no max wind reporting.

Example 3

Observation requirements:

AMDAR data are required from this aircraft which is being returned to service following an extensive maintenance period.  All settings have been set to the default values following power up but changes are now required to some settings according to the following requirements:

- Data are to be reported during night hours only using the exclusion time window as defined in the updated Table 4.3.10.9-1 (0700 - 2100);

- All profiles and enroute data are required in the southern hemisphere.  Enroute data only is required in the northern hemisphere except over regions covering the US and Europe as defined in 2 regional exclusion Lat.-Long. boxes in the updated Table 4.3.10.2-1, i.e., (50N - 15N, 125W - 60W) and (90N - 40N, 15W - 40E);

- Targeted profile observations are required for Singapore, Hong Kong and Bangkok (as defined in an updated Table 4.3.10.3-1) but no other northern hemisphere airport. By specifying these airports, profiles at all other airports in the northern hemisphere will be automatically inhibited.

- Ascent data are required as shown in the updated Table 4.3.10.5-1 at the pre-set higher density pressure values contained in List 1 of pre-stored Table G-10 in Appendix G. The additional level flight timer is also required to produce data during pauses in the ascent.

- Enroute data at the default interval of 7 minutes and maximum wind reports are required in the updated Table 4.3.10.4-1;

- Descent data are required as shown in the updated Table 4.3.10.7-1 at the pre-set higher density pressure values contained in List 1 of the pre-stored Table G-10 of Appendix G. The additional level flight timer is also required to produce data during pauses in the descent;

- At the end of saving all table updates, a downlinked configuration report for all tables is required.

Command String:

AWR041111111223450709/0290N00N180W180E00S90S180W180E:0250N15N125W060W90N40N015W040E/03WSSSVHHHVTBD:03WSSSVHHHVTBD:00:000/071/0060902005120011/004020011/0721/

| Character Number | Data Value | Meaning/Action |
| --- | --- | --- |
| 1 | A | IMI |
| 2 | W | IMI |
| 3 | R | IMI |
| 4 | 0 | Version no. (04) |
| 5 | 4 |  |
| 6 | 1 | AMDAR is enabled |
| 7 | 1 | Use Exclusive time window to report overnight. Exclude observations between 7am and 9pm. Refer to Char. 21 and updated Table 4.3.10.9-1 |
| 8 | 1 | Report globally except in regions over US and Europe. Refer to Char. 14 and updated Table 4.3.10.2-1 |
| 9 | 1 | Use inclusive airport selection for ascents and descents. Refer to Chars. 14 & 15 and updated Tables 4.3.10.2-1& 4.3.10.3-1. |
| 10 | 1 | High density pressure triggered Ascent is selected. Refer to Char. 17 & updated Table 4.3.10.5-1. |
| 11 | 1 | Enroute is selected at the default time interval. Refer to Char. 16 and Table 4.3.10.4-1 (default). |
| 12 | 1 | High density pressure triggered Descent is selected. Refer to Char. 19 & Table 4.3.10.7-1. |
| 13 | 2 | Transmit all tables in downlinked Status Report after saving of updated tables. |
| 14 | 2 | Update Table 4.3.10.2-1 - Define new regions. |
| 15 | 3 | Update Table 4.3.10.3-1 - Define new list of inclusive airports for ascent & descent. |
| 16 | 4 | Update Table 4.3.10.4-1 - Retain default 7 minute intervals; enable maximum wind. |
| 17 | 5 | Update Table 4.3.10.5-1 - Select pressure level trigger for ascent at high resolution. |
| 18 | 0 | No change to Table 4.3.10.6-1 - Retain default setting. Routine observations on ascent not required. |
| 19 | 7 | Update Table 4.3.10.7-1 - Select pressure level trigger for descent at high resolution |
| 20 | 0 | No change to Table 4.3.10.8-1. Retain default setting. Routine observations on descent not required. |
| 21 | 9 | Update Table 4.3.10.9-1 - Set exclusion window to 0700-2100 |
| 22 | / | End of basic configuration commands. Store Table 1 updates. |
| 23 | 0 | Commence Table 4.3.10.2-1 update. Define 2 inclusion boxes, southern hemisphere (profiles & enroute) and northern hemisphere (enroute only). |
| 24 | 2 |  |
| 25 | 9 |  |
| 26 | 0 |  |
| 27 | N |  |
| 28 | 0 |  |
| 29 | 0 |  |
| 30 | N |  |
| 31 | 1 |  |
| 32 | 8 |  |
| 33 | 0 |  |
| 34 | W |  |
| 35 | 1 |  |
| 36 | 8 |  |
| 37 | 0 |  |
| 38 | E |  |
| 39 | 0 |  |
| 40 | 0 |  |
| 41 | S |  |
| 42 | 9 |  |
| 43 | 0 |  |
| 44 | S |  |
| 45 | 1 |  |
| 46 | 8 |  |
| 47 | 0 |  |
| 48 | W |  |
| 49 | 1 |  |
| 50 | 8 |  |
| 51 | 0 |  |
| 52 | E |  |
| 53 | : | End inclusive regional boxes |
| 54 | 0 | Commence Exclusion regional boxes. 2 are required |
| 55 | 2 | Report globally except in these 2 boxes |
| 56 | 5 | Commence defining first box (50N-15N; 125W-60W) |
| 57 | 0 |  |
| 58 | N |  |
| 59 | 1 |  |
| 60 | 5 |  |
| 61 | N |  |
| 62 | 1 |  |
| 63 | 2 |  |
| 64 | 5 |  |
| 65 | W |  |
| 66 | 0 |  |
| 67 | 6 |  |
| 68 | 0 |  |
| 69 | W |  |
| 70 | 9 | Commence defining second box (90N-40N; 15W-40E) |
| 71 | 0 |  |
| 72 | N |  |
| 73 | 4 |  |
| 74 | 0 |  |
| 75 | N |  |
| 76 | 0 |  |
| 77 | 1 |  |
| 78 | 5 |  |
| 79 | W |  |
| 80 | 0 |  |
| 81 | 4 |  |
| 82 | 0 |  |
| 83 | E |  |
| 84 | / | End of defining exclusion boxes. |
| 85 | 0 | Define 3 airports for ascent reporting in northern hemisphere box. All other NH ascents are inhibited |
| 86 | 3 |  |
| 87 | W |  |
| 88 | S |  |
| 89 | S |  |
| 90 | S |  |
| 91 | V |  |
| 92 | H |  |
| 93 | H |  |
| 94 | H |  |
| 95 | V |  |
| 96 | T |  |
| 97 | B |  |
| 98 | D |  |
| 99 | : |  |
| 100 | 0 | Define same 3 airports for descent reporting in NH. All other descents are NH inhibited |
| 101 | 3 |  |
| 102 | W |  |
| 103 | S |  |
| 104 | S |  |
| 105 | S |  |
| 106 | V |  |
| 107 | H |  |
| 108 | H |  |
| 109 | H |  |
| 110 | V |  |
| 111 | T |  |
| 112 | B |  |
| 113 | D |  |
| 114 | : |  |
| 115 | 0 | No airfields are selected for inhibiting ascents |
| 116 | 0 |  |
| 117 | : |  |
| 118 | 0 | No airfields are selected for inhibiting descents |
| 119 | 0 |  |
| 120 | 0 | Disable routine sampling of profiles. |
| 121 | / | End of Table 4.3.10.3-1 update. Store new Table 4.3.10.3-1 |
| 122 | 0 | Commence update to Table 4.3.10.4-1. Retain 7 min. intervals; |
| 123 | 7 |  |
| 124 | 1 | Enable maximum wind reporting |
| 125 | / |  |
| 126 | 0 | Commence update to Table 4.3.10.5-1. Enable Pressure level triggering during ascent phase |
| 127 | 0 | } |
| 128 | 6 | } |
| 129 | 0 | } |
| 130 | 9 | } |
| 131 | 0 | } No changes to default settings |
| 132 | 2 | } |
| 133 | 0 | } |
| 134 | 0 |  |
| 135 | 5 | } |
| 136 | 1 | } |
| 137 | 2 | } |
| 138 | 0 | } |
| 139 | 0 | } |
| 140 | 1 | Enable Table 4.3.10.10-1 List 1 high resolution pressure triggers |
| 141 | 1 | Enable additional level flight timer during ascent |
| 142 | / | End of Table 4.3.10.5-1 update |
| 143 | 0 | Commence update to Table 4.3.10.7-1. Enable Pressure level triggering during descent phase |
| 144 | 0 | } |
| 145 | 4 | } |
| 146 | 0 | } |
| 147 | 2 | } No changes to default settings |
| 148 | 0 | } |
| 149 | 0 | } |
| 150 | 1 | Enable Table 4.3.10.10-1 List 1 high resolution pressure triggers |
| 151 | 1 | Enable additional level flight timer during descent |
| 152 | / | End of update to Table 4.3.10.7-1 |
| 153 | 0 | Commence update to Table 4.3.10.9-1. Set Exclusion time window 0700-2100 |
| 154 | 7 |  |
| 155 | 2 |  |
| 156 | 1 |  |
| 157 | / | End of update to Table 4.3.10.9-1. Save all Tables. Downlink status report |

### Refuel – Administrative and General Purpose Refuel Uplinks – Label ‘RE’

These messages are exchanged between ground fueling systems and airborne fuel AOC application.

The message content is defined in ARINC Specification 633.

These messages may contain one or more optional supplementary addresses.

### CG Targeting Refuel Uplinks – Label ‘RF’

These messages are exchanged between ground fueling systems and airborne fuel systems capable of CG targeting (refueling of the aircraft does not support a predefined, static fuel distribution, like ‘wing’, ‘center’, ‘trim’, but a dynamic fuel distribution, that targets a certain take off center of gravity ).

The message content is defined in ARINC Specification 633.

These messages may contain one or more optional supplementary addresses.

### Reserved for Data Loading Uplinks – MFI or Label ‘DL’

These messages are exchanged between ground maintenance systems and airborne data loading function. These messages should contain the label (or MFI) characters ‘DL.’

These messages may contain one or more optional supplementary addresses.

COMMENTARY

The specification of a data loading uplink is to be defined by ARINC Specification 633.

### Technical (Cockpit) E-Logbook Uplinks – MFI or Label ‘LT’

These messages are exchanged between ground maintenance systems and airborne E-logbook function (technical, i.e. cockpit related logbook). These messages should contain the label (or MFI) characters ‘LT’.

These messages may contain one or more optional supplementary addresses.

COMMENTARY

ATA developed a Technical Logbook specification. It was published in June 2009 as ATA Spec 2000, Chapter 17.

### Reserved for Cabin E-Logbook Uplinks – MFI or Label ‘LC’

These messages are exchanged between ground maintenance systems and airborne Cabin E-logbook function. These messages should contain the label (or MFI) characters ‘LC’.

These messages may contain one or more optional supplementary addresses.

### De-Icing uplinks – Label ‘DI’

These messages are exchanged between ground airline operation systems (or De-Icing company ground system) and airborne De-Icing datalink application. These messages should contain the label characters ‘DI’.

These messages may contain one or more optional supplementary addresses.

The message content is defined in ARINC Specification 633.

### Meteorological Report Command Uplink, Version 5 – MFI or Label H4

The following uplink report specifies the command structure for altering the configuration of reporting for the Meteorological Report, Version 5 (see Section 5.3.13.5).

The Uplink Control Programming Notes for Version 4 Onboard Software, provided as Appendix G, is still applicable to Version 5; however, the changes made as outlined for Version 5 need to be taken into consideration, particularly in relation to the changes that affect Appendix G Tables G-1, G-5, G-7 and G-10 in Appendix G.

For examples of the use of Command Uplinks, see Section 4.3.10.10.

Automatic Weather Report (AWR) algorithm limits (see Section 5.3.13.5) can be changed via an ACARS uplink command using the following format:

#### Basic Configuration Data

Table 4.3.17.1-1 – Basic Configuration Data

| Number of Characters | Data | Description | Default Value | Remarks |
| --- | --- | --- | --- | --- |
| 1 | A | IMI |  |  |
| 1 | W | IMI |  |  |
| 1 | R | IMI |  |  |
| 2 | 05 | Version number |  |  |
| 1 | 0, 1, 9 | Enable AMDAR | 1 | 0 = disable, 1 = enable, 9 = no change |
| 1 | 0, 1, 9 | Inhibit reporting in selected time interval See Note 2. | 0 | 0 = disable (report through 24hrs every day), 1 = enable, 9 = no change. If enabled see Table 4.3.10.9-1. |
| 1 | 0, 1, 9 | Report in designated region See Note 3. | 0 | 0 = disable, 1 = enable, 9 = no change. If enabled see Table 4.3.10.2-1. |
| 1 | 0, 1, 9 | Airport selection See Note 4. | 0 | 0 = disable, 1 = enable, 9 = no change. If enabled see Table 4.3.10.3-1. |
| 1 | 0, 1, 9 | Ascent selection See Note 5. | 1 | 0 = disable, 1 = enable. If enabled see Tables 4.3.17.5-1 and 4.3.10.3-1. If disabled and airport selection is disabled see Tables 4.3.10.6-1 and 4.3.10.4.1-9 = no change |
| 1 | 0, 1, 9 | Enroute selection See Note 6. | 1 | 0 = disable, 1 = enable, 9 = no change. If enabled see Tables 4.3.10.4-1 and 4.3.10.3-1. |
| 1 | 0, 1, 9 | Descent selection See Note 7. | 1 | 0 = disable, 1 = enable. If enabled see Tables 4.3.17.7-1 and 4.3.10.3-1. If disabled see Tables 4.3.10.8-1 and 4.3.10.4-1. 9 = no change |
| 1 | 0-2 | Downlink configuration tables See Note 8. | 0 | 0 = do nothing, 1 = downlink Table1, 2 = downlink Tables 4.3.10.1-1, 4.3.10.2-1, 4.3.10.3-1, 4.3.10.4-1, 4.3.17.5-1, 4.3.10.6-1, 4.3.17.7-1, 4.3.10.8-1 and 4.3.10.9-1 (see downlink report Label H4) |
| 8 | E2 E3 E4 E5 E6 E7 E8 E9 | Extended message indicator See Note 9. | 00000000 | E2= 2 means Table 4.3.10.2-1 follows, 0 means not included (and unchanged). E.g., 03450700 means Tables 4.3.10.3-1, 4.3.10.4-1, 4.3.17.5-1 and 4.3.17.7-1 follow in that order. |
| 1 | 0-3 | Parameter configuration See Note 10 | 0 | This value specifies the configuration for reporting of optional parameters within the Meteorological Report, Version 5 (Section 5.3.13.5), as described below in note 10. |
| 1 | / | Delimiter |  | End of Table 4.3.17.1-1 (this table) commands |

Notes:

- This table is the basic configuration table. It is the smallest message that can be uplinked and the information content is stored on board as Table 4.3.17.1-1. The information actually stored is determined by the commands contained in characters 6 – 12. Following a complete system reset and/or initialization, Table 4.3.17.1-1 contains the default characters (0 or 1) corresponding to characters 6 to 12. These can be changed by the uplinked message as necessary. Uplinked commands can be made to enable or disable the appropriate functions or leave the previous command unchanged. Each character gives links to further on board data that affects the downlinked message required and, as necessary, updates to these data can be appended. Further explanation of each command follows.

- Inhibit reporting in selected time interval, if enabled, points to Table 4.3.10.9-1. This command allows reporting to be inhibited for a selected period in any consecutive 24-hour period. When disabled, reporting is continuous unless inhibited by subsequent commands.

- Report in designated region, if enabled, points to 
Table 4.3.10.2-1. Table 4.3.10.2-1 allows specific regions to be designated for enabling reporting or inhibiting reporting. When disabled, reports are to be made globally unless inhibited by subsequent commands.

- Airport selection, if enabled, points to Table 4.3.10.3-1 which allows specific airfields to be selected for enabling ascent and/or descent reports or inhibiting ascent and/or descent reporting from specific airfields. If disabled, ascent and descent reports are required in all regions where AMDAR is enabled.

- If Ascent selection is enabled, it points to Table 4.3.17.5-1 that specifies the ascent reporting scheme to be followed.  If disabled, it overrides all previous commands and inhibits all ascent reporting. However, if Airport selection is disabled also, routine, timed reports can be enabled by reference to Table 4.3.10.6-1 using time intervals designated in Table 4.3.10.4-1. If Ascent selection is disabled and Airport selection is enabled it points to Table 4.3.10.3-1 to determine if routine reports are required during ascent from designated airfields.

- Enroute selection, if disabled, overrides all previous commands and disables all enroute reporting. If enabled, enroute reporting is determined according to the commands linked to characters 6,7 and 8.

- If Descent selection is enabled, it points to Table 4.3.17.7-1 that specifies the descent reporting scheme to be followed.  If disabled, it overrides all previous commands and inhibits all descent reporting. However, if Airport selection is disabled also, routine, timed reports can be enabled by reference to Table 4.3.10.8-1 using time intervals designated inTable 4.3.10.4-1. If Descent selection is disabled and Airport selection is enabled, it points to Table 4.3.10.3-1 to determine if routine reports are required during descent from designated airfields.

- Downlink configuration tables, if set to 0 is ignored. If set to 1 the basic configuration (Table 4.3.17.1-1), as amended by the current message, is to be downlinked after the current uplink message has been processed. If set to 2, all configuration tables are to be downlinked after the current uplink message has been processed.

- The Extended message indicator indicates which updated configuration table data to be uplinked follows, as necessary.

- The addition of parameter groups within the Meteorological Report, Version 5 (see Section 5.3.13.5), depends on the value of the Parameter Configuration:

Parameter Configuration Value

| Parameter Configuration | TAS | CNF |
| --- | --- | --- |
| 0 | no | No |
| 1 | yes | No |
| 2 | no | Yes |
| 3 | yes | Yes |

#### Region Data

Region Data is configured identically as per Section 4.3.10.2.

#### Airport Data (1)

Airport Data (1) is configured identically as per Section 4.3.10.3.

#### Interval and Wind Reporting Status

Interval and Wind Reporting Status is configured identically as per Section 4.3.10.4.

### Meteorological Report Command Uplink, Version 6 – MFI or Label H4

This section makes provisions for the uplink command structure for altering the configuration of reporting for the Meteorological Report, Version 6 (see Section 5.3.13.6.).

For examples of the use of Command Uplinks, see Section [REFERENCE BELOW].

#### Basic Configuration Data

Table 4.3.18.1-1 provides the data content for the uplink command string which, upon reception by the ACARS system, is passed to the onboard Meteorological Report application for processing to affect alteration of the onboard configuration of the application. The size of the message is dependent upon the number and type of changes made to the configuration but will consist of a 21 character string as a minimum (for example, a Status Report request with no other configuration changes requested would consist of 21 characters only – AWR06190999999999999/). In most instances, the 9 digit is used to indicate when no change to a particular configuration is required. When a change is required, the Data will indicate either the change to be made or that the configuration change is indicated by the command string following the Data and as defined in the referenced table. The Default Values in Table 4.3.19.1-1 define the recommended default configuration. These values are changed by the uplink command message as necessary and become permanent (i.e. are restored upon system intialisation and/or reset) unless otherwise indicated.

[Issues]

1. The Report Activation flag requires a value of 9 = no change?

2. How is a status report activated in previous versions? Surely we need a parameter in the Basic Config. Parameters table to activate it?

[/Issues]

Table 4.3.18.1-1 – Basic Configuration Parameters

| Number of Characters | Data | Description | Default Value | Content |
| --- | --- | --- | --- | --- |
| 1 | A | IMI |  |  |
| 1 | W | IMI |  |  |
| 1 | R | IMI |  |  |
| 2 | 06 | Version number |  |  |
| 1 | 0 or 1 | Configuration Status Report Request See Note 1. | Not applicable | 0 = No request for Configuration Status Report 1 = Request Configuration Status Report after uplink command processing |
| 1 | 0-7 or 9 | Report Activation flag See Note 2. | 7 | 0 = Reporting OFF 1 = Descent Phase ONLY Active 2 = En-route Phase ONLY Active 3 = En-route AND Descent Phases Active 4 = Ascent Phase ONLY Active 5 = Ascent AND Descent Phases Active 6 = Ascent AND En-route Phases Active 7 = ALL Flight Phases Active 9 = No change |
| 1 | 0 or 1 | Permanent Activation Flag | Not applicable | 0 = Report Activation for one flight only 1 = Report Activation is Permanent This Flag applies to the Report Activation flag only and has no effect if the Report Activation flag is set to 9 (No change). |
| 4 | H1H1H2H2 | Inhibit Reporting Between Selected Hours (00-23) UTC, every day. See Note 3. | 0000 | H1H1 = Start of Inhibit Period (00-23) H2H2 = End of Inhibit Period (00-23) 9999 = No change 0000 = Disabled |
| 1 | 0, 1 or 9 | Activation of Reporting in Defined Geographical Boxes See Note 4. | 0 | 0 = Disabled, 1 = Enabled, 9 = No change If Enabled insert configuration parameters from Table 4.3.18.2-1 |
| 1 | 0, 1 or 9 | Activation of Airport Reporting Selection See Note 5 | 0 | 0 = Disabled, 1 = Enabled, 9 = no change If Enabled insert configuration parameters from Table 4.3.18.3-1 |
| 1 | 1 or 9 | Ascent Configuration See Note 6. | Not applicable | 9 = No change 1 = Modify If Modify, insert configuration parameters from Table 4.3.18.5-1. |
| 1 | 1 or 9 | Routine Observations Configuration See Note 7. | Not applicable | 9 = No change 1 = Modify If Enabled, insert configuration parameters from Table 4.3.18.4-1. |
| 1 | 1 or 9 | Descent Configuration See Note 8. | Not applicable | 9 = No change 1 = Modify If Modify, insert configuration parameters from Table 4.3.18.6-1. |
| 1 | 0, 1 or 9 | Routine EDR Reporting See Note 9. | 0 | 9 = No change 0 = Disabled 1 = Enabled |
| 1 | 0,1 or 9 | EDR Event Reporting See Note 10. | 0 | 9 = No change 0 = Disabled 1 = Enabled |
| 1 | 0, 1 or 9 | Optional Parameter Configuration See Note 11. | 0 | 9 = No change 0 = Disabled 1 = Enabled If Enabled, insert required Header Indicator string from Table 5.3.13.6-5. |
| 1 | / | Delimiter |  | End of Table 4.3.18.1-1 (this table) commands |

Notes:

- A Configuration Status Report is requested by setting this switch to the value 1. The Configuration Status Report, if available from the onboard application, is compiled and downlinked after the full command string is processed and according to the specification in 5.3.65. The Status Report consists of the configuration settings held by the onboard application.

- The Report Activation Flag determines the basic Meteorological Report reporting status. The Reporting OFF setting takes priority over all other configuration settings. The Airfield Reporting and Activation of Reporting in Defined Geographical Boxes configurations take priority over Report Activation settings 1-7 only. The Airfield Reporting takes priority over the Activation of Reporting in Defined Geographical Boxes.

- Inhibit Reporting Between Selected Hours, if enabled, allows reporting to be inhibited for a selected (inclusive) period in any consecutive 24-hour period. When disabled, reporting is continuous unless inhibited by subsequent commands. The Inhibit Reporting Between Selected Hours configuration takes priority over all other configurations except the Reporting OFF configuration.

- Activation of Reporting in Defined Geographical Boxes determines whether reporting is enabled or inhibited as defined in Table 4.3.18.2-1. If set to Enable, then the required parameters from Table 4.3.18.2-1 are included in the uplink command and will consist of only the End of Table delimiter if no change to the onboard configuration of Reporting in Defined Geographical Boxes is necessary. This Table allows specific regions to be defined for either enabled or inhibited reporting within the region. When disabled, reports are to be made globally unless inhibited by other configuration settings. See Note 2 for configuration priorities.

- Activation of Airport Reporting Selection determines whether reporting is enabled or inhibited for a list of airports as defined in Table 4.3.18.3-1. If set to Enable, then the required parameters from Table 4.3.18.3-1 are included in the uplink command and will consist of only the End of Table delimiter if no change to the onboard configuration of Airfield Reporting Selection is necessary. This Table allows specific Airfields to be defined for reporting Ascent, Descent or both. When disabled, reports should still be made according to other configuration settings. See Note 2 for configuration priorities.

- If Ascent Configuration is set to Modify, then the parameters from Table 4.3.18.5-1 are included in the uplink command to specify the reporting scheme during the Ascent phase.

- If Routine Observations Configuration is set to Modify, then the parameters from Table 4.3.18.4-1 are included in the uplink command to specify the Routine Observations reporting scheme.

- If Descent Configuration is set to Modify, then the parameters from Table 4.3.18.6-1 are included in the uplink command to specify the reporting scheme during the Descent phase.

- If Routine EDR Reporting is Enabled, then the reporting of Routine Eddy Dissipation Rate (EDR) is activated according to the provisions made in Table 5.3.13.6-5. If the onboard application is unable to report Routine EDR Content will be padded with the solidii character (/).

- If EDR Event Reporting is Enabled and this function is available to the Meteorological Report application, then the reporting of turbulence EDR Event-triggered reporting is activated according to the provisions made in section 5.3.65.

- If Optional Parameter Configuration is Enabled, then the optional parameters required to be reported in the Meteorological Report are configured by inserting the appropriate string according to the Header Indicator in Table 5.3.13.6-5. When the Optional Parameter Configuration has been Enabled, the Optional Parameter Indication in the Data Header in Table 5.3.13.6-2 is altered accordingly. If the onboard application is unable to report the requested Optional Parameter, then the Content will be padded with the solidii character (/).

#### Region Data

#### This table defines uplink configuration settings for reporting in configurable geographical areas when the Activation of Reporting in Defined Geographical Boxes (Table 4.3.18.1-1), is enabled. It allows up to NMNM latitude/longitude boxes that define regions in which profile and enroute observations are either Reported or Inhibited. Where overlap occurs, Inhibited areas take precedence over Reported areas. If no change is required to the existing onboard configuration then the command string will consist of only the End of Table Delimiter (/).

Table 4.3.18.2-1 – Region Data

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 2 | NRNR | Number boxes following | NRNR 00 - NMNM (where NMNM is the maximum configurable geographical boxes). Default = 00 |
| 1 | L1L1 A1L2L2A2 L3 L3L3 B1L4L4 L4B2 | Defines the Lat/Long box | Lat in degrees north (A = N) or south (A = S) Lon in degrees east (B = E) or west (B = W) Convention is L1L1 to L2L2 (N -S) And L3L3L3 to L4L4L4 (W-E). |
| 1 | 0 or 1 | Reported or Inhibited | 0 = Inhibited. 1 = Reported. Inhibited has priority over Reported. |
| Repeat above two rows NRNR-1 times | As above | As above |  |
| 1 | / | Delimiter | End of Table 4.3.18.2-1 data. |

#### Airport Configuration Parameters

#### This table defines uplink configuration settings for reporting on ascent or descent when Activation of Airport Reporting Selection (Table 4.3.18.1-1), is enabled. It allows up to NMNM Airports to be configured for reporting according to the Airport Activation Flag. If no change is required to the existing onboard configuration then the command string will consist of only the End of Table Delimiter (/).

Table 4.3.18.3-1 – Airport Configuration Parameters

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 2 | NANA | Number of Airports following | NANA = 00-NMNM ( where NMNM is the maximum configurable Airports). Default = 00 |
| 4 | AAAA | ICAO Airfield Designator |  |
| 1 | 0 - 3 | Airport Activation Flag | 0 = Ascent ON / Descent ON (Default) 1 = Ascent ON / Descent OFF 2 = Ascent OFF / Descent ON 3 = Ascent OFF/ Descent OFF |
| Repeat above two rows NRNR-1 times | As above | As above |  |
| 1 | / | Delimiter | End of Table 4.3.18.3-1 data |

#### Routine Observations and Wind Reporting Status

#### This table defines uplink settings for Routine Observations configuration and interval of reporting and enables or disables reporting of the maximum wind observation (AOSFRS, 3.3.4) during the enroute flight phase (only). This configuration is relevant only when the corresponding phase of flight is Active based on the Report Activation configuration in Table 4.3.18.1-1

Table 4.3.18.4-1 – Interval and Wind Reporting Status

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 1, 2, 9 | Routine Observations Configuration | 9 = No change 1 = Routine Observations during enroute phase only (Default) 2 = Routine Observations during all phases |
| 2 | mm | Routine Observations Interval (minutes) | 99 = No change Default = 07 Range = 01 – 60 |
| 1 | 0 or 1 | Enable or Disable maximum wind reporting | 9 = No change Default = 1 (enable) Disable = 0 |
| 1 | / | Delimiter | End of Table 4.3.18.4-1 data |

#### Ascent Configuration Parameters

This table is used to configure reporting during the Ascent phase. It is uplinked when the Ascent Configuration flag is set to Modify (See Tables 4.3.18.1-1.).

Table 4.3.18.5-1 – Ascent Configuration Parameters

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Pressure based scheme (0) or Time based scheme (1) | Ascent sampling mode Default = 0 See Note 1 |
| 2 | ss | Ascent Part 1 time intervalsl (seconds) | Time based scheme Default = 06 Range = 03 – 20 |
| 3 | sss | Ascent Part 1 duration (seconds) | Time based scheme Default = 090 Range = 030– 200 |
| 2 | ss | Ascent Part 2 time intervals (seconds) | Time based scheme Default = 20 Range = 20 – 60 |
| 3 | sss | Ascent Total Duration (seconds x 10) | Time based scheme Default = 051 Range = 051 – 111 See Note x |
| 2 | NN | Ascent Part 1 pressure intervals (hPa) | Pressure based scheme Default = 10 Range = 1-20 |
| 2 | NN | Number of observations made during Ascent Part 1 pressure intervals | Pressure based scheme Value = 10 or 20 Default = 10 NOTE: Ascent Part 1 pressure interval x Ascent Part 1 Number of observations must be 100. |
| 2 | NN | Ascent Part 2 pressure intervals (hPa) | Pressure based scheme Default = 50 Range = 20-50 |
| 3 | hhh | Top of climb (x100FT) | Default = 200 Range = 150 – 350 |
| 1 | / | Delimiter | End of Table 4.3.18.5-1 data |

Notes:

- The first field indicates whether the Time or Pressure Based Scheme is selected for the ascent phase. The next 4 fields give the required parameters for the Time Based Scheme. Fields 6 to 8 give the required parameters to define the Pressure Based Scheme. For a full description of the flight phases and reporting schemes, see AOSFRS, 3.4.

- When the Pressure Based Scheme is active, the Routine Observations Interval (Field 1 of Table 4.3.18.4-1) is used during the Ascent phase to ensure  that observations are still made if there is a pause in the Ascent phase. This function is not active if Ascent selection is disabled in Table 4.3.18.1-1.

- The Ascent phase is deemed to be complete and En-route phase commenced when either the Top of Climb has been reached or the Ascent Total Duration has elapsed.

#### Descent Configuration Parameters

This table is used to configure reporting during the Descent phase. It is uplinked when the Modify Descent Configuration field is set to Modify (See Tables 4.3.18.1-1.).

When the Pressure Based Scheme is active, the Routine Observations Interval (Field 2 of Table 4.3.18.4-1) is used during the Descent phase to ensure that observations are still made if there is a pause in the Descent phase. This function is not active if Descent selection is disabled in Table 4.3.18.1-1.

Table 4.3.18.6-1 – Descent Configuration Parameters

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Pressure based scheme (0) or Time based scheme (1) | Descent sampling mode Default = 0 See note 1 |
| 3 | sss | Descent Part 1 and 2 time interval (seconds) | Time based scheme Default = 040 Range = 010 – 300 |
| 2 | NN | Descent Part 1 pressure interval (hPa) | Pressure based scheme Value = 25 or 50 Default = 50 (from top of Descent to final 100hPa) |
| 2 | NN | Descent Part 2 pressure interval (hPa) | Pressure based scheme Value = 05 or 10 Default = 10 (for the final 100hPa) |
| 3 | hhh | Top of descent (x 100FT) | Default = 200 Range = 150 – 350 See note 3 |
| 1 | / | Delimiter | End of Table 4.3.18.7-1 data |

Notes:

- The first field indicates whether the Time or Pressure Based Scheme is selected for the descent phase. The next field gives the required time interval for the Time Based Scheme. Field 3 gives the required interval for the Pressure Based Scheme.

- The Descent phase is deemed to have commenced when the pressure altitude falls below the Top of Descent.

# 5

## 3

## 3

## 3

### 12

### 12

### 12

### 12

### 12

### 12

### 12

### 12

### 12

### 12

### 12

### 12

### Meteorological Report – Label or MFI H2

Sub-systems onboard the aircraft may be programmed to provide automatic downlinks of meteorological data at pre-determined altitudes, timed intervals, or pressure levels as specified by the user. These Meteorological Report downlink messages should contain the Label (or MFI) characters H2.

There are four versions of Meteorological Report defined. Version 1 provides a unified format for all flight phases. Version 2 divides the report data and associated data sampling times into three flight regimes. Version 2 divides the report data and associated data sampling times into three flight regimes. Version 3 is similar to Version 2 but provides timing interval information at the beginning of the message. Version 4 contains the ability to report at specified pressure intervals, controlling functions for system optimization and remote targeting of data, and a suggested algorithm for compressing the downlinked report. These should be used in conjunction with the appropriate Meteorological Report Command Uplink in Sections 4.3.9 and 4.3.10. Version 4 also is associated with the Meteorological Report Configuration Downlink in Section 5.3.54.

Special Meteorological Note

For data propriety and security reasons, the airline may require the receiving Met Office to ensure that all identification marks, such as carrier code/flight number and aircraft registration are removed from the AMDAR message before it is distributed for operational use and to the WMO. This can be done either by the airline host, the service provider or the receiving Met office.

#### Meteorological Report, Version 1 – MFI or Label H2

Table 5.3.13.1-1 – Meteorological Reports, Version 1

| Number of Characters | Character Content | Notes |
| --- | --- | --- |
| 10 | Standard Message Header | Refer to Section 3.4 of ARINC Specification 618 |
| 2 | Version Number (01) |  |
| 7 | Flight Identifier | See Note 1 |
| 7 | Registration Number |  |
| 36 | Data Sample 1 | See Note 6 |
| 36 | Data Sample 2 |  |
| . | . |  |
| . | . |  |
| 36 | Data Sample 5 |  |

Notes:

- The Flight Identifier is made up from the 3 letter ICAO Airline code and the 4 digit (or) alpha character Flight Number.

- The format of latitude and longitude are with North/South (abbreviated N/S) and East/West (abbreviated E/W) following the values of latitude and longitude and a resolution in degrees and minutes.

For example:	4811N12030W or 3530S14845E.

Latitude		Longitude

DDMM (N/S)		DDDMM (E/W)

4811N			02030W

3530S			14845E

- The character F followed by 3 numerals. For example:  F350.

- The range of Static Air Temperature is from -99 to +99 Celsius. The format used is 4 characters. The characters MS are used to indicate a negative value and PS are used to indicate a positive value followed by temperature in degrees Celsius (2 numerals). For example:  MS23 or PS24.

- If the roll angle exceeds 5 degrees, then the characters RA are used, otherwise the field is filled with 2 space characters.

- Up to 5 samples can be included in a report. Each data sample will contain the following data.

| Number of Characters | Data Sample | Notes |
| --- | --- | --- |
| 5 | Latitude | See Note 2 |
| 6 | Longitude | See Note 2 |
| 6 | Date/Time (UTC) of Observation | Format: ddhhmm |
| 4 | Flight Level | See Note 3 |
| 4 | Static Air Temperature (Celsius) | See Note 4 |
| 3 | Wind Direction (degrees) | Range: 000-359 |
| 3 | Wind Speed (knots) | Range: 000-999 |
| 2 | Roll Angle Flag | See Note 5 |
| 3 | Humidity | Range: 0 to 100 percent |

#### Meteorological Report, Version 2 – MFI or Label H2

There are three flight phases with regard to meteorological data gathering and reporting. The expected sequence and timing of meteorological data acquisition the timing of meteorological reports are enumerated below.

ASCENT REPORTS

At the end of the sampling period a single Ascent report (message) is prepared and sent consisting of:

Initial	Meteorological data measured at the time of the OFF event (take-off).

Series #1	Following the Initial sample, Series #1 data measurement samples are accumulated at intervals from 3 to 20 seconds (modifiable via uplink; default to 6 seconds) until the limit of 30 to 200 seconds (modifiable via uplink, default to 90 seconds) after OFF event. A delimiter (Slash </>) is used to designate the conclusion of Series #1 data.

Series #2	Series #2 data samples are accumulated from the expiration of the Series #1 data acquisition period. Series #2 data samples are taken at intervals from 20 to 60 seconds (modifiable via uplink; default to 20 seconds) until 510-1110 seconds (modifiable via uplink, default to 510 seconds).

ENROUTE REPORTS

Series #1	One Enroute report is sent consisting of six consecutive data measurement samples. The interval of data measurement is from 1 to 60 minutes; the default interval is 3 minutes. Enroute data measurements should begin at the conclusion of data sampling for the Ascent report and terminate when Descent report measurements commence.

Although discouraged, the Ascent and Descent reports may be inhibited and only the Enroute report generated. This option can be selected via data link uplink. In this case, the first Enroute data sample should be taken at the OFF event and data accumulation should continue at a uniform interval until the ON event unless the interval is modified by an uplink message.

DESCENT REPORTS

Series #1	Normally more than one Descent report will be sent consisting of ten data measurement samples taken over a period of approximately 10 minutes. Descent data measurements begin at 18,000 to 30,000 feet (top of descent). The point of initiation of Descent data measurement sampling is modifiable via uplink (default to 25,000 feet). The interval of Descent data measurement samples is 20 to 300 seconds, modifiable via uplink (default to 60 seconds). Descent reports for downlink will be assembled after every 10 samples and sent as one message. The final report is sent at the ON event (when the wheels touch down).

The format of the Meteorological Report Messages should be as follows:

Table 5.3.13.2-1 – Ascent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  |  |
| 11-12 | 2 | Version Number | 02 |  |
| 13 | 1 | Type of Met Format | A, E, D | 2 |
| 14-15 | 2 | Date Message Assembled | dd |  |
| 16-19 | 4 | Time Message Assembled | hhmm |  |
| 20-23 | 4 | Departure Station | xxxx |  |
| 24-27 | 4 | Destination Station | xxxx |  |
| Initial report: |
|  |  | Latitude | ADDMM | 3 |
|  |  | Longitude | ADDDMMT | 4 |
|  | 2 | Date of Observation |  | dd |
|  |  | Time of Observation | hhmm | 5 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  |  | WV Mixing Ratio | nnnQ | 9 |
| Series #1 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  |  | WV Mixing Ratio | nnnQ | 9 |
| Delimiter | 1 | Slash </> | / | Indicates end of Series #1 data/ beginning of Series #2 data |
| Series #2 |
|  |  | Latitude | ADDMM | 3 |
|  |  | Longitude | ADDDMM | 4 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  |  | WV Mixing Ratio | nnnQ | 9 |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.2-2 – Enroute Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 02 |  |
| 13 | 1 | Type of Met Format | A, E, D | 2 |
| 14-15 | 2 | Date of Message Assembly | dd |  |
| 16-19 | 4 | Departure Station | xxxx |  |
| 20-23 | 4 | Destination Station | xxxx |  |
| Series #1 |
|  |  | Latitude | ADDMM | 3 |
|  |  | Longitude | ADDDMM | 4 |
|  |  | Time of Observation | hhmm | 5 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  |  | WV Mixing Ratio | nnnQ | 9 |
|  | 5 | Turbulence | Cnnnn | 10 |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.2-3 – Descent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 02 |  |
| 13 | 1 | Type of Met Format | A, E, D | 2 |
| 14-15 | 2 | Date of Message Assembly | dd |  |
| 16-19 | 4 | Departure Station | xxxx |  |
| 20-23 | 4 | Destination Station | xxxx |  |
| Series #1 |
|  |  | Latitude | ADDMM | 3 |
|  |  | Longitude | ADDDMM | 4 |
|  |  | Time of Observation | hhmm | 5 |
|  | 4 | Pressure Altitude | nnnn | 4 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  |  | WV Mixing Ratio | nnnQ | 9 |
|  | 4 | Turbulence | nnnn | 11 |
|  |  | End of Text | <ETX> |  |

Notes:

- See ARINC Specification 618.

- (A = Ascent, E = Enroute, D = Descent). Each type has the same order of relevant meteorological information (latitude, longitude, time, pressure (or altitude), wind direction, wind speed, roll angle flag, water vapor, turbulence) but actual information and frequency of reporting levels varies with type.

- A = N (North) or S (South), D = degrees, M = minutes, 
T = tenths of minutes.

- A = E (East) or W (West), D = degrees, M = minutes, 
T = tenths of minutes.

- h = hours, m = minutes

- Resolution in tens of feet

- The value of a is encoded either P (plus) or M (minus), units are tens, ones, tenths of a degree centigrade

- If Roll angle exceeds 5 degrees set to [B], otherwise set to [G]

- nnn = n1 n2 n3 which implies n1 . n2 x 10-n3 ; e.g., 123 = 
1.2x10-3. Q is a quality control character to be determined after contract award for WVSS.

- C is a code where if C = Z then no turbulence above threshold and no data (characters) follow; if C = Q then some data problem exists and no data (characters) follow; if C = an integer n = 0 to 9, then 4n hexadecimal characters follow where the first two characters in a group of four are the average values of the turbulence metric and the last two characters are the peak values of the turbulence metric over a one-minute period.

- nnnn: First two hexadecimal characters represent the average turbulence metric. The last two hexadecimal characters represent the peak turbulence metric.

#### Meteorological Report, Version 3 – MFI or Label H2

Ascent data measurements continue until top of climb, 18,000 to 30,000 feet. The point of institution of Enroute data measurement samples is modifiable via uplink (default to 25,000 feet).

The format of the Meteorological Report Messages should be as follows:

Table 5.3.13.3-1 – Ascent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  | 1 |
| 11-12 | 2 | Version Number | 03 |  |
| 13 | 1 | Type of Met Format | A, E, D | 2 |
| 14-15 | 2 | Date of Message Assembly | dd |  |
| 16-19 | 4 | Time of Message Assembly | hhmm |  |
| 20-23 | 4 | Departure Station | xxxx |  |
| 24-27 | 4 | Destination Station | xxxx |  |
| 28-29 | 2 | Series #1 time interval | ss | seconds |
| 30-31 | 2 | Series #2 time interval | ss | seconds |
| Initial report: |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 2 | Date of Observation | dd |  |
|  | 4 | Time of Observation | hhmm | 5 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 4 | WV Mixing Ratio | nnnQ | 9 |
| Series #1 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 4 | WV Mixing Ratio | nnnQ | 9 |
| Delimiter | 1 | Slash </> | / | Indicates end of Series #1 data/ beginning of Series #2 data |
| Series #2 |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 4 | WV Mixing Ratio | nnnQ | 9 |
|  |  | End of Text | <ETX> |  |

Note:	The Version 3 Ascent Report will be followed by Version 2 Enroute and Descent Reports. Refer to Tables 5.3.13.2-2 and Table 5.3.13.2-3. Refer to Section 5.3.13.2 for Notes to this Table.

#### Meteorological Report, Version 4 – MFI or Label H2

There are three flight phases with regard to meteorological data gathering and reporting. The expected sequence and timing of meteorological data acquisition and the timing of meteorological reports are enumerated below. A suggested algorithm to minimize the number of transmitted characters by compressing the downlink report is given in Appendix H.

##### Ascent Reports

At the end of the sampling period, a single Ascent report (message) is prepared and sent consisting of:

###### Initial

Meteorological data measured at the time of the OFF event (take-off).

###### Series #1

Following the Initial sample, Series #1 data measurement samples are accumulated at intervals from 3 to 20 seconds (modifiable via uplink; default to 6 seconds) until the duration limit of 30 to 200 seconds (modifiable via uplink, default to 90 seconds) after OFF event.

Alternatively measurement samples can be accumulated at target heights according to pre-set, tabulated values corresponding to target pressure levels. If this pressure-based method of sampling is employed, ascent sampling commences with the Series #2 format (i.e., Series #1 is skipped). A delimiter (Slash </>) is used to designate the conclusion of Series #1 data.

###### Series #2

Series #2 data samples are accumulated from the expiration of the Series #1 data acquisition period. Series #2 data samples are taken at intervals from 20 to 60 seconds (modifiable via uplink; default to 20 seconds) until 510-1110 seconds from the OFF event (modifiable via uplink, default to 510 seconds).

Alternatively, if a pressure-based ascent sampling scheme with additional default time interval option (selectable by uplink) is employed, sampling commences using the Series #2 format immediately after the initial report. Sampling commences at 10hPa intervals (modifiable to 5hPa by uplink; Table 5.3.13.4-4 reference). The first sample is the first target height above the pressure altitude taken for the initial sample. 10 samples are taken if 10hPa intervals are selected. If 5hPa intervals are selected (by uplink command), 20 samples are taken. Thereafter, samples are taken at target altitudes corresponding to 50hPa intervals (modifiable to 25hPa by uplink). The first sample is taken at the target height corresponding to the 50hPa (or 25hPa if selected) level above the final 10hPa (or 5hPa if selected) sample. The final sample is taken at the pre-set top of ascent (modifiable via uplink between 15,000 ft and 25,000 ft; default 20,000 ft.). An additional mode is included (de-selectable through uplink command) that enables default timed samples to be taken if a sample has not been taken for a pre-defined time period. The default time interval is the same as the enroute time interval (modifiable by uplink command). This scheme ensures data are still produced if there is a pause during the ascent phase for a short period of level flight. Samples continue to be treated as ascent data and are included in the ascent report. Pressure-based ascent sampling resumes once the next target altitude is reached.

##### Enroute Reports

###### Series #1

Only time-based sampling is used. One Enroute report is sent consisting of six consecutive data measurement samples. The interval of data measurement is from 1 to 60 minutes; the default interval is 7 minutes. Enroute data measurements should begin at the conclusion of data sampling for the Ascent report and terminate when Descent report measurements commence. If pressure-based sampling is used during ascent but the pre-set top of ascent is not reached, the default timing mode (if selected) will automatically become the enroute sampling mode. The Maximum Wind option (de-selectable via uplink command), provides an additional data measurement sample that is taken at the time of occurrence of the peak wind measurement. The sample is included in the enroute report using the maximum wind indicator.

Although discouraged, the Ascent and Descent reports may be inhibited and only the Enroute report generated. This option can be selected via data link uplink. In this case, the first Enroute data sample should be taken at the OFF event and data accumulation should continue at a uniform interval until the ON event unless the interval is modified by an uplink message.

Default settings for the upper limit of Ascent Series 2 (time or height) data and the commencement of Descent data must be chosen to match operational profiles of the aircraft, i.e., they must be set lower than the expected cruise altitude.

###### Maximum Wind Report

This facility is required to aid in locating jet stream cores and is applied in level flight phase only. The highest wind speed measured between a sequential pair of routine observations is labeled maximum wind. Maximum wind is derived according to these criteria:

Aircraft is in level flight, above 600hPa (13,800 ft.)

Maximum wind exceeds 60k.

Maximum wind exceeds by at least 10kt the value of wind speed measured at the previous routine observation.

Maximum wind exceeds by at least 10kt the value of wind speed measured at the subsequent routine observation.

##### Descent Reports

###### Series #1

Normally more than one descent report will be sent consisting of ten data measurement samples taken over a period of approximately 6 minutes. Sampling may be triggered either by time or pressure based schemes. Descent data measurements begin at 15,000 to 25,000 feet (top of descent). The point of initiation of descent data measurement sampling is modifiable via uplink (default to 20,000 feet). The interval of descent data measurement samples is 20 to 300 seconds, modifiable via uplink (default to 40 seconds). A descent report for downlink will be assembled after every 10 samples and sent as one message. For time-based sampling, Series #1 reporting continues from top of descent to the ON event (at wheels touch down) when the final report is sent. Series #2 reporting is not used.

Whichever interval (pressure or time) is designated for descent profiling, the descent flight phase will start on passing through the pre-set value for the top of descent except in the event that the enroute altitude is already lower than top of descent. In this case, 5.3.13.4.3.1 the descent phase shall commence on descending through two consecutive 25hPa target altitudes taken from Table 5.3.13.4-4 reference, List 1. For example, if cruise level is 24,000 ft and top of descent is set to 25,000 ft, descent sampling shall commence at target level 82 (22,160 ft).

Alternatively, a pressure-based descent sampling scheme with additional time interval option (selectable through uplink) may be employed. The ascent and descent phase profiles are designed to be similar with higher density sampling during the lowest 100hPa layer and lesser density sampling above this layer.

Once the descent phase has been detected, Series #1 reporting commences initially at intervals corresponding to 50hPa levels (modifiable to 25hPa by uplink) and continues until the 700hPa (target height 71, 9882 ft) level is reached. All Series #1 samples from top of descent to 700hPa including the 700hPa sample are transmitted in one report. If the pre-set top of descent is lower than the cruise (enroute reporting phase) altitude, descent phase sampling shall commence when the aircraft descends through the first 50hPa or 25hPa (as appropriate) target height encountered below top of descent. For example if top of descent is set to 20,000 ft, and the selected pressure target list points to Table 5.3.13.4-4 reference, List 2, descent sampling starts at height 79 (18,289 ft). Thereafter sampling continues at 50hPa target intervals until level 71 is reached.

An additional mode is included (de-selectable through uplink command) that enables default timed samples to be taken if a sample has not been taken for a pre-defined time period. The default time interval is the same as the enroute time interval (modifiable by uplink command). This scheme ensures sampling continues if there is a pause during the descent phase for a period of level flight. Samples continue to be treated as descent data and are included in the descent report. Pressure-based descent sampling resumes once the next target altitude is reached.

In the event that the enroute altitude is already lower than top of descent and the descent phase has been detected, the first sample shall be taken at the first target height encountered i.e., the second of the two trigger levels if List 1 is used and the first available trigger at or immediately following the second 25hPa value if List 2 is used. For example, if cruise level is 24,000 ft and top of descent is set to 25,000 ft, and List 2 is selected, descent sampling shall commence at target level 41 (20,812 ft) and continue at 50hPa intervals. In this case the sample levels are 23,574 ft and 22,160 ft, and 20,812 ft is the first available List 2 sample altitude following the decision that descent is under way. If the selected pressure target list had pointed to List 1, descent sampling would have started at target height 82 and continued at 25hPa intervals. Sampling then continues as described above until Level 71 (700hPa) is reached.

###### Series #2

On passing through 700hPa (target level 71 at 9882 ft), data sampling is increased to 10hPa intervals and stored until touchdown. On touchdown, the most recent (lowest) 10 samples at 10hPa intervals above touchdown altitude are used together with integer multiples of 50hPa above this 100hPa layer to Level 61. The remaining 10hPa samples are discarded. All Series #2 samples are sent in one report (in more than one message if necessary) containing samples at 50hPa intervals down to 100hPa above touchdown altitude followed by 10, 10hPa samples for the lowest portion of the profile. The format of the Series #1 and Series #2 reports is the same and no delimiter is required to separate them because the samples are transmitted in separate messages. If the selected pressure target list had pointed to List 1, on passing through 700hPa (target height 71) descent sampling would be increased to 5hPa intervals (target heights 70, 69, 68, 67…) until touchdown. On touchdown, the most recent (lowest) 20 samples at 5hPa intervals above touchdown altitude are used together with integer multiples of 25hPa above this 100hPa layer to Level 66. The remaining 5hPa samples are discarded. The same additional default time triggering process is included (de-selectable via uplink command) as in the Series #1 part of the profile, i.e., if a sample has not been taken for a pre-defined time period, a reduced rate of sampling continues during pauses in the descent phase.

##### Data Smoothing

It is desirable to smooth individual sensor data samples to standardize measurements, improve representativeness of data according to sampling interval, and reduce quantizing errors and random noise. Ideally such filtering would be varied with all changes in sampling interval which itself varies with application. In practice two smoothing rates are recommended, one for profile use (ascent/descent) and one for cruise (enroute or level flight).

For profile measurement, 10 second averaging is recommended. This equates roughly to 50m in the vertical plane and 1km in the horizontal plane. For cruise level sampling, 30 second averaging is recommended equating roughly to 8km in the horizontal plane.

The suggested smoothing times are given as the arithmetic averages of raw data measurements (for example the average of 10 one-second interval temperature measurements from the air data computer). An efficient, simple to code alternative is a continuous exponential smoothing function as given below:

If yn is the nth raw data sample, t the raw data update interval, T the averaging time and Yn the corresponding smoothed value, then:

Yn = 3t(yn – Yn-1)/ T + Yn-1

##### Optimization

Additional automated functionality is included to provide a highly flexible optimized data collection system. Software variables, selectable through uplink command, control the time and location where data sampling is required. The system operates globally. Details are provided in Sections 4.3.9 and 4.3.10 – MeteorologicalReport Command Uplink.

The format of the Meteorological Report Messages should be as follows:

Table 5.3.13.4-1 – Ascent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  | 1 |
| 11-12 | 2 | Version Number | 04 |  |
| 13 | 1 | Type of Met Format | A or C or Q or R | 2 |
| 14 | 1 | Altitude Pressure Reference | P or B | 11 |
| 15-16 | 2 | Date Message Assembled | dd |  |
| 17-20 | 4 | Time Message Assembled | hhmm |  |
| 21-24 | 4 | Departure Station | xxxx |  |
| 25-28 | 4 | Destination Station | xxxx |  |
| Initial report: |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 2 | Date of Observation | dd |  |
|  | 4 | Time of Observation | hhmm | 5 |
|  | 2 | Series #1 time interval (seconds) | ss | 11 |
|  | 2 | Series #2 time interval (seconds) | ss | 11 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 4 | WV/Humidity | nnnQ | 9 |
| Series #1 |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 4 | WV/Humidity | nnnQ | 9 |
| Delimiter | 1 | Slash </> | / Indicates end of Series #1data/ beginning ofSeries #2 data |  |
| Series #2 |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 4 | Time of Observation | hhmm | 5 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 4 | WV/Humidity | nnnQ | 9 |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.4-2 – Enroute Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 04 |  |
| 13 | 1 | Type of Met Format | E or S | 2 |
| 14 | 1 | Altitude Pressure Reference | P or B | 11 |
| 15-16 | 2 | Date of Message Assembly | dd |  |
| 17-20 | 4 | Departure Station | xxxx |  |
| 21-24 | 4 | Destination Station | xxxx |  |
| Sample Format (up to 6 samples) |  |  |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 4 | Time of Observation | hhmm | 5 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag/Max Wind | n | 8 |
|  | 4 | WV/Humidity | nnnQ | 9 |
|  | 2+ | variable blocks of 4 |  |  |
|  |  | Turbulence | CCnnnn…nnnn | 10 |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.4-3 – Descent Weather Report Format

| Series #1 and Series #2 |
| --- |
| Character Number | # of Char | Character Content | Format | Notes |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 04 |  |
| 13 | 1 | Type of Met Format | D or P or U or V | 2 |
| 14 | 1 | Altitude Pressure Reference | P or B | 11 |
| 15-16 | 2 | Date of Message Assembly | dd |  |
| 17-20 | 4 | Departure Station | xxxx |  |
| 21-24 | 4 | Destination Station | xxxx |  |
|  | 6 | Latitude | ADDMMT | 3 |
|  | 7 | Longitude | ADDDMMT | 4 |
|  | 4 | Time of Observation | hhmm | 5 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 4 | WV/Humidity | nnnQ | 9 |
|  | 2+ | variable blocks of 4 |  |  |
|  |  | Turbulence | CCnnnn…nnnn | 10 |
|  |  | End of Text | <ETX> |  |

Notes:

- See ARINC Specification 618.

- A/C = Ascent, E = Enroute, D/P = Descent). Each type has the same order of relevant meteorological information (latitude, longitude, time, pressure (or altitude), wind direction, wind speed, roll angle flag, water vapor, turbulence) but actual information and frequency of reporting levels varies with type. Codes A and D indicate samples are selected by time intervals only. Codes C and P indicate samples are selected by target pressure levels in Ascent (C) and Descent (P). See also Notes 6 and 8. Enroute is coded E. If required by uplink command, maximum wind can be reported during Enroute (E) phase (see Note 8 for max. wind flag). If downlink data compression is used, characters A, C, E, D, P are replaced respectively by Q, R, S, U, V.

| Level | Ascent | Enroute | Descent |
| --- | --- | --- | --- |
| Selection | Normal | Compressed | Normal | Compressed | Normal | Compressed |
| Time | A | Q | E | S | D | U |
| Pressure | C | R |  |  | P | V |

- A = N (North) or S (South), D = degrees, M = minutes, 
T = tenths of minutes

- A = E (East) or W (West), D = degrees, M = minutes, 
T = tenths of minutes

- h  hours, m = minutes

- Resolution in tens of feet. If negative, first character is M. If positive, first character is part of altitude value.

- The value of a is encoded either P (plus) or M (minus), units are tens, ones, tenths of a degree Celcius.

- Steady flight means roll angle less than or equal to 5o, or both roll and pitch angles less than or equal to 3o.

Unsteady flight means roll angle greater than 5o,or both roll and pitch angles greater than 3o.

For all phases of flight (Format A, Q, C, R, E, S, D, U, P and V) except maximum wind reports, set steady flight to G; otherwise set Unsteady to B. For maximum wind event, set Steady to W; otherwise set unsteady to U.

- Water Vapor/Humidity is measured and reported either as mixing ratio or relative humidity, depending on the type of sensor employed. Mixing Ratio is reported as nnn = n1n2n3which implies a mixing ratio of n1n2 x 10(-1 - n3) kg/kg; e.g., 123 = 12 x 10(-1 - 3) = 12 x 10-4 kg/kg.

Q is a quality control character to be determined after contract award for WVSS.

Relative Humidity is reported as nnn where the range of nnn is between 000 and 100 per cent.

In this case, Q is the Humidity indicator U.

- CC is a code where if CC = ZZ then no turbulence above threshold and no data (characters) follow;

if CC = QQ then some data problem exists and no data (characters) follow;

if CC= two integers nn where nn = 00 to 99, then nn multiples of 4 hexadecimal characters follow where the first two characters in a group of four are the average values of the turbulence metric and the last two characters are the peak values of the turbulence metric over a one-minute period. nn is the reporting interval in minutes between samples during enroute and descent phases of flight. If pressure-based sampling is invoked, nn can vary substantially during the descent phase. Note that the case where nn=00 occurs during descent and indicates a reporting interval of less than one minute where insufficient turbulence data samples have been taken since the previous sample and no data (characters) follow.

Each of the two character pairs 00 to FF are the hexadecimal representation of decimal values 0-255 of the turbulence metric Eddy Dissipation Rate (EDR) (m2/3s-1) scaled by a factor of 100, i.e., edr values of 0.00 to 2.55.

- For pressure-based observations, insert spaces for ss.

P = PALT (Pressure Altitude in ICAO Standard Atmosphere)

B = BALT (Barometric Altitude in QNH adjusted atmosphere)

If BALT is reported, conversion to the Pressure Altitude (PALT) scale will be necessary in ground processing using runway or area QNH at the time of the observation. This is essential before data can be used or exchanged. If both PALT and BALT are available, PALT is preferred.

Table G-10 within Appendix G provides the preset target heights based on pressure level selection. An explanation of its derivation and use in accordance with the definition of the ICAO Standard Atmosphere is also provided.

#### Meteorological Report, Version 5 – MFI or Label H2

Meteorological Report, Version 5 is an update and extension of Meteorological Report, Version 4. Therefore, where appropriate and where the two specifications are identical, specification of Version 5 is made through reference to Section 5.3.13.4.

Note that the Uplink Control Programming Notes For Version 4 Onboard Software, provided as Appendix G, is still applicable to Version 5; however, the changes made as outlined for Version 5 need to be taken into consideration, particularly in relation to the changes that affect Appendix G Tables G-1, G-5, G-7 and G-10.

Also note that the compression technique for Version 4 as specified in Appendix H, Meteorological Report Compression, is also applicable to the downlink messages for Version 5. The compression formats for Version 5 have been defined within Appendix H, Section H-6.

Meteorological Report, Version 5 incorporates the following additional functionality to Version 4:

- For the Ascent Data, the Series 1 duration (seconds), the allowable maximum range has been extended from 200 to 600 seconds and the Top of Climb allowable maximum range from 250 to 350 (ftx100).

- For the Descent Data, the Descent Interval allowable minimum range has been extended from 20 to 10 seconds and the Top of Descent allowable maximum range has been extended from 250 to 350 (ftx100).

- The Turbulence parameter has been added to both series of the Ascent Report.

- The data width of the turbulence parameter, Eddy Dissipation Rate (EDR), has been extended from 4 characters to 8 characters.

- The Time Message Assembled parameters in all reports have been extended to a resolution of seconds

- The resolution of the Time of Observation parameter has been increased from minutes to seconds.

- The resolution of reporting of Latitude and Longitude has been increased from tenths of minutes to 1 second for all reports in all flight phases.

- Global Navigation Satellite System (GNSS) Altitude has been added as a parameter to be reported in all flight phases.

- The resolution of the Water Vapor (WV) /Humidity parameter has been increased.

- The parameter Icing has been added to report the status of ice accretion within the Meteorological Report.

- The parameters, True Airspeed, True Heading, De-icing and Aircraft Configuration have been added to be optionally reportedwithin two parameter groupings to facilitate enhanced quality control of other meteorological parameters.

- The use of the Roll Angle Flag has been modified to provide an alternative mode in which the aircraft roll angle can be reported as lying within a series of range bins.

##### Ascent Reports

The series of Ascent Reports are specified identically as per Section 5.3.13.4.1. However, the updated format for Ascent Reports is specified in Section 5.3.13.5.5 and Table 5.3.13.5-1.

##### Enroute Reports

The series of Enroute Reports are specified identically as per Section 5.3.13.4.2. However, the updated format for Enroute Reports is specified in Section 5.3.13.5.5 and Table 5.3.13.5-2.

##### Descent Reports

Descent Reports are specified identically as per Section 5.3.13.4.3. However, the updated format for Descent Reports is specified in Section 5.3.13.5.5 and Table 5.3.13.5-3.

##### Data Smoothing

See Section 5.3.13.4.4.

##### Ascent, Enroute and Descent Weather Report Formats

The format of the Meteorological Report Messages should be as follows:

Table 5.3.13.5-1 – Ascent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  | 1 |
| 11-12 | 2 | Version Number | 05 |  |
| 13 | 1 | Type of Met Format | A or C or Q or R | 2 |
| 14 | 1 | Altitude Pressure Reference | P or B | 11 |
| 15-16 | 2 | Date Message Assembled | dd |  |
| 17-22 | 6 | Time Message Assembled | hhmmss |  |
| 23-26 | 4 | Departure Station | xxxx |  |
| 27-30 | 4 | Destination Station | xxxx |  |
| 31 | 1 | Parameter Configuration | n |  |
| Initial report: |
|  | 7 | Latitude | ADDMMSS | 3 |
|  | 8 | Longitude | ADDDMMSS | 4 |
|  | 2 | Date of Observation | dd |  |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 2 | Series #1 time interval (seconds) | ss | 11 |
|  | 2 | Series #2 time interval (seconds) | ss | 11 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | GNSS Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 6 | WV/Humidity | nnnnnQ | 9 |
|  | 1 | Icing | n | 14 |
| Series #1 |
|  | 7 | Latitude | ADDMMSS | 3 |
|  | 8 | Longitude | ADDDMMSS | 4 |
|  | 6 | Time of Observation | hhmmss |  |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | GNSS Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 6 | WV/Humidity | nnnnnQ | 9 |
|  | 1 | Icing | n | 14 |
|  | 1 or 9 | Turbulence | C or Cnnnnnnnn | 10 |
|  | 3 | True airspeed | nnn | 12 |
|  | 4 | True Heading | nnnn |  |
|  | 1 | De-icing | n | 13 |
|  | 2 | Aircraft Configuration | nn |  |
| Delimiter | 1 | Slash </> | / Indicates end of Series #1data/ beginning ofSeries #2 data |  |
| Series #2 |
|  | 7 | Latitude | ADDMMSS | 3 |
|  | 8 | Longitude | ADDDMMSS | 4 |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | GNSS Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 6 | WV/Humidity | nnnnnQ | 9 |
|  | 1 | Icing | n | 14 |
|  | 1 or 9 | Turbulence | C or Cnnnnnnnn | 10 |
|  | 3 | True airspeed (knots) | nnn | 12 |
|  | 4 | True Heading | nnnn |  |
|  | 1 | De-icing | n | 13 |
|  | 2 | Aircraft Configuration | nn |  |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.5-2 – Enroute Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 05 |  |
| 13 | 1 | Type of Met Format | E or S | 2 |
| 14 | 1 | Altitude Pressure Reference | P or B | 11 |
| 15-16 | 2 | Date Message Assembled | dd |  |
| 17-22 | 6 | Time Message Assembled | hhmmss |  |
| 23-26 | 4 | Departure Station | xxxx |  |
| 27-30 | 4 | Destination Station | xxxx |  |
| 31 | 1 | Parameter Configuration | n |  |
| Sample Format (up to 6 samples) |  |  |
|  | 7 | Latitude | ADDMMSS | 3 |
|  | 8 | Longitude | ADDDMMSS | 4 |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | GNSS Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 6 | WV/Humidity | nnnnnQ | 9 |
|  | 1 | Icing | n | 14 |
|  | 1 or 9 | Turbulence | C or Cnnnnnnnn | 10 |
|  | 3 | True airspeed | nnn | 12 |
|  | 4 | True Heading | nnnn | 12 |
|  | 1 | De-icing | n | 13 |
|  | 2 | Aircraft Configuration | nn | 13 |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.5-3 – Descent Weather Report Format

| Series #1 and Series #2 |
| --- |
| Character Number | # of Char | Character Content | Format | Notes |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 05 |  |
| 13 | 1 | Type of Met Format | D or P or U or V | 2 |
| 14 | 1 | Altitude Pressure Reference | P or B | 11 |
| 15-16 | 2 | Date Message Assembled | dd |  |
| 17-22 | 6 | Time Message Assembled | hhmmss |  |
| 23-26 | 4 | Departure Station | xxxx |  |
| 27-30 | 4 | Destination Station | xxxx |  |
| 31 | 1 | Parameter Configuration | n |  |
|  | 7 | Latitude | ADDMMSS | 3 |
|  | 8 | Longitude | ADDDMMSS | 4 |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 4 | Altitude | nnnn | 6 |
|  | 4 | GNSS Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction (Degrees true) | nnn |  |
|  | 3 | Wind Speed (Knots) | nnn |  |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 1 | Icing | n | 14 |
|  | 6 | WV/Humidity | nnnnnQ | 9 |
|  | 1 or 9 | Turbulence | C or Cnnnnnnnn | 10 |
|  | 3 | True airspeed | nnn | 12 |
|  | 4 | True Heading | nnnn | 12 |
|  | 1 | De-icing | n | 13 |
|  | 2 | Aircraft Configuration | nn | 13 |
|  |  | End of Text | <ETX> |  |

Notes:

- See ARINC Specification 618.

- A/C = Ascent, E = Enroute, D/P = Descent). Each type has the same order of relevant meteorological information (latitude, longitude, time, pressure (or altitude), wind direction, wind speed, roll angle flag, water vapor, turbulence) but actual information and frequency of reporting levels varies with type. Codes A and D indicate samples are selected by time intervals only. Codes C and P indicate samples are selected by target pressure levels in Ascent (C) and Descent (P). See also Notes 6 and 8. Enroute is coded E. If required by uplink command, maximum wind can be reported during Enroute (E) phase (see Note 8 for max. wind flag). If downlink data compression is used, characters A, C, E, D, P are replaced respectively by Q, R, S, U, V.

| Level | Ascent | Enroute | Descent |
| --- | --- | --- | --- |
| Selection | Normal | Compressed | Normal | Compressed | Normal | Compressed |
| Time | A | Q | E | S | D | U |
| Pressure | C | R |  |  | P | V |

- A = N (North) or S (South), D = degrees, M = minutes, 
S = seconds

- A = E (East) or W (West), D = degrees, M = minutes, 
S = seconds

- h = hours, m = minutes, s = seconds

- Altitude and GNSS (Global Navigations Satellite System) Altitude are reported with a resolution in tens of feet. If negative, first character is M. If positive, first character is part of altitude value.

- The value of a is encoded either P (plus) or M (minus), units are tens, ones, tenths of a degree celcius.

- The Roll Angle Flag is used optionally in one of two modes: either as a quality indicator for wind speed and direction based on the aircraft roll and pitch angles, RA and PA respectively (Mode 1), or, alternatively, to provide an indication of which range bin the aircraft roll angle value lies within.

In Mode 1, the Roll Angle Flag will take the value B, G, H, W or U, with the corresponding meaning provided in the table below.

In Mode 2, the Roll Angle Flag will take either the value H, W or U with the same meaning for Mode 1, or an integer value from 0 to 9.

The values W and U are used within an Enroute Weather Report only to indicate that the Wind Speed constitutes a Maximum Wind Report as per the criteria defined in Section 5.3.13.4.2.2.

| Roll Angle Flag Value | Meaning | Mode |
| --- | --- | --- |
| B | ¦RA¦ ≥ 5˚ or (¦RA¦ ≥ 3˚ and ¦PA¦ ≥ 3˚) | 1 |
| G | ¦RA¦ < 5˚ or (¦RA¦< 3˚ and ¦PA¦ < 3˚) | 1 |
| H | Roll angle unavailable or undefined | 1 and 2 |
| W | Maximum wind event and RA and PA correspond to value G. | 1 and 2 |
| U | Maximum wind event and RA and PA correspond to value B. | 1 and 2 |
| 0 | 0˚ ≤ ¦RA¦ < 1˚ | 2 |
| 1 | 1˚ ≤ ¦RA¦ < 2˚ | 2 |
| 2 | 2˚ ≤ ¦RA¦ < 3˚ | 2 |
| 3 | 3˚ ≤ ¦RA¦ < 4˚ | 2 |
| 4 | 4˚ ≤ ¦RA¦ < 5˚ | 2 |
| 5 | 5˚ ≤ ¦RA¦ < 7˚ | 2 |
| 6 | 7˚ ≤ ¦RA¦ < 10˚ | 2 |
| 7 | 10˚ ≤ ¦RA¦ < 14˚ | 2 |
| 8 | 14˚ ≤ ¦RA¦ < 20˚ | 2 |
| 9 | 20˚ ≤ ¦RA¦ | 2 |

- Water Vapor/Humidity is measured and reported either as mass mixing ratio or relative humidity, depending on the type of instrument or sensor employed.

The source of the parameter WV/Humidity is from an instrument which does not belong to the standard aircraft equipment, therefore, the parameter value (nnnnn) as well as the corresponding quality indicator (Q) cannot be obtained from any of the standard avionics data buses.

Reporting of WV/Humidity from the WVSS-II Instrument

In the case of the reporting of WV/Humidity from a spectrometric instrument providing measurement of water vapor mass mixing ratio and a quality parameter via an ARINC 429 interface, the aircraft communication unit should be able to read this serial data stream. Its specification should be provided in the supplier’s documentation, which can be subject to upgrades. Hence, the appropriately current version shall be taken for implementing the on-board software.

The parameters to be obtained from the ARINC 429 data stream are as follows:

        - Octal label 303:  WVSS-II mass mixing ratio value

        - Octal label 270: WVSS-II Status Message(quality indicator)

The mass mixing ratio value is to be reported as nnnnn = n1n2n3n4n5 which implies a mass mixing ratio value of (n1n2n3n4) x 10(-3 - n5)kg/kg; e.g., if nnnnn = 12345, then the mass mixing ration is given by 1234 x 10(-3 - 5) = 1234 x 10-8kg/kg.

Reporting of WV/Humidity as Relative Humidity

In the case a humidity sensor is employed, the implementation in the ARINC 429 interface protocol will be provided by the instrument documents.

A WV/Humidity value reported as a relative humidity percentage value is reported in hundredths of percent and with Q = U, i.e. nnnnnU. For example, 05000U indicates that water vapor is reported as humidity with a value of 50.00%.

No report of WV/Humidity

In the case that no water vapor or humidity sensor is deployed and no report of WV/Humidity is made, the parameter will be reported as blanks or spaces with the quality character “9”, i.e., report nnnnnQ = <sp><sp><sp><sp><sp>9 (<sp> = space or blank character).

- C is a code where:

If C = X, then the turbulence algorithm is not implemented and no data (characters) follow.

If C= Z, then no turbulence above threshold was detected and no data (characters) follow.

If C = Q, then an algorithm or data-related problem exists and no data (characters) follow.

If C = E, the 8 encoded characters representing the output from the Eddy Dissipation Rate (EDR) algorithm follow.

The 8-character value contains the following encoded information:

- Tenths of seconds

- Running minimum confidence

- Running number of Bad samples

- Algorithm version

- EDR peak

- EDR mean

- Peak EDR confidence

- Mean EDR confidence

- Peak location

- Number of Good EDRs

Details of the EDR algorithm and the encoding process will be provided ina future supplement to this standard.

- When pressure-based observations are activated, insert spaces for Series #1 and Series #2 timer intervals in place of ss.

P = PALT (Pressure Altitude in ICAO Standard Atmosphere)

B = BALT (Barometric Altitude in QNH adjusted atmosphere)

If BALT is reported, conversion to the Pressure Altitude (PALT) scale will be necessary in ground processing using runway or area QNH at the time of the observation. This is essential before data can be used or exchanged. If both PALT and BALT are available, PALT is preferred.

Table 10 within Appendix G provides the preset target heights based on pressure level selection. An explanation of its derivation and use in accordance with the definition of the ICAO Standard Atmosphere is also provided.

- The two parameters, True Airspeed and True Heading are grouped together under the Parameter Configuration grouping defined as TAS. This parameter group is optionally reportable (configurable by uplink) and reported when the Configuration Parameter has value 1 or 3 (see Section 4.3.17.1), otherwise it is not reported.

True Airspeed is to be reported in whole units of knots.
True Heading is to be reported in tenths of degrees (0.0 to 359.9)

- The two parameters, De-icing and Aircraft Configuration are grouped together under the Parameter Configuration grouping defined as CNF. This parameter group is optionally reportable (configurable by uplink) and reported when the Configuration Parameter has value 2 or 3 (see Section 4.3.17.1).

De-icing will be reported as value 1 when the aircraft’s de-icing system is not activated, as value 2 when the aircraft’s de-icing system is activated and as 0 when the status of de-icing is not able to be determined.

The parameter, Aircraft Configuration, is assigned a value according to the configuration status of the aircraft as defined within the following table (see Section 4.3.17.1 Note 10):

| Value | Meaning |
| --- | --- |
| 0 | configuration undefined / not reportable |
| 1 | clean configuration, gear retracted |
| 2 | first position of flaps extension, gear retracted |
| 3 | second position of flaps extension, gear retracted |
| 4 | third position of flaps extension, gear retracted |
| 5 to 7 | Reserved |
| 8 | only landing gear down and in place |
| 9 | first position of flaps extension + landing gear down and in place |
| 10 | second position of flaps extension + landing gear down and in place |
| 11 | third position of flaps extension + landing gear down and in place |
| 12 to 14 | Reserved |
| 15 | weight on wheels = True |

- Icing will be reported as value 1 when the aircraft icing sensor indicates no ice accretion, as value 2 when the sensor indicates ice accretion is occurring, and as value 0 when the status of icing is not able to be determined.

#### 5.3.13.6 Meteorological Report, Version 6 – MFI or Label H2

[ISSUES]

1. Do we include the Status Report in the downlink formats? [Done]

2. Do we remove previous versions of the Met. Report or leave for Supplement 8 with a view to removing in the next Supp.?

3. Lat and Lon in the AOSFRS have resolution of minutes. This should be changed to seconds for consistency with the ARINC 620. [Done]

4. Is there a better way of referencing Table 5.3.13.6-1?

[/ISSUES]

Meteorological Report, Version 6 provides a more efficient, adaptable and extensible downlink format for the reporting of Aircraft Meteorological Data Relay (AMDAR) data from an aircraft platform using ACARS. In effect it supersedes versions 1 to 5 of the Meteorological Report. The format specification is consistent and to be used in conjunction with the World Meteorological Organization AMDAR Onboard Software Functional Requirements Specification (ASOFRS), [Reference].

The AOSFRS provides a comprehensive functional specification for the development of AMDAR onboard software applications for suitable avionics platforms. Such applications can then make automated near-real time weather reports using the Meteorological Report downlink format for ACARS.

The requirements for onboard configuration of the applications developed for weather reports are also described in detail in the AOSFRS, along with the means for modifying the configuration by uplink command, for which the formats are defined within section 4.3.18.

Appendix G is not relevant to version 6 of the Meteorological Report and the AOSFRS should be referred to for the provision of information and requirements for onboard avionics applications development.

The Meteorological Report data content can optionally be compressed using a scheme which employs an extended character set for representation of numbers in base 40 rather than base 10. While this compression scheme, as defined in Appendix H, is consistent with the AOSFRS and is therefore applicable to version 6, it is recommended that the AOSFRS is referred to for a more detailed and complete description of its application to this format specifically.

The format of downlink messages for meteorological reports (that is, a series of meteorological “observations” reported within a single message block) is consistent, irrespective of flight phase, i.e. whether the aircraft is ascending, enroute or descending.

The AOSFRS, Chapter 3 describes in detail the requirements for data handling, calculation of derived parameter, reporting schemes, determination of flight phases, the observations to be reported during these flight phases and the calculation or derivation of observations parameters.

While, theoretically, any number of observations can be reported within the format structure defined below, the meteorological transmission requirements for timeliness, as defined in the AOSFRS should be complied with and will determine the size of message blocks.

Each meteorological report consists of at least the message headers (Tables 5.3.13.6-1 and 5.3.13.6-2) and 1 or more observations. Each observation consists of at least the Basic Observations Sequence (Table 5.3.13.6-3), which may be followed by 1 or more Optional Parameters (Table 5.3.13.6-5), which can be enabled or disabled by uplink command (see section 4.3.18).

A Configuration Status Report, which provides the current configuration of the onboard Meteorological Report application, can be requested by uplink command, for which the format specification is provided in section 5.3.65.

Meteorological Report, version 6 makes provision for routine reporting of the turbulence metric, Eddy Dissipation Rate (EDR) and, additionally, event-triggered reporting of EDR, as described in section 5.3.66. If the reporting of EDR is available to the Meteorological Report application (a separate application is required to generate the required 1-minute EDR data), then both its routine and event-triggered reporting can be controlled via the uplink command functionality described in 4.3.18.

##### 5.3.13.6.2	Meteorological Report Downlink Format

The format of the Meteorological Report Messages is defined as follows.

Table 5.3.13.6-1 – Standard Message Header

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  | 1 |

Notes:

- See ARINC Specification 618.

Table 5.3.13.6-2 – Data Header

| Line Number | Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-3 | 3 | Meteorological Report Version | “A06” |  |
| 2 | 1-26 | 1 to 26 | Optional Parameter Indication | # or A thru Z | 1 |
| 3 | 1-6 | 6 | AMDAR Aircraft Identifier | AANNNN | 2 |
| 3 | 7 | 1 | Normal (N) or Compressed (C) | N or C | 3 |
| 3 | 8 | 1 | Time Based (0) or Pressure Based Scheme (1) | 0 or 1 |  |
| 3 | 9-12 | 4 | Departure Airport | AAAA | 4 |
| 3 | 13-16 | 4 | Arrival Airport | AAAA | 4 |

Notes:

- # indicates no optional parameters follow the Basic Observations Sequence. See Table 5.3.13.6-3 for Optional Parameters.

- The AMDAR Identifier is assigned by the requesting Meteorological Office and should take the form AANNNN, where AA indicates the country of the AMDAR Program and NNNN is the unique identifier of the aircraft. To comply with the requirement not to disclose airline proprietary information, the aircraft call-sign should not be utilized or revealed within this identifier.

- Normal means the data are not compressed. Compressed means the data are encoded using the compression scheme described in AOSFRS, Appendix D.

- Departure and Arrival airport are represented by their ICAO code. Reporting of these fields is optional but if available, strongly recommended.

- Unused characters should be blank and left-pad the character Content.

Table 5.3.13.6-3 – Data Block, Basic Observation Sequence

| Character Number | # of Char | Content | Format | Notes or Reference |
| --- | --- | --- | --- | --- |
| 1 | 1 | Observation Type Indicator | N | 1 |
| 2-8 | 7 | Latitude in seconds | snnnnnn | south is negative e.g. 30 15’ 15’’ S = -108915 |
| 9-15 | 7 | Longitude in seconds | snnnnnn | west is negative e.g. 120 20’ 50’’ W = 433250 |
| 16-22 | 7 | Day/Time | nnnnnnn | 2 |
| 23-26 | 4 | Altitude in tens of feet | nnnn | AOSFRS, Ch 3 |
| 27-30 | 4 | Static Air Temperature tenths of C | snnn | s = + or – AOSFRS, Ch 3 |
| 31-33 | 3 | Wind direction in whole degrees | nnn | AOSFRS, Ch 3 |
| 34-36 | 3 | Wind Speed in knots | nnn | AOSFRS, Ch 3 |
| 37 | 1 | Roll Angle Flag | n | AOSFRS, 3.2.4.4 |

Notes:

- Observation Type Indicator is defined as follows:

Table 5.3.13.6-4 – Observation Type Indicator

| Observation Type | Observation Type Indicator |
| --- | --- |
| Ascent Intial | 0 |
| Ascent | 1 |
| Ascent Routine | 2 |
| Enroute | 3 |
| Maximum Wind | 4 |
| Descent | 5 |
| Descent Routine | 6 |
| EDR Routine | 7 |
| Touch-down | 8 |

See AOSFRS, 3.3 for observation defintions and reporting requirements.

- The Day/Time is provided as seconds into the month in UTC.

For example, 12:31:15pm on the 10th day of the month:

= (9*86400 +  12*3600 + 31*60 + 15) =  822675

- Unused characters of Content should be blank and left-pad the character Content.

- Missing, invalid or unavailable values should be padded with the solidii character (/).

Table 5.3.13.6-5 – Data Block, Optional Parameters

| Header Indicator | # of char | Content | Format | Notes or AOSFRS Reference |
| --- | --- | --- | --- | --- |
| n/a | 1 or 9 | Routine EDR | c or cnnnnnnnn | 1 AOSFRS, 3.3.5 |
| A | 3 | DEVG | nnn | AOSFRS, 3.2.4.2 |
| B | 3 | True Airspeed | nnn | AOSFRS, 3.1 |
| C | 4 | True Heading in tenths of degrees | nnnn | AOSFRS, 3.1 |
| D |  | GNSS altitude | nnnn | AOSFRS, 3.1 |
| E | 1 | Anti-ice | n | 2 |
| F | 2 | Aircraft Configuration Indicator | nn | AOSFRS, 3.2.4.5 |
| G | 6 | Water Vapor | nnnnnq | AOSFRS, Appendix C.2 |
| H | 6 | Relative Humidity | nnnnnq | AOSFRS Appendix C.2 |
| I | 1 | Icing | n | 3 |

Notes:

- No header indicator is assigned to routine EDR. When a routine EDR is triggered, an extra observation is inserted in the message containing the basic observation sequence plus any defined optional parameters, amended with the routine EDR value. To identify the observation as a routine EDR observation the Observation Type Indicator is set as per Table 5.3.13.6-4. The EDR event-based messages are separate messages (see REFERENCE BELOW). For more information about EDR reporting algorithms see AOSFRS, C.1.2

- Anti-ice shall be reported using the following logic:

1 = Anti-ice not activated

2 = Anti-ice active

/ = Anti-ice undetermined or invalid:

- Icing will be reported as value 1 when the aircraft icing sensor indicates no ice accretion, as value 2 when the sensor indicates ice accretion is occurring, and as value 0 when the status of icing is not able to be determined.

- Missing, invalid or unavailable fields should be padded with the solidii character (/).

#### 5.3.65	Configuration Status Report for Meteorological Report Version 6 Application

The following specification of the Configuration Status Report downlink message format defines the content of a downlink message that provides the current configuration status of the onboard Meteorological Report application. The report is produced in response to the uplink command request that is defined in section 4.3.18.1.

The Configuration Status Report will have the following format.

Table 5.3.65-1 – Standard Message Header

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  | 1 |

Notes:

- See ARINC Specification 618.

Table 5.3.65-2 – Configuration Status

| Number of Characters | Data | Description | Content |
| --- | --- | --- | --- |
| 1 | A | IMI |  |
| 1 | C | IMI |  |
| 1 | S | IMI |  |
| 2 | 06 | Version number |  |
| 1 | 0-7 | Report Activation flag | 0 = Reporting OFF 1 = Descent Phase ONLY Active 2 = En-route Phase ONLY Active 3 = En-route AND Descent Phases Active 4 = Ascent Phase ONLY Active 5 = Ascent AND Descent Phases Active 6 = Ascent AND En-route Phases Active 7 = ALL Flight Phases Active |
| 4 | H1H1H2H2 | Inhibit Reporting Between Selected Hours (00-23) UTC, every day. | H1H1 = Start of Inhibit Period (00-23) H2H2 = End of Inhibit Period (00-23) 0000 = Disabled |
| 1 And content of configuration table | 0 or 1 And content of configuration table | Activation of Reporting in Defined Geographical Boxes | 0 = Disabled, 1 = Enabled Insert configuration status from Table 4.3.18.2-1 |
| 1 And content of configuration table | 0 or 1 And content of configuration table | Activation of Airport Reporting Selection | 0 = Disabled, 1 = Enabled Insert configuration status from Table 4.3.18.3-1 |
| Content of configuration table | Content of configuration table | Ascent Configuration | Insert configuration status from Table 4.3.18.5-1. |
| Content of configuration table | Content of configuration table | Routine Observations Configuration | Insert configuration status from Table 4.3.18.4-1. |
| Content of configuration table | Content of configuration table | Descent Configuration | Insert configuration status from Table 4.3.18.6-1. |
| 1 | 0, or 1 | Routine EDR Reporting See Note 10. | 0 = Disabled 1 = Enabled |
| 1 | 0, or 1 | EDR Event Reporting See Note 11. | 0 = Disabled 1 = Enabled |
| 1 And Optional Parameter Indication in Table 5.3.13.6-2 | 0 or 1 And Optional Parameter Indication in Table 5.3.13.6-2 | Optional Parameter Configuration See Note 9. | 0 = Disabled 1 = Enabled |
| 1 | / | Delimiter | End of Table 5.3.65-2 (this table) Configuration Status |

#### 5.3.66	Turbulence EDR Event-triggered Downlink Messaging

This section makes provision for automated, event-triggered reporting of the turbulence metric, Eddy Dissipation Rate (EDR).  The reporting events are based on and triggered by the peak and mean EDR values. The downlink information includes required meteorological data.

The format specification is consistent and to be used in conjunction with the World Meteorological Organization AMDAR Onboard Software Functional Requirements Specification (ASOFRS), [Reference].

For a detailed description of associated algorithmic logic see AOSFRS, C.1.2.2. The format for the EDR event-triggered messages is described below.

Turbulence EDR event-triggered reporting can be applied in conjunction with the Meteorological Report, version 6 as described in section 5.3.13.6, which makes provision for reporting of Routine EDR. If the reporting of EDR is available to the Meteorological Report application (a separate application is required to generate the 1-minute EDR data), then its activation and deactivation can be controlled via the uplink command functionality described in 4.3.18.

The format of the EDR Event-triggered downlink messaging is defined as follows.

Table 5.3.65-1 – Standard Message Header

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  | 1 |

Table 5.3.65-2: EDR event message header

| Line number | Character number | # of char | Content | Format | Notes |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-3 | 3 | EDR Event Message Version | “EDR01” |  |
| 2 | 1-2 | 2 | EDR Event Type Indication | AA | 1 |
| 2 | 3 | 0 or 1 | Follow Up Report | A | 2 |
| 3 | 1-7 | 8 | AMDAR Aircraft Identifier | AANNNN | 3 |
| 3 | 8 | 1 | Normal (N) or Compressed (C) | N or C | 4 |
| 3 | 9 | 1 | time based (0) or pressure based scheme (1) | 0 or 1 |  |
| 3 | 10-13 | 4 | Departure Airport | AAAA | 5 |
| 3 | 14-17 | 4 | Arrival Airport | AAAA | 5 |

Notes:

- T1 for type 1, T2 for type 2, T3 for type 3. See AOSFRS, C.1.2.

- ‘F’ if the report is a follow-up report

- The AMDAR Identifier is assigned by the requesting Meteorological Office and should take the form AANNNN, where AA indicates the country of the AMDAR Program and NNNN is the unique identifier of the aircraft. To comply with the requirement not to disclose airline proprietary information, the aircraft call-sign should not be utilized or revealed within this identifier.

- Normal means the data are not compressed. Compressed means the data are encoded using the compression scheme described in AOSFRS, Appendix D.

- Departure and Arrival airport are represented by their ICAO code. Reporting of these fields is optional but if available, strongly recommended.

Table 5.3.65-2: EDR Observation format

| Character Number | # of Char | Content | Format | Note or Reference |
| --- | --- | --- | --- | --- |
| 1 | 1 | Observation Type Indicator | N | 1 |
| 2-8 | 7 | Latitude in seconds | snnnnnn | s = + or - south is negative e.g. 30 15’ 15’’ S = -108915 |
| 9-15 | 7 | Longitude in seconds | snnnnnn | s = + or - west is negative e.g. 120 20’ 50’’ W = 433250 |
| 16-22 | 7 | Day/Time | nnnnnnn | 2 |
| 23-26 | 4 | Altitude in tens of feet | nnnn | AOSFRS, Ch 3 |
| 27-30 | 4 | Static Air Temperature tenths of C | snnn | s = + or – AOSFRS, Ch 3 |
| 31-33 | 3 | Wind direction in whole degrees | nnn | AOSFRS, Ch 3 |
| 34-36 | 3 | Wind Speed in knots | nnn | AOSFRS, Ch 3 |
| 37 | 1 | Roll Angle Flag | n | AOSFRS, 3.2.4.4 |
| 38-46 | 9 | EDR | cnnnnnnnn | AOSFRS, C.1.2 |

Notes:

- Observation Type Indicator is as defined in Table 5.3.13.6-4

- The Day/Time is provided as seconds into the month in UTC.

For example, 12:31:15pm on the 10th day of the month:

= (9*86400 +  12*3600 + 31*60 + 15) =  822675

- Unused characters of Content should be blank and left-pad the character Content.

- Content for missing, invalid or unavailable values should be padded with the solidii character (/).

UPLINK CONTROL PROGRAMMING NOTES FOR VERSION 4 ONBOARD 	SOFTWARE

G-1	Introduction

Version 4 of the ARINC Specification 620 Meteorological Report specification defines the protocols to be used to automatically collect and report meteorological observations on board appropriately equipped aircraft using the Aircraft Communications and Reporting System (ACARS).This version enhances previous versions by defining a number of onboard functions to control where and when observations are taken in order to meet operational requirements of all data users.New functions include the ability to optimize collection of data and to be able to target or inhibit the collection of observations only in specific areas or at defined airports.These control functions are used to provide more efficient and effective national and regional data collection programs.

Version 4 differs from previous versions in several important respects:

- Profile (ascent and/or descent) reports may be selected by pressure interval instead of time interval.

- Geographical areas for enabling and/or inhibiting reports may be selected.

- Specific airports may be selected to enable ascents and/or descents to be reported and/or specific airports may be selected to inhibit ascent and/or descent reports.

- Reporting can be inhibited during a pre-set interval in each 24hr (UTC) period.

- Maximum wind reporting can be enabled during the enroute reporting phase.

The options in previous versions for modifying reporting parameters are retained.

G-2	Options

In order to obtain maximum flexibility in the use of the various options, default values of relevant control variables are stored onboard as part of the basic software.These values can only be changed by reprogramming the software.The default values are used to populate look-up tables and are stored in volatile memory following a complete system reset and/or initialization.The initial set of default variables if left unchanged automatically enable the AMDAR system to run a basic program almost identical in format to Version 2 of the Downlink Meteorological Report.Any variables can be modified by uplink command and additional variables can be uplinked to expand the functionality of each table as required.Any changes are retained in volatile memory until the next system reset and/or initialization whereupon the default values are reinstalled.The data table contents are given as follows:

Table G-1 – Basic Configuration

| Element Number | Default Value | Description | Possible Value(s) | Link to Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Enable AMDAR | 0 |  | 0 = disable, 1 = enable |
|  |  |  | 1 |  |  |
| 2 | 0 | Inhibit reporting in selected time interval. | 0 |  | 0 = disable (report through 24hrs every day), 1 = enable |
|  |  |  | 1 | 9 |  |
| 3 | 0 | Report in designated region | 0 |  | 0 = disable, 1 = enable |
|  |  |  | 1 | 2 |  |
| 4 | 0 | Airport selection | 0 |  | 0 = disable, 1 = enable |
|  |  |  | 1 | 3 |  |
| 5 | 1 | Ascent selection | 0 | 6, 4 | 0 = disable, 1= enable |
|  |  |  | 1 | 5, 3 |  |
| 6 | 1 | Enroute selection | 0 |  | 0 = disable, 1 = enable |
|  |  |  | 1 | 4, 3 |  |
| 7 | 1 | Descent selection | 0 | 8, 4 | 0 = disable, 1 = enable |
|  |  |  | 1 | 7, 3 |  |

The above table shows defaults and possible values for the basic configuration.It is used as follows:

- Element 1 enables AMDAR.If set to 0 by uplink command AMDAR is disabled.

- Element 2 if set to 1 allows an interval stored in Table G-9 to be used to inhibit AMDAR reporting in every 24 hour period.Default is 0.

- Element 3 if set to 1 points to Table 2 where reporting and/or non-reporting regions (defined by latitude/longitude boxes) are stored.Default is 0 meaning report globally.

- Element 4 if set to 1 points to Table G-3 where airports selected or inhibited for profile (ascent/descent) reporting are stored.Default is 0 meaning report all ascents/descents (wherever AMDAR is enabled).

- Element 5 if set to 0 means inhibit all ascent reports and points to Tables G-6 and 4.Default is 1 meaning report at all airports in selected regions as determined by Elements 3 and 4 and points to Tables 5 and 3.

- Element 6 if set to 0 means inhibit Enroute reporting.Default is 1 meaning enable Enroute reporting and points to Table 4.

- Element 7 if set to 0 means inhibit all descent reports and points to Tables 8 and 4.Default is 1 meaning report at all airports in selected regions as determined by Elements 3 and 4 and points to Tables G-7 and G-3.

Table G-2 – Report in Designated Region

| Element Number | Default value | Description | Possible Values | Link to Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 00 | Number (n) of boxes following | 00-16 | 3 (n = 00) | Up to 16 boxes |
| 2 to (n+1), omitted if n=0 | L1L1 A1L2L2A2 L3 L3L3 B1L4L4 L4B2 | Report in Lat/ Long box | 90N-90S, 180W-180E | 3 | Lat in degrees north (A = N) or south (A = S) Lon in degrees east (B = E) or west (B = W) Convention is L1L1 to L2L2 (N -S) and L3L3L3 to L4L4L4 (W-E). |
| (n+2) | 00 | Number (nn) of boxes following | 00-16 |  | Up to 16 boxes |
| (n+3) – (n + 2 + nn), omitted if nn=0 | L1L1 A1L2L2A2 L3 L3L3 B1L4L4 L4B2 | Inhibit reporting in Lat/ Long box | As above |  | Inhibit has priority over enable |

Table G-2 stores up to 16 geographical boxes in which AMDAR is enabled, meaning all ascent and descent profiles and enroute data are reported unless modified by subsequent commands, and up to 16 boxes in which reporting is inhibited.Following a complete system reset and/or initialization, n and nn are set to 00 and the table contains 2 elements only.The elements are used as follows:

- Element 1 indicates the number (n) of reporting boxes following.If n= 00, global reporting is enabled.A link to Table 3 checks if specific airports are designated for profile reporting.

- Elements 2 – (n+1) define the geographical areas for reporting.

- Element (n+2) indicates the number (nn) of boxes following in which all reporting is to be inhibited.Specified boxes have priority over reporting boxes.Thus if Element 1 is 00 and Element 2 is 01 all regions except the one following are designated reporting regions.

- Elements (n+3) to (n+2+nn) define the inhibit regions

- The minimum number of elements stored (i.e., following a complete system reset and/or initialization) is 2 (00,00).

Table G-3 – Airport Selection

| Element Number | Default Value | Description | Possible Values | Link to Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 00 | Number (n) of airfields following | 00-20 |  | Up to 20 airfields may be selected for ascent reporting |
| 2 to (n+1), omitted if n = 00 |  | Airfieldselected for ascent | 4 character airfield code |  |  |
| n+2 | 00 | Number (nn) of airfields following | 00-20 |  | Up to 20 airfields may be selected for descent reporting |
| (n+3) to (n+2+nn), omitted if nn = 00 |  | Airfield selected for descent | 4 character airfield code |  |  |
| (n+nn +3) | 00 | Number (N) of airfields following | 00-20 |  | Up to 20 airfields may be inhibited for reporting ascents |
| (n+nn+4) to (n+nn+3+N), omitted if N= 00 |  | Airfieldinhibited for ascent | 4 character airfield code |  |  |
| (n+nn+N+4) | 00 | Number (NN) of airfields following | 00-20 |  | Up to 20 airfields may be inhibited for reporting descents |
| (n+nn+N+5) to (n+nn+N+4+NN), omitted if NN= 00 |  | Airfield inhibited for descent | 4 character airfield code |  |  |
| (n+nn+N+NN+5) | 0 | Routine observations: enabled = (1), disabled = (0) | 0-1 | 4 (if enabled) | 1 = enable routine observations during ascent and descent for above selected (inhibited) airfields. Routine observations are observations made at set intervals as defined in Table 4. 0 = no routine observations to be made at any above selected airfields. |

Table G-3 stores airfield address codes for either selecting or inhibiting profile (ascent/descent) reporting. Following a complete system reset and/or initialization n, nn, N and NN are set to 00 and the table contains 5 elements only.The elements are used as follows:

- Element 1 indicates the number (n) following of airports designated for ascent reporting in any region where AMDAR is enabled for reporting.The default value 00 means this function is to be ignored and all ascents in reporting areas shall be reported unless disabled in the basic configuration table (Table 1, Element 5).

- Elements 2 to (n+1) give the 4-character ICAO airfield code for airfields designated for ascent reporting by uplink command. If n = 00 the elements are omitted.

- Element (n+2) gives the number (nn) following of airports designated for descent reporting. The default value 00 means this function is to be ignored and all descents in reporting areas shall be reported unless disabled in the basic configuration table (Table G-1, Element 7).

- Elements (n+3) to (n+2+nn) give the 4-character airfield code for airfields designated for descent reporting by uplink command. If n = 00 the elements are omitted.

- Element (n+nn+3) gives the number (N) following of airports inhibited in reporting regions from ascent reporting. The default value 00 means no airports inhibited.

- Elements (n+nn+4) to (n+nn+3+N) give the 4-character airfield code for airfields designated for inhibiting ascent reporting by uplink command. If 
N = 00 the elements are omitted.

- Element (n+nn+N+4) gives the number (NN) following of airports inhibited in reporting regions from descent reporting. The default value 00 means no airports inhibited.

- Elements (n+nn+N+5) to (n+nn+N+4+NN) give the 4-character airfield code for airfields designated for inhibiting descent reporting by uplink command. If NN = 00 the elements are omitted.

- Element (n+nn+N+NN+5) can be set to allow routine reporting during ascents and descents (as appropriate) even if airports are inhibited from reporting profiles. Routine reports are observations taken at fixed enroute intervals regardless of flight phase.The default value 0 means no routine reports are to be made during the profile phase for any selected airfield.If set to 1 reports are required at the interval set in Table G-4.

- The minimum no of elements stored (following a complete system reset and/or initialization) is 5.

Table G-4 – Routine-Enroute Observing Interval and Maximum Wind Reporting

| Element Number | Default value | Description | Possible Values | Link to Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 07 | Routine-level flight observing interval (min) | 01-60 | 1,3,4,6,8 | Used if enroute or routine reporting enabled |
| 2 | 1 | Maximum wind reporting: enabled = (1), disabled = (0) | 0-1 | 1 | Applicable to enroute reporting. |

Table G-4 gives the routine-enroute observing interval and allows maximum wind to be reported during the enroute observing phase.The default value for Element 1 is 07 meaning that reports (observations) are required at 7 minute intervals in the enroute flight phase if enabled (Table 1, Element 6) or if required, during pauses in ascent and/or descent flight phases for periods of level flight (Table G-5, Element 8).Also, the selected value may be required in ascent and/or descent phase if profile reporting is disabled (Table 1, Elements 5 and 7; Table 3, last element; Table G-6; Table G-8).The default value for Element 2 is 1 indicating that maximum wind reporting is required.If set to 1 maximum wind identification and reporting is enabled during the enroute phase.

Table G-5 – Ascent Profile Options

| Element Number | Default Value | Description | Possible Values | Link to Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Pressure level (0) or Time interval (1) selection | 0-1 | 1 | Designates ascent profile intervals as time or pressure intervals. |
| 2 | 06 | Series 1 time intervals(s) | 03-20 |  | See downlink message format |
| 3 | 090 | Series 1 duration(s) | 030-200 |  |  |
| 4 | 20 | Series 2 intervals(s) | 20-60 |  |  |
| 5 | 051 | Total duration (sx10) | 051-111 |  | Series 1 + Series 2 or total duration of climb |
| 6 | 200 | Top of climb (ftx100) | 150-250 |  |  |
| 7 | 2 | Pressure target list selected | 1-2 |  | See Table 10, List 1 and 2 |
| 8 | 1 | Level flight reporting: enable = (1), disable = (0) | 0-1 | 4 | Enables level flight reports during pauses in ascent |

This table designates the ascent profile parameters either for time interval or pressure interval selection.If ascent reporting is enabled in any region (Table G-1, Elements 1, 3, 4 and 5; Table G-3) this Table is used as follows:

- Element 1 determines if time or pressure intervals are to be used.The default 1 indicates time interval selection as detailed in the following Elements 2-5.

- If set to 0, pressure intervals are to be used determined according to pre-set pressure heights stored in Table G-10 and to the flag set in Element 7.

- Element 2 gives the time interval for the first ascent (series 1) phase of flight after the initial sample (observation) is taken at take-off.The default interval is 6 seconds in an allowed range of 3-20 seconds.

- Series 1 observations continue until the duration set by Element 3 is reached. The default value is 90 seconds (090) in a range of 30-200 seconds.

- Element 4 gives the time interval for observations in the second ascent phase (series 2).The default value is 20 seconds in a range of 20-60 seconds.

- Element 5 gives the total duration of Ascent series1 and series 2 sampling, after which AMDAR goes into the enroute flight phase.The default value is 510 seconds in a range of 510 to 1,110 seconds.

- Element 6 gives the top of climb as a pressure altitude.The default value is 200 (20,000 ft) in a range of 150-250.The enroute phase shall commence when the aircraft first reaches the limit set by element 5 (time) or the limit set by Element 6 (pressure) irrespective of the method of profile interval in use.

- Element 7 points to one of two pressure-altitude target lists contained in a stored table (Table G-10).The default value is 2 meaning that Table G-10; List 2 shall be used for pressure interval selection. List 2 contains target heights designed for 10hPa interval and 50hPa interval selection and is used as follows: After the initial observation is made at take-off, 10 measurement samples are taken at 10hPa intervals, starting at the first target height after the pressure altitude at take-off.For example if the take-off pressure altitude is 100 ft the first sample will be taken at height 11 (364 ft) and the last 10hPa sample will be taken at height 29 (2,994 ft).Thereafter samples shall continue at 50hPa intervals until top of climb (element 6) is exceeded or total duration (Element 5) is exceeded.In the example, if top of climb is set to 200 (20,000 ft) samples will be taken at height 31 (3,243 ft), 41(4,781 ft), 51 
(6,394 ft) 81 (20,812 ft) assuming the total duration is not exceeded. (Note. If an aircraft does not reach the top of climb altitude the total duration set (Element 5) will ensure reaching the enroute flight phase unless the total flight duration is less than this pre-set duration.In this case ascent observation samples will cease at the last 50hPa interval target level reached and, if enabled, descent sampling will commence when the aircraft descends through target altitudes at or below the target set for initiating the descent phase (Table G-7).

- For pressure based sampling, Element 8 enables the selection of timed reporting in level flight during pauses in the ascent phase and points to Element 1 of Table G-4 for the routine observations interval.This function is disabled if ascent is not selected in Table G-1 Element 5.In the event that the top of climb is not reached, this element automatically enables detection of the enroute phase.These samples are transmitted as part of the ascent report even though pressure altitude may not be changing during the pause in ascent.

Table G-6 – Enable Routine Observations During Ascent

| Element Number | Default Value | Description | Possible Values | Link to Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Routine observations enabled = (1), disabled = (0) | 0-1 | Table 1 | Enables or disables routine observations when ascent profiling is disabled. |

This Table is used only if ascents are disabled in Table G-1 (Element 5).If set to the default value, routine observing intervals (Table 4) will be used during ascent instead of detailed profile interval as given in Table G-5.

Table G-7 – Descent Profile Options

| Element Number | Default Value | Description | Possible Values | Link To Table(s) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Pressure interval (0)/time interval (1) selection | 0-1 | 1 | Designates descent profile sampling at time or pressure intervals. |
| 2 | 040 | Descent intervals | 020-300 |  |  |
| 3 | 200 | Top of descent(PALT) (ft x 100) | 150-250 |  |  |
| 4 | 2 | Pressure target list selected | 1-2 |  | See Table 10, List 1 and 2. |
| 5 | 1 | Level flight sampling: enable = (1), disable = (0) | 0-1 | 4 | Enables or disables timed level flight reports during pauses in descent |

This table designates the descent profile parameters either for time interval or pressure interval selection.If descent reporting is enabled in any region (Table G-1, Elements 1, 3, 4 and 7; Table 3), the Table is used as follows:

- Element 1 determines if time or pressure intervals are too be used.The default 1 indicates time interval selection as determined by Element 2.If set to 0, pressure intervals are to be used determined according to pre-set pressure heights stored in Table 10 and to the flag set in Element 4.

- Element 2 sets the descent time interval.The default value is 40 seconds in a range of 20-300 seconds.

- Element 3 sets the top of descent. The default value is 200 (20,000ft) in a range of 150-250 (15,000-25,000ft).Whichever interval (pressure or time) is designated for descent profiling the descent flight phase will start on passing though this pre-set value.In the event that the enroute altitude is already lower than top of descent, the descent phase shall commence on descending through two consecutive 25hPa target altitudes taken from Table 10, List 1.For example, if cruise level is 24,000ft and top of descent is set to 25,000ft, descent sampling shall commence at target level 82 (22,160ft).

- Element 4 points to one of two pressure-altitude target lists contained in a stored table (Table 10).The default value is 2 meaning that Table G-10; List 2 shall be used for pressure interval selection. List 2 contains target heights designed for 10hPa interval and 50hPa interval selection.List 1 contains target heights designed for higher density profiles with 5hPa interval and 25hPa interval selection

- Table 10 is used as follows:

  - For pressure based sampling, if Element 3 (top of descent) is lower than the cruise (enroute reporting phase) altitude, descent phase sampling shall commence when the aircraft descends through the first 50hPa or 25hPa (as appropriate) target height encountered. For example if Element 3 is set to 20,000ft, and Element 4 points to Table 10, List 2, descent sampling starts at height 79 (18,289ft).Sampling continues at 50hPa target intervals until the 700hPa level is reached.All samples from the top of descent to 700hPa including the 700hPa sample are transmitted in one report.On passing through 700hPa (target height 71, samples are taken at 10hPa intervals and stored until touchdown.On touchdown, the most recent 10 samples at 10hPa intervals above touchdown altitude are retained.Above this 100hPa layer, samples at integer multiples of 50hPa are taken from the stored 10hPa samples and transmitted with the most recent 10hPa samples in one report.All remaining intermediate 10hPa samples are discarded.The profile thus contains 50hPa samples from 750hPa to 100hPa above touchdown altitude followed by 10, 10hPa samples for the lowest portion of the profile. If element 4 had pointed to List 1, descent sampling would have started at target height 80 and continued at 25hPa intervals until and including 700hPa.These samples would be transmitted in one report.On passing through 700hPa (target height 71) additional samples would then have been taken at 5hPa intervals (target heights 70,69,68,67…) until touchdown. The 20 most recent 5hPa samples are retained.Above this 100hPa layer, samples at integer multiples of 25hPa are taken from the stored 10hPa samples and transmitted with the most recent 10hPa samples in one report.All remaining intermediate 10hPa samples are discarded.The profile thus contains 25hPa samples from 750hPa to 100hPa above touchdown altitude followed by 20, 5hPa samples for the lowest portion of the profile.

- In the event that the enroute altitude is already lower than top of descent, the descent phase shall commence on descending through two consecutive 25hPa target altitudes taken from Table 10, List 1.The first sample shall be taken at the first target height encountered i.e., the second of the two trigger levels if List 1 is used and the first available trigger at or immediately following the second 25hPa value if List 2 is used (as defined by Element 4).For example, if cruise level is 24,000ft and top of descent is set to 25,000 ft, Element 4 set to 2, descent sampling shall commence at target level 41 
(20,812). In this case the trigger levels are 23,574ft and 22,160ft. and 20,812 is the first available list 2 trigger following the decision that descent is under way.

- For pressure based sampling, Element 5 enables the selection of timed reporting in level flight during pauses in the descent phase and points to Element 1 of Table G-4 for the interval of routine sampling.This function is disabled if descent is not selected in Table G-1 Element 7.These samples are transmitted as part of the descent report.

Table G-8 – Enable Routine Observations During Descent

| Element Number | Default Value | Description | Possible Values | Link To Table(S) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Routine observations: enabled = (1), disabled = (0) | 0-1 | Table 1 | Routine observations are enabled when descent profiling is disabled. |

This Table is used only if descents are disabled in Table G-1 (Element 7).If set to the default value, routine observing intervals (Table G-4) will be used during descent instead of detailed profile interval as specified in Table G-7.

Table G-9 – Inhibit Reporting in Selected Time Interval

| Element Number | Default Value | Description | Possible Values | Link To Table(S) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | 0000 | Disable observations between selected hours (00-23) UTC, every day | 00-23,00-23 | Table 1 | First two chars = start of inhibit period Second two chars = end of inhibit period |

This table allows AMDAR to be disabled for one selected period each 24 hrs.The Default value 0000 means report through 24 hrs. When enabled, the times set are interpreted as first two characters give start of inhibit period, second two characters give end of inhibit period.Thus 0918 means inhibit from 0900UTC to 1800UTC. 2304 means inhibit at 2300UTC through 0000 to 0400UTC.

Table G-10 – Preset Target Heights based on Pressure Level Selection

This table is not uplinked but stored in the on-board AMDAR program

| Pressure (hPa) | Height (ft) | List 1 | List 2 | Height No (nn) |
| --- | --- | --- | --- | --- |
| 1050 | -989 | 1 | 1 | 01 |
| 1045 | -856 | 2 |  | 02 |
| 1040 | -723 | 3 | 2 | 03 |
| 1035 | -589 | 4 |  | 04 |
| 1030 | -454 | 5 | 3 | 05 |
| 1025 | -319 | 6 |  | 06 |
| 1020 | -184 | 7 | 4 | 07 |
| 1015 | -48 | 8 |  | 08 |
| 1010 | 89 | 9 | 5 | 09 |
| 1005 | 226 | 10 |  | 10 |
| 1000 | 364 | 11 | 6 | 11 |
| 995 | 502 | 12 |  | 12 |
| 990 | 641 | 13 | 7 | 13 |
| 985 | 780 | 14 |  | 14 |
| 980 | 920 | 15 | 8 | 15 |
| 975 | 1061 | 16 |  | 16 |
| 970 | 1202 | 17 | 9 | 17 |
| 965 | 1344 | 18 |  | 18 |
| 960 | 1486 | 19 | 10 | 19 |
| 955 | 1629 | 20 |  | 20 |
| 950 | 1773 | 21 | 11 | 21 |
| 945 | 1917 | 22 |  | 22 |
| 940 | 2062 | 23 | 12 | 23 |
| 935 | 2207 | 24 |  | 24 |
| 930 | 2353 | 25 | 13 | 25 |
| 925 | 2500 | 26 |  | 26 |
| 920 | 2647 | 27 | 14 | 27 |
| 915 | 2795 | 28 |  | 28 |
| 910 | 2944 | 29 | 15 | 29 |
| 905 | 3093 | 30 |  | 30 |
| 900 | 3243 | 31 | 16 | 31 |
| 895 | 3394 | 32 |  | 32 |
| 890 | 3545 | 33 | 17 | 33 |
| 885 | 3697 | 34 |  | 34 |
| 880 | 3850 | 35 | 18 | 35 |
| 875 | 4003 | 36 |  | 36 |
| 870 | 4157 | 37 | 19 | 37 |
| 865 | 4312 | 38 |  | 38 |
| 860 | 4468 | 39 | 20 | 39 |
| 855 | 4624 | 40 |  | 40 |
| 850 | 4781 | 41 | 21 | 41 |
| 845 | 4939 | 42 |  | 42 |
| 840 | 5098 | 43 | 22 | 43 |
| 835 | 5257 | 44 |  | 44 |
| 830 | 5417 | 45 | 23 | 45 |
| 825 | 5578 | 46 |  | 46 |
| 820 | 5739 | 47 | 24 | 47 |
| 815 | 5902 | 48 |  | 48 |
| 810 | 6065 | 49 | 25 | 49 |
| 805 | 6229 | 50 |  | 50 |
| 800 | 6394 | 51 | 26 | 51 |
| 795 | 6560 | 52 |  | 52 |
| 790 | 6727 | 53 | 27 | 53 |
| 785 | 6894 | 54 |  | 54 |
| 780 | 7062 | 55 | 28 | 55 |
| 775 | 7232 | 56 |  | 56 |
| 770 | 7402 | 57 | 29 | 57 |
| 765 | 7573 | 58 |  | 58 |
| 760 | 7745 | 59 | 30 | 59 |
| 755 | 7917 | 60 |  | 60 |
| 750 | 8091 | 61 | 31 | 61 |
| 745 | 8266 | 62 |  | 62 |
| 740 | 8442 | 63 | 32 | 63 |
| 735 | 8618 | 64 |  | 64 |
| 730 | 8796 | 65 | 33 | 65 |
| 725 | 8974 | 66 |  | 66 |
| 720 | 9154 | 67 | 34 | 67 |
| 715 | 9334 | 68 |  | 68 |
| 710 | 9516 | 69 | 35 | 69 |
| 705 | 9699 | 70 |  | 70 |
| 700 | 9882 | 71 | 36 | 71 |
| 675 | 10817 | 72 |  | 72 |
| 650 | 11780 | 73 | 37 | 73 |
| 625 | 12774 | 74 |  | 74 |
| 600 | 13801 | 75 | 38 | 75 |
| 575 | 14862 | 76 |  | 76 |
| 550 | 15962 | 77 | 39 | 77 |
| 525 | 17103 | 78 |  | 78 |
| 500 | 18289 | 79 | 40 | 79 |
| 475 | 19524 | 80 |  | 80 |
| 450 | 20812 | 81 | 41 | 81 |
| 425 | 22160 | 82 |  | 82 |
| 400 | 23574 | 83 | 42 | 83 |
| 375 | 25061 | 84 |  | 84 |
| 350 | 26631 | 85 | 43 | 85 |
| 325 | 28294 | 86 |  | 86 |
| 300 | 30065 | 87 | 44 | 87 |
| 275 | 31959 | 88 |  | 88 |
| 250 | 33999 | 89 | 45 | 89 |
| 225 | 36211 | 90 |  | 90 |

Notes:

- For pressure-based observations during ascent and descent phases of flight, sampling takes place at multiples of 10 or 50hPa if List2 is selected and at multiples of 5 and 25hPa if List1 is selected. However, the initial observation following the Off event and the predefined tops of ascent and descent are defined in thousands of feet.

The following four equations are used in the process to calculate pressure (P(hPa)) from pressure altitude (PALT) and pressure altitude from pressure if Table 10 is not used to determine pressure target heights.

Four equations are necessary, as the ICAO Standard Atmosphere defines different temperature lapse rates for the troposphere and the stratosphere. The tropopause is defined to occur at 11,000 m above ICAO MSL (corresponding to an altitude of 36,089 feet and pressure of 226.32hPa) and the point at which the temperature lapse rate changes from 0.0065Km-1 to 0.0Km-1.

For calculations at or below 36,089ft or 226.32hPa, use equations1 and2 to calculate pressure P(hPa) and PALT(ft) respectively:

P (hPa) = 1013.25  x  (1 – 10-6 x 6.8756 x PALT (ft)) 5.2559	(1)

PALT (ft) = 145442 x (1 - (P(hPa) / 1013.25)0.19026)	(2)

For calculations above the tropopause at pressure lower than 226.32hPa (i.e., above 11,000m or 36,089ft), use equations 3 and 4:

P (hPa) = 226.32 x EXP(-4.80635 x 10-5 x (PALT(ft) – 36089))	(3)

PALT (ft) = - ln (P(hPa) / 226.32) x 20,806 + 36,089		(4)

Meteorological report compression

H-1	Introduction

The following proposal for the Meteorological Report downlink compressed format is intended to increase efficiency and reduce message congestion by sending fewer characters (and AIRCOM data blocks) for each Meteorological Report. Some aspects of this proposal may need further reviewing in light of formal decisions to be taken on the format of the Downlink Meteorological Report.

Two simple coding techniques have been applied to the standard Meteorological Report, Version 4:

The first technique codes all numerical values using all available printable characters (i.e., a range of –20 to +19 can be mapped onto 40 printable characters). For this purpose the limited Teledyne character set has been used which it is understood has only 44 characters available.

The second technique reduces the magnitude of some of the numerical values by coding them as delta changes from their previous value.  This method provides a saving because many of the quantities are physical values that vary slowly with time.

H-2	Assumptions

It is desirable that each observation be kept to a fixed length format where each field occupies the same character positions in every record of the same type.  However, due to the way turbulence is proposed to be reported, this is not possible.

There are 44 printable characters available in the communication character (Teledyne limitation).

H-3	Compression Method

The following tables summarize the effect of the compression method when applied to Meteorological Report, Version 4.

Only 40 of the available characters will be used.  The CR and LF will not be used to represent data and the space character <sp> will be reserved to:

- Indicate that an error has occurred during the integer to character string conversion process.

- Show that a value is unavailable or out of range.

- The / character is reserved to signify a change from Ascent series#1 to Ascent series #2.

The ARINC 620 Type of Met Format character will be used to identify a compressed Meteorological Report. Unique characters will be used to identify samples selected by time interval or by pressure level for each individual flight phase (ascent, enroute or descent message).

H-4	Tables – for compression of meteorological report version 4

The following tables provide a description of the element to be encoded with units and resolution as appropriate, the type of character used in the code (alpha character, absolute value or change in value (delta)), the range of absolute values permissible, and the number of compressed characters required.

The first sample: For each report the first sample will contain every field, coded as absolute values mapped directly to the 40 usable characters. A single character can therefore represent any value in the range –20 to +19. Two characters can represent any integer between –800 to +799, and so on, the numbers increasing as 40n where n is the number of characters. All numerical values are reduced to a quantity of a single unit – e.g., longitude is reduced to a signed number representing tenths of minutes north and east of the meridian.

Subsequent samples: All subsequent observation records are coded as a mixture of absolute values and delta changes (coded as incremental changes from the previous corresponding observation). If any of the delta values exceeds the allowed range then the observation is terminated with a space, carriage return (CR) and line feed (LF) characters and the meteorological report transmitted. A new report is then started where the next observation is coded in absolute values. In this way the exception cases are naturally dealt with. It is anticipated that the exception overheads should be very small under normal circumstances.

CRLF characters are needed at least every 69 characters due to an ARINC/SITA restriction. The use of these characters is specified in the message format description below. The Committee is invited to determine if this situation is still valid.

Ascent Meteorological Report – CompressedFormat

| Ascent Header Block |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Standard message header | Character code | N/A | 10 |
| Version number | Absolute value | 0 to +20 | 1 |
| Type of message format | Character code | N/A | 1 |
| Date message assembled (day) | Absolute value | 0 to +31 | 2 |
| Time message assembled (in minutes) | Absolute value | 0 to +1439 | 3 |
| Departure station | Character code | N/A | 4 |
| Destination station | Character code | N/A | 4 |
| Total number of characters |  |  | 25 |

| Ascent Initial Report |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Absolute value | -54,000 to +54,000 | 4 |
| Longitude (in tenths of minutes) | Absolute value | -107,999 to +108,000 | 4 |
| Date of observation | Absolute value | 0 to +31 | 2 |
| Time of observation (minutes) | Absolute value | 0 to +1439 | 3 |
| Series 1 time interval (seconds) | Absolute value | +3 to +20 | 1 |
| Series 2 time interval (seconds) | Absolute value | +20 to +60 | 2 |
| Pressure altitude (tens of feet) | Absolute value | -99 to +799 | 2 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Total number of characters |  |  | 24 |

| Ascent Series #1 – FirstSample |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Absolute value | -54,000 to +54,000 | 4 |
| Longitude (in tenths of minutes) | Absolute value | -107,999 to +108,000 | 4 |
| Pressure Altitude | Absolute value | -99 to +799 | 2 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Total number of characters |  |  | 21 |

| Ascent Series #1 – SubsequentSamples |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Longitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Pressure Altitude | Delta | -800 to +799 | 2 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Total number of characters |  |  | 19 |

| Ascent Series #2 – FirstSample |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Absolute value | -54,000 to +54,000 | 4 |
| Longitude (in tenths of minutes) | Absolute value | -107,999 to +108,000 | 4 |
| Time of observation (minutes) | Absolute value | 0 to +1,439 | 3 |
| Pressure altitude (tens of feet) | Absolute value | -99 to +5,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Total number of characters |  |  | 25 |

| Ascent Series #2 – SubsequentSamples |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Longitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Time of observation (minutes) | Delta | 0 to +800 | 2 |
| Pressure altitude (tens of feet) | Delta | -800 to +799 | 2 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Total number of characters |  |  | 21 |

Enroute Meteorological Report – CompressedFormat

| Enroute Header Block |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Standard message header | Character code | N/A | 10 |
| Version number | Absolute value | 0 to +20 | 1 |
| Type of message format | Character code | N/A | 1 |
| Date message assembled (day) | Absolute value | 0 to +31 | 2 |
| Departure station | Character code | N/A | 4 |
| Destination station | Character code | N/A | 4 |
| Total number of characters |  |  | 22 |

| Enroute – First Sample |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Absolute value | -54,000 to +54,000 | 4 |
| Longitude (in tenths of minutes) | Absolute value | -107,999 to +108,000 | 4 |
| Time of observation (minutes) | Absolute value | 0 to +1,439 | 3 |
| Pressure altitude (tens of feet) | Absolute value | -99 to +5,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +799 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Turbulence code (ZZ, QQ, integers nn) | Character or absolute value | N/A or 00 to +99 | 2 |
| Turbulence data (variable multiples of 4 characters) | Character | 0000 to +FFFF | 4nn |
| Total number of characters |  |  | 27+4nn |

| Enroute – SubsequentSamples |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Longitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Time of observation (minutes) | Delta | 0 to +799 | 2 |
| Pressure Altitude (tens of feet) | Delta | -800 to +799 | 2 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +799 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Absolute value | N/A | 1 |
| Turbulence code (ZZ, QQ, integers nn) | Character or absolute value | N/A or 00 to +99 | 2 |
| Turbulence data (variable multiples of 4 characters) | Character | 0000 to +FFFF | 4nn |
| Total number of characters |  |  | 23+4nn |

Descent Meteorological Report – CompressedFormat

| Descent Header Block |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Standard Message Header | Character code | N/A | 10 |
| Version Number | Absolute value | 0 to +20 | 1 |
| Type of Message Format | Character code | N/A | 1 |
| Date Message Assembled (Day) | Absolute value | 0 to +31 | 2 |
| Departure station | Character code | N/A | 4 |
| Destination station | Character code | N/A | 4 |
| Total number of characters |  |  | 22 |

| Descent – First Sample |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Absolute value | -54,000 to +54,000 | 4 |
| Longitude (in tenths of minutes) | Absolute value | -107,999 to +108,000 | 4 |
| Time of observation (minutes) | Absolute value | 0 to +1439 | 3 |
| Pressure altitude (tens of feet) | Absolute value | 0 to +5,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | 0 to +799 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Turbulence code (ZZ, QQ, integers nn) | Character or absolute value | N/A or 00 to +99 | 2 |
| Turbulence data (variable multiples of 4 characters) | Character | 0000 to +FFFF | 4nn |
| Total number of characters |  |  | 27+4nn |

| Descent – Subsequent Samples |
| --- |
| Description | Type | Absolute Range | Number of Encoded Characters |
| Latitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Longitude (in tenths of minutes) | Delta | -7999 to +8000 | 3 |
| Time of observation (minutes) | Delta | 0 to +799 | 2 |
| Pressure Altitude (tens of feet) | Delta | -800 to +799 | 2 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 2 |
| Wind speed (knots) | Absolute value | -800 to +799 | 2 |
| Roll angle flag/flight phase | Character | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +999 | 3 |
| WV mixing ratio quality | Character | N/A | 1 |
| Turbulence code (ZZ, QQ, integers nn) | Character or absolute value | N/A or 00 to +99 | 2 |
| Turbulence data (variable multiples of 4 characters) | Character | 0000 to +FFFF | 4nn |
| Total number of characters |  |  | 23+4nn |

H-5	The Resulting Message

When accumulating samples at target heights using default settings a flight departing from an airport with surface pressure 1035hPa, with an enroute duration of 2 hours 50 minutes and arriving at an airport with surface pressure 1035hPa, will generate the following number of Weather Reports:

| Phase of Flight | Message | Number of reports generated | Number of samples within each report | Number of samples during flight phase | Number of characters |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Standard | Compressed |
| Ascent | Header Block | 1 | - | - | 27 | 25 |
| Ascent | Initial report | 1 | 1 | 1 | 35 | 24 |
| Ascent | Series #1 | 1 | 15 | 15 | 480 | 287 |
| Ascent | "/" character | 1 | - | - | 1 | 1 |
| Ascent | Series #2 | 1 | 21 | 21 | 756 | 445 |
| Enroute | Header Block | 4 | - | - | 92 | 88 |
| Enroute | Series #1 | 4 | 6 | 24 | 1584 | 1228 |
| Descent | Header Block | 2 | - |  | 46 | 44 |
| Descent | Series #1 | 2 | 10 and 9 | 19 | 1188 | 973 |
| Totals |  | 80 | 4,209 | 3,115 |

This result indicates that the total number of characters transmitted will be reduced by nearly 30%. A larger character set would allow this compression ratio to be increased.

H-6	Tables – For compression of Meteorological Report Version 5

The following tables provide the alternative compressed format of the downlink Meteorological Report Version 5, which is defined in Section 5.3.13.5.

Note that the use of the Base 40 compression technique is applied likeVersion 4 (see H-4), except that, for Version 5, the offset is either zero (used when the Absolute Range uses only the positive integer domain) or half the allowable Base 40 range provided by the number of encoded characters (used when the Absolute Range uses both the positive and negative integer domains).

The Header block defined in the first table is the same for each of the Ascent, Enroute and Descent reports.

| Header Block |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Standard message header | Character code | N/A | N/A | 10 |
| Version number | Absolute value | N/A | N/A | 2 |
| Type of message format | Character code | N/A | N/A | 1 |
| Altitude Pressure Reference | Character code | N/A | N/A | 1 |
| Date message assembled (day) | Absolute value | 0 to +31 | 0 | 1 |
| Time message assembled (in seconds) | Absolute value | 0 to +86399 | 0 | 4 |
| Departure station | Character code | N/A | N/A | 4 |
| Destination station | Character code | N/A | N/A | 4 |
| Parameter Configuration | Absolute value | 0 to 9 | 0 | 1 |
| Total number of characters |  |  |  | 28 |

Enroute Meteorological Report – CompressedFormat

The Header block is followed by the following data blocks:

| Ascent Initial Report |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Absolute value | -324000 to +324000 | 1,280,000 | 4 |
| Longitude (in seconds) | Absolute value | -647999 to +648000 | 1,280,000 | 4 |
| Date of observation | Absolute value | 0 to +31 | 0 | 1 |
| Time of observation (seconds) | Absolute value | 0 to +86399 | 0 | 4 |
| Series 1 time interval (seconds) | Absolute value | +3 to +20 | 0 | 1 |
| Series 2 time interval (seconds) | Absolute value | +20 to +60 | 0 | 2 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Total number of characters |  |  |  | 30 |

| Ascent Series #1 – FirstSample |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Absolute value | -324000 to +324000 | 1,280,000 | 4 |
| Longitude (in seconds) | Absolute value | -647999 to +648000 | 1,280,000 | 4 |
| Time of observation (seconds) | Absolute value | 0 to +86399 | 1,280,000 | 4 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 32+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

| Ascent Series #1 – SubsequentSamples |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Delta | -32000 to +31999 | 32,000 | 3 |
| Longitude (in seconds) | Delta | -32000 to +31999 | 32,000 | 3 |
| Time of observations (seconds) | Delta | 0 to +32000 | 0 | 3 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 29+ * |
| * Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section, 5.3.15.5.5 Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.Ascent Series #2 – FirstSample |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Absolute value | -324000 to +324000 | 1,280,000 | 4 |
| Longitude (in seconds) | Absolute value | -647999 to +648000 | 1,280,000 | 4 |
| Time of observation (seconds) | Absolute value | 0 to +86399 | 0 | 4 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 32+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

| Ascent Series #2 – SubsequentSamples |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Delta | -32000 to +31999 | 32,000 | 3 |
| Longitude (in seconds) | Delta | -32000 to +31999 | 32,000 | 3 |
| Time of observations (seconds) | Delta | 0 to +32000 | 0 | 3 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 29+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

Enroute Meteorological Report – CompressedFormat

The Header block is followed by the following data blocks:

| Enroute – First Sample |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Absolute value | -324000 to +324000 | 1,280,000 | 4 |
| Longitude (in seconds) | Absolute value | -647999 to +648000 | 1,280,000 | 4 |
| Time of observation (seconds) | Absolute value | 0 to +86399 | 0 | 4 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 32+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

| Enroute – Subsequent Samples |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Absolute value | -324000 to +324000 | 1,280,000 | 4 |
| Longitude (in seconds) | Absolute value | -647999 to +648000 | 1,280,000 | 4 |
| Time of observations (seconds) | Delta | 0 to +32000 | 0 | 3 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 31+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

Descent Meteorological Report – CompressedFormat

The Header block is followed by the data blocks:

| Descent – First Sample |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Absolute value | -324000 to +324000 | 1,280,000 | 4 |
| Longitude (in seconds) | Absolute value | -647999 to +648000 | 1,280,000 | 4 |
| Time of observation (seconds) | Absolute value | 0 to +86399 | 0 | 4 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 32+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

| Descent – Subsequent Samples |
| --- |
| Description | Type | Absolute Range | Base 40 Offset | Number of Encoded Characters |
| Latitude (in seconds) | Delta | -32000 to +31999 | 32,000 | 3 |
| Longitude (in seconds) | Delta | -32000 to +31999 | 32,000 | 3 |
| Time of observations (seconds) | Delta | 0 to +32000 | 0 | 3 |
| Pressure altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| GNSS altitude (tens of feet) | Absolute value | -100 to 5000 | 32,000 | 3 |
| Static air temperature (tenths of deg C) | Absolute value | -800 to +799 | 800 | 2 |
| Wind direction (degrees true) | Absolute value | 0 to +360 | 0 | 2 |
| Wind speed (knots) | Absolute value | 0 to +800 | 0 | 2 |
| Roll angle flag/flight phase | Character | N/A | N/A | 1 |
| WV mixing ratio | Absolute value | 0 to +99999 | 0 | 4 |
| WV mixing ratio quality | Character | N/A | N/A | 1 |
| Icing | Absolute value | 0 to +2 | 0 | 1 |
| Turbulence | Character | N/A | N/A | 1 + 8* |
| True airspeed (knots) | Absolute value | 0 to +999 | 0 | 2* |
| True heading (tenths of degrees) | Absolute value | 0 to +3590 | 0 | 3* |
| De-icing | Absolute value | 0 to +2 | 0 | 1* |
| Aircraft Configuration | Absolute value | 0 to +15 | 0 | 1* |
| Total number of characters |  |  |  | 29+ * |

* Indicates that the number of characters contributed is either as indicated or zero (0), depending on the value of C in the case of turbulence (see Section 5.3.15.5.5, Note 10), or, on the value of Parameter Configuration (see Section 5.3.15.5.5, Notes 12 and 13) in all other cases.

EXAMPLE OF BASE 40 MAPPING TECHNIQUE

Base Chart: The table below illustrates how the 40 characters are mapped to the integer values 0 to 39. Taking 27 as an example, this number is represented by the character R.

|  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0X | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| 1X | A | B | C | D | E | F | G | H | I | J |
| 2X | K | L | M | N | O | P | Q | R | S | T |
| 3X | U | V | W | X | Y | Z | : | , | - | . |

Negative Numbers: To allow negative values to be represented the conversion routine must also do the following:

- Find the range (or the number of characters) required to represent the value (see table below).

- Add an offset value (40y)/2 to the value to compress, where y is the same y value as in the previous step. This provides a new value that falls into the range [0, (40y) – 1].

- Take the new value and convert to a base 40 character string using the existing method.

| Number of characters (y) | Smallest Value Represented 0 – (40y)/2 | Largest Value Represented (40y)/2 – 1 | Offset Value (40y)/2 |
| --- | --- | --- | --- |
| 1 | -20 | +19 | +20 |
| 2 | -800 | +799 | +800 |
| 3 | -32,000 | +31,999 | +32,000 |
| 4 | -1,280,000 | +1,279,999 | +1,280,000 |
| 5 | -51,200,000 | +51,199,999 | +51,200,000 |

COMPRESSION EXAMPLE:

(To code latitude 3º43’30’’ South in seconds)

Step1 (if required)
Convert value into the required units.  3º43’30’’ 
South = ((3 x 3600)+(43 x 60)+30) x (-1) = -13,410 seconds

Step 2
The Absolute Range for Latitude specifies that 4 characters are utilized to provide the required range of values. Therefore the Offset Value to be added to the converted value is 1,280,000.

Step 3
Add the required offset to the value to get the coded value:

Coded value 	= -13,410 + (404)/2 = -13,410 + 1,280,000 = 1,266,590

Step 4
Convert the coded value into base 40 using the Base Chart table above:

Character 1 (most significant):	Trunc (1,266,590/(403)) = 19

From look up table 19 = J

Remainder = 1,266,590 - (19 x 403) = 50590

Character 2				Trunc(50,590/(402)) = 31

From look up table 31 = V

Remainder = 50,590 - (31 x 402) = 990

Character 3				Trunc (990/(401)) = 24

From look up table 24 = O

Remainder = 990 - (24 x 401) = 30

Character 4 (least significant)	From look up table 30 = U

Result
Coded character string is JVOU

Decompression
Decompression of the base 40 value is accomplished with the following steps:

Step 1
Note the number of characters (y) used to represent the full range of the base 40 value: cycy-1...c1

Step 2
Obtain the corresponding integer values nyny-1...n1 for each base 40 character of the base 40 value, cycy-1...c1 from the Base Chart table.

Step 3
Convert the base 40 string to the integer representation of this value:

Integer value = (nYx 40y-1) + (nY-1 x 40y-2) + ... + (n1 x 400)

Step 4
From this integer value subtract (40y)/2 to get the original coded value.

Using the above example with the base 40 value = JVOU:
Integer value = (19 x 403) + (31 x 402) + (24 x 401) + (30 x 400) = 1,266,590

Coded value = 1,266,590 – ((404)/2) = -13,410

# Comments

Confirm this is a requirement for optimisation systems(HRS) If left in, need to change chararcter references.

Review Table to be consistent with AOS

Review Table to be consistent with AOS

This and the following table indicate that it is possible to have a different reporting scheme (time or pressure) for ascent and descent. If we want both to use the same scheme, then we could have a single field in the Basic Configuration table only?

This is clearly intended to  make sure reporting continues during a holding pattern, however I think it makes for an unnecessary complication in the programming and suggest it is removed? If the descent phases ceases then it will resume when the aircraft completes it’s landing.

Review Table to be consistent with AOS

Review Table to be consistent with AOS

# Text boxes

c-4

c-4

c-4

c-4

c-4

c-4