| WORLD METEOROLOGICAL ORGANIZATION __________________ COMMISSION FOR INSTRUMENTS AND METHODS OF OBSERVATION OPAG-SURFACE EXPERT TEAM ON SURFACE TECHNOLOGY AND MEASUREMENT TECHNIQUES Second Session (Geneva, Switzerland, 22-26 September 2008) |  | CIMO/OPAG-SURFACE/ ET-ST&MT-2/Doc. 3.1(1), REV. (18.IX.2008) _____ ITEM: 3.1 Original: ENGLISH |
| --- | --- | --- |

REPORTS ON THE PROGRESS IN ADDRESSING THE WORK PLAN OF THE EXPERT TEAM

Standardization in instrumentation and observations

Identification of siting, performance, classifications and metadata standards

for systems and sensors

(Submitted by Mr Wei Li)

_________________________________________________________________

Summary and purpose of document

This document presents a proposal for siting, performance classification and metadata standards for systems and individual sensors that should eventually cover systems and sensors used for Synoptic and mesoscale meteorology, Climate Marine, Agrometeorology, Hydrology, Urban and Roadway purposes.

_________________________________________________________________

ACTION PROPOSED

The meeting is invited to review this proposal and agree on their adequacy for further development and inclusion on the CIMO Guide.

______________

Siting Classification of AWS

Since AWSs can be very expensive, the stations’ facilities can also be used to satisfy the common and specific needs and requirements of several applications, such as synoptic, aeronautical and agricultural meteorology, hydrology and climatology.

So we can divide siting of AWS into basic observation field, radiation field, extended field, supplemental field.

1.	Basic observation field

To serve for almost all purpose as basic meteorological elements configuration  including air temperature, air humidity, air pressure, wind direction, wind speed, precipitation.  Based on different data applying aim, such as climate Reference standard, climate change and prediction, weather forecasting service, common intelligence service, and others specific service, we can choose suitable site according to specific applying aim.

2.	Radiation observation field

The radiation observation needs specific siting terms.  We can classify radiation siting into reference field and national field.

3.	Extended observation field

(1)	The basic observation elements could not satisfy the observation requirements including surface temperature, soil temperature, and evaporation.  The signal of these sensors will be transferred into AWS processor.

(2)	Individual observation instruments including both sensor and data processor connected with AWS processor including electrical wire ice, snow depth, visibility, cloud amount, cloud type, cloud height, meteorological phenomena and so on.  Those instruments have their own siting technological requirements.

4.	Supplemental observation field

(1)	To carry out parallel observation for same observation elements using different observation instruments.  The similar observation environment and similar observation underlying must be ensured, so the sampled data can be compared.

(2)	To meet special observation aims including nuclear power safety, air and water quality, and road meteorology observation.  Those instruments have their own siting technological requirements, the signal of these sensors will be transferred into AWS processor.

The general principle is that a station should provide measurements that are, and remain, representative of the surrounding area, the size of which depends on the meteorological application.  Existing guidelines for conventional stations are also valid for AWSs and are given in Part I as well as in WMO (1989a; 1990b; 2003a).

Furthermore electromagnetic frequency interference, surrounding environment effect such as environmental elevator, pollution source, radiation effect, traffic effect, supporting condition such as water, electricity and maintenance need to be considered to ensure instrument keeping sable running.

To ensure AWS stale running and get high quality observation data, metadata of AWS must be paid attention too

Metadata of AWSs include contents such as:

  - the testing and calibration of the instruments;

  - the replacement of the collector and sensor;

  - upgrading of the embedded software and operational software;

  - the change of algorism;

  - sensors instalment change; and

  - the environmental change, notes to the systematic bias of the observational data, change of the near surface environmental parameter (including soil property and the surrounding vegetation condition) and the surrounding observational environment, the interference source for observational recording, etc..

All the contents are input in the file according to the XML data structure, with the specification that different data structure following the different properties of the historical data.

AWS is taken as the example:

| No. | Record Item | Record Content | Structure Description |
| --- | --- | --- | --- |
|  | Location change for the observatory | Date of change Latitude Longitude Altitude of the observation site address Geographical environment Distance and direction from the original location |  |
|  | Related parameters changed, no change for location of the observatory | Date of change Latitude Longitude Altitude of the observation site address Geographical environment |  |
|  | Obstruction change | Date of change Position Title of the obstruction Elevation angle Width angle Distance |  |
|  | Increased observational elements | Date of change Elements Sensor Installing height (from the platform or surface) Height form the platform to the surface Sampling frequency |  |
|  | Reduced observational elements | Date of change Elements Sensor |  |
|  | Change with the installation of the sensor | Date of change Sensor Installing height (from the platform or surface) Height form the platform to the surface Notes |  |
|  | Change with the installation parameter, no change with the installation of the sensor | Date of change Time Sensor Installing height (from the platform or surface) Height form the platform to the surface Notes |  |
|  | Variations with the sensitivity of the radiation sensor | Date of change Time Sensor Sensitivity Notes |  |
|  | Change with the sampling frequency | Date of change Time Sensor Original sampling frequency Changed sampling frequency Notes |  |
|  | Change with the algorism of the observed value | Date of change Time Sensor Original algorism Changed algorism Notes |  |
|  | On-site collaboration of the auto-weather station | Date of collaboration Time for the replacement Collector Type Model No. Manufacturer Version of the embedded software Collaborated sensor Collaborating person |  |
|  | Replacement of the collector | Date of change Time Collector Type Model No. Manufacturer Time for collaboration Version of the embedded software Person for replacing |  |
|  | Replacement of the sensor | Date of change Time Sensor Type Model No. Manufacturer Time for collaboration Parameter Person for replacing | <change-sensor> <date>yyyy-mm-dd</date> <time>hh:nn</time> <name>sensor name</name> <type>sensor type</type> <serial>code</serial> <company>manufacturer </company> <inspect-date>inspectdate</inspect-date> <parameter > <para-name1>parameter 1<para-name1> <para-name2> parameter 2<para-name1> <para-name3> parameter 3<para-name1> </parameter> <change-name>change person</change-name> </change-sensor> |
|  | Debugging of the tilting bucket raingauge | Date of debugging Time Sensor Original volume/measured value 1 Original volume/measured value 2 Original volume/measured value3 Debugging person |  |
|  | Upgrading of the software | Date of change Time Original version number for the software Upgraded version number for the software |  |
|  | Change of the soil property | Date of change Time Change description of the soil property Elements likely to be impacted |  |
|  | Change of the surrounding vegetation | Date of change Change description of the vegetation |  |
|  | Rearrangement of the geothermal field | Date of rearrangement Time Description of the soil condition (wet/dry) Rearranging person |  |
|  | Snow accumulation for geothermal sensors | Commencing date for snow accumulation Commencing time for snow accumulation Ending date for snow accumulation Ending time for snow accumulation Snow covered sensors Description of the snow accumulation |  |
|  | Water accumulation for geothermal sensors | Commencing date for water accumulation Commencing time for water accumulation Ending date for water accumulation Ending time for water accumulation Water covered sensors Description of the water accumulation |  |
|  | Grass cover rearrangement for grass temperature observation | Date of rearrangement Time Description of the grass cover Rearranging person |  |
|  | Change of the grass temperature and snow surface observation | Commencing date at the snow surface Commencing time at the snow surface Ending date for snow accumulation Ending time for snow accumulation Sensor Description of the snow accumulation |  |
|  | Notes to the systematic bias of the observational data | Commencing date Commencing time Ending date Ending time Elements Bias description |  |

________________