Тезисы

В докладе представлены методические основы для объективной оценки погрешностей гидрометрических данных в зависимости от частоты и погрешностей измерений расходов воды, характеристик пропускной способности русел и применяемых методик подсчета стока. Количественные оценки погрешностей учета стока получены по данным стандартных измерений на гидрологической сети Росгидромета. Последовательное использование корреляционно-гидравлических характеристик пропускной способности русла с корректной статистической интерпретацией гидрометрических данных позволяет получить для каждого конкретного гидроствора объективные оценки погрешностей учета стока с различной степенью их осреднения от ежедневных (среднесуточных) до среднегодовых. В работе приведены результаты оценки погрешностей учета стока для наиболее   сложных условий протекания потоков и выполнения измерений расходов воды, таких как неустановившийся режим потока в период прохождения паводков (для гидрологических постов горной части бассейна Кубани), ледовые явления  в зимний и переходный периоды (реки северного региона России) и зарастание летом (реки ЕТС России).

T.I.Yakovleva,

(Russia)

ABSTRACT

Estimation of the error in hydrometric consideration of river runoff

Methodological bases for the objective estimation of the error in hydrometric consideration of river runoff depending  on the frequency and precision of measurements, characteristics of river channel capacity, and method of discharge computation are presented in the paper. Quantitative characteristics of the errors are given as applied to the   standard measurements at the hydrological network of the Roshydromet, The model uses some hydraulic characteristics of river channel capacity along with a statistic interpretation of hydrometric data and allows us to obtain an objective estimate of river discharge error for individual gauging stations and for different averaging time periods ranging from daily to annual. The results of estimation the errors for more difficult conditions runoff and measurements such as during ice-affected periods (for rivers of cold region of Russia),  vegetal and aquatic growths at the gauging station at summer (for rivers of Europe path of Russia) and  for mountains rivers (for gauging station of rivers basin of Kubun) are adduced in this paper.