| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/ Doc. 2.1(11) _______ (26.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

GRIB2  for general unstructured grids

Submitted by Sibylle Krebber (DWD)

________________________________________________________________

Summary and Purpose of Document

This document contains proposals from Luis Kornblueh and Uwe Schulzweida (Max-Planck-Institute for Meteorology, Germany)  for the representation of general unstructured grids in GRIB2

_________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the submitted proposal and to consider the possible allocation of the requested template

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

[2]  Reference for CF convention: http://cf-pcmdi.llnl.gov/

[3]  Lecture "ICON – Icosahedral Non-hydrostatic Model", D.Majewski, March 2008

Discussion

#### 1. Background

Currently models with fully unstructured grids are in development in a joint effort between Deutscher Wetterdienst (DWD) and the Max Planck Institute for Meteorology. The grid description is rather large and requires 8 byte IEEE floating-point numbers for sufficient precision for high resolution models. The overhead in saving those in a GRIB record would contradict the most important property which is small size. As well the variety of grids possible would make it difficult to define a simple description. So we propose to reference the grid description in section 3. The referenced files should be made available by the centre given in section 1. It would be highly appreciated, if WMO could hosts a server with referenced files made available. We propose to use the CF convention for describing the unstructured grid, which has been developed in a large international effort with the climate modelling community. This convention develops currently to the de-facto standard.

#### 2. Proposals

Section 3 Grid Definition Section

Grid template 3.101  General Unstructured Grid

Octet no.

15 Shape of the Earth (see Code Table 3.2)

16 – 18 Number of grid used (defined by originating centre)

19 Number of grid in reference (to allow annotating for

Arakawa C-grid on arbitrary grid)  (Note 1)

Notes:

(1) The Number is associated with an attribute of the respective grid

description which consists of the centre longitude/latitude and

the longitude/latitude of the boundary polygon vertices.

Variables can be defined on different positions an the triangle.

This leads to different sets of geo locations, e.g.:

- triangles (i) (pressure, temperature,..)

- quads  (l) (wind velocity ..)

- hexagons respectively pentagons (v) (vorticity)

Example:

Horizontal grid

(primary (Delaunay, triangle) and dual grid (Voronoi, hexagon, pentagon)

ICON grid with three refinement levels

Horizontal grid und grid optimisation

Triangle-C-Grid with mass point, wind point und vorticity point