| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/ Doc. 2.1(12) _______ (26.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

GRIB2 new compression method – CCSDS szip

Submitted by Sibylle Krebber (DWD)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal from Luis Kornblueh and Uwe Schulzweida (Max-Planck-Institute for Meteorology, Germany)  a new compression method in GRIB2

_________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the submitted proposal and to consider the possible allocation of the compression method for validation

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

[2]  Consultative Committee for Space Data Systems: Lossless Data Compression.

CCSDS Recommendation for Space System Data Standards,

CCSDS 121.0-B-1, Blue Book, May 1997.

Discussion

#### 1. Background

Improved packaging of GRIB data is already available by jpeg2000 and png.  We would like to add another algorithm - CCSDS szip. Tests have shown that this compression method is very, very fast and reaches very high compression rates the same time. The proposal is following the previous compression add-ons in Data Representation Template 5.40 and 5.41.

#### 2. Proposals

Data Representation Template 5.42: Grid point and spectral data - CCSDS szip

Preliminary note: For most templates, details of the packing process are described

in regulation 92.9.4

Octet Number(s)		Contents

12-15	        Reference value (R) (IEEE 32-bit floating-point value)

16-17           Binary scale factor (E)

18-19  	        Decimal scale factor (D)

20	        Number of bits required to hold the resulting scaled and referenced data values.

21	        Type of original field values (see Code Table 5.1)

22                szip options mask

23                szip bits per pixel

27-28           szip pixels per block

29-30           szip pixels per scan line

Notes:

(1) The intent of this template is to scale the grid point data to

obtain desired precision, if appropriate, and then subtract out

reference value from the scaled field as is done using Data

Representation Template 5.0.  After this, the resulting grid point

field can be treated as a grayscale image and is then encoded into the

CCSDS szip code stream format.  To unpack the data field, the CCSDS szip

code stream is decoded back into an image, and the original field is

obtained from the image data as described in regulation 92.9.4, Note (4).

(2) The Consultative Committee for Space Data Systems (CCSDS) szip is the

standard used by space agencies for the compression of scientific data

transmitted from satellites and other space instruments. CCSDS szip is

a very fast predictive compression algorithm based on the

extended-Rice algorithm, it uses Golomb-Rice codes for entropy

coding. The sequence of prediction errors is divided into blocks. Each

block is compressed using a two-pass algorithm. In the first pass

the best coding method for the whole block is determined. In the second

pass, output of the marker of the selected coding method as a side

information is done along with prediction errors encoded.

The coding methods include:

- Golomb-Rice codes of a chosen rank

- Unary code for transformed pairs of prediction errors

- Fixed-length natural binary code if the block is found to be incompressible

- Signaling to the decoder empty block if all prediction errors are zeroes

A detailed description can be found in [2].

Note: CCSDS szip is often confused with a general-purpose

compression utility by Schindler, which is also called szip.