| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C Doc. 2.1(8) _______ (15.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

New GRIB2 template for atmospheric aerosols

Submitted by Dr Enrico Fucile (Ecmwf)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new GRIB2 template for aerosol representation.

_________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve

the contents for preoperational implementation.

BACKGROUND AND DISCUSSION

There is a growing need to encode fields related to aerosols. This arises from projects like GEMS or from the recent developments of the environmental models. The principal characteristics of aerosols are the type of aerosol describing the chemical or physical constituent and the range of sizes of the particles composing the aerosol.  The solution of defining some tables containing the size intervals is prone to produce a multiplication of entries as the needs to define new intervals can grow indefinitely. To avoid this problem we propose a new template for aerosol, containing a definition of the range of sizes through the definition of the size limits and the relation defining the interval from code table 4.91.

PROPOSAL

Product Definition Template 4.44: Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for Aerosol

Octet Number(s)		Contents

10		Parameter category (see Code Table 4.1).

11		Parameter number (see Code Table 4.2).

12-13	Aerosol type (see Code Table 4.233)

14               Type of interval for first and second size (see Code Table 4.91)

15		Scale factor of first size

16-19	Scaled value of second size

20		Scale factor of first size

21-24	Scaled value of second size

25		Type of generating process (see Code Table 4.3)

26		Background generating process identifier (defined by originating centre)

27		Analysis or forecast generating processes identifier (defined by originating centre)

28-29	Hours of observational data cutoff after reference time (see Note 1)

30		Minutes of observational data cutoff after reference time

31		Indicator of unit of time range (see Code Table 4.4)

32-33	Forecast time in units defined by octet 18

34		Type of first fixed surface (see Code Table 4.5)

35		Scale factor of first fixed surface

36-39	Scaled value of first fixed surface

40		Type of second fixed surface (see Code Table 4.5)

41		Scale factor of second fixed surface

42-45	Scaled value of second fixed surface

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.45: Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time for Aerosol

Octet Number(s)		Contents

10 		Parameter category (see Code Table 4.1)

11			Parameter number (see Code Table 4.2)

12-13	Aerosol type (see Code Table 4. 233)

14               Type of interval for first and second size (see Code Table 4.91)

15		Scale factor of first size

16-19	Scaled value of second size

20		Scale factor of first size

21-24	Scaled value of second size

25		Type of generating process (see Code Table 4.3)

26		Background generating process identifier (defined by originating Centre)

27 		Forecast generating process identifier (defined by originating Centre)

28-29 	Hours after reference time of data cutoff  (see Note 1)

30    	Minutes after reference time of data cutoff

31		Indicator of unit of time range (see Code Table 4.4)

32-35	Forecast time in units defined by octet 18

36 		Type of first fixed surface (see Code Table 4.5)

37  		Scale factor of first fixed surface

38-41 	Scaled value of first fixed surface

42		Type of second fixed surface (see Code Table 4.5)

43		Scale factor of second fixed surface

44-47	Scaled value of second fixed surface

48		Type of ensemble forecast (see Code Table 4.6)

49		Perturbation number

50		Number of forecasts in ensemble

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.46: Average, accumulation, and/or extreme values or other statistically processed values at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval for Aerosol

Octet Number(s)		Contents

10 	Parameter category (see Code Table 4.1)

11 	Parameter number (see Code Table 4.2)

12-13	Aerosol type (see Code Table 4. 233)

14               Type of interval for first and second size (see Code Table 4.91)

15		Scale factor of first size

16-19	Scaled value of second size

20		Scale factor of first size

21-24	Scaled value of second size

25		Type of generating process (see Code Table 4.3)

26		Background generating process identifier (defined by originating Centre)

27		Analysis or Forecast generating process identifier (defined by originating Centre)

28-29	Hours after reference time of data cut-off  (see Note 1)

30		Minutes after reference time of data cut-off

31		Indicator of unit of time range (see Code Table 4.4)

32-35	Forecast time in units defined by octet 18 (see Note 2)

36		Type of first fixed surface (see Code Table 4.5)

37		Scale factor of first fixed surface

38-41	Scaled value of first fixed surface

42		Type of second fixed surface (see Code Table 4.5)

43		Scale factor of second fixed surface

44-47	Scaled value of second fixed surface

48-49	Year		|

50		Month		|

51		Day		|Time of end of overall time interval

52		Hour		|

53		Minute		|

54		Second

55		n - Number of time range specifications describing the time intervals used to calculate the statistically processed field

56-59	Total number of data values missing in statistical process.

60-71	Specification of the outermost (or only) time range over which statistical processing is done

60		Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10)

61		Type of time increment between successive fields used in the statistical processing (see Code Table 4.11)

62		Indicator of unit of time for time range over which statistical processing is done (see Code Table 4.4)

63-66		Length of the time range over which statistical processing is done, in units defined by the previous octet

67		Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4)

68-71	Time increment between successive fields, in units defined by the previous octet (see Notes 3 and 4)

71-nn	These octets are included only if n>1, where nn = 59 + 12 *  n

71-74	As octets 47 to 58, next innermost step of processing

75-nn		Additional time range specifications, included in accordance with the value of n.  Contents as octets 60 to 71, repeated as necessary.

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples.  Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.

(4)	The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 61, 72 ...).  For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

Product definition template 4.47 -	Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval for Aerosol

Octet No.		Contents

10	Parameter category (see Code table 4.1)

11	Parameter number (see Code table 4.2)

12	Type of generating process (see Code table 4.3)

12-13		Aerosol type (see Code Table 4. 233)

14                	Type of interval for first and second size (see Code Table 4.91)

15		Scale factor of first size

16-19		Scaled value of second size

20		Scale factor of first size

21-24		Scaled value of second size

25	Background generating process identifier (defined by originating centre)

26	Forecast generating process identifier (defined by originating centre)

27-28	Hours after reference time of data cut-off (see Note 1)

29	Minutes after reference time of data cut-off

30	Indicator of unit of time range (see Code table 4.4)

31-34	Forecast time in units defined by octet 18 (see Note 2)

35	Type of first fixed surface (see Code table 4.5)

36	Scale factor of first fixed surface

37-40	Scaled value of first fixed surface

41	Type of second fixed surface (see Code table 4.5)

42	Scale factor of second fixed surface

43-46	Scaled value of second fixed surface

47	Type of ensemble forecast (see Code table 4.6)

48	Perturbation number

49	Number of forecasts in ensemble

50-51	Year of end of overall time interval

52	Month of end of overall time interval

53	Day of end of overall time interval

54	Hour of end of overall time interval

55	Minute of end of overall time interval

56	Second of end of overall time interval

57	n — number of time range specifications describing the time intervals used to calculate the statistically-processed field

58-61	Total number of data values missing in statistical process

62-73	Specification of the outermost (or only) time range over which statistical processing is done

62	Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code table 4.10)

63	Type of time increment between successive fields used in the statistical processing (see Code table 4.11)

64	Indicator of unit of time for time range over which statistical processing is done (see Code table 4.4)

65-68	Length of the time range over which statistical processing is done, in units defined by the previous octet

69	Indicator of unit of time for the increment between the successive fields used (see Code table 4.4)

70-73	Time increment between successive fields, in units defined by the previous octet (see Note 3)

74-nn	These octets are included only if n>1, where nn = 61 + 12 x n

74-85	As octets 62 to 73, next innermost step of processing

74-nn		Additional time range specifications, included in accordance with the value of n. Contents as octets 62 to 73, repeated as necessary

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples.  Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a raingauge.  The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 63, 75 ...).  For all but the innermost (last) time range, the next inner range is then processed using these references and forecast times as the initial reference and forecast time.

New entries in table 4.0

Code Table 4.0:		Product Definition Template Number

Number		Description

44	Aerosol analysis or forecast at a horizontal level or in a horizontal layer at a point in time

45	Aerosol individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time

46	Aerosol average, accumulation, and/or extreme values or other statistically processed values at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

47	Aerosol individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer in a continuous or non continuous time interval for Aerosol

New code table type of interval.

Code Table 4.91: 	Type of Interval

Code figure	Meaning

0		Smaller than first limit

1		Greater than second limit

2		Between first and second limit. The range includes the first limit but not the second limit.

3		Greater than first limit

4		Smaller than second limit

5 		Smaller or equal first limit

6 		Greater or equal second limit

7  			Between first and second. The range includes the first limit and the second limit.

8  		Greater or equal first limit

9  		Smaller or equal second limit

10  		Between first and second limit. The range includes the second limit but not the first limit.

11		Equal to first limit.

12-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.233:	Aerosol type

Code figure	Meaning

0		Total

1		Dust dry

2		Water in ambient

4		Ammonium dry

5		Nitrate dry

6		Nitric acid trihydrate

7		Sulphate dry

8		Mercury dry

9		Sea salt dry

10 		Black carbon dry

11		Particulate organic matter dry

12		Primary particulate organic matter dry

13		Secondary particulate organic matter dry

14-65535	Reserved