| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/ Doc. 2.1(9) _______ (26.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

# New GRIB2  table entries

# Submitted by Dörte Liermann, Sibylle Krebber (DWD)

________________________________________________________________

# Summary and Purpose of Document

This document contains a proposal for the addition of new GRIB2 table entries.

_________________________________________________________________

# ACTION PROPOSED

# The meeting is requested to review the document and approve

the contents for pre-operational implementation.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

Discussion

#### 1. Background

The Deutscher Wetterdienst (DWD) operates global and regional numerical forecast models.  In order to encode the output into GRIB2, new GRIB2 table entries are required as shown below, and a request is made for pre-operational approval of these entries.

Additionally we kindly ask to define a sign convention for meteorological fluxes; we propose that the flux sign convention is positive downwards.

# Meteorological products, Moisture and Cloud category:

- Precipitation parameters can still be found as „amounts“ or „rates“, although it was stated (ET-DRC meetings in 2006 and 2007), that precipitation (amount) is an accumulated (time-integrated) precipitation rate. Therefore the entries for precipitation should be in „rates“, and precipitation amounts should be coded with the statistical process accumulation (using the statistical product definition template 4.8 or 4.11). According to this statement, entries of precipitation amounts should be deprecated. Additionally needed precipitation rates are catalogued below.

- As there is no clear distinction between moisture and cloud category, both categories contain mixing ratios and corresponding total column integrated parameters (e.g. for rain, snow, cloud water, cloud ice, hail and graupel). In our opinion, all of these parameters should be entries in the moisture category and should not be split between cloud and moisture category.

# Meteorological products, Vegetation/Biomass and Soil category:

- It is our opinion that soil temperature and moisture belong to the soil and not to the vegetation category. Therefore our new entries concerning soil moisture are proposed for the soil category.

The corresponding parameters in the Vegetation/Biomass category should be deprecated.

- Additionally we propose new soil type entries in Table 4.213.

# Oceanographic products, Wave category:

ET-WS members, mainly Thomas Bruns (DWD) and Jean Bidlot (ECMWF), have identified missing parameters needed by the wave modelling groups. The final proposal is listed below.

One main problem is the representation of wave spectra, being a function of frequency and direction. To encode these wave spectra a new product definition template is proposed, which is done separately in an additional document.

#### 2. Proposals

# New regulation: The flux sign convention is positive downwards.

# New entries in Code Table 4.2:

| Meteorological products, temperature category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 0 | 18 | Snow temperature (top of snow) | K |
| 0 | 0 | 19 | Turbulent transfer coefficient for heat | 1 |
| 0 | 0 | 20 | Turbulent diffusion coefficient for heat | m² s-1 |

| Meteorological products, moisture category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 1 | 69 | Total column integrated cloud water | kg m-2 |
| 0 | 1 | 70 | Total column integrated cloud ice | kg m-2 |
| 0 | 1 | 71 | Hail mixing ratio | kg kg-1 |
| 0 | 1 | 72 | Total column integrated hail | kg m-2 |
| 0 | 1 | 73 | Hail precipitation rate | kg m-2 s-1 |
| 0 | 1 | 74 | Total column integrated graupel | kg m-2 |
| 0 | 1 | 75 | Graupel (snow pellets) precipitation rate | kg m-2 s-1 |
| 0 | 1 | 76 | Convective rain rate | kg m-2 s-1 |
| 0 | 1 | 77 | Large scale rain rate | kg m-2 s-1 |
| 0 | 1 | 78 | Total column integrated water (all components incl. precipitation) | kg m-2 |
| 0 | 1 | 79 | Evaporation rate | kg m-2 s-1 |
| Parameters which should be deprecated (should be coded as rates): |
| 0 | 1 | 47 | Large scale water precipitation (non-convective) | kg m-2 |
| 0 | 1 | 48 | Convective water precipitation | kg m-2 |
| 0 | 1 | 49 | Total water precipitation | kg m-2 |
| 0 | 1 | 50 | Total snow precipitation | kg m-2 |

| Meteorological products, momentum category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 2 | 31 | Turbulent diffusion coefficient for momentum | m2 s-1 |

| Meteorological products, cloud category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 6 | 25 | Height of convective cloud base | m |
| 0 | 6 | 26 | Height of convective cloud top | m |
| 0 | 6 | 27 | Number concentration of cloud droplets | kg-1 |
| 0 | 6 | 28 | Number concentration of cloud ice | kg-1 |
| 0 | 6 | 29 | Number density of cloud droplets | m-3 |
| 0 | 6 | 30 | Number density of cloud ice | m-3 |
| Parameter to be deprecated (moved to moisture category): |
| 0 | 6 | 17 | Total Condensate | kg kg-1 |
| 0 | 6 | 18 | Total Column-Integrated Cloud Water | kg m-2 |
| 0 | 6 | 19 | Total Column-Integrated Cloud Ice | kg m-2 |
| 0 | 6 | 20 | Total Column-Integrated Condensate | kg m-2 |
| 0 | 6 | 23 | Cloud ice mixing ratio | kg kg-1 |

| Meteorological products, Thermodynamic Stability category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 7 | 13 | Showalter index | K |

| Meteorological products, Aerosol category: could be coded according to Proposal 2.1(5), if accepted |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 13 | 1 | Optical depth of total sulfate aerosol | 1 |
| 0 | 13 | 2 | Optical depth of total soil dust aerosol | 1 |
| 0 | 13 | 3 | Optical depth of organic aerosol | 1 |
| 0 | 13 | 4 | Optical depth of black carbon aerosol | 1 |
| 0 | 13 | 5 | Optical depth of sea salt aerosol | 1 |

| Meteorological products, Radar category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 15 | 9 | Reflectivity of cloud droplets | dB |
| 0 | 15 | 10 | Reflectivity of cloud ice | dB |
| 0 | 15 | 11 | Reflectivity of snow | dB |
| 0 | 15 | 12 | Reflectivity of rain | dB |
| 0 | 15 | 13 | Reflectivity of graupel | dB |
| 0 | 15 | 14 | Reflectivity of hail | dB |

| Meteorological products, Physical Atmospheric properties category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 19 | 20 | Convective turbulent kinetic energy | J kg-1 |
| 0 | 19 | 21 | Weather Interpretation ww (WMO) | - |

| Meteorological products, Miscellaneous category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 0 | 191 | 1 | Geographical latitude | deg N |
| 0 | 191 | 2 | Geographical longitude | deg E |

| Land Surface products, Vegetation/Biomass category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 2 | 0 | 28 | Leaf area index | 1 |
| 2 | 0 | 29 | Evergreen forest | 1 |
| 2 | 0 | 30 | Deciduous forest | 1 |
| 2 | 0 | 31 | Normalized differential vegetation index (NDVI) | 1 |
| 2 | 0 | 32 | Root depth of vegetation | m |
| Parameters which should be set obsolete (moved to soil category): |
| 2 | 0 | 2 | Soil Temperature | K |
| 2 | 0 | 22 | Soil moisture | kg m-3 |
| 2 | 0 | 23 | Column-integrated soil water | kg m-2 |

| Land Surface products, Soil category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| 2 | 3 | 18 | Soil Temperature | K |
| 2 | 3 | 19 | Soil moisture | kg m-3 |
| 2 | 3 | 20 | Column-integrated soil moisture | kg m-2 |
| 2 | 3 | 21 | Soil ice | kg m-3 |
| 2 | 3 | 22 | Column-integrated soil ice | kg m-2 |

# New entries in CODE TABLE 4.213: SOIL TYPE

Code figure            		Meaning

- Loam

- Peat

- Rock

- Ice

- Water

New entries for Oceanographic products, wave category

New table entries for the wave modelling group are given in a structured way, distinguishing between total waves, wind and swell waves. For the sake of clarity the already defined parameter numbers are additionally given in bold numbers.

Wave spectra, a function of frequency and/or direction, could be encoded with Data Representation Template 5.1 (Matrix values at grid point). This template has the disadvantage of creating very large arrays, e.g. a global grid of spectra with 36 directions and 30 frequencies would result in file sizes about 1000 times larger than usual. For large grids we therefore recommend to use Data Representation Template 5.0 (Grid point data), e.g. spectral energy is stored as a field of scalars for each frequency-direction bin, in combination with a new Product Definition Template. For a complete reconstruction of a global field of wave spectra, information on direction, frequency, total number of directions and frequencies must be available. So we suggest creating a new Product Definition Template 4.50: Analysis or forecast of a multi component parameter or matrix element at a point in time, in this special case: Analysis or forecast of Spectral Wave Energy at a given direction and frequency at a point in time. The proposal for this new Product Definition Template will be presented in a separate document Doc. 2.1(10).

| Oceanographic products, wave category |
| --- |
| DISCIPLINE | CATEGORY | Proposed PARAMETER number | PARAMETER NAME | Unit |
| Wave Spectra (Wave Energy normalized by (g, directional bins are *degree true*, i.e. oceanographic convention) |
| 10 | 0 | 0 | 2-dim Spectral Energy Density E(f,() | m²s |
| 10 | 0 | 14 | Log-10-based 2-dim Spectral Energy Density E(f,() | non-dim |
| 10 | 0 | 1 | Frequency Spectral Energy Density E(f) = (E(f,()d( | m²s |
| 10 | 0 | 2 | Directional Spectral Energy Density E(()= (E(f,()df /m0 | non-dim |

| Spectral Source Terms Si(f,() of the Energy Balance Equation |
| --- |
| 10 | 0 | 15 | Wind Input Source Term | m²s |
| 10 | 0 | 16 | Quadruplet Wave-Wave Interaction Source Term | m²s |
| 10 | 0 | 17 | Triad Wave-Wave Interaction Source Term | m²s |
| 10 | 0 | 18 | White-Capping Dissipation Source Term | m²s |
| 10 | 0 | 19 | Swell Dissipation Source Term | m²s |
| 10 | 0 | 20 | Surf Breaking Dissipation Source Term | m²s |
| 10 | 0 | 21 | Bottom Friction Dissipation | m²s |
| 10 | 0 | 22 | Bottom Scattering Source Term | m²s |

| Integral Parameters of Wave Spectra |
| --- |
| Spectral Moments of the Total Spectrum mn = ( fn E(f) df |
| 10 | 0 | 23 | 0’th order Moment m0 | m² |
| 10 | 0 | 24 | 1st order Moment m1 | m²/s |
| 10 | 0 | 25 | 2nd order Moment m2 | m²/s² |
| 10 | 0 | 26 | 3rd order Moment m3 | m²/s³ |
| 10 | 0 | 27 | 4’th order Moment m4 | m²/s4 |
| 10 | 0 | 28 | 1st order negative Moment m-1 | m²s |
| 10 | 0 | 29 | 2nd order negative Moment m-2 | m²s² |
| Characteristics of the Total Spectrum |
| 10 | 0 | 3 | Significant Wave height | m |
| 10 | 0 | 30 | Significant Height of Waves with Periods below 10s | m |
| 10 | 0 | 31 | Significant Height of Waves with Periods below 12s | m |
| 10 | 0 | 32 | Mean Wave Direction *) | Deg true |
| 10 | 0 | 33 | Wave u-component | m |
| 10 | 0 | 34 | Wave v-component | m |
| 10 | 0 | 35 | Wave Spectral Directional Width *) | Deg true |
| 10 | 0 | 36 | Directional Spreading | non-dim |
| 10 | 0 | 37 | Mean (Energy) Wave Period (Tm-10) *) | s |
| 10 | 0 | 38 | Wave Period (Tm01) *) (corresponding to the Mean Frequency) | s |
| 10 | 0 | 39 | Mean Wave Period (Tm02) *) (corresponding to the Mean Zero-Downcrossing Period Tz) | s |
| 10 | 0 | 40 | Peak Wave Period | s |
| 10 | 0 | 41 | Peak Period of 1D-Frequency Spectra | s |
| 10 | 0 | 42 | Wave Steepness *) | non-dim |
| 10 | 0 | 43 | Mean Square Slope | non-dim |
| 10 | 0 | 44 | Kurtosis of Sea Surface Elevation *) | non-dim |
| 10 | 0 | 45 | Peakedness (after Goda) *) | non-dim |
| 10 | 0 | 46 | Benjamin-Feir-Index *) | non-dim |
| 10 | 0 | 47 | Maximum Height of an Individual Wave | m |
| 10 | 0 | 48 | Period of Maximum Individual Wave | s |
| *) see definitions in section 6.7 of http://www.ecmwf.int/research/ifsdocs/CY31r1/WAVES/IFSPart7.pdf |

| Characteristics of Wind Waves |
| --- |
| 10 | 0 | 5 | Significant Height of Wind Waves | m |
| 10 | 0 | 4 | Mean Direction of Wind waves | Deg true |
| 10 | 0 | 49 | u-component of Wind Waves | m |
| 10 | 0 | 50 | v-component of Wind Waves | m |
| 10 | 0 | 51 | Wave Spectral Directional Width of Wind Waves | non-dim |
| 10 | 0 | 52 | Directional Spreading of Wind Waves | non-dim |
| 10 | 0 | 6 | Mean (Energy) Period (Tm-10 ) of Wind Waves | s |
| 10 | 0 | 53 | Mean Period (Tm01) of Wind Waves | s |
| 10 | 0 | 54 | Mean Period (Tm02) of Wind Waves | s |
| 10 | 0 | 55 | Peak Period of Wind Waves | s |
| 10 | 0 | 56 | Peak Direction of Wind Waves | Deg true |
| 10 | 0 | 57 | Peak Length of Wind Waves | m |
| 10 | 0 | 58 | Peak Phase Velocity of Wind Waves | m/s |
| 10 | 0 | 59 | Peak Group Velocity of Wind Waves | m/s |

| Characteristics of (Total) Swell Waves (Residual of Total Spectrum minus Wind Sea Spectrum) |
| --- |
| 10 | 0 | 8 | Significant Height of Swell Waves | m |
| 10 | 0 | 7 | Mean Direction of Swell waves | Deg true |
| 10 | 0 | 60 | u-component of Swell Waves | m |
| 10 | 0 | 61 | v-component of Swell Waves | m |
| 10 | 0 | 62 | Wave Spectral Directional Width of Swell Waves | non-dim |
| 10 | 0 | 63 | Directional Spreading of Swell Waves | non-dim |
| 10 | 0 | 9 | Mean (Energy) Period (Tm-10 ) of Swell Waves | s |
| 10 | 0 | 64 | Mean Period (Tm01) of Swell Waves | s |
| 10 | 0 | 65 | Mean Period (Tm02) of Swell Waves | s |
| 10 | 0 | 66 | Peak Period of Swell Waves | s |
| 10 | 0 | 67 | Peak Direction of Swell Waves | Deg true |
| 10 | 0 | 68 | Peak Length of Swell Waves | m |
| 10 | 0 | 69 | Peak Phase Velocity of Swell Waves | m/s |
| 10 | 0 | 70 | Peak Group Velocity of Swell Waves | m/s |

| Characteristics of Primary Swell Waves |
| --- |
| 10 | 0 | 71 | Significant Height of Primary Swell Waves | m |
| 10 | 0 | 72 | Mean Direction of Primary Swell Waves | Deg true |
| 10 | 0 | 73 | u-component of Primary Swell Waves | m |
| 10 | 0 | 74 | v-component of Primary Swell Waves | m |
| 10 | 0 | 75 | Wave Spectral Directional Width of Primary Swell Waves | non-dim |
| 10 | 0 | 76 | Directional Spreading of Primary Swell Waves | non-dim |
| 10 | 0 | 77 | Mean (Energy) Period (Tm-10) of Primary Swell Waves | s |
| 10 | 0 | 78 | Mean Period (Tm01) of Primary Swell Waves | s |
| 10 | 0 | 79 | Mean Period (Tm02) of Primary Swell Waves | s |
| 10 | 0 | 80 | Peak Period of Primary Swell Waves | s |
| 10 | 0 | 81 | Peak Direction of Primary Swell Waves | Deg true |
| 10 | 0 | 82 | Peak Length of Primary Swell Waves | m |
| 10 | 0 | 83 | Peak Phase Velocity of Primary Swell Waves | m/s |
| 10 | 0 | 84 | Peak Group Velocity of Primary Swell Waves | m/s |

| Characteristics of Secondary Swell Waves (Residual) |
| --- |
| 10 | 0 | 85 | Significant Height of Secondary Swell Waves | m |
| 10 | 0 | 86 | Mean Direction of Secondary Swell Waves | Deg true |
| 10 | 0 | 87 | u-component of Secondary Swell Waves | m |
| 10 | 0 | 88 | v-component of Secondary Swell Waves | m |
| 10 | 0 | 89 | Wave Spectral Directional Width of Secondary Swell Waves | non-dim |
| 10 | 0 | 90 | Directional Spreading of Secondary Swell Waves | non-dim |
| 10 | 0 | 91 | Mean (Energy) Period (Tm-10) of Secondary Swell Waves | s |
| 10 | 0 | 92 | Mean Period (Tm01) of Secondary Swell Waves | s |
| 10 | 0 | 93 | Mean Period (Tm02) of Secondary Swell Waves | s |
| 10 | 0 | 94 | Peak Period of Secondary Swell Waves | s |
| 10 | 0 | 95 | Peak Direction of Secondary Swell Waves | Deg true |
| 10 | 0 | 96 | Peak Length of Secondary Swell Waves | m |
| 10 | 0 | 97 | Peak Phase Velocity of Secondary Swell Waves | m/s |
| 10 | 0 | 98 | Peak Group Velocity of Secondary Swell Waves | m/s |

| Characteristics of Primary Waves (Spectral Partitioning without using Wind Information) |
| --- |
| 10 | 0 | 99 | Significant Height of Primary Waves | m |
| 10 | 0 | 10 | Mean Direction of Primary Waves | Deg true |
| 10 | 0 | 100 | u-component of Primary Waves | m |
| 10 | 0 | 101 | v-component of Primary Waves | m |
| 10 | 0 | 102 | Wave Spectral Directional Width of Primary Waves | non-dim |
| 10 | 0 | 103 | Directional Spreading of Primary Waves | non-dim |
| 10 | 0 | 11 | Mean (Energy) Period (Tm-10) of Primary Waves | s |
| 10 | 0 | 104 | Mean Period (Tm01) of Primary Waves | s |
| 10 | 0 | 105 | Mean Period (Tm02) of Primary Waves | s |
| 10 | 0 | 106 | Peak Period of Primary Waves | s |
| 10 | 0 | 107 | Peak Direction of Primary Waves | Deg true |
| 10 | 0 | 108 | Peak Length of Primary Waves | m |
| 10 | 0 | 109 | Peak Phase Velocity of Primary Waves | m/s |
| 10 | 0 | 110 | Peak Group Velocity of Primary Waves | m/s |

| Characteristics of Secondary Waves (Residual) |
| --- |
| 10 | 0 | 111 | Significant Height of Secondary Waves | m |
| 10 | 0 | 12 | Mean Direction of Secondary Waves | Deg true |
| 10 | 0 | 112 | u-component of Secondary Waves | m |
| 10 | 0 | 113 | v-component of Secondary Waves | m |
| 10 | 0 | 114 | Wave Spectral Directional Width of Secondary Waves | non-dim |
| 10 | 0 | 115 | Directional Spreading of Secondary Waves | non-dim |
| 10 | 0 | 116 | Mean (Energy) Period (Tm-10) of Secondary Waves | s |
| 10 | 0 | 13 | Mean Period (Tm01) of Secondary Waves | s |
| 10 | 0 | 117 | Mean Period (Tm02) of Secondary Waves | s |
| 10 | 0 | 118 | Peak Period of Secondary Waves | s |
| 10 | 0 | 119 | Peak Direction of Secondary Waves | Deg true |
| 10 | 0 | 120 | Peak Length of Secondary Waves | m |
| 10 | 0 | 121 | Peak Phase Velocity of Secondary Waves | m/s |
| 10 | 0 | 122 | Peak Group Velocity of Secondary Waves | m/s |

| Wave Measurements *) |
| --- |
| 10 | 0 | 123 | (Gridded) Altimeter Wave Height | m |
| 10 | 0 | 124 | (Gridded) corrected Altimeter Wave Height | m |
| 10 | 0 | 125 | (Gridded) Altimeter Range Relative Correction | m |
| *) see definitions in section 6.7 of http://www.ecmwf.int/research/ifsdocs/CY31r1/WAVES/IFSPart7.pdf |

| Wave Model Forcing Parameters |
| --- |
| 10 | 0 | 126 | Wave Model Wind Speed *) | m/s |
| 10 | 0 | 127 | Wave Model Wind Direction | Deg true |
| 10 | 0 | 128 | Wave Model Wind Speed U-Comp. | m/s |
| 10 | 0 | 129 | Wave Model Wind Speed V-Comp. | m/s |
| 10 | 0 | 130 | Friction Velocity | m/s |
| 10 | 0 | 131 | Drag Coefficient | non-dim |
| 10 | 0 | 132 | Wave Stress | N/m² |
| *) see definitions in section 6.7 of http://www.ecmwf.int/research/ifsdocs/CY31r1/WAVES/IFSPart7.pdf |