| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C Doc. 3.1.12(1) _______ (22.VII.2008) ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for GFA data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new BUFR descriptors to be used in the reporting of GFA  (Graphical Forecast AIRMET) data.

_________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve

the contents for preoperational implementation.

BACKGROUND AND DISCUSSION

During the past two years, the U.S. NCEP Aviation Weather Center (AWC) has worked to develop an application for the generation of GFA (Graphical Forecast AIRMET) messages.  The resulting graphical output depicts significant aviation hazards and elements over short time scales, and in much greater detail than can be represented within the official ICAO AIRMET text format.  This detailed information is of great interest to certain elements of the U.S. aviation community as well as other potential customers in Canada and elsewhere, so in order to easily disseminate such information to these customers, new BUFR sequences were developed and tested.  During this process, an effort was made to utilize many of the same BUFR descriptors and sequences that were previously approved for use in the reporting of SIGMET messages; however, a few additional descriptors and sequences were also required as shown in the below proposal.  Even though this is not an official ICAO requirement, the new GFA application will nevertheless allow AWC to provide the requested level of detail to those customers who are able to receive and process BUFR messages, while at the same time continuing to provide backward-capable generation of the ICAO AIRMET text format for others.

An initial draft of the below proposal, along with several sample BUFR files and corresponding documentation, was provided via email to the ET/DR+C in October 2006, and a formal follow-up proposal was presented to the ET/DR+C meeting at Darmstadt in April 2007, at which time several other centers expressed a willingness to assist in validation.  To that end, a final proposal, along with sample BUFR files and extensive documentation, was provided via email to the ET/DR+C membership in May 2008.  No responses have been received to date, so given the apparent lack of interest in this data by other centers, we respectfully request that the below proposal be accorded preoperational status.  This would allow AWC to begin disseminating GFA messages to select customers (under a bilateral arrangement) during September 2008.  In making this request, we would again emphasize that this proposal, which does not evolve from any actual ICAO requirement, is intended to represent a superset of the information available within the ICAO AIRMET text format, rather than just merely the information available within that format.

PROPOSAL

#### Proposed Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 01 039 | Graphical Area Forecast (GFA) sequence identifier | CCITT IA5 | 0 | 0 | 40 | Character | 0 | 5 |
| 0 20 006 | Flight Rules | Code Table | 0 | 0 | 3 | Code Table | 0 | 1 |

Add the following new code/flag table values for BUFR/CREX Table B descriptors:

0 08 040

34	Freezing level base

35	Freezing level top

36	Flight level base

37	Flight level top

0 08 041

8	IFR Ceiling and Visibility

9	Mountain obscuration

10	Strong surface wind

11	Freezing level

12	Multiple freezing level

0 20 023

13	Wind shear

0 20 025

14	Cloud

15 	Precipitation

Code tables for proposed new Table B descriptors:

| Code Figure | 0 20 006 Flight Rules |
| --- | --- |
| 0 | Low Instrument Flight Rules - Ceiling < 500 feet and/or Visibility < 1 mile |
| 1 | Instrument Flight Rules - Ceiling < 1000 feet and/or Visibility < 3 miles |
| 2 | Marginal Visual Flight Rules – 1000 feet <= Ceiling < 3000 feet and/or 3 miles <= Visibility < 5 miles |
| 3 | Visual Flight Rules - Ceiling >= 3000 feet and/or Visibility >= 5 miles |
| 4-6 | Reserved |
| 7 | Missing value |

New Table D descriptors:

|  |  | (Graphical AIRMET Sierra) |
| --- | --- | --- |
| 3 16 051 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 055 | GFA IFR Ceiling and Visibility |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 056 | GFA Mountain Obscuration |
|  |  | (Graphical AIRMET Tango) |
| 3 16 052 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 057 | GFA Turbulence |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 058 | GFA Strong Surface Wind |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 059 | GFA Low-Level Wind Shear |
|  |  | (Graphical AIRMET Zulu) |
| 3 16 053 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 060 | GFA Icing |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 061 | GFA Freezing Level |

|  |  | (GFA Identifier and Observed/Forecast Location) |
| --- | --- | --- |
| 3 16 054 | 0 01 039 | GFA sequence identifier |
|  | 0 08 021 | Time significance, 4=Forecast, 16=Analysis |
|  | 3 01 014 | Time period (for which hazard is being observed/forecast) |
|  | 3 01 027 | Description of Feature |
|  | 0 08 021 | Time Significance, Missing=Cancel |

|  |  | (GFA IFR Ceiling and Visibility) |
| --- | --- | --- |
| 3 16 055 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 8=IFR Ceiling and Visibility |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 006 | Flight rules, 1=IFR |
|  | 0 33 042 | Type of limit represented by following (cloud base) value, 2=Exclusive upper limit, 7=Missing |
|  | 0 20 013 | Height of base of cloud |
|  | 0 33 042 | Type of limit represented by following (visibility) value, 2=Exclusive upper limit, 7=Missing |
|  | 0 20 001 | Horizontal visibility |
|  | 0 20 025 | Obscuration |
|  | 0 20 026 | Character of obscuration, 6=Blowing, 15=Missing |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Mountain Obscuration) |
| 3 16 056 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 9=Mountain obscuration |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 006 | Flight rules, 1=IFR |
|  | 0 20 025 | Obscuration |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Turbulence) |
| 3 16 057 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 011 | Meteorological feature, 13=Turbulence |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 11 031 | Degree of turbulence, 6=Moderate |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Strong Surface Wind) |
| 3 16 058 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 10=Strong surface wind |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 33 042 | Type of limit represented by following (wind speed) value, 0=Exclusive lower limit |
|  | 0 11 012 | Wind speed at 10 m |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |

|  |  | (GFA Low-Level Wind Shear) |
| --- | --- | --- |
| 3 16 059 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 011 | Meteorological feature, 16=Phenomenon |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 023 | Other weather phenomena, bit 12=Wind shear |
|  | 0 20 024 | Intensity of phenomena |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |

|  |  | (GFA Icing) |
| --- | --- | --- |
| 3 16 060 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 011 | Meteorological feature, 15=Airframe Icing |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 041 | Airframe icing, 4=Moderate Icing |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Freezing Level) |
| 3 16 061 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 11=Freezing level, 12=Multiple freezing level |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |