| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/ Doc. 3.1.13(1) _______ (26.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

# Entries for volume (3-D) radar data

# Submitted by Thomas Hohmann and Sibylle Krebber (DWD)

________________________________________________________________

# Summary and Purpose of Document

This document contains review results of the proposal for volume radar data (ET/DR&C/Doc. 3.6(6), 2007, Darmstadt)

________________________________________________________________

# ACTION PROPOSED

# The meeting is invited to discuss the content of this document and approve the contents for pre-operational implementation.

# References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

1. Background

Radar volume data is encoded in FM94-BUFR in several national weather services including DWD.  Within DWD this encoding is pre-operational and will become operational until the end of the year.

# 2. Review results

BUFR Table B  entries :

2.1. Evaluated descriptors :

| Table reference |  | BUFR |
| --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width |
| 0 01 097 | Unique product definition | CCITTIA5 | 0 | 0 | 2048 |
| 0 02 137 | Radar DualPRF ratio | Code table | 0 | 0 | 4 |
| 0 02 138 | Antenna rotation direction | Code table | 0 | 0 | 2 |
| 0 05 035 | Maximum size of X-dimension | Numeric | 0 | 0 | 12 |
| 0 06 035 | Maximum size of Y-dimension | Numeric | 0 | 0 | 12 |
| 0 07 035 | Maximum size of Z-dimension | Numeric | 0 | 0 | 12 |
| 0 07 036 | Level index of Z | Numeric | 0 | 0 | 12 |
| 0 21 022 | Range bin offset | m | 1 | 0 | 14 |
| 0 21 023 | Range bin size | m | 0 | 0 | 14 |
| 0 21 024 | Azimuth offset | Degree | 1 | 0 | 12 |
| 0 21 025 | Azimuthal resolution | Degree | 1 | 0 | 8 |
| 0 30 033 | Number of bins along the radial | Numeric | 0 | 0 | 12 |
| 0 30 034 | Number of azimuths | Numeric | 0 | 0 | 12 |

0 02 137

# Radar DualPRF ratio

| Code figure |  |  |
| --- | --- | --- |
| 1 |  | 3:2 |
| 2 |  | 4:3 |
| 3 |  | 5:4 |
| 4-14 |  | Reserved |
| 15 |  | Missing value |

0 02 138

Antenna rotation direction

| Code figure |  |  |
| --- | --- | --- |
| 1 |  | clockwise rotation |
| 2 |  | counterclockwise rotation |
| 3 |  | Missing value |

0 29 001

# Projection type

| Code figure |  |
| --- | --- |
| 0 | Gnomonic projection |
| 1 | Polar stereographic projection |
| 2 | Lambert's conformal conic projection |
| 3 | Mercator's projection |
| 4 | Scanning Cone (radar)* |
| 5 | no projection |
| 6 | Reserved |
| 7 | Missing value |

2.2. Descriptors to be adapted:

| F X Y | Element name | Unit | Scale | Reference value | Data width |
| --- | --- | --- | --- | --- | --- |
| 0 21 018 | extended NYQUIST velocity | m s–1 | 1 | 0 | 10 |
| 0 21 019 | high NYQUIST velocity | m s–1 | 1 | 0 | 10 |

2.3. Descriptor for further validation:

The "Type of product" (descriptor 0 01 098) seems to be redundant information. The information needed can be encoded using descriptor from category 30 (0 30 001 – 0 30 004, 0 30 031 for images and 0 21 XXX for data). So descriptor 0 01 098 should stay in validation status for further discussions.