| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.1.14(1) (22.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

# BUFR Table B and Table D entries for encoding of JASON2 data

# Submitted by EUMETSAT

________________________________________________________________

# Summary and Purpose of Document

This document contains a proposal for addition of new entries in BUFR Tables B and D.

________________________________________________________________

# ACTION PROPOSED

# The meeting is invited to discuss the content of this document and approve the contents for pre-operational status.

# References:

[1] ET/DR&C/Doc. 3.6(7) from ET/DR&C Meeting, Darmstadt, 23-27 April, 2007

[2] Final Report of ET/DR&C Meeting, Darmstadt, 23-27 April, 2007

[3] Manual on Codes, WMO-No. 306, Volume I.2

1. Background

EUMETSAT is encoding the OGDR (operational geophysical data record) data from JASON2 in BUFR in order to exchange these data (in the coming months) on the GTS and via satellite dissemination on EUMETCast.  In reference document [1] new entries to BUFR Tables B and D were proposed for validation.  This proposal was endorsed by the ET/DR&C as per Section 3.3.7 of reference document [2].

During the intervening validation period, some small modifications have been made, resulting in the final Table B and D entries now being used.  The BUFR data are routinely exchanged between EUMETSAT, CNES and NOAA, and the format has been validated by these partners and ECMWF.

In this document, the final BUFR Table B and D entries are presented and proposed fro pre-operational status.

# 2. Expanded descriptor sequence

It is proposed to use the following sequence of entries for the encoding of the JASON2 OGDR data (new entries are in italicised and underlined):

| BUFR | Description | Unit | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
| F X Y | Satellite |  |  |  |  |
| 0 01 007 | SATELLITE IDENTIFIER |  |  |  |  |
| 0 02 019 | SATELLITE INSTRUMENTS |  |  |  |  |
| 0 01 096 | ACQUISITION STATION IDENTIFIER |  |  |  |  |
| 0 25 061 | SOFTWARE IDENTIFICATION |  |  |  |  |
| 0 05 044 | SATELLITE CYCLE NUMBER |  |  |  |  |
| 0 05 040 | ORBIT NUMBER |  |  |  |  |
| 0 01 030 | NUMERICAL MODEL IDENTIFIER |  |  |  |  |
|  | Datation |  |  |  |  |
| 0 04 001 | YEAR |  |  |  |  |
| 0 04 002 | MONTH |  |  |  |  |
| 0 04 003 | DAY |  |  |  |  |
| 0 04 004 | HOUR |  |  |  |  |
| 0 04 005 | MINUTE |  |  |  |  |
| 0 04 007 | SECONDS WITHIN A MINUTE |  |  |  |  |
|  | Location and Surface Type |  |  |  |  |
| 0 05 001 | LATITUDE (HIGH ACCURACY) |  |  |  |  |
| 0 06 001 | LONGITUDE (HIGH ACCURACY) |  |  |  |  |
| 0 08 029 | REMOTELY SENSED SURFACE TYPE |  |  |  |  |
| 0 08 074 | ALTIMETER ECHO TYPE |  |  |  |  |
| 0 08 077 | RADIOMETER SENSED SURFACE TYPE | CODE TABLE | 0 | 0 | 7 |
|  | Flags |  |  |  |  |
| 0 40 011 | INTERPOLATION FLAG | FLAG TABLE | 0 | 0 | 8 |
| 0 25 097 | ORBIT STATE FLAG | CODE TABLE | 0 | 0 | 4 |
| 0 25 095 | ALTIMETER STATE FLAG | CODE TABLE |  |  |  |
| 0 25 098 | ALTIMETER DATA QUALITY FLAG | FLAG TABLE | 0 | 0 | 9 |
| 0 25 099 | ALTIMETER CORRECTION QUALITY FLAG | FLAG TABLE | 0 | 0 | 9 |
| 0 21 144 | ALTIMETER RAIN FLAG |  |  |  |  |
| 0 25 096 | RADIOMETER STATE FLAG |  |  |  |  |
| 0 40 012 | RADIOMETER DATA QUALITY FLAG | FLAG TABLE | 0 | 0 | 8 |
| 0 40 013 | RADIOMETER BRIGHTNESS TEMPERATURE INTERPRETATION FLAG | CODE TABLE | 0 | 0 | 3 |
| 0 21 169 | ICE PRESENCE INDICATOR | CODE TABLE | 0 | 0 | 2 |
|  | Altimeter: Ku Band |  |  |  |  |
| 0 22 151 | KU BAND OCEAN RANGE |  |  |  |  |
| 0 22 162 | RMS OF 20 Hz KU BAND OCEAN RANGE | M | 3 | 0 | 16 |
| 0 22 163 | NUMBER OF 20Hz VALID POINTS FOR KU BAND | NUMERIC | 0 | 0 | 10 |
| 0 25 160 | KU BAND NET INSTRUMENTAL CORRECTION | M | 4 | -120000 | 18 |
| 0 25 133 | SEA STATE BIAS CORRECTION ON KU BAND |  |  |  |  |
| 0 22 156 | KU BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 164 | RMS 20 HZ KU BAND SIGNIFICANT WAVE HEIGHT | M | 3 | 0 | 16 |
| 0 22 165 | NUMBER OF 20HZ VALID POINTS FOR KU BAND SIGNIFICANT WAVE HEIGHT | NUMERIC | 0 | 0 | 10 |
| 0 22 166 | KU BAND NET INSTRUMENTAL CORRECTION FOR SIGNIFICANT WAVE HEIGHT | M | 3 | -1000 | 11 |
| 0 21 137 | KU BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 21 138 | STD KU BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 22 167 | NUMBER OF VALID POINTS FOR KU BAND BACKSCATTER | NUMERIC | 0 | 0 | 10 |
| 0 21 139 | KU BAND NET INSTRUMENTAL CORRECTION FOR AGC |  |  |  |  |
| 0 21 118 | ATTENUATION CORRECTION ON SIGMA-0 |  |  |  |  |
| 0 21 145 | KU BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 13 |
| 0 21 146 | RMS KU BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 8 |
| 0 21 147 | NUMBER OF VALID POINTS FOR KU BAND AUTOMATIC GAIN CONTROL | NUMERIC | 0 | 0 | 5 |
|  | Altimeter: C band |  |  |  |  |
| 0 22 168 | C BAND OCEAN RANGE | M | 3 | 0 | 31 |
| 0 22 169 | RMS OF C BAND OCEAN RANGE | M | 3 | 0 | 16 |
| 0 22 170 | NUMBER OF 20Hz VALID POINTS FOR C BAND | NUMERIC | 0 | 0 | 10 |
| 0 25 161 | C BAND NET INSTRUMENTAL CORRECTION | M | 4 | -120000 | 18 |
| 0 25 162 | SEA STATE BIAS CORRECTION ON C BAND | M | 4 | -6000 | 13 |
| 0 22 171 | C BAND SIGNIFICANT WAVE HEIGHT | M | 3 | 0 | 16 |
| 0 22 172 | RMS 20HZ C BAND SIGNIFICANT WAVE HEIGHT | M | 3 | 0 | 16 |
| 0 22 173 | NUMBER OF 20HZ VALID POINTS FOR C BAND SIGNIFICANT WAVE HEIGHT | NUMERIC | 0 | 0 | 10 |
| 0 22 174 | C BAND NET INSTRUMENTAL CORRECTION FOR SIGNIFICANT WAVE HEIGHT | M | 3 | -1000 | 11 |
| 0 21 170 | C BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT | DB | 2 | -32768 | 16 |
| 0 21 171 | RMS C BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT | DB | 2 | -32768 | 16 |
| 0 22 175 | NUMBER OF VALID POINTS FOR C BAND BACKSCATTER | NUMERIC | 0 | 0 | 10 |
| 0 21 172 | C BAND NET INSTRUMENTAL CORRECTION FOR AGC | DB | 2 | -2048 | 12 |
| 0 21 118 | ATTENUATION CORRECTION ON SIGMA-0 |  |  |  |  |
| 0 21 173 | C BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 13 |
| 0 21 174 | RMS C BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 9 |
| 0 21 175 | NUMBER OF VALID POINTS FOR C BAND AUTOMATIC GAIN CONTROL | NUMERIC | 0 | 0 | 10 |
|  | Radiometer |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 13 090 | RADIOMETER WATER VAPOR CONTENT |  |  |  |  |
| 0 13 091 | RADIOMETER LIQUID CONTENT |  |  |  |  |
|  | Wind |  |  |  |  |
| 0 07 002 | HEIGHT OR ALTITUDE |  |  |  |  |
| 0 11 097 | WIND SPEED FROM ALTIMETER | M/S | 2 | 0 | 12 |
| 0 11 098 | WIND SPEED FROM RADIOMETER | M/S | 2 | 0 | 12 |
| 0 07 002 | HEIGHT OR ALTITUDE |  |  |  |  |
| 0 11 095 | U COMPONENT OF THE MODEL WIND VECTOR |  |  |  |  |
| 0 11 096 | V COMPONENT OF THE MODEL WIND VECTOR |  |  |  |  |
|  | Dynamic Topography |  |  |  |  |
| 0 10 096 | MEAN DYNAMIC TOPOGRAPHY | M | 3 | -131072 | 18 |
| 0 10 081 | ALTITUDE OF COG ABOVE REFERENCE ELLIPSOID |  |  |  |  |
| 0 10 082 | INSTANTANEOUS ALTITUDE RATE |  |  |  |  |
| 0 10 083 | OFF NADIR ANGLE OF THE SATELLITE FROM PLATFORM DATA |  |  |  |  |
| 0 10 101 | SQUARED OFF NADIR ANGLE OF THE SATELLITE FROM WAVEFORM DATA | DEGREES^2 | 2 | -32768 | 16 |
| 0 25 132 | IONOSPHERIC CORRECTION FROM MODEL ON KU BAND |  |  |  |  |
| 0 25 163 | ALTIMETER IONOSPHERIC CORRECTION ON KU BAND | M | 3 | -32768 | 16 |
| 025 126 | MODEL DRY TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 25 128 | MODEL WET TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 25 164 | RADIOMETER WET TROPOSPHERIC CORRECTION | M | 4 | -5000 | 13 |
| 0 10 085 | MEAN SEA SURFACE HEIGHT |  |  |  |  |
| 0 10 097 | MEAN SEA SURFACE HEIGHT FROM ALTIMETER ONLY | M | 3 | -131072 | 18 |
| 0 10 086 | GEOID'S HEIGHT |  |  |  |  |
| 0 10 087 | OCEAN DEPTH/LAND ELEVATION |  |  |  |  |
| 0 10 092 | SOLID EARTH TIDE HEIGHT |  |  |  |  |
| 0 10 088 | GEOCENTRIC OCEAN TIDE HEIGHT SOLUTION 1 |  |  |  |  |
| 0 10 089 | GEOCENTRIC OCEAN TIDE HEIGHT SOLUTION 2 |  |  |  |  |
| 0 10 098 | LOADING TIDE HEIGHT GEOCENTRIC OCEAN TIDE SOLUTION 1 | M | 4 | -2000 | 12 |
| 0 10 099 | LOADING TIDE HEIGHT GEOCENTRIC OCEAN TIDE SOLUTION 2 | M | 4 | -2000 | 12 |
| 0 10 090 | LONG PERIOD TIDE HEIGHT |  |  |  |  |
| 0 10 100 | N0N-EQUILIBRIUM LONG PERIOD TIDE HEIGHT | M | 4 | -2000 | 12 |
| 0 10 093 | GEOCENTRIC POLE TIDE HEIGHT |  |  |  |  |
| 0 25 127 | SEA SURFACE HEIGHT CORRECTION DUE TO PRESSURE LOADING |  |  |  |  |
| 0 40 014 | HIGH FREQUENCY FLUCTUATIONS OF THE SEA SURFACE TOPOGRAPHY CORRECTION | M | 4 | -3000 | 13 |

It is proposed to allocate the Table D entry 3 40 005 for the above sequence.

3. Proposal for code and flag tables

Code Table 0 08 255 (Radiometer sensed surface type) should be based on existing entries 0 08 012 (Land/sea qualifier) and 0 08 029 (Remotely sensed surface type).

0 08 077

# Radiometer sensed surface type

| Code figure |  |
| --- | --- |
| 0 | Land |
| 1 | Sea |
| 2 | Coastal |
| 3 | Open ocean or semi-enclosed sea |
| 4 | Enclosed sea or lake |
| 5 | Continental ice |
| 6-126 | Reserved |
| 127 | Missing value |

0 40 011

# Interpolation flag

| Bit number |  |
| --- | --- |
| 1 | Mean sea surface (MSS) interpolation flag |
| 2 | Ocean tide solution 1 interpolation flag (0=4 points over ocean, 1=less than 4 points) |
| 3 | Ocean tide solution 2 interpolation flag (0=4 points over ocean, 1=less than 4 points) |
| 4 | Meteorological data interpolation flag (0=4 points over ocean, 1=less than 4 points) |
| 5 | Spare |
| 6 | Spare |
| 7 | Spare |
| All 8 bits | Missing |

# 0 25 090

# Orbit state flag

| Code figure |  |
| --- | --- |
| 0 | Orbit computed during a manoeuvre |
| 1 | Adjusted mission operations orbit |
| 2 | Extrapolated mission operations orbit |
| 3 | Adjusted (preliminary/precise) orbit |
| 4 | (preliminary/precise) orbit is estimated during a manoeuvre period |
| 5 | (preliminary/precise) orbit is interpolated over a tracking data gap |
| 6 | (preliminary/precise) orbit is extrapolated for a duration less than 1 day |
| 7 | (preliminary/precise) orbit is extrapolated for a duration that ranges from 1 day to 2 days |
| 8 | (preliminary/precise) orbit is extrapolated for a duration larger than 2 days, or that the orbit is extrapolated just after a manoeuvre |
| 9 | DORIS† DIODE‡ navigator orbit |
| 10 - 14 | Reserved |
| 15 | Missing value |

† DORIS stands for “Doppler Orbitography and Radio-positioning Integrated by Satellite”.

‡ DIODE means "Détermination Immédiate d'Orbite par Doris Embarqué" or immediate onboard orbit determination by DORIS. It is part of the DORIS instrument, which calculates the satellite's position and velocity.

# 0 25 097

# Three dimensional error estimate of the navigator orbit

| Code figure |  |
| --- | --- |
| 0 | Ranges between 0 and 30 cm |
| 1 | Ranges between 30 and 60 cm |
| 2 | Ranges between 60 and 90 cm |
| 3 | Ranges between 90 and 120 cm |
| 4 | Ranges between 120 and 150 cm |
| 5 | Ranges between 150 and 180 cm |
| 6 | Ranges between 180 and 210 cm |
| 7 | Ranges between 210 and 240 cm |
| 8 | Ranges between 240 and 270 cm |
| 9 | Ranges larger than 270 cm |
| 10 - 14 | Reserved |
| 15 | Missing value |

0 25 098

# Altimeter data quality flag

| Bit number | (0 is good, 1 is bad) |
| --- | --- |
| 1 | Ku band range |
| 2 | C band range |
| 3 | Ku band SWH* |
| 4 | C band SWH* |
| 5 | Ku band backscatter coefficient |
| 6 | C band backscatter coefficient |
| 7 | Off nadir angle from Ku band waveform parameters |
| 8 | Off nadir angle from platform |
| All 9 bits | Missing |

* SWH stands for “Significant wave height”

0 25 099

# Altimeter correction quality flag

| Bit number | (0 is good, 1 is bad) |
| --- | --- |
| 1 | Ku band range instrumental correction |
| 2 | C band range instrumental correction |
| 3 | Ku band SWH* instrumental correction |
| 4 | C band SWH* instrumental correction |
| 5 | Ku band backscatter coefficient instrumental correction |
| 6 | C band backscatter coefficient instrumental correction |
| 7 | Spare |
| 8 | Spare |
| All 9 bits | Missing |

* SWH stands for “Significant wave height”

0 40 012

# Radiometer data quality flag

| Bit number | (0 is good, 1 is bad) |
| --- | --- |
| 1 | 18.7 GHz brightness temperature |
| 2 | 23.8 GHz brightness temperature |
| 3 | 34 GHz brightness temperature |
| 4 | Spare |
| 5 | Spare |
| 6 | Spare |
| 7 | Spare |
| All 8 bits | Missing |

0 40 013

# Radiometer brightness temperature interpretation flag

| Code figure |  |
| --- | --- |
| 0 | Interpolation with no gap between JMR§ data |
| 1 | Interpolation with gaps between JMR§ data |
| 2 | Extrapolation of JMR§ data |
| 3 | Failure of extrapolation and interpolation |
| 4 - 6 | Reserved |
| 7 | Missing |

§ JMR stands for “JASON-1 Microwave Radiometer”

0 21 169

# Ice presence indicator

| Code figure |  |
| --- | --- |
| 0 | No ice present |
| 1 | Ice present |
| 2 | Reserved |
| 3 | Missing |

4. Summary

The Meeting is invited to consider the now validated Table B and Table D entries, and the associated Code and Flag Tables.  Based upon the multi-party validation of these entries with live satellite data from JASON2, the Meeting is requested to assign these entries pre-operational status, with a view to their automatically becoming operational at the next opportunity.