| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.1.15(1) ITEM: 3.1 (12. 8. 2008) ENGLISH ONLY |
| --- | --- | --- |

Proposal for BUFR Template TM308011 and TM308012

Submitted by Weiqing Qu (Australia)

________________________________________________________________

Summary and Purpose of Document

This document contains proposal for BUFR template TM 308011 and TM 308012 for

the wave observations from different platforms suitable for WAVEOB data.

.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] Doc8.2, Data Buoy Cooperation Panel, 21st Session, Buenos Aires, Argentina, 17-21

October 2005

1. Background.

Attempt has been made to use the template given in the paragraph 5.4.3 of the final report from ET-DRC Montreal meeting (8-12 May 2006) to convert Australian wave observations in WAVEOB (FM65) into BUFR. However, this template (refer as BuoyTM below), which is originated from Data Buoy Cooperation Panel 21st Session, Buenos Aires, Argentina, 17-21 Oct 2005, is primarily designed to encode data from a PDE buoy, and not suitable for converting TAC WAVEOB or reporting wave observations in BUFR. The major problems for using this template to encode WAVEOB report are as follow:

1).The identification part of BuoyTM cannot handle observations from platforms other than buoy. TAC WAVEOB, however, allows wave observations from different platform (buoy, fixed sea station, ship, satellite).

2) In WAVEOB, the wave data can be expressed as frequency or as wave number, which are different in terms of unit and physical meaning, and has to be handled separately. BuoyTM does not distinguish those two types of wave observations, which makes the conversion of WAVEOB using BuoyTM extremely difficult.

3) BuoyTM does not handle wave observations from different wave sensors.

4) More than two third of the descriptors in BuoyTM are for reporting meteorological observations from a buoy, not for wave observations. Using BuoyTM to encode WAVEOB means that majority of descriptor has to be set missing, which is inefficient.

In summary, BuoyTM seems hand-picked some fields from WAVEOB that suits the PDE buoy, and consequently cannot handle a full WAVEOB report. For this reason two templates have been drafted for converting TAC WAVEOB reports into BUFR, and hopefully also suitable for reporting wave observations in BUFR.

2. Proposal

Two templates have been proposed. The difference between the two is one for reporting wave observations expressed as frequency, and the other for reporting wave observations expressed as wave number. Three new descriptors and one new code table have been introduced (see Notes in the ANNEX).

3. Acknowledgment

The author would like to thank Mr Charles Sanders for his comments and suggestions to the templates. The author also thanks everyone who made the comments in emails prior to the submission of this document.

ANNEX 1: TM 308011 – BUFR template for WAVEOB data expressed as frequency (Ia=0 in FM-65 WAVEOB)

| # | Descriptor | Name (unit) | Expanded descriptors | Remark, Corresponding groups in FM-65 WAVEOB |
| --- | --- | --- | --- | --- |
|  |  | Identification |  |  |
| 1 | 001003 | WMO region | 001003 | A1 - First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO region sub-area | 001020 | bw - Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | nb - Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 001011 | Ship or mobile land station identifier | 001011 | D …… D |
| 5 | 001205 | Satellite Identifier | 001205 | I6 I6 I6 |
| 6 | 001001 | WMO block number | 001001 | II |
| 7 | 001002 | WMO station number | 001002 | iii – IIiii only apply to fixed sea stations. |
| 8 | 002044 | Indicator for method of calculating spectral wave data. | 002044 | Im – TAC code table 1744, BUFR code table 2044 |
| 9 | 002045 | Indicator for type of plateform | 002045 | Ip – TAC code table 1747, BUFR code table 2045 |
| 10 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | J - Date of observation MM YY |
| 11 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | GG - Time of observation Gg |
| 12 | 301021 | Latitude and longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Qc La La La La Lo Lo Lo Lo Lo |
|  |  | Basic data (WAVEOB Section 0) |  |  |
| 13 | 022063 | Total water depth (m) | 022063 | 1hhhh |
| 14 | 105002 | Replecation 5 desc 2 times | 105002 | Replicate over sensor type |
| 15 | 002098 | Type of wave sensor | 002098 | Code table 2098, 0=heave sensor. 1=slope sensor. |
| 16 | 022070 | Significant wave height (m) | 022070 | 2HsHsHsHs or 6HseHseHseHse - section 0 |
| 17 | 022071 | Spectral peak wave period (s) | 022071 | 3PpPpPpPp or 7PspPspPspPsp - section 0 |
| 18 | 022073 | Maximum wave height | 022073 | 4Hm Hm Hm Hm |
| 19 | 022074 | Average wave period (s) | 022074 | 5PaPaPaPa or 8PsaPsaPsaPsa - section 0 |
| 20 | 002098 | Type of wave sensor | 002098 | Set to missing to cancel the previous value. |
| 21 | 022076 | Direction of coming dominant waves (deg) | 022076 | 9dd dd - section 0 |
| 22 | 022077 | Directional spread of dominant wave (deg) | 022077 | ds ds - section 0 |
| 23 | 022094 | Total Number Of Wave Bands | 022094 | 111 BT BT – Section 1 |
| 24 | 025043 | Wave sampling interval (Time, s) | 025043 | SSSS – Section 1 |
| 25 | 022078 | Duration of wave record (s) | 022078 | D’D’D’D’ – Section 1 |
|  |  | Spectral Data (WAVEOB Section 1 – 5) |  |  |
| 26 | 121000 | Replecation 21 desc | 121000 | Replication over sensor type |
| 27 | 031001 | Replication factor | 031001 | (0,1,2) normally 1 |
| 28 | 002098 | Type of wave sensor | 002098 | Code table 2098, 0=heave sensor. 1=slope sensor. |
| 29 | 022082 | Maximum Non-Directional Spectral Wave Density (m2/Hz) | 022082 | Cm Cm Cm - Section 2 or Csm Csm Csm - Section 3 |
| 30 | 022084 | Band Containing Maximum Non-Directional Spectral Wave Density | 022084 | nmnm - Section 2 or nsmnsm - Section 3 |
| 31 | 116000 | Delayed replication 16 descriptors | 116000 | Replication over bands. |
| 32 | 031001 | Replication Factor | 031001 | 111 BT BT – Section 1 (Num of band) |
| 33 | 022080 | Waveband central frequency (Hz) | 022080 | 1f1 f1 f1 f1 x …. – Section 1 |
| 34 | 022085 | Spectral Wave Density Ratio | 022085 | 1 c1 c1 c2 c2 …. – Section 2 or 1 cs1 cs1 cs2 cs2 …. – Section 3 |
| 35 | 022086 | Mean Direction From Which Waves Are Coming (deg) | 022086 | 1da1da1 – Section 4 |
| 36 | 022087 | Principal Direction From Which Waves Are Coming (deg) | 022087 | da2da2 - Section 4 |
| 37 | 022088 | First Normalized Polar Coordinate From Fourier Coefficients | 022088 | r1r1 - Section 4 |
| 38 | 022089 | Second Normalized Polar Coordinate From Fourier Coefficients | 022089 | r2r2 - Section 4 |
| 39 | 103000 | Delayed Replication 3 Descriptors | 103000 |  |
| 40 | 031001 | Replication Factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 1 (Directional) |
| 41 | 022090 | Non-Directional Spectral Estimate By Wave Frequency (m2/Hz) | 022090 | 1 A1 A1 A1 x…… - Section 5 |
| 42 | 022212 | Direction From Which Waves Are Coming (deg) | 022212 | 1 d1 d1 - Section 5 |
| 43 | 022213 | Directional Spread Of Wave (deg) | 022213 | ds ds - Section 5 |
| 44 | 103000 | Delayed Replication 3 Descriptors | 103000 |  |
| 45 | 031001 | Replication Factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 0 (Non-Drectional) |
| 46 | 022092 | Directional Spectral Estimate By Wave Frequency (M2/Hz/Radian) | 022092 | 1 A1 A1 A1 x…… - Section 5 |
| 47 | 022212 | Direction From Which Waves Are Coming (deg) | 022212 | 1 d1 d1 - Section 5 |
| 48 | 022213 | Directional Spread Of Wave (deg) | 022213 | ds ds - Section 5 |
| 49 | 002098 | Type of wave sensor | 002098 | Set to missing to cancel the previous value. |

ANNEX 2: TM 308012 - BUFR template for WAVEOB data expressed as the wave number (Ia=1 in FM-65 WAVEOB).

| # | Descriptor | Name | Expanded descriptors | Remark, Corresponding groups in FM-65 WAVEOB |
| --- | --- | --- | --- | --- |
|  |  | Identification |  |  |
| 1 | 001003 | WMO region | 001003 | A1 - First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO region sub-area | 001020 | bw - Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | nb - Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 001011 | Ship or mobile land station identifier | 001011 | D …… D |
| 5 | 001205 | Satellite Identifier | 001205 | I6 I6 I6 |
| 6 | 001001 | WMO block number | 001001 | II |
| 7 | 001002 | WMO station number | 001002 | iii – IIiii only apply to fixed sea stations. |
| 8 | 002044 | Indicator for method of calculating spectral wave data. | 002044 | Im – TAC code table 1744, BUFR code table 2044 |
| 9 | 002045 | Indicator for type of plateform | 002045 | Ip – TAC code table 1747, BUFR code table 2045 |
| 10 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | J - Date of observation MM YY |
| 11 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | GG - Time of observation Gg |
| 12 | 301021 | Latitude and longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Qc La La La La Lo Lo Lo Lo Lo |
|  |  | Basic data (WAVEOB Section 0) |  |  |
| 13 | 022063 | Total water depth (m) | 022063 | 1hhhh |
| 14 | 105002 | Replecation 5 desc 2 times | 105002 | Replication over sensor type |
| 15 | 002098 | Type of wave sensor | 002098 | Code table 2098, 0=heave sensor. 1=slope sensor. |
| 16 | 022070 | Significant wave height (m) | 022070 | 2HsHsHsHs or 6HseHseHseHse - section 0 |
| 17 | 022072 | Spectral peak wave length (m) | 022072 | 3PpPpPpPp - section 0 |
| 18 | 022073 | Maximum wave height | 022073 | 4Hm Hm Hm Hm |
| 19 | 022075 | Average wave length (m) | 022075 | 5PaPaPaPa - section 0 |
| 20 | 002098 | Type of wave sensor | 002098 | Set to missing to cancel the previous value. |
| 21 | 022076 | Direction of coming dominant waves (deg) | 022076 | 9dd dd - section 0 |
| 22 | 022077 | Directional spread of dominant wave (deg) | 022077 | ds ds - section 0 |
| 23 | 022094 | Total Number Of Wave Bands | 022094 | 111 BT BT – Section 1 |
| 24 | 025044 | Wave sampling interval (Space, m) | 025044 | SSSS – Section 1 |
| 25 | 022079 | Length of wave record (m) | 022079 | D’D’D’D’ – Section 1 |
|  |  | Spectral Data (WAVEOB Section 1 – 5) |  |  |
| 26 | 121000 | Replecation 21 desc | 121000 | Replication over sensor type |
| 27 | 031001 | Replication factor | 031001 | (0,1,2) normally 1 |
| 28 | 002098 | Type of wave sensor | 002098 | Code table 2098, 0=heave sensor. 1=slope sensor. |
| 29 | 022083 | Maximum Non-Directional Spectral Wave Number (m3) | 022083 | Cm Cm Cm - Section 2 or Csm Csm Csm - Section 3 |
| 30 | 022084 | Band Containing Maximum Non-Directional Spectral Wave Density | 022084 | nmnm - Section 2 or nsmnsm - Section 3 |
| 31 | 116000 | Delayed replication 16 descriptors | 116000 | Replication over band |
| 32 | 031001 | Replication Factor | 031001 | 111 BT BT – Section 1 (Num of band) |
| 33 | 022081 | Waveband central wave number (1/m) | 022081 | 1f1 f1 f1 f1 x …. – Section 1 |
| 34 | 022085 | Spectral Wave Density Ratio | 022085 | 1 c1 c1 c2 c2 …. – Section 2 or 1 cs1 cs1 cs2 cs2 …. – Section 3 |
| 35 | 022086 | Mean Direction From Which Waves Are Coming (deg) | 022086 | 1da1da1 - Section 4 |
| 36 | 022087 | Principal Direction From Which Waves Are Coming (deg) | 022087 | da2da2 - Section 4 |
| 37 | 022088 | First Normalized Polar Coordinate From Fourier Coefficients | 022088 | r1r1 - Section 4 |
| 38 | 022089 | Second Normalized Polar Coordinate From Fourier Coefficients | 022089 | r2r2 - Section 4 |
| 39 | 103000 | Delayed Replication 3 Descriptors | 103000 |  |
| 40 | 031001 | Replication Factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 1 (Directional) |
| 41 | 022091 | Non-Directional Spectral Estimate By Wave Number (m3) | 022091 | 1 A1 A1 A1 x…… - Section 5 |
| 42 | 022212 | Direction From Which Waves Are Coming (deg) | 022212 | 1 d1 d1 - Section 5 |
| 43 | 022213 | Directional Spread Of Wave (deg) | 022213 | ds ds - Section 5 |
| 44 | 103000 | Delayed Replication 3 Descriptors | 103000 |  |
| 45 | 031001 | Replication Factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 0 (Non-Drectional) |
| 46 | 022093 | Directional Spectral Estimate By Wave Number (m4) | 022093 | 1 A1 A1 A1 x…… - Section 5 |
| 47 | 022212 | Direction From Which Waves Are Coming (deg) | 022212 | 1 d1 d1 - Section 5 |
| 48 | 022213 | Directional Spread Of Wave (deg) | 022213 | ds ds - Section 5 |
| 49 | 002098 | Type of wave sensor | 002098 | Set to missing to cancel the previous value. |

Notes:

1. Because WAVEOB can be reported from different platform, the descriptors for identification of all possible platforms are all included in the template. The irrelevant descriptors for identification shell be set to missing.

2. New descriptors

002098 is introduced to express the type of wave sensor.

022212 is introduced to express the direction of “any wave”, as appose to the direction of “dominant wave” (022076), “mean direction” (022086), and “principal direction” (022087).

022213 is introduced to express the directional spread of “any wave”, as appose to the directional spread of “dominant wave” (022077).

| TABLE REFERENCE | TABLE ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
|  |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| F | X | Y |  |  |  |  |  |  |  |  |
| 0 | 02 | 098 | Type of wave sensor | Code table | 0 | 0 | 4 | Character | 0 | 2 |
| 0 | 22 | 212 | Direction from which waves are coming | Degree true | 0 | 0 | 9 | Character | 0 | 3 |
| 0 | 22 | 213 | Directional spread of wave | Degree | 0 | 0 | 9 | Character | 0 | 3 |

Code table 002098 (New table)

Code figure

0             Heave sensor.

1             Slope sensor.

2-14        Reserved

15	          Missing Value