| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.1.16(1) ITEM: 3.1 (27. 8. 2008) ENGLISH ONLY |
| --- | --- | --- |

A proposal for Universal BUFR template for representation of Lightning data

Formulated in August 2008

Submitted by Paul Taylor (United Kingdom)

________________________________________________________________

Summary and Purpose of Document

The document contains a preliminary version of a Universal

BUFR template for representation of high resolution Lightning data from any source.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2]  http://www.wmo.ch/pages/prog/www/WMOCodes/OperationalCodes.html

1. Background

As part of the Public Weather Services, the UK Met office have provided a GTS Long range lightning message  from the 1940s in the form old SFLOC messages which covered an area of 40W to 40E, 30 N to 70N. This was declared obsolete, as it no longer reflected the accuracy obtainable by modern systems. A replacement was sought as there was not a suitable alternative available.

Currently the only National BUFR representation of Lightning Data in use is that developed by DWD, all of the elements are included here, but has been expanded to give further elements for other systems.

A early draft of this proposal was presented to the EUMETNET Lightning task force meeting (Exeter 12 to 13 March 2008) Representatives were from France , Germany, Croatia and other countries

The intention is to provide this data to all WMO region 1 National Met Centres over GTS.

Following correspondence with Prof Hans-Dieter Betts (LINNET) for DWD some minor modifications were added to the tables,

Acknowledgements to Stan Kellett, Brian Barwell and Myles Turp of UK Met Office.

### ATDNet Overview

ATDNet was launched 11th December 2007. It is based on the original Arrival Time Difference (ATD) Sferics Very Low Frequency (VLF) sensors that have been in use since 1988, but now the predecessors DSP hardware is now software based, and is hosted on National Instruments plug in cards on a PC. Developments in communications have allowed us to base the connections over the Internet. At the time of writing Sensors are deployed at Keflavik, Helsinki, Lerwick, Valentia, Exeter, Camborne, Payerne, Gibraltar Akrotiri, Azores and La-Reunion. There is intention to deploy others in South Africa and South Atlantic regions. The process uses Global Positioning System (GPS) disciplined Rubidium Oscillators to time stamp a waveform of the received Sferic, this is sent to a Flash Location Processor that correlates the waveforms for all the sensors and then quality controls this data and stores for use. A process then currently gathers the data in five minute periods and distributes the data in various formats, this process is configurable for different time periods.

2. Proposal

Where possible existing code sequences have been adopted, new and modified descriptors are detailed below and are in the annex table.

Note: some form of time replication may be needed for the whole table as there are about 10-40 strokes recorded per second, this really depends on the frequency of sending the messages.

a) Existing code

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 04 007 | Second Within a Minute (Microsecond accuracy) | Second | 6 | 0 | 26 |

Here ATDNet records to a point of a microsecond or 100 nano-seconds. This could be rounded up or truncated, or even  a new value added using an operator 202129 to increase the accuracy to 10**-7, But doing so will cause problems to non 64 bit systems processing the data. I would recommend truncation, but  what do the ETDRC  recommendation here?

An actual value here would be for example 55.1885403 rounded/truncated  to 55.188540

b)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 111 | X-axis error ellipse major component | Km | 2 | 0 | 17 |

Actual value e.g 6.40 Km  range 0.00 to 1000.00 Km

c)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 112 | Y-axis error ellipse minor component | Km | 2 | 0 | 17 |

Here, if  x=y then it is a radial error, and the angle (see 020114) will be zero

Actual value 2.41 Km, range 0.00 to 1000.00 Km

d)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 113 | Z-axis error ellipse component | Km | 2 | 0 | 17 |

Here, if  x=y=z then it is a spherical error, and the angle (see 020115) will be zero

Actual Value 2.46 Km, range as above

e)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 114 | Angle of X-axis in error ellipse | Degree | 2 | -18000 | 16 |

Here is the angle of the error defined in b & c above. Cartesian with sign bit

Actual value 33.40 range -180.00 to 180.00

f)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 115 | Angle of Z-axis in error ellipse | Degree | 2 | -18000 | 16 |

Here is the angle of the error defined in b,c  & d above. Cartesian with sign bit

Actual value 12.45

g)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 116 | Emission Height of Cloud Stroke | M | 0 | 0 | 16 |

This parameter is used by DWD(LINNET)  for height above ground of stroke

Actual Value 1200m range 0-20000

h)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 117 | Amplitude of Lightning Strike | A | 0 | 0 | 18 |

Here we would need to introduce a amplitude measure in Amps or kA. This value was first developed nationally by DWD.

Example 5.6KA coded as 5600 range 0 to 320000

i)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 118 | Lightning Detection Error | M | 0 | 0 | 19 |

This seems to be radial error measured in Metres or Km. An alternative for systems not capable of describing in x,y and z. This value was first developed nationally by DWD.

Example 6900m range 0 to 500000

j)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 119 | Polarity of Stroke | Code table | 0 | 0 | 2 |

| 0 | Not Defined |
| --- | --- |
| 1 | Positive |
| 2 | Negative |
| 3 | Missing Data |

Here we have a simple table self explanatory

k) 020120	Decision Method for Polarity (V or A)			Code table	0,0,3 bits

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 120 | Decision Method for Polarity | Code table | 0 | 0 | 3 |

| 0 | Not Defined |
| --- | --- |
| 1 | Individual voltage deflection |
| 2 | Current based, above a threshold |
| 3 | Voltage based, above a threshold |
| 4 | Consensus of sensors, Current above a threshold |
| 5 | Consensus of sensors, Voltage above a threshold |
| 6 | Reserved |
| 7 | Missing Data |

Certain sensors use a current decision above a threshold, others directly measure the voltage deflection

l)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 121 | Threshold value for Polarity Decision | V | 0 | 0 | 16 |

Used with k) 020120 or all zero if not defined, typically +1 Volt.

m)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 122 | Threshold value for Polarity Decision | A | 0 | 0 | 16 |

Used with k) 020120 or all zero if not defined, typically +2000 A.

n)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 123 | Minimum Threshold for Detection | V/M | 3 | 0 | 16 |

This is the minimum signal level acceptable for processing.

e.g. 0.005v or 5mv , or typically just above the noise floor of the detector.

o)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 124 | Lightning Stroke or Flash | Code table | 0 | 0 | 2 |

| 0 | Not Defined |
| --- | --- |
| 1 | Lightning Stroke |
| 2 | Lightning Flash, by manual observation, or if equipment insensitive to stroke resolution |
| 3 | Missing Data |

Another Simple table

p)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 125 | Modified Residual | Numeric | 2 | 0 | 13 |

Here the modified residual calculated from the loci of the sensors and signal to noise ratios for the flash. Actual  value 0.71 range 0.00 to 10.00

q) Existing code

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 023 | Other Weather | Flag table | 0 | 0 | 18 |

Used to indicate cloud to ground or cloud to cloud.

r)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 126 | Central Processor or system Identifier | Code table | 0 | 0 | 8 |

| 0 | Not Defined |
| --- | --- |
| 1 | Main Processor |
| 2 | Backup Processor |
| 3-254 | Reserved |
| 255 | Missing Data |

This is where we identify the Flash Location Processor or system  identity so that in multi integrated system we can identify where the event location was developed. Typically 1 here

s)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 1 00 001 | Delayed replication of 1 descriptor |  |  |  |  |
| 0 31 002 | Extended delayed descriptor replication factor | Numeric |  |  |  |
| 3 03 054 | New Sequence Descriptor |  |  |  |  |

As presented, this will define the number or sensors and locations taking part in the lightning stroke. This would be a minimum of 4 for ATDNet, typically 8 sensors contributing to the actual strike.

t) existing code

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 02 184 | Type of Lightning Sensor | Code table | 0 | 0 | 4 |

Here we need to introduce at least the ATDNet VLF waveform correlated sensor. Or code as 4

u) Existing code

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 02 121 | Mean Frequency | Hertz | -8 | 0 | 7 |

Here this is where systems could be split into cells that work on different frequencies

You would need to know which sensors are associated with this frequency

Actual value 13777 Hz so we change scales, with 202136,201236, before and reset after with 201000 and 202000.

In summary, we need at least 16 new descriptors.

ANNEX

Universal BUFR  template for representation of Lightning data.

This template is suitable for representation of high resolution lightning data from Land, Ship, Mobile, Aircraft or Satellite. Developed by Paul Taylor Observations Development UK Met Office.

|  |  | Date/time of lightning event |  |
| --- | --- | --- | --- |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
|  | 0 04 007 | Second within a minute (Microsecond accuracy) | Second |
|  |  | Horizontal and vertical coordinates of lightning event |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 20 111 | X-Axis error ellipse | Km scale 2,0,17 |
|  | 0 20 112 | Y-Axis error ellipse | Km scale 2,0,17 |
|  | 0 20 113 | Z-Axis error ellipse | Km scale 2,0,17 |
|  | 0 20 114 | Angle of X-Axis in error ellipse | Degree scale 2,-18000,16 |
|  | 0 20 115 | Angle of Z-Axis in error ellipse | Degree scale 2,-18000,16 |
|  | 0 20 116 | Emission Height of cloud stroke | M scale 0,0,16 |
|  |  | Emission information |  |
|  | 0 20 117 | Amplitude of Lightning Strike | A, scale 1,0,15 |
|  | 0 20 118 | Lightning Detection Error | M, scale 0,0,15 |
|  | 0 20 119 | Polarity of stroke | Code table scale 0,0,2 |
|  | 0 20 120 | Decision Method for Polarity (V or A) | Code table scale 0,0,3 |
|  | 0 20 121 | Threshold value for Polarity decision | V scale 0,0,16 |
|  | 0 20 122 | Threshold value for Polarity decision | A scale 0,0,16 |
|  | 0 20 123 | Minimum threshold for Detection | V/M scale 3,0,16 |
|  | 0 20 124 | Lightning Stroke or Flash | Code table scale 0,0,2 |
|  | 0 20 125 | Modified Residual | Numeric scale2,0,13 |
|  | 0 20 023 | Other Weather (for c2g or c2c identification) | Flag table scale 0,0,18 |
|  |  | Sensor Processing |  |
|  | 0 20 126 | Central Processor Identifier | Code table, scale 0,0,8 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor Number of Sensors contributing | Numeric |
| 3 03 055 |  | Identification of sensor site and instrumentation |  |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 001 | Type of Station | Code table |
|  | 0 02 184 | Type of Lightning Detection Sensor | Code table |
|  | 0 02 189 | Capability to Discriminate Lightning Strike | Flag table |
|  | 0 02 036 | Atmospherics Location Method | Code table |
| 202136 |  |  |  |
| 201136 |  |  |  |
|  | 0 02 121 | Mean Frequency (to define centre frequency, if used) | Hertz,scale1,7 |
| 201000 |  |  |  |
| 202000 |  |  |  |
|  | 0 25 061 | Software identification and version number | CCITT IA5 |
|  | 3 01 021 | Latitude (high accuracy) of sensor | Degree, scale 5 |
|  |  | Longitude (high accuracy) of sensor | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 032 | Height of sensor above local ground (for lightning) | m, scale 1 |