| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/ Doc. 3.1.6(1), ADD.1 ITEM: 3.1 (29. 8. 2008) ENGLISH ONLY |
| --- | --- | --- |

BUFR template for representation of SYNOP data

with supplementary information on one-hour observations

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains the latest version of BUFR template suitable

for reporting SYNOP data and surface observations from one-hour period based on discussion with Météo-France this week.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Final Report, Joint meeting of Coordination Team on Migration to TDCF and Expert Team on

Data Representation and Codes, Montreal, Canada, 8 to 12 May 2006

[3] Final Report, Meeting of Expert Team on Data Representation and Codes, Darmstadt,

Germany, 23 to 27 April 2007

[4] Final Report, Meeting of Expert Team on Requirements for Data from Automatic Weather

Stations, Geneva, Switzerland, 5 to 9 May 2008

BUFR template for representation of SYNOP data with supplementary information on one-hour observations (August 2008)

This template is proposed to be used for representation of surface observation data from both automatic stations and manned stations.  This template is also suitable for SYNOP observation data, by including parameters covering periods longer than one hour.

Entries from the SYNOP BUFR template TM 307080 are indicated by an asterisk * in the column S. Entries from the AWS BUFR template TM 307091 are indicated by an asterisk * in the column A.

Entries used by both templates are not marked.

The very recent modifications and additions are written in blue and bold.

TM 307096 - BUFR template for representation of SYNOP data with supplementary

information on one-hour observations

| 3 07 096 |  | Sequence for representation of SYNOP data with supplementary information on one-hour observations |
| --- | --- | --- |
|  | 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates |
|  | 3 01 089 | National station identification |
|  | 0 08 010 | Surface qualifier (for temperature data) |
|  | 3 01 091 | Surface station instrumentation |
|  | 3 02 084 | “Instantaneous” data of sequence 307096 |
|  | 3 02 085 | “Period” data of sequence 307096 |
|  | 0 33 005 | Quality information (AWS data) |
|  | 0 33 006 | Internal measurement status information (AWS) |

This BUFR template further expands as follows:

|  |  |  |  | S | A |  | Unit, scale |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 01 090 |  |  |  |  |  | Surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 |  |  |  |  | Surface station identification |  |
|  |  | 0 01 001 |  |  |  | WMO block number | Numeric, 0 |
|  |  | 0 01 002 |  |  |  | WMO station number | Numeric, 0 |
|  |  | 0 01 015 |  |  |  | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 |  |  |  | Type of station | Code table, 0 |
|  | 3 01 011 | 0 04 001 |  |  |  | Year | Year, 0 |
|  |  | 0 04 002 |  |  |  | Month | Month, 0 |
|  |  | 0 04 003 |  |  |  | Day | Day, 0 |
|  | 3 01 012 | 0 04 004 |  |  |  | Hour | Hour, 0 |
|  |  | 0 04 005 |  |  |  | Minute | Minute, 0 |
|  | 3 01 021 | 0 05 001 |  |  |  | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 |  |  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  |  |  |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  |  |  |  | Height of barometer above mean sea level | m, 1 |
| 3 01 089 |  |  |  |  | * | National station identification |  |
|  | 0 01 101 |  |  |  | * | State identifier (see Note 1) | Code table, 0 |
|  | 0 01 102 |  |  |  | * | National station number (see Note 1) | Numeric, 0 |
| 0 08 010 |  |  |  |  | * | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  |  |  |  | * | Surface station instrumentation |  |
|  | 0 02 180 |  |  |  | * | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 |  |  |  | * | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 |  |  |  | * | Visibility measurement system | Code table, 0 |
|  | 0 02 183 |  |  |  | * | Cloud detection system | Code table, 0 |
|  | 0 02 184 |  |  |  | * | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 |  |  |  | * | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 |  |  |  | * | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 |  |  |  | * | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 |  |  |  | * | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 |  |  |  | * | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 084 |  |  |  |  |  | “Instantaneous” data of sequence 307096 |  |
|  | 3 02 031 |  |  |  |  | Pressure data |  |
|  |  | 3 02 001 | 0 10 004 |  |  | Pressure | Pa, –1 |
|  |  |  | 0 10 051 |  |  | Pressure reduced to mean sea level | Pa, –1 |
|  |  |  | 0 10 061 |  |  | 3-hour pressure change | Pa, –1 |
|  |  |  | 0 10 063 |  |  | Characteristic of pressure tendency | Code table, 0 |
|  |  | 0 10 062 |  | * |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  |  | 0 07 004 |  |  |  | Pressure (standard level) | Pa, –1 |
|  |  | 0 10 009 |  |  |  | Geopotential height of the standard level | gpm, 0 |
|  | 3 02 072 |  |  |  |  | Temperature and humidity data |  |
|  |  | 0 07 032 |  |  |  | Height of sensor above local ground | m, 2 |
|  |  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  |  | 0 12 101 |  |  |  | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  |  | 0 12 103 |  |  |  | Dew-point temperature (scale 2) | K, 2 |
|  |  | 0 13 003 |  |  |  | Relative humidity | %, 0 |
|  | 1 03 000 |  |  |  |  | Delayed replication of 3 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 1 01 005 |  |  |  | * | Replicate one descriptor five times |  |
|  | 3 07 063 | 0 07 061 |  |  | * | Depth below land surface | m, 2 |
|  |  | 0 12 130 |  |  | * | Soil temperature (scale 2) | K, 2 |
|  | 0 07 061 |  |  |  | * | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
|  |  |  |  |  |  | Visibility data |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 069 | 0 07 032 |  |  |  | Height of sensor above local ground | m, 2 |
|  |  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  |  | 0 33 041 |  |  | * | Attribute of following value | Code table, 0 |
|  |  | 0 20 001 |  |  |  | Horizontal visibility | m, –1 |
|  | 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  | 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  |  |  |  | Marine data |  |
|  | 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 20 031 |  |  |  | * | Ice deposit (thickness) | m, 2 |
|  | 0 20 032 |  |  |  | * | Rate of ice accretion | Code table, 0 |
|  | 0 02 038 |  |  |  | * | Method of sea surface temperature measurement | Code table, 0 |
|  | 0 22 043 |  |  |  | * | Sea/water temperature (scale 2) | K, 2 |
|  | 3 02 021 | 0 22 001 |  |  | * | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 |  |  | * | Period of waves | s, 0 |
|  |  | 0 22 021 |  |  | * | Height of waves | m, 1 |
|  |  |  |  |  |  | State of ground and snow depth measurement |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 078 | 0 02 176 |  |  | * | Method of state of ground measurement | Code table, 0 |
|  |  | 0 20 062 |  |  |  | State of ground (with or without snow) | Code table, 0 |
|  |  | 0 02 177 |  |  | * | Method of snow depth measurement | Code table, 0 |
|  |  | 0 13 013 |  |  |  | Total snow depth | m, 2 |
|  | 0 12 113 |  |  | * |  | Ground minimum temperature (scale 2), past 12 hours snTgTg | K, 2 |
|  |  |  |  |  |  | Cloud data |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 |  |  |  | Cloud cover (total) | %, 0 |
|  |  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  |  | 0 20 011 |  | * |  | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 |  | * |  | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 |  | * |  | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 |  | * |  | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 |  | * |  | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  |  |  |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  |  |  |  | Cloud amount | Code table, 0 |
|  | 0 20 012 |  |  |  |  | Cloud type | Code table, 0 |
|  | 0 33 041 |  |  |  | * | Attribute of following value | Code table, 0 |
|  | 0 20 013 |  |  |  |  | Height of base of cloud | m, -1 |
|  |  |  |  |  |  | Clouds with bases below station level |  |
|  | 3 02 036 | 1 05 000 |  | * |  | Delayed replication of 5 descriptors |  |
|  |  | 0 31 001 |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  |  | 0 20 011 |  | * |  | Cloud amount N’ | Code table, 0 |
|  |  | 0 20 012 |  | * |  | Cloud type C’ | Code table, 0 |
|  |  | 0 20 014 |  | * |  | Height of top of cloud H’H’ | m, -1 |
|  |  | 0 20 017 |  | * |  | Cloud top description Ct | Code table, 0 |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  |  |  |  | * |  | Direction of cloud drift 6DLDMDH |  |
|  | 3 02 047 | 1 02 003 |  | * |  | Replicate 2 descriptors 3 times |  |
|  |  | 0 08 002 |  | * |  | Vertical significance (7= low cloud, 8= middle cloud, 9 = high cloud) | Code table, 0 |
|  |  | 0 20 054 |  | * |  | True direction from which clouds are moving DLDMDH | Degree true, 0 |
|  | 0 08 002 |  |  | * |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  |  | * |  | Direction and elevation of cloud 57CDaeC |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 048 | 0 05 021 |  | * |  | Bearing or azimuth Da | Degree true, 2 |
|  |  | 0 07 021 |  | * |  | Elevation angle eC | Degree, 2 |
|  |  | 0 20 012 |  | * |  | Cloud type C | Code table, 0 |
|  |  | 0 05 021 |  | * |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  |  | 0 07 021 |  | * |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
| 3 02 085 |  |  |  |  |  | “Period” data of sequence 307096 |  |
|  |  |  |  |  |  | Present and past weather data |  |
|  | 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 20 003 |  |  |  |  | Present weather (see Note 2) | Code table, 0 |
|  | 1 03 002 |  |  |  |  | Replicate 3 descriptors 2 times |  |
|  | 0 04 024 |  |  |  |  | Time period (= -1 hour in 1. replication, -x hours in 2. replication, x corresponding to the time period of W1W2 in the SYNOP report) | Hour, 0 |
|  | 0 20 004 |  |  |  |  | Past weather (1) | Code table, 0 |
|  | 0 20 005 |  |  |  |  | Past weather (2) | Code table, 0 |
|  |  |  |  |  | * | Intensity of precipitation, size of precipitation element |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 075 | 0 08 021 |  |  | * | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  |  | 0 13 055 |  |  | * | Intensity of precipitation | kg m-2s-1, 4 |
|  |  | 0 13 058 |  |  | * | Size of precipitation element | m, 4 |
|  |  | 0 08 021 |  |  | * | Time significance (= missing value) | Code table, 0 |
|  |  |  |  |  |  | Precipitation, obscuration and other phenomena |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 3 02 076 |  |  |  | * | Precipitation, obscuration and other phenomena |  |
|  |  | 0 20 021 |  |  | * | Type of precipitation | Flag table, 0 |
|  |  | 0 20 022 |  |  | * | Character of precipitation | Code table, 0 |
|  |  | 0 26 020 |  |  | * | Duration of precipitation (see Note 3) | Minute, 0 |
|  |  | 0 20 023 |  |  | * | Other weather phenomena | Flag table, 0 |
|  |  | 0 20 024 |  |  | * | Intensity of phenomena | Code table, 0 |
|  |  | 0 20 025 |  |  | * | Obscuration | Flag table, 0 |
|  |  | 0 20 026 |  |  | * | Character of obscuration | Code table, 0 |
|  |  |  |  |  |  | Lightning data |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 059 |  |  |  | * | Number of flashes | Numeric, 0 |
|  |  |  |  |  |  | Wind data |  |
|  | 0 07 032 |  |  |  |  | Height of sensor above local ground | m, 2 |
|  | 0 07 033 |  |  |  | * | Height of sensor above water surface | m, 1 |
|  | 0 08 021 |  |  |  |  | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 |  |  |  |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  | 0 11 001 |  |  |  |  | Wind direction | Degree true, 0 |
|  | 0 11 002 |  |  |  |  | Wind speed | m s-1, 1 |
|  | 0 08 021 |  |  |  |  | Time significance (= missing value) | Code table, 0 |
|  | 1 03 003 |  |  |  |  | Replicate next 3 descriptors 3 times |  |
|  | 0 04 025 |  |  |  |  | Time period (= -10 minutes in 1. replication, = - 60 minutes in 2. replication, = - 60*3 or 60*6 minutes in 3. replication) | Minute, 0 |
|  | 0 11 043 |  |  |  |  | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 |  |  |  |  | Maximum wind gust speed | m s-1, 1 |
|  | 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 11 016 |  |  |  | * | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 |  |  |  | * | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
|  |  |  |  |  |  | Extreme temperature data |  |
|  | 3 02 077 | 0 07 032 |  |  | * | Height of sensor above local ground | m, 2 |
|  |  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  |  | 0 04 025 |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
|  |  | 0 12 111 |  |  | * | Maximum temperature (scale 2) at height and over period specified | K, 2 |
|  |  | 0 12 112 |  |  | * | Minimum temperature (scale 2) at height and over period specified | K, 2 |
|  |  | 0 07 032 |  |  | * | Height of sensor above local ground (for ground temperature) | m, 2 |
|  |  | 0 04 025 |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
|  |  | 0 12 112 |  |  | * | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, 2 |
|  | 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  | 3 02 041 | 0 07 032 |  | * |  | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 |  | * |  | Time period | Hour, 0 |
|  |  | 0 04 024 |  | * |  | Time period (see Notes 4 and 5) | Hour, 0 |
|  |  | 0 12 111 |  | * |  | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 |  | * |  | Time period | Hour, 0 |
|  |  | 0 04 024 |  | * |  | Time period (see Note 5) | Hour, 0 |
|  |  | 0 12 112 |  | * |  | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  |  |  |  | Precipitation measurement |  |
|  | 1 06 000 |  |  |  |  | Delayed replication of 6 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 07 032 |  |  |  |  | Height of sensor above local ground | m, 2 |
|  | 0 02 175 |  |  |  | * | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 |  |  |  | * | Method of liquid water content measurement of precipitation | Code table, 0 |
|  | 1 02 005 |  |  |  |  | Replicate 2 descriptors 5 times |  |
|  | 0 04 024 |  |  |  |  | Time period in hours tR (= - 1 hour in the first replication, = - 3, -6, -12 and - 24 hours in the other replications) | Hour, 0 |
|  | 0 13 011 |  |  |  |  | Total precipitation / total water equivalent of snow | kg m-2, 1 |
|  | 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  |  |  |  | Evaporation data |  |
|  | 1 03 000 |  |  |  |  | Delayed replication of 3 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 02 185 |  |  |  | * | Method of evaporation measurement | Code table, 0 |
|  | 1 01 002 |  |  |  |  | Replicate 1 descriptor 2 times |  |
|  | 3 02 044 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  |  | 0 02 004 |  | * |  | Type of instrument for evaporation measurement or type of crop | Code table, 0 |
|  |  | 0 13 033 |  |  |  | Evaporation /evapotranspiration | kg m-2, 1 |
|  |  |  |  |  |  | Total sunshine data |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
|  | 3 02 039 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  |  | 0 14 031 |  |  |  | Total sunshine | Minute, 0 |
|  |  |  |  |  |  | Radiation data |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
|  |  | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  |  | 0 14 002 |  |  |  | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  |  | 0 14 004 |  |  |  | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  |  | 0 14 016 |  |  |  | Net radiation, integrated over period specified | J m-2, -4 |
|  |  | 0 14 028 |  |  |  | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  | 0 14 029 |  |  |  | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  | 0 14 030 |  |  |  | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  |  |  | * |  | Temperature change gr. 54g0sndT |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 046 | 0 04 024 |  | * |  | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 |  | * |  | Time period or displacement (see Note 6) | Hour, 0 |
|  |  | 0 12 049 |  | * |  | Temperature change over period specified sndT | K, 0 |
|  |  |  |  |  | * | First order statistics of P, W, T, U data |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 083 | 0 04 025 |  |  | * | Time period (= -10 minutes ) | Minute, 0 |
|  |  | 0 08 023 |  |  | * | First order statistics (see Note 7) (= 9 (best estimate of standard deviation)) | Code table, 0 |
|  |  | 0 10 004 |  |  | * | Pressure | Pa, –1 |
|  |  | 0 11 001 |  |  | * | Wind direction | Degree true, 0 |
|  |  | 0 11 002 |  |  | * | Wind speed | m s-1, 1 |
|  |  | 0 12 101 |  |  | * | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  |  | 0 13 003 |  |  | * | Relative humidity | %, 0 |
|  |  | 0 08 023 |  |  | * | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  |  |  |  | * | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  |  |  |  | * | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- The WMO international identification 0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported as mandatory if available for the particular station. 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) may be used to identify a station within the national numbering system. If the WMO station identification is not available for the particular station, the National station identification shall be used.

- When reported, present weather shall be always represented by 0 20 003. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should also be used, if applicable.

- Duration of precipitation represents number of minutes in which precipitation was registered.

- Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

- Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

- To construct the required time range, descriptor 004024 has to be included two times.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

- Additional parameters required by regional or national reporting practices shall be accommodated in a similar way as recommended in Regulations B/C 1.9 and B/C 1.14 – Regulations for reporting SYNOP data in TDCF.