| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.1.6(1) ITEM: 3.1 (30. 7. 2008) ENGLISH ONLY |
| --- | --- | --- |

“Merged” BUFR template for representation of SYNOP data

and surface observations from one-hour period

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a new version of BUFR template suitable

for reporting both SYNOP data and surface observations

from one-hour period.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Final Report, Joint meeting of Coordination Team on Migration to TDCF and Expert Team on

Data Representation and Codes, Montreal, Canada, 8 to 12 May 2006

[3] Final Report, Meeting of Expert Team on Data Representation and Codes, Darmstadt,

Germany, 23 to 27 April 2007

[4] Final Report, Meeting of Expert Team on Requirements for Data from Automatic Weather

Stations, Geneva, Switzerland, 5 to 9 May 2008

1. Background

At the Joint meeting of ET DR&C and CT MTDCF (Montreal, 8 to 12 May 2006), a proposal for a BUFR template, blending the current AWS and SYNOP BUFR templates was submitted by Mr Michel Leroy, the representative of EUMETNET. As requested by the Meeting [2], this combined AWS-SYNOP template was revised in June 2006 and sent to the authors of the proposal with explanations of the modifications. No objections being received, the revised template was submitted to the Meeting of ET DR&C (Darmstadt, 23 to 27 April 2007). The Meeting discussed the usage of this combined template and its consequences and recommended the template for further validation [3].

Meanwhile, the template for reporting one-hour AWS surface observations had been further developed and improved. National station identification 3 01 089 was added for representation of national station numbering system and extensive usage of short delayed replications was introduced to allow reduction of the message volume, especially in case of stations with limited instrumentation [3]. The current version of this template (TM 307091) is included in document CT-MTDCF/ET-DR&C/Doc. 3.1.5(1).

2. Output of Meeting of ET-AWS (Geneva, 5 to 9 May 2008)

The Meeting of Expert Team on Requirements for Data from Automatic Weather Stations  noted that the requirements for the “merged” BUFR template for surface observations from one-hour period and for reporting SYNOP data in BUFR (revised, June 2006) was addressed by ET-DR&C, but it still requires validation. The meeting recommended that the validation of the template including proposed national station identification such be done as a matter of urgency. It accepted with pleasure an offer by M. Leroy, Météo-France, to take lead in this validation. The ET-AWS emphasised the need for the adoption of the relevant amendments to the Manual on Codes (WMO-No. 306) by CBS-XIV so that this “merged” template could be used instead of the B/C1 – SYNOP template for reporting SYNOP data in BUFR during and after the transition phase for the migration from traditional alphanumeric codes (TAC) to Table Driven Codes Forms (TDCF). In this regard, the ET-AWS adopted Recommendation 9:

Considering:

The need for validation of the merged BUFR Template for Surface Observations from one hour period and for reporting SYNOP data;

The expert team recommended that:

Météo France be requested to take a lead in the validation of the BUFR Template for Surface Observations from one hour period and for reporting of SYNOP data, to implement this template and adjust it as appropriate, in collaboration with CBS and ET-DR&C and with the view of its approval by CBS-XIV. [4]

According to the ET-AWS Detailed Work Plan [4], implementation and validation of BUFR template for SYNOP/AWS reporting (including national station identification) should be accomplished by December 2008.

3. Recent development of the “Merged BUFR AWS-SYNOP template”

In May 2008, e-mail exchange between Mr. Michel Leroy of Météo France and the author of this document took place and a new version (version 3) of the “merged” BUFR AWS-SYNOP template was developed as shown in the ANNEX: national station identification and the extensive usage of delayed replications were introduced in compliance with the template TM 307091 for surface observations from one-hour period. Moreover, Météo France agreed with representation of extreme temperatures using 3 02 077 (one-hour extreme temperatures) and 3 02 041 (SYNOP extreme temperatures) and other modifications that had been suggested in June 2006 and shown in [3]. The problem of specification of data subcategories was also discussed, but the proposals 4b) and 4c) below were finalized only at the stage of writing of this document.

4.  Specification of data sub-categories for the “Merged BUFR AWS-SYNOP template” data

As stated in [3], if data are to be encoded using this combined AWS-SYNOP template for the international exchange, new data sub-categories will have to be defined for this type of data and, consequently also new telecommunication headers for the BUFR messages.

There are three alternative proposals for specification of the data sub-categories:

- 0, 1, 2 (preferably only 0) for data from manned stations and 6 for data from automatic stations (Michel Leroy).

- 10, 11 and 12 for data from hourly, intermediate and main synoptic times, respectively (Eva Červená).

- 0, 1 and 2 for data from hourly, intermediate and main synoptic times, respectively, provided that the SYNOP data are mandatory (Eva Červená).

Comments on the above proposals:

- The data sub-categories are proposed to be specified taking into consideration type of station, which is a Section 4 entry.

- Completely new data sub-categories are proposed for the data of the Merged AWS-SYNOP template, and consequently also new telecommunication headers should be defined for the BUFR messages. And the proposed data sub-categories are proposed to be defined not only for data category 0 (surface land data) but also for data category 1 (surface sea data), because template TM 307091 applies to both data categories.

- If the “merged BUFR AWS-SYNOP template” is considered to be used as a “BUFR template for representation of SYNOP data with supplementary information on one-hour observations”, the existing sub-categories 0, 1 and 2 might be used, and consequently also telecommunication headers ISNxii, ISIxii and ISMxii, for hourly, intermediate and main synoptic observations, respectively. However, synoptic data would have to be considered as mandatory in this case, including WMO station identification, and Note (1) modified accordingly. Besides that the order of 3 01 089 and 3 01 090 in the template should be reversed.

ANNEX

“MERGED” BUFR TEMPLATE FOR SURFACE OBSERVATIONS FROM ONE-HOUR PERIOD AND FOR REPORTING SYNOP DATA IN BUFR (Version 3, May 2008)

This template is proposed to be used for representation of surface observation data from both automatic stations and manned stations.  This template is also suitable for SYNOP observation data, by including parameters covering periods longer than one hour.

Entries used by both templates are not marked.

Entries from the SYNOP BUFR template TM 307080 are indicated by an asterisk * in the column S. Entries from the AWS BUFR template TM 307091 are indicated by an asterisk * in the column A.

Recent modifications and additions are written in blue or red.

|  |  |  | S | A |  | Unit, scale |
| --- | --- | --- | --- | --- | --- | --- |
| 3 01 089 |  |  |  | * | National station identification |  |
|  | 0 01 101 |  |  | * | State identifier (see Note 1) | Code table, 0 |
|  | 0 01 102 |  |  | * | National station number (see Note 1) | Numeric, 0 |
| 3 01 090 |  |  |  |  | Surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 |  |  |  | Surface station identification |  |
|  |  | 0 01 001 |  |  | WMO block number | Numeric, 0 |
|  |  | 0 01 002 |  |  | WMO station number | Numeric, 0 |
|  |  | 0 01 015 |  |  | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 |  |  | Type of station | Code table, 0 |
|  | 3 01 011 | 0 04 001 |  |  | Year | Year, 0 |
|  |  | 0 04 002 |  |  | Month | Month, 0 |
|  |  | 0 04 003 |  |  | Day | Day, 0 |
|  | 3 01 012 | 0 04 004 |  |  | Hour | Hour, 0 |
|  |  | 0 04 005 |  |  | Minute | Minute, 0 |
|  | 3 01 021 | 0 05 001 |  |  | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 |  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  |  |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  |  |  | Height of barometer above mean sea level | m, 1 |
| 0 08 010 |  |  |  | * | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  |  |  | * | Surface station instrumentation |  |
|  | 0 02 180 |  |  | * | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 |  |  | * | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 |  |  | * | Visibility measurement system | Code table, 0 |
|  | 0 02 183 |  |  | * | Cloud detection system | Code table, 0 |
|  | 0 02 184 |  |  | * | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 |  |  | * | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 |  |  | * | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 |  |  | * | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 |  |  | * | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 |  |  | * | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 031 |  |  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 |  |  | Pressure | Pa, –1 |
|  |  | 0 10 051 |  |  | Pressure reduced to mean sea level | Pa, –1 |
|  |  | 0 10 061 |  |  | 3-hour pressure change | Pa, –1 |
|  |  | 0 10 063 |  |  | Characteristic of pressure tendency | Code table, 0 |
|  | 0 10 062 |  | * |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  |  |  | Pressure (standard level) | Pa, –1 |
|  | 0 10 009 |  |  |  | Geopotential height of the standard level | gpm, 0 |
| 3 02 072 |  |  |  |  | Temperature and humidity data |  |
|  | 0 07 032 |  |  |  | Height of sensor above local ground | m, 2 |
|  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  | 0 12 101 |  |  |  | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 12 103 |  |  |  | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 |  |  |  | Relative humidity | %, 0 |
| 1 03 000 |  |  |  |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  |  |  | * | Replicate one descriptor five times |  |
| 3 07 063 | 0 07 061 |  |  | * | Depth below land surface | m, 2 |
|  | 0 12 130 |  |  | * | Soil temperature (scale 2) | K, 2 |
| 0 07 061 |  |  |  | * | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
|  |  |  |  |  | Visibility data |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 | 0 07 032 |  |  |  | Height of sensor above local ground | m, 2 |
|  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  | 0 33 041 |  |  | * | Attribute of following value | Code table, 0 |
|  | 0 20 001 |  |  |  | Horizontal visibility | m, –1 |
| 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  |  |  | Marine data |  |
| 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  |  |  | * | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  |  |  | * | Rate of ice accretion | Code table, 0 |
| 0 02 038 |  |  |  | * | Method of sea surface temperature measurement | Code table, 0 |
| 0 22 043 |  |  |  | * | Sea/water temperature (scale 2) | K, 2 |
| 3 02 021 | 0 22 001 |  |  | * | Direction of waves | Degree true, 0 |
|  | 0 22 011 |  |  | * | Period of waves | s, 0 |
|  | 0 22 021 |  |  | * | Height of waves | m, 1 |
|  |  |  |  |  | State of ground and snow depth measurement |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 | 0 02 176 |  |  | * | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 |  |  |  | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 |  |  | * | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 |  |  |  | Total snow depth | m, 2 |
| 0 12 113 |  |  | * |  | Ground minimum temperature (scale 2), past 12 hours snTgTg | K, 2 |
|  |  |  |  |  | Cloud data |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 004 | 0 20 010 |  |  |  | Cloud cover (total) | %, 0 |
|  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | * |  | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  | 0 20 013 |  | * |  | Height of base of cloud h | m, –1 |
|  | 0 20 012 |  | * |  | Cloud type (low clouds CL) CL | Code table, 0 |
|  | 0 20 012 |  | * |  | Cloud type (middle clouds CM) CM | Code table, 0 |
|  | 0 20 012 |  | * |  | Cloud type (high clouds CH) CH | Code table, 0 |
| 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
| 0 31 001 |  |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
| 0 08 002 |  |  |  |  | Vertical significance | Code table, 0 |
| 0 20 011 |  |  |  |  | Cloud amount | Code table, 0 |
| 0 20 012 |  |  |  |  | Cloud type | Code table, 0 |
| 0 33 041 |  |  |  | * | Attribute of following value | Code table, 0 |
| 0 20 013 |  |  |  |  | Height of base of cloud | m, -1 |
|  |  |  |  |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | * |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | * |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | * |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | * |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | * |  | Cloud top description Ct | Code table, 0 |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  |  |  | * |  | Direction of cloud drift 6DLDMDH |  |
| 3 02 047 | 1 02 003 |  | * |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | * |  | Vertical significance (7= low cloud, 8= middle cloud, 9 = high cloud) | Code table, 0 |
|  | 0 20 054 |  | * |  | True direction from which clouds are moving DLDMDH | Degree true, 0 |
| 0 08 002 |  |  | * |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | * |  | Direction and elevation of cloud 57CDaeC |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 048 | 0 05 021 |  | * |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | * |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | * |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | * |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | * |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  |  |  | Present and past weather data |  |
| 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 003 |  |  |  |  | Present weather (see Note 2) | Code table, 0 |
| 1 03 002 |  |  |  |  | Replicate 3 descriptors 2 times |  |
| 0 04 024 |  |  |  |  | Time period (= -1 hour in 1. replication, -x hours in 2. replication, x corresponding to the time period of W1W2 in the SYNOP report) | Hour, 0 |
| 0 20 004 |  |  |  |  | Past weather (1) | Code table, 0 |
| 0 20 005 |  |  |  |  | Past weather (2) | Code table, 0 |
|  |  |  |  | * | Intensity of precipitation, size of precipitation element |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 075 | 0 08 021 |  |  | * | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 055 |  |  | * | Intensity of precipitation | kg m-2s-1, 4 |
|  | 0 13 058 |  |  | * | Size of precipitation element | m, 4 |
|  | 0 08 021 |  |  | * | Time significance (= missing value) | Code table, 0 |
|  |  |  |  |  | Precipitation, obscuration and other phenomena |  |
| 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
| 3 02 076 |  |  |  | * | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 |  |  | * | Type of precipitation | Flag table, 0 |
|  | 0 20 022 |  |  | * | Character of precipitation | Code table, 0 |
|  | 0 26 020 |  |  | * | Duration of precipitation (see Note 3) | Minute, 0 |
|  | 0 20 023 |  |  | * | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 |  |  | * | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 |  |  | * | Obscuration | Flag table, 0 |
|  | 0 20 026 |  |  | * | Character of obscuration | Code table, 0 |
|  |  |  |  |  | Lightning data |  |
| 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
| 0 13 059 |  |  |  | * | Number of flashes | Numeric, 0 |
|  |  |  |  |  | Wind data |  |
| 0 07 032 |  |  |  |  | Height of sensor above local ground | m, 2 |
| 0 07 033 |  |  |  | * | Height of sensor above water surface | m, 1 |
| 0 08 021 |  |  |  |  | Time significance (= 2 (time averaged)) | Code table, 0 |
| 0 04 025 |  |  |  |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
| 0 11 001 |  |  |  |  | Wind direction | Degree true, 0 |
| 0 11 002 |  |  |  |  | Wind speed | m s-1, 1 |
| 0 08 021 |  |  |  |  | Time significance (= missing value) | Code table, 0 |
| 1 03 003 |  |  |  |  | Replicate next 3 descriptors 3 times |  |
| 0 04 025 |  |  |  |  | Time period (= -10 minutes in 1. replication, = - 60 minutes in 2. replication, = - 60*3 or 60*6 minutes in 3. replication) | Minute, 0 |
| 0 11 043 |  |  |  |  | Maximum wind gust direction | Degree true, 0 |
| 0 11 041 |  |  |  |  | Maximum wind gust speed | m s-1, 1 |
| 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
| 0 11 016 |  |  |  | * | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
| 0 11 017 |  |  |  | * | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
|  |  |  |  |  | Extreme temperature data |  |
| 3 02 077 | 0 07 032 |  |  | * | Height of sensor above local ground | m, 2 |
|  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  | 0 04 025 |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 111 |  |  | * | Maximum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 12 112 |  |  | * | Minimum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 07 032 |  |  | * | Height of sensor above local ground (for ground temperature) | m, 2 |
|  | 0 04 025 |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 112 |  |  | * | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, 2 |
| 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 3 02 041 | 0 07 032 |  | * |  | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  | 0 04 024 |  | * |  | Time period | Hour, 0 |
|  | 0 04 024 |  | * |  | Time period (see Notes 4 and 5) | Hour, 0 |
|  | 0 12 111 |  | * |  | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  | 0 04 024 |  | * |  | Time period | Hour, 0 |
|  | 0 04 024 |  | * |  | Time period (see Note 5) | Hour, 0 |
|  | 0 12 112 |  | * |  | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  |  |  | Precipitation measurement |  |
| 1 06 000 |  |  |  |  | Delayed replication of 6 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 0 07 032 |  |  |  |  | Height of sensor above local ground | m, 2 |
| 0 02 175 |  |  |  | * | Method of precipitation measurement | Code table, 0 |
| 0 02 178 |  |  |  | * | Method of liquid water content measurement of precipitation | Code table, 0 |
| 1 02 005 |  |  |  |  | Replicate 2 descriptors 5 times |  |
| 0 04 024 |  |  |  |  | Time period in hours tR (= - 1 hour in the first replication, = - 3, -6, -12 and - 24 hours in the other replications) | Hour, 0 |
| 0 13 011 |  |  |  |  | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  |  |  | Evaporation data |  |
| 1 03 000 |  |  |  |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 0 02 185 |  |  |  | * | Method of evaporation measurement | Code table, 0 |
| 1 01 002 |  |  |  |  | Replicate 1 descriptor 2 times |  |
| 3 02 044 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  | 0 02 004 |  | * |  | Type of instrument for evaporation measurement or type of crop | Code table, 0 |
|  | 0 13 033 |  |  |  | Evaporation /evapotranspiration | kg m-2, 1 |
|  |  |  |  |  | Total sunshine data |  |
| 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
| 3 02 039 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -x hours in 2. replication) | Hour, 0 |
|  | 0 14 031 |  |  |  | Total sunshine | Minute, 0 |
|  |  |  |  |  | Radiation data |  |
| 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
| 3 02 045 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  | 0 14 002 |  |  |  | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 |  |  |  | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 |  |  |  | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 |  |  |  | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 |  |  |  | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 |  |  |  | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  |  | * |  | Temperature change gr. 54g0sndT |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 046 | 0 04 024 |  | * |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | * |  | Time period or displacement (see Note 6) | Hour, 0 |
|  | 0 12 049 |  | * |  | Temperature change over period specified sndT | K, 0 |
|  |  |  |  | * | First order statistics of P, W, T, U data |  |
| 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 | 0 04 025 |  |  | * | Time period (= -10 minutes ) | Minute, 0 |
|  | 0 08 023 |  |  | * | First order statistics (see Note 7) (= 9 (best estimate of standard deviation)) | Code table, 0 |
|  | 0 10 004 |  |  | * | Pressure | Pa, –1 |
|  | 0 11 001 |  |  | * | Wind direction | Degree true, 0 |
|  | 0 11 002 |  |  | * | Wind speed | m s-1, 1 |
|  | 0 12 101 |  |  | * | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 13 003 |  |  | * | Relative humidity | %, 0 |
|  | 0 08 023 |  |  | * | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  |  |  | * | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  |  |  | * | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) shall be used to identify a station within the national numbering system that is completely independent of the WMO international numbering system. The WMO international identification 0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station.

- When reported, present weather shall be always represented by 0 20 003. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should also be used, if applicable.

- Duration of precipitation represents number of minutes in which precipitation was registered.

- Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

- Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

- To construct the required time range, descriptor 004024 has to be included two times.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

- Additional parameters required by regional or national reporting practices shall be accommodated as prescribed in B/C1 – Regulations for reporting SYNOP data in TDCF.