| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C / Doc.3.1.7(1) (21.8.2008) ENGLISH ONLY |
| --- | --- | --- |

Proposal for updated template for temperature profiles, descriptors and new or updated code table entries.

Submitted by Hester Viola for JCOMM and IOC

________________________________________________________________

Summary and Purpose of Document

The document contains the proposed new version of BUFR template for XBT data. It contains several proposals to modify existing Code Tables.

It contains proposals for one new code table and also one new sequence.

It describes the future plan for how to look at ways to standardize the content across templates and restructure templates

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and outline the process for validation of the additions and modifications to templates and code tables..

#### 1. Summary of JCOMM activities

JCOMM has made some progress in its work relating to Table Driven Code Forms since the last meeting of the ET/DR&C. JCOMM is addressing the issues associated with adopting Table Driven Code Forms seriously and is carefully taking all the requirements into account.

The META-T Pilot Project has progressed with defining the instrumental metadata required for GTS distribution in real time as far as water temperature and SST measurements are concerned. Based on work completed relating to Real-time Metadata of Ocean Observing Systems (Meta-T project http://marinemetadata.org/examples/external/meta-t/) the new XBT template proposed below includes many of the required metadata fields. It will form a test case of the feasibility of including so much metadata in the real time message.

JCOMM working groups have been encouraged to take a holistic view when developing templates and consider requirements for consistency between the different templates moving away from the platform based approach to GTS messages.

The current message formats which come under the area of interest of JCOMM are summarised with the actions undertaken this year included :

#### 2. Progress on JCOMM related templates

| Template / Data Type | Current Status | Work completed or plans |
| --- | --- | --- |
| BUOY | Operational use. | No changes required. Metadata to be included in future has been documented as part of the Meta-T pilot project. Main data processing centre (CLS Argos) is commited to BUFR and has built up significant expertise in this area. |
| TRACKOB | Testing and in progress on a simple template. Validation should go ahead in the next few months. | Template tested and validated from NOAA AOML. Additional descriptors are proposed. Presented at the 2nd Joint GOSUD/SAMOS Workshop, Seattle, 10-12 June 2008. e.g. Intake Depth TSG Instrument type External Ref SST (with depth & instrument type) Calibration Date QC flags Plus common elements from the BATHY template These have not been fully specified yet though, so a new template will be proposed in 2009 |
| XBT | Testing in progress of existing template. Validation successfully completed by NCEP | New Template proposed just for XBT platforms in section 2 of this document. Includes more metadata than the previous template based on the requirements defined by the Meta-T Pilot project. |
| XCTD |  | New template will be developed in line with the XBT template, as required. |
| SHIP | No change | Metadata fields which need to be included within BUFR messages have been fully specified as part of the Meta-T pilot project. This has not been transitioned into a new template yet though by the Ship Observations Team or the JCOMM Data Management Programme Area. New template will be completed in 2009 |
| TESAC | Operational use (Japan) | No changes requested for now |
| WAVEOB |  | Review of the template completed by BOM - Input by Australia |
| CLIMAT SHIP |  | No progress |
| PILOT SHIP TEMP SHIP |  | No progress |
| CLIMAT TEMP SHIP |  | No progress |
| Ocean Current | (Acoustic Doppler Current Profilers) | No Progress |

#### 3. Proposed new BUFR template for XBT Temperature Profile data (sequence 3 15 004)

| Descriptor | Name | Data Type | Units | Comment |
| --- | --- | --- | --- | --- |
| NEW 0 22 176? | Unique identifier for the profile | CCITT IA5 (Data Width 72) | - | As in GTSPP Hash function or CRC |
| 0 01 003 | WMO region |  |  | non compulsory |
| 0 01 020 | WMO region sub-area |  |  | non compulsory |
| 0 01 087 | WMO Marine observing platform extended identifier |  |  | non compulsory |
| 0 01 005 | Buoy/platform identifier |  |  |  |
| 0 01 011 | Ship call sign |  |  |  |
| NEW 0 01 103? | IMO Number. Unique Lloyd's registry. 0 to 99999999999 | Numeric (Data Width 14) | - | Optional additional ship description |
| 0 01 080 | Ship line number according to SOOP |  |  |  |
| 0 05 036 | Ship transect number according to SOOP |  |  |  |
| 0 01 036 | Agency in charge of operating the observing platform |  |  | Important field |
| 0 07 030 | Height of station above MSL |  |  |  |
| 0 01 013 | Speed of motion of moving observing platform |  |  |  |
| 0 01 012 | Direction of motion of moving observing platform |  |  |  |
| 0 02 040 | Method of removing platform direction and speed from current |  |  |  |
| NEW 0 22 177? | Height of XBT/XCTD Launcher | Numeric | m | from 5m to 50 m |
| 0 07 032 | Height of thermometer above station platform |  |  | 0 07 032 Here height of thermometer (for a BUOY) |
| 0 22 068 | Water temperature profile recorder type |  |  |  |
| 0 22 067 | Instrument type for water temperature profile measurement |  |  |  |
| NEW 0 22 178? | XBT/XCTD launcher Type | NEW Code Table ( 0 22 178) |  |  |
| NEW 0 22 179? | Software version of profile recorder | CCITT IA5 (Data Width 256) |  |  |
| NEW 0 22 180? | Autolauncher software version number | CCITT IA5 (Data Width 256) |  |  |
| NEW 0 22 181? | Instrument manufacturer's serial number | CCITT IA5 (Data Width 32) |  |  |
| 3 01 011 | Manufacturing Date | Date |  |  |
| 0 08 041 | Date Significance |  |  | NEW Value : 8? XBT Manufacture Date |
| 0 02 032 | Indicator for digitization |  |  |  |
| 3 01 011 | Date |  |  |  |
| 3 01 012 | Time |  |  |  |
| 3 01 021 | Latitude and longitude (high accuracy) |  |  | 10-5 precision |
| 0 11 002 | Wind speed |  |  |  |
| 0 11 001 | Wind direction |  |  |  |
| 3 02 021 | Waves |  |  |  |
| 3 02 056 | Sea Surface Temperature |  |  | [0 22 001],[0 22 011],[0 22 021] |
| NEW 3 15 004 ? | Water temperature profile |  |  | NEW Sequence containing the profile itself |
| 0 22 063 | Total depth of water |  |  |  |
| 0 12 101 | Dry-bulb temperature (scale 2) |  |  |  |
| 0 12 103 | Dew-point temperature (scale 2) |  |  |  |
| 0 07 032 | Height of anemometer above station platform |  |  | Here height of anemometer |
| 3 06 005 | Depth, Direction, Speed and Method of current measurement |  |  | 0 02 031, 0 07 062, 0 22 004, 0 22 031 at depths |
| 0 08 080 | Qualifier for quality class |  |  | Value: 0=global water pressure profile |
| 0 33 050 | Global GTSPP quality class |  |  | For global water pressure profile as qualified above |
| 0 08 080 | Qualifier for quality class |  |  | Value: 1=global water temperature profile |
| 0 33 050 | Global GTSPP quality class |  |  | For global water temperature profile as qualified above |
| (1) integer, assigned by the operator, incremented for each new transect (i.e. all drop have the same transect number while the ship is moving from one end point of the line to the other end point; as soon as the ship arrived to port and goes back to start a new transect then transect number is incremented), initial value and subsequent values for transect numbers do not matter provided that each new transect by a ship on a line has a transect number higher than previous transect numbers for the same line and the same ship. In case a single cruise follows more than one SOOP line in a row, then transect number should be incremented each time the cruise changes line |
| (2)This field is indeed to be computed in quasi real-time and this is practically difficult to do. It is used in relation with the height of the typical weather instruments (e.g. air temp). It is not related to the height of the XBT recorder as this would be meaningless (the XBT depth is being provided anyway with each data point). In practice it can be left empty. On the other hand, this annex presents the existing template which we are going to deprecate and replace by the new one we are working at. |

#### 4. Proposed addition of new Code Table

# 0 22 178

# XBT/XCTD Launcher Type

| Code figure |  |
| --- | --- |
| 0 | Unknown |
| 1 | LM-2A Deck-mounted |
| 2 | LM-3A Hand-Held |
| 3 | LM-4A Thru-Hull |
| 4-9 | Reserved |
| 10 | AL-12 TSK Autolauncher (up to 12 Probes) |
| 11-19 | Reserved |
| 20 | SIO XBT Autolauncher (up to 6 probes) |
| 21-29 | Reserved |
| 30 | AOML XBT V6 Autolauncher (up to 6 Deep Blue probes) |
| 31 | AOML XBT V8.0 Autolauncher (up to 8 Deep Blue probes) |
| 32 | AOML XBT V8.1 Autolauncher (up to 8 Deep Blue&Fast Deep probes) |
| 33-89 | Reserved |
| 90 | CSIRO Devil Autolauncher |
| 91-99 | Reserved |
| 100 | MFSTEP Autolauncher (Mediterraneen) |
| 101-254 |  |
| 255 | Missing |

#### 5. Proposed modifications to Code Tables

Shading indicates new values or corrections. Numbers are just suggestions and should be changed as required.

0 02 148

Data Collection or Location System

| Code Figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | Argos |
| 2 | GPS |
| 3 | GOES DCP |
| 4 | METEOSAT DCP |
| 5 | ORBCOMM |
| 6 | INMARSAT |
| 7 | Iridium |
| 8 | Iridium and GPS |
| 9 | Missing |
| 10-15 | Reserved |

0 02 149

Type of data buoy

| Code Figure |  |
| --- | --- |
| 0 | Unspecified drifting buoy |
| 1 | SVP Standard Lagrangian drifter (Global Drifter Programme) |
| 2 | Standard FGGE type drifting buoy (non-Lagrangian meteorological drifting buoy) |
| 3 | Wind measuring FGGE type drifting buoy (non-Lagrangian meteorological drifting buoy) |
| 4 | Ice float |
| 5 | POPS Ice Buoy/Float |
| 6 | SVP-B Barometer drifter |
| 7 | SVPW (drifter with wind sensors) |
| 8 | Unspecified sub-surface float |
| 9 | SOFAR |
| 10 | ALACE |
| 11 | MARVOR |
| 12 | RAFOS |
| 13 | PROVOR |
| 14 | SOLO |
| 15 | APEX |
| 16 | Unspecified moored buoy |
| 17 | Nomad |
| 18 | 3-metre discus |
| 19 | 10-12-metre discus |
| 20 | ODAS 30 series |
| 21 | ATLAS (e.g. TAO area) |
| 22 | TRITON buoy |
| 23 | Reserved |
| 24 | Omnidirectional waverider |
| 25 | Directional waverider |
| 26 | Sub-surface ARGO float |
| 27 | PALACE |
| 28 | NEMO |
| 29 | NINJA |
| 32 | SVP-T Hurricane Drifter with Thermistor string |
| 33 | SVPS (drifter with salinity sensors) |
| 34 | Mooring Oceanographic (Timeseries) |
| 35 | Mooring Meteorlogical |
| 36-62 | Reserved |
| 63 | Missing value |

0 08 080

# Qualifier for GTSPP quality flag

| Code figure |  |
| --- | --- |
| 10 | Water pressure/Depth at a level |

N.B This is a change in descriptor text only.

Code table 4770-XRXR Recorder type - for alphanumeric codes
BUFR  Code Table 0 22 068 Water temperature profile recorder types

The proposed changes are that the Oceanographic/Animal Tracking communities would like to be able to identify an instrument on a Sea-Mammal in TESAC (or BATHY) code forms, so would like to add to the COMMON CODE TABLE C-4: Water temperature profile recorder types

| ? | SMRU CTD uncorrected salinity |
| --- | --- |
| ? | SMRU CTD corrected salinity |

0 33 050

Global GTSPP quality flag

| 9 | Good for operational use; Caution; check literature for other uses |
| --- | --- |

0 08 041]

Date Significance

| 8 | XBT Manufacture Date |
| --- | --- |

0 01 009

JCOMM GTS message identifier

| 10 | UUAA TEMP SHIP |
| --- | --- |
| 11-14 | Reserved |
| 15 | Missing |

Proposed addition of “Missing” value in code tables for Master Table 10:

0 01 007, 0 02 028, 0 02 007 (therefore 0 02 148),“Missing” value, described in Document 3.4

#### 6. Proposed new descriptors

| [0 22 176] | Unique identifier for the profile | CCITT IA5 |  | As in GTSPP Hash function or CRC. Data Width 72 |
| --- | --- | --- | --- | --- |
| [0 01 103] | IMO Number. Unique Lloyd's registry. | Numeric |  | Data width 14 |
| [0 22 177] | Height of XBT/XCTD Launcher | Numeric | m | from 5m to 50 m |
| [0 22 178] | XBT/XCTD launcher Type | Code Table |  |  |
| [0 22 179] | Software version of profile recorder | CCITT IA5 |  | Data Width 256 |
| [0 22 180] | Autolauncher software version number | CCITT IA5 |  | Data Width 256 |
| [0 22 181] | Instrument manufacturer's serial number | CCITT IA5 |  | Data Width 32 |

Numbers are just suggestions and should be changed as required.

#### 7. Proposed new sequence

3 15 004

Water Temperature Profile

(Temperature profile observed by XBT or Buoy)

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- |
| F | X | Y |  |  |
| 3 | 15 | 004 | 1 | 06 | 000 | Delayed replication of 6 descriptors |
|  |  |  | 0 | 31 | 001 | Replication factor |
|  |  |  | 0 | 07 | 063 | Depth below sea surface |
|  |  |  | 0 | 08 | 080 | Qualifier for quality class (qualifier = 10) |
|  |  |  | 0 | 33 | 050 | GTSPP quality class for depth |
|  |  |  | 0 | 22 | 045 | Subsurface sea temperature |
|  |  |  | 0 | 08 | 080 | Qualifier for quality class (qualifier = 11) |
|  |  |  | 0 | 33 | 050 | GTSPP quality class |

Sequence number is just suggestions and should be changed as required.

#### 8. Outstanding issues

- The template for Argo float profiles does not have a descriptor for oxygen. These data are being collected now and so needs to be included. Also the oxygen sensor produces a temperature profile as well that needs to be distinguished from the temperature measured by the CTD. So this means there will need to be another descriptor 022067 pointing to another temperature profile.

- The template for Buoy and XBT data needs to allow for fluorescence and CO2 as a variable. These are now being measured on moored buoys but there is no way to report them. This should have the same characteristic as a temperature profile with, of course, some other descriptor to identify the sensor.The TRACKOB template needs to accommodate fluorescence, pCO2 and additionally pH. This is also discussed in document 3.4.

- In late 2007, Bob Keeley, Chair of the JCOMM Data Management Programme Area, prepared a draft discussion document looking at sequences and commonalities across JCOMM templates to begin the process of simplifying the templates and attempting to group information more logically – based on data type rather than platform or message type.	 
This will be further developed, by the Data Management Programme Area, in 2009 for operational use and therefore new templates (and complex sequences) will be proposed to suit the needs of JCOMM data users. This standardisation of information contents should help in decoding the messages and also in compiling new templates in future.