| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.1.9(1) ITEM: 3.1 (16.7. 2008) ENGLISH ONLY |
| --- | --- | --- |

Proposal for BUFR template TM 307079

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains proposal for BUFR template TM 307079 for

synoptic reports from fixed land stations suitable for SYNOP data

and for maritime data from coastal and island stations.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2]  http://www.wmo.ch/pages/prog/www/WMOCodes.html

1. Background

In April 2007, Ms Sibylle Krebber of the DWD expressed their requirements for availability of a BUFR template that would be capable of representation not only synoptic data from land stations, but also maritime data from coastal and island stations. First proposal of the TM 307079 template was developed in May 2007 and consequently discussed in detail with members of the ET DR&C and with some RA VI colleagues. Based on this discussion, the template was gradually refined and included in the file Entries for Validation at http://www.wmo.ch/pages/prog/www/WMOCodes.html in November 2007.

RA VI members were informed on availability of the template TM 307079 and the RA VI Regional Rapporteur on Migration to TDCF encouraged participation of RA VI maritime countries on validation of this template as the author could not do much in that respect, the Czech Republic being an inland country.

The last modification of the TM 307079 template was done in February 2008 by addition of a new descriptor for representation of “Visibility seawards from a coastal station” based on the requirement expressed by Mr. Roger Vanlierde of Belgium.

2. Proposals

a)  A new descriptor 0 20 058 (Visibility seawards from a coastal station) is proposed:

|  |  | BUFR | CREX |
| --- | --- | --- | --- |
| Table reference | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 058 | Visibility seawards from a coastal station | m | -1 | 0 | 13 | m | -1 | 4 |

b) TM 307079 as included in the ANNEX is proposed for pre-operational usage, provided that testing of the template takes place by the end of 2008.

ANNEX

TM 307079 - BUFR template for synoptic reports from fixed land stations suitable for SYNOP data and for maritime data from coastal and island stations

| 3 07 079 |  | Sequence for representation of synoptic reports from fixed land stations suitable for SYNOP data and for maritime data from coastal stations |
| --- | --- | --- |
|  | 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates |
|  | 3 02 031 | Pressure data |
|  | 3 02 035 | Basic synoptic “instantaneous” data |
|  | 3 02 036 | Clouds with bases below station level |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 047 | Direction of cloud drift |
|  | 0 08 002 | Vertical significance |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 048 | Direction and elevation of cloud |
|  | 3 02 037 | State of ground, snow depth, ground minimum temperature |
|  | 1 02 000 | Delayed replication of 2 descriptors |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 0 22 061 | State of the sea |
|  | 0 20 058 | Visibility seawards from a coastal station |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 056 | Sea/water surface temperature, method of measurement, depth below water surface |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 055 | Icing and ice |
|  | 3 02 043 | Basic synoptic “period” data |
|  | 3 02 044 | Evaporation data |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 001 | Delayed descriptor replication factor |
|  | 3 02 045 | Radiation data |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 046 | Temperature change |

TM 307079 (BUFR template for synoptic reports from fixed land stations suitable for SYNOP data

and for maritime data from coastal and island stations) further expands as follows:

|  |  |  |  | Unit, scale |
| --- | --- | --- | --- | --- |
| 3 01 090 |  |  | Fixed surface station identification, time, horizontal and vertical coordinates |  |
|  | 3 01 004 | 0 01 001 | WMO block number II | Numeric, 0 |
|  |  | 0 01 002 | WMO station number iii | Numeric, 0 |
|  |  | 0 01 015 | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 031 |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  | 0 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  | Pressure (standard level) a3 | Pa, –1 |
|  | 0 10 009 |  | Geopotential height of the standard level hhh | gpm, 0 |
| 3 02 035 |  |  | Basic synoptic “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature and humidity measurement) | m, 2 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 033 | 0 07 032 | Height of sensor above local ground (for visibility measurement) | m, 2 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  |  |  | Individual cloud layers or masses |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  |  |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | Cloud top description Ct | Code table, 0 |
|  |  |  | Direction of cloud drift gr. 56DLDMDH |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 047 | 1 02 003 |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | Vertical significance = 7 (low cloud) = 8 (middle cloud) = 9 (high cloud) | Code table, 0 |
|  | 0 20 054 |  | True direction from which clouds are moving DL, DM, DH | Degree true, 0 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Direction and elevation of cloud gr. 57CDaeC |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 048 | 0 05 021 |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  | State of ground, snow depth, ground minimum temperature |  |
| 3 02 037 | 0 20 062 |  | State of ground (with or without snow) E or E’ | Code table, 0 |
|  | 0 13 013 |  | Total snow depth sss | m, 2 |
|  | 0 12 113 |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, 2 |
|  |  |  | State of the sea |  |
| 1 02 000 |  |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 22 061 |  |  | State of the sea S | Code table, 0 |
| 0 20 058 |  |  | Visibility seawards from a coastal station VS | m, -1 |
|  |  |  | Sea/water surface temperature, method of measurement, and depth below sea surface |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 056 | 0 02 038 |  | Method of sea/water temperature measurement | Code table, 0 |
|  | 0 07 063 |  | Depth below sea/water surface (for sea surface temperature measurement) | m, 2 |
|  | 0 22 043 |  | Sea/water temperature ssTwTwTw or 925TwTw | K, 2 |
|  | 0 07 063 |  | Depth below sea/water surface (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Icing and ice |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 055 | 0 20 031 |  | Ice deposit (thickness) EsEs | m, 2 |
|  | 0 20 032 |  | Rate of ice accretion Rs | Code table, 0 |
|  | 0 20 033 |  | Cause of ice accretion Is | Flag table, 0 |
|  | 0 20 034 |  | Sea ice concentration ci | Code table, 0 |
|  | 0 20 035 |  | Amount and type of ice bi | Code table, 0 |
|  | 0 20 036 |  | Ice situation zi | Code table, 0 |
|  | 0 20 037 |  | Ice development Si | Code table, 0 |
|  | 0 20 038 |  | Bearing of ice edge Di | Degree true, 0 |
| 3 02 043 |  |  | Basic synoptic “period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Sunshine data (from 1 hour and 24 hour period) |  |
|  | 1 01 002 |  | Replicate 1 descriptors 2 times |  |
|  | 3 02 039 | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 14 031 | Total sunshine SS and SSS | Minute, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 041 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 042 | 0 07 032 | Height of sensor above local ground (for wind measurement) | m, 2 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Evaporation data |  |
| 3 02 044 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 02 004 |  | Type of instrument for evaporation or crop type for evapotranspiration iE | Code table, 0 |
|  | 0 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1 |
|  |  |  | Radiation data (from 1 and/or 24 hour period) |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  |  | Delayed descriptor replication factor | Numeric, 0 |
| 3 02 045 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified 553SS 4FFFF or 553SS 5FFFF, 55SSS 4F24F24F24F24 or 55SSS 5F24F24F24F24 | J m-2, -3 |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified 553SS 6FFFF, 55SSS 6F24F24F24F24 | J m-2, -3 |
|  | 0 14 016 |  | Net radiation, integrated over period specified 553SS 0FFFF or 553SS 1FFFF, 55SSS 0F24F24F24F24 or 55SSS 1F24F24F24F24 | J m-2, -4 |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified 553SS 2FFFF, 55SSS 2F24F24F24F24 | J m-2, -2 |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified 553SS 3FFFF, 55SSS 3F24F24F24F24 | J m-2, -2 |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified 55408 4FFFF, 55508 5F24F24F24F24 | J m-2, -2 |
|  |  |  | Temperature change group 54g0sndT |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 046 | 0 04 024 |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | Time period or displacement (see Note 3) | Hour, 0 |
|  | 0 12 049 |  | Temperature change over period specified sndT | K, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)	To construct the required time range, descriptor 004024 has to be included two times.