| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.2(1) (12.VIII. 2008) ENGLISH ONLY |
| --- | --- | --- |

CREX SYNOP FOR WEST AFRICA

Submitted by Secretariat

________________________________________________________________

Summary and Purpose of Document

This document considers the requirement for a new Template for the transmission in CREX of SYNOP from African Countries who are Members of ASECNA.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Operational templates, see B/C1 - SYNOP:

http://www.wmo.int/pages/prog/www/WMOCodes/TemplateExamples.html

[3] Preoperational additions, page 8:

http://www.wmo.int/pages/prog/www/WMOCodes/OperationalCodes.html#NewAdditions

BACKGROUND

1.	For the purpose of taking full advantage of BUFR and CREX flexibility to satisfy the requirements of various regions in the world, several templates for SYNOP information have been defined.  The list of SYNOP templates with the regulations (see:
 http://www.wmo.int/pages/prog/www/WMOCodes/TemplateExamples.html)

includes templates adapted to the need of 5 regions.

2.	For RA I, presently two definitions exist; the one in the official template of the WMO web list (see Annex I) and the one already declared preoperational to be used for CREX in East Africa (see Annex II).

REQUIREMENT

3.	However, during a workshop on TDCF for ASECNA countries (16 Members) in September 2007 in Lomé, Togo the need for another template was expressed (see Annex III), since the stations managed by ASECNA are not reporting all the parameters listed in the previous templates, and are not planning to do it.

PROPOSAL

4.	It is therefore proposed to define another CREX template for ASECNA countries as listed in Annex IV.  This template defined for validation should be validated and declared pre-operational as soon as possible.

ANNEX I

ANNEX to B/C1 – Regulations for reporting SYNOP data in TDCF

Regional regulations for reporting SYNOP data in BUFR/CREX

TM 307081 - BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA I

3 07 081:

| 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- |
| 3 02 031 | Pressure data |  |
| 3 02 035 | Basic synoptic “instantaneous” data |  |
| 3 02 036 | Clouds with bases below station level |  |
| 3 02 047 | Direction of cloud drift |  |
| 0 08 002 | Vertical significance (= missing to cancel the previous value) | Code table, 0 |
| 3 02 048 | Direction and elevation of cloud |  |
| 3 02 037 | State of ground, snow depth, ground minimum temperature (past 12 hours) |  |
| 0 12 122 | Ground minimum temperature of the preceding night snTgTg | K, 2 |
| 0 13 056 | Character and intensity of precipitation Rc | Code table, 0 |
| 0 13 057 | Time of beginning or end of precipitation Rt | Code table, 0 |
| 0 20 101 | Locust (acridian) name Ln | Code table, 0 |
| 0 20 102 | Locust (maturity) color Lc | Code table, 0 |
| 0 20 103 | Stage of development of locusts Ld | Code table, 0 |
| 0 20 104 | Organization state of swarm or band of locusts Lg | Code table, 0 |
| 0 20 105 | Size of swarm or band of locusts and duration of passage of swarm sL | Code table, 0 |
| 0 20 106 | Locust population density dL | Code table, 0 |
| 0 20 107 | Direction of movements of locust swarm DL | Code table, 0 |
| 0 20 108 | Extent of vegetation ve | Code table, 0 |
| 3 02 043 | Basic synoptic “period” data |  |
| 3 02 044 | Evaporation data |  |
| 1 01 002 | Replicate next descriptor 2 times |  |
| 3 02 045 | Radiation data (from 1 hour and/or 24 hour period) |  |
| 3 02 046 | Temperature change |  |

Regulations:

General

- BUFR template TM 307081 shall not be mandatory for Member States in Region I. Either the template TM 307080 or any of the templates TM 307081 to TM 307086, whichever is the most convenient, may be used.

- Regulations B/C 1.1 to B/C 1.9, inclusive, shall apply.

- Regulations B/C 1.10 to B/C 1.14, inclusive, shall apply.

B/C 1.9.1 “Instantaneous” data required by reporting practices in RA I

B/C 1.9.1.1 Ground minimum temperature of the preceding night

Ground minimum temperature of the preceding night (0 12 122) shall be reported in degrees Kelvin (with precision in hundredths of a degree Kelvin); if produced in CREX, in degrees Celsius (with precision in hundredths of a degree Celsius).

Notes (1), (2) and (3) under Regulation B/C 1.8.3 shall apply.

This datum shall be reported by all Members at 0600 UTC. [1/12.6.1]

B/C 1.9.1.2 Character, intensity and time of beginning or end of precipitation

Character and intensity of precipitation (Code table 0 13 056) and Time of beginning or end of precipitation (Code table 0 13 057) shall be reported by all Members at 0600 UTC to meet requirements of agrometerological monitoring in the Region. [1/12.6.1] Inclusion of these data into reports at 0000 and 1200 UTC shall be left to national decision. [1/12.6.3]

B/C 1.9.1.3 Locust control-related observations

Following data shall be reported by all Members capable of doing so:

- Locust (acridian) name (Code table 0 20 101),

- Locust (maturity) color (Code table 0 20 102),

- Stage of development of locusts (Code table 0 20 103),

- Organization state of swarm or band of locusts (Code table 0 20 104),

- Size of swarm or band of locusts and duration of passage of swarm (Code table 0 20 105),

- Locust population density (Code table 0 20 106),

- Direction of movements of locust swarm (Code table 0 20 107),

- Extent of vegetation (Code table 0 20 108). [1/12.14.1]

ANNEX II

PREOPERATIONAL

TM D07089 - Template for synoptic reports from fixed land stations suitable for SYNOP data manually encoded in CREX

| D 07 089 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data manually encoded in CREX |
| --- | --- | --- |
|  | D 07 087 | “Instantaneous” parameters of sequence D07089 |
|  | D 07 088 | “Period” parameters of sequence D07089 |

Notes:

- “Instantaneous” parameter is a parameter that is not coupled to a time period descriptor, e.g. B04024.

- “Period” parameter is a parameter that is coupled to a time period descriptor, e.g. B04024.

This CREX template for synoptic reports from fixed land stations further expands as follows:

| D 07 087 |  |  | “Instantaneous” parameters of sequence D07089 |  |
| --- | --- | --- | --- | --- |
|  |  |  | Surface station identification, time, horizontal and vertical coordinates | in CREX |
|  | D 01 001 | B 01 001 | WMO block number II | Numeric, 0, 2 |
|  |  | B 01 002 | WMO station number iii | Numeric, 0, 3 |
|  | B 02 001 |  | Type of station (ix) | Code table, 0, 1 |
|  | D 01 011 | B 04 001 | Year | Year, 0, 4 |
|  |  | B 04 002 | Month | Month, 0, 2 |
|  |  | B 04 003 | Day YY | Day, 0, 2 |
|  | D 01 012 | B 04 004 | Hour GG | Hour, 0, 2 |
|  |  | B 04 005 | Minute gg | Minute, 0, 2 |
|  | D 01 023 | B 05 002 | Latitude (course accuracy) | Degree, 2, 4 |
|  |  | B 06 002 | Longitude (course accuracy) | Degree, 2, 5 |
|  | B 07 030 |  | Height of station ground above msl | m, 1, 5 |
|  | B 07 031 |  | Height of barometer above msl | m, 1, 5 |
|  |  |  | Pressure data |  |
|  | D 02 001 | B 10 004 | Pressure PoPoPoPo | Pa, –1, 5 |
|  |  | B 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1, 5 |
|  |  | B 10 061 | 3-hour pressure change ppp | Pa, –1, 4 |
|  |  | B 10 063 | Characteristic of pressure tendency a | Code table, 0, 2 |
|  | B 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1, 4 |
|  | B 07 004 |  | Pressure (standard level) a3 = 925, 850, 700, ..hPa = missing for lowland stations | Pa, –1, 5 |
|  | B 10 009 |  | Geopotential height of the standard level hhh = missing for lowland stations | gpm, 0, 5 |
|  |  |  | Temperature and humidity |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 12 101 |  | Temperature/dry-bulb temperature (sc. 2) snTTT | °C, 2, 4 |
|  | B 12 103 |  | Dew-point temperature (sc. 2) snTdTdTd | °C, 2, 4 |
|  | B 13 003 |  | Relative humidity | %, 0, 3 |
|  | B 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2, 5 |
|  |  |  | Visibility |  |
|  | B 20 001 |  | Horizontal visibility VV | m, –1, 4 |
|  |  |  | Cloud data |  |
|  | D 02 004 | B 20 010 | Cloud cover (total) N If N = 9, then B 20 010 = 113 %, if N = /, then B 20 010 = missing. | %, 0, 3 |
|  |  | B 08 002 | Vertical significance if CL are observed, then B 08 002 = 7 (low cloud), if CL are not observed and CM are observed, then B 08 002 = 8 (middle cloud), if only CH are observed, B 08 002 = 0, if N = 9, then B 08 002 = 5, if N = 0, then B 08 002 = 62, if N = /, then B 08 002 = missing. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount (of low or middle clouds) Nh If N = 0, then B 20 011 = 0, if N = 9, then B 20 011 = 9, if N = /, then B 20 011 = missing. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud h If N = 0 or /, then B 20 013 = missing. | m, –1, 4 |
|  |  | B 20 012 | Cloud type (low clouds) CL B 20 012 = CL + 30, if N = 0, then B 20 012 = 30, if N = 9 or /, then B 20 012 = 62. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (middle clouds) CM B 20 012 = CM + 20, if N = 0, then B 20 012 = 20, if N = 9 or / or CM = /, then B 20 012 = 61. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (high clouds) CH 0 20 012 = CH + 10, if N = 0, then B 20 012 = 10, if N = 9 or / or CH = /, then B 20 012 = 60. | Code table, 0, 2 |
|  | R 01 000 |  | Delayed replication of the next 1 descriptor |  |
|  | D 02 005 | B 08 002 | Vertical significance In any Cb layer, B 08 002 = 4 , else: in the first replication: if N = 9, then B 08 002 = 5, if N = /, then B 08 002 = missing, else B 08 002 = 1; in the other replications B 08 002 = 2, 3, 4. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount Ns In the first replication: If N = /, then B 20 011 = missing, else B 20 011 = Ns; in the other replications B 20 011 = Ns. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type C if N = 9 or /, then B 20 012 = missing, else B 20 012 = C. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud hshs | m, -1, 4 |
| D 07 088 |  |  | “Period” parameters of sequence D 07 089 |  |
|  |  |  | Present and past weather |  |
|  | B 20 003 |  | Present weather ww | Code table, 0, 3 |
|  | B 04 024 |  | Time period At 00, 06, 12, 18 UTC = - 6. At 03, 09,15, 21 UTC = - 3. | Hour, 0, 4 |
|  | B 20 004 |  | Past weather (1) W1 | Code table, 0, 2 |
|  | B 20 005 |  | Past weather (2) W2 | Code table, 0, 2 |
|  |  |  | Evaporation |  |
|  | B 04 024 |  | Time period in hours = - 24 | Hour, 0, 4 |
|  | B 02 004 |  | Type of instrument for evaporation or iE crop type for evapotranspiration | Code table, 0, 2 |
|  | B 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1, 4 |
|  |  |  | Sunshine |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours In the first replication = - 24, in the second replication = - 1. | Hour, 0, 4 |
|  | B 14 031 |  | Total sunshine in minutes In the first replication SSS in the second replication SS | Minute, 0, 4 |
|  |  |  | Precipitation |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours tR | Hour, 0, 4 |
|  | B 13 011 |  | Total precipitation RRR no precipitation = 0 trace = - 0.1 | kg m-2, 1, 5 Encoded as: -00001 |
|  |  |  | Extreme temperatures |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 111 |  | Maximum temperature at height and over period specified snTxTxTx | °C, 2, 4 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 112 |  | Minimum temperature at height and over period specified snTnTnTn | °C, 2, 4 |
|  |  |  | Wind data |  |
|  | B 07 032 |  | Height of sensor above local ground (for wind measurement) | m, 2, 5 |
|  | B 02 002 |  | Type for instrumentation for wind measurement iw | Flag table, 0, 2 |
|  | B 08 021 |  | Time significance = 2 (time averaged) | Code table, 0, 2 |
|  | B 04 025 |  | Time period = - 10 (or number of minutes after a significant change of wind, if any) | Minute, 0, 4 |
|  | B 11 001 |  | Wind direction dd If dd = 00 (calm) or dd = 99 (variable), B 11 001 = 0. | Degree true, 0, 3 |
|  | B 11 002 |  | Wind speed ff | m s-1, 1, 4 |
|  | B 08 021 |  | Time significance (set to missing to cancel the previous value) | Code table, 0, 2 |

Notes:

- CREX Edition 1 is recommended for manual encoding of data.

- If the addition of another “instantaneous” parameter is required, the sequence descriptor D07089 shall be replaced by D07087 D07088, and the B-descriptor for this parameter shall be placed between D07087 and D07088.

- If the addition of another “period” parameter is required, the sequence D 07 089 shall be supplemented by the relevant B-descriptor provided no additional “instantaneous” parameter is needed.

Example

CREX++

T000103 A000 D07089++

63 894 1 2006 02 22 06 00 -0687 03920 00552 00564 10062 10122 //// // 0000 ///// ///// 00125  2900 2320 071 ///// 2500 038 07 03 0073 31 20 10 0001 01 03 08 0073 005 -0006 00 00 -0024 01 0085 -0024 0690 -0001 0060 -0024 00000 //// ///// 00125 //// //// -0012 2210 01000 14 02 -0010 060 0025 //++
7777

Example with optional check digits:

CREX++

T000103 A000 D07089 E++

063 1894 21 32006 402 522 606 700 8-0687 903920 000552 100564 210062 310122 4//// 5// 60000 7///// 8///// 900125 02900 12320 2071 3///// 42500 5038 607 703 80073 931 020 110 20001 301 403 508 60073 7005 8-0006 900 000 1-0024 201 30085 4-0024 50690

6-0001 70060 8-0024 900000 0//// 1///// 200125 3//// 4////  5-0012 62210 701000 814 902

0-0010 1060 20025 3//++
7777

ANNEX III

CREX

ZONE ASECNA

D07087 Paramètre instantanés

| Descripteur Table D | Descripteur Table B | Station de Surface et horodatage | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
| D 01 001 | B 01 001 | Indicateur OMM | Num 0, 2 | II |
|  | B 01 002 | Indicateur OMM de la station | Num 0 , 3 | iii |
|  | B 02 001 | Type de station | Table de code | ix |
| D 01 011 | B 04 001 | Année | Année 0 ,4 |  |
|  | B 04 002 | Mois | Mois 0 ,2 |  |
|  | B 04 003 | Jour | Jour 0 , 2 | YY |
| D 01 012 | B 04 004 | Heure | Heure 0 , 2 | GG |
|  | B 04 005 | Minute | Minute 0 , 2 | gg |

| Descripteur Table D | Descripteur Table B | Coordonnées horizontales Et verticales | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
| D 01 023 | B 05 002 | Latitude (faible précision) | Degrés 2 , 4 |  |
|  | B 06 002 | Longitude | Degrés 2 , 5 |  |
|  | B 07 030 | Altitude du sol de la station | m 1 ,5 |  |
|  | B 07 031 | Altitude de la cuvette du baromètre | m 1 ,5 |  |

| Descripteur Table D | Descripteur Table B | Données de pression | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
| D 02 001 | B 10 004 | Pression station | Pa -1 , 5 | P0P0P0P0 |
|  | B 10 051 | Pression Réduite niveau mer | Pa -1 , 5 | PPPP |
|  | B 10 061 | Variation de pression En 3h | Pa, -1 , 4 | ppp |
|  | B 10 063 | Tendance barométrique | Table de Code 0 , 2 | a |
|  | B 10 062 | Variation de pression En 24h | Pa, -1 , 4 | P24P24P24P24 |
|  | B 07 004 | Surface isobare Standard (925 ,850,700 …hPa) | Pa, -1 , 5 | a3 |
|  | B 10 009 | Géopotentiel de la surface standard | Mgp ,0 ,5 | hhh |

| Descripteur Table D | Descripteur Table B | Température et humidité | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
|  | B 07 032 | Hauteur du capteur de température au dessus du sol | m ,2 ,5 |  |
|  | B 12 101 | Température du thermomètre sec | °C ,2, 4 | SnTTT |
|  | B 12 103 | Température du point de rosé | °C ,2, 4 | SnTdTdTd |
|  | B 13 003 | Humidité relave | % , 0,3 |  |
|  | B 07 032 | Hauteur du capteur …du sol | ///// |  |

| Descripteur Table D | Descripteur Table B | Donnée de visibilité | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
|  | B 20 001 | Visibilité horizontale | m, -1 ,4 | VV |

| Descripteur Table D | Descripteur Table B | Données de nuages Section 1 du synop | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
| D 02 004 | B 20 010 | Nébulosité totale Si N= 9 , alors B 20 010 = 113% Si N=/ , alors B 20 010 = manquant. | %, 0, 3 | N |
|  | B 08 002 | Caractéristique verticale Si CL sont observés Alors B 08 002 = 7 (des nuages bas) Si CL ne sont observés et CM sont observés alors B 08 002 = 8(des nuages moyens), Si seulement CH sont observés, B 08002= 0 , Si N =9, alors B 08 002 = 5, Si N = 0, alors B 08 002 = 62, Si N=/ , alors B 20 010 = manquant. | Table de code, 0 , 2 | CL où CM |
|  | B 20 011 | Etendue de la couche de nuages (nuages bas et nuages moyens) Si N= 0, alors B 20 011 = 0 Si N=9, alors B 20 011= 9 Si N= /, alors B 20 011 = manquant. | Table de code, 0 , 2 | Nh |
|  | B 20 013 | Hauteur de la base des nuages Si N=0 où /, alors B 20 01 3 = manquant. | m, -1, 4 | h |
|  | B 20 012 | Types de nuages ( nuages bas) B 20 012 = CL +30, Si N = 0, alors B 20 012 = 30 , Si N=9 où /, alors B 20 01 2 = 62. | Table de code, 0 , 2 | CL |
|  | B 20 012 | Types de nuages ( nuages moyens) B 20 012 = CM +20, Si N = 0, alors B 20 012 = 20 , Si N=9 où /où CM = /, alors B 20 01 2 = 61 | Table de code, 0 , 2 | CM |
|  | B 20 012 | Types de nuages ( nuages supérieurs) B 20 012 = CH +10, Si N = 0, alors B 20 012 = 10 , Si N=9 où /où CH = /, alors B 20 01 2 = 60 | Table de code, 0 , 2 | CH |

| Descripteur Table D | Descripteur Table B | Données de nuages Section 3 du synop | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
| R 01 000 |  | Répétition différéé d’un descripteur |  |  |
| D 02 005 | B 08 002 | Caractéristique verticale Dans une couche de Cb, B 08 002 = 4 , sinon dans la première répétion : Si N = 9, alors B 08 002 = 5, Si N = /, alors B 08 002 = manquant, Sinon B 08 002 = 1 ; Dans les autres répétitions B 08 002 = 2 , 3 où 4. NB : première couche autre que Cb B 08 002 = 1. | Table de code, 0 , 2 |  |
|  | B 20 011 | Nébulosité partielle de la couche Dans la première répétiton : Si N = /, alors B 20 011= manquant, Sinon B 20 011 = Ns dans les autres répétition. | Table de code, 0 , 2 | Ns |
|  | B 20 012 | Type de nuages Si N = 9 ou / alors B 20 012 = manquant | Table de code, 0 , 2 | C |
|  | B 20013 | Hauteur de la base des nuages | Table de code, 0 , 2 | hshs |

D 07094 Paramètres périodiques (Liste racourcie)

| Descripteur Table D | Descripteur Table B | Temps présent et passé | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
|  | B 20 003 | Temps présent | Table de code, 0 , 2 | ww |
|  | B 04 024 | Période de temps A 00, 06, 12 ,18 UTC = -6 A 03, 09, 15, 21 UTC = -3 |  |  |
|  | B 20 004 | Temps passé (1) | Table de code, 0 , 2 | W1 |
|  | B 20 005 | Temps passé (2) | Table de code, 0 , 2 | W2 |

| Descripteur Table D | Descripteur Table B | Précipitation | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
|  | B 04 024 | Période de mesure en heures (00 UTC –6, 06UTC –24, 12 UTC, manquant, 18 UTC –12) Dernières 6 heures = -6 Dernières 12 heures = -12 Dernières 24 heures = -24 | Heure, 0, 4 | tR |
|  | B 13 011 | Précipitation totale Pas de précipitation=0 Trace=-0.1 | Kg.m-2, 1, 5 | RRR |

| Descripteur Table D | Descripteur Table B | Températures extrêmes | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
|  | B 07 032 | Hauteur du capteur au dessus du sol (Pour la mesure de la température) | m, 2, 5 |  |
|  | B 04 024 | Période de mesure en heures= -24 (18 UTC, sinon manquant)) | Heure, 0, 4 |  |
|  | B 12 111 | Temprérature maximale à une hauteur et sur une période spécifiée | °C, 2, 4 | TXTXTX |
|  | B 04 024 | Période de mesure en heures= -24 (06 UTC, sinon manquant), | Heure, 0, 4 | TnTnTn |
|  | B 12 111 | Temprérature minimale à une hauteur et sur une période spécifiée | °C, 2, 4 |  |

| Descripteur Table D | Descripteur Table B | Données de vents | Description des Eléments (Table B) | Synop |
| --- | --- | --- | --- | --- |
|  | B 07 032 | Hauteur du capteur au dessus du sol (Pour la mesure du vent) | m, 2, 5 |  |
|  | B 02 002 | Type d’instrument pour la mesure du vent | Table d’indicateurs, 0, 2 | iw |
|  | B 08 021 | Signification temporelle = 2 (moyenne sur 10 mn) | Table de code, 0, 2 |  |
|  | B 04 025 | Période de temps -10 (ou nombre de minutes après un changement significatif du vent, s’il y a lieu) | minute, 0, 4 |  |
|  | B 11 001 | Direction du vent à 10 m Si dd=à (calme) ou dd = 99 (variable) B 11 001 = 0 | degré vrai, 0, 3 | dd |
|  | B 11 002 | Vitesse du vent à 10 m | m.s-1, 1, 4 | ff |
|  | B 08 021 | Signification temporelle (mis manquant pour annuler la valeur temporelle) | // |  |

ANNEX IV

FOR VALIDATION

TM D07095 - Template for synoptic reports from fixed land stations suitable for SYNOP data manually encoded in CREX (in ASECNA Countries)

| D 07 095 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data manually encoded in CREX |
| --- | --- | --- |
|  | D 07 087 | “Instantaneous” parameters |
|  | D 07 094 | “Period” parameters |

Notes:

- “Instantaneous” parameter is a parameter that is not coupled to a time period descriptor, e.g. B04024.

- “Period” parameter is a parameter that is coupled to a time period descriptor, e.g. B04024.

This CREX template for synoptic reports from fixed land stations further expands as follows:

| D 07 087 |  |  | “Instantaneous” parameters “ |  |
| --- | --- | --- | --- | --- |
|  |  |  | Surface station identification, time, horizontal and vertical coordinates | in CREX |
|  | D 01 001 | B 01 001 | WMO block number II | Numeric, 0, 2 |
|  |  | B 01 002 | WMO station number iii | Numeric, 0, 3 |
|  | B 02 001 |  | Type of station (ix) | Code table, 0, 1 |
|  | D 01 011 | B 04 001 | Year | Year, 0, 4 |
|  |  | B 04 002 | Month | Month, 0, 2 |
|  |  | B 04 003 | Day YY | Day, 0, 2 |
|  | D 01 012 | B 04 004 | Hour GG | Hour, 0, 2 |
|  |  | B 04 005 | Minute gg | Minute, 0, 2 |
|  | D 01 023 | B 05 002 | Latitude (course accuracy) | Degree, 2, 4 |
|  |  | B 06 002 | Longitude (course accuracy) | Degree, 2, 5 |
|  | B 07 030 |  | Height of station ground above msl | m, 1, 5 |
|  | B 07 031 |  | Height of barometer above msl | m, 1, 5 |
|  |  |  | Pressure data |  |
|  | D 02 001 | B 10 004 | Pressure PoPoPoPo | Pa, –1, 5 |
|  |  | B 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1, 5 |
|  |  | B 10 061 | 3-hour pressure change ppp | Pa, –1, 4 |
|  |  | B 10 063 | Characteristic of pressure tendency a | Code table, 0, 2 |
|  | B 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1, 4 |
|  | B 07 004 |  | Pressure (standard level) a3 = 925, 850, 700, ..hPa = missing for lowland stations | Pa, –1, 5 |
|  | B 10 009 |  | Geopotential height of the standard level hhh = missing for lowland stations | gpm, 0, 5 |
|  |  |  | Temperature and humidity |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 12 101 |  | Temperature/dry-bulb temperature (sc. 2) snTTT | °C, 2, 4 |
|  | B 12 103 |  | Dew-point temperature (sc. 2) snTdTdTd | °C, 2, 4 |
|  | B 13 003 |  | Relative humidity | %, 0, 3 |
|  | B 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2, 5 |
|  |  |  | Visibility |  |
|  | B 20 001 |  | Horizontal visibility VV | m, –1, 4 |
|  |  |  | Cloud data |  |
|  | D 02 004 | B 20 010 | Cloud cover (total) N If N = 9, then B 20 010 = 113 %, if N = /, then B 20 010 = missing. | %, 0, 3 |
|  |  | B 08 002 | Vertical significance if CL are observed, then B 08 002 = 7 (low cloud), if CL are not observed and CM are observed, then B 08 002 = 8 (middle cloud), if only CH are observed, B 08 002 = 0, if N = 9, then B 08 002 = 5, if N = 0, then B 08 002 = 62, if N = /, then B 08 002 = missing. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount (of low or middle clouds) Nh If N = 0, then B 20 011 = 0, if N = 9, then B 20 011 = 9, if N = /, then B 20 011 = missing. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud h If N = 0 or /, then B 20 013 = missing. | m, –1, 4 |
|  |  | B 20 012 | Cloud type (low clouds) CL B 20 012 = CL + 30, if N = 0, then B 20 012 = 30, if N = 9 or /, then B 20 012 = 62. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (middle clouds) CM B 20 012 = CM + 20, if N = 0, then B 20 012 = 20, if N = 9 or / or CM = /, then B 20 012 = 61. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (high clouds) CH B 20 012 = CH + 10, if N = 0, then B 20 012 = 10, if N = 9 or / or CH = /, then B 20 012 = 60. | Code table, 0, 2 |
|  | R 01 000 |  | Delayed replication of the next 1 descriptor | 000r |
|  | D 02 005 | B 08 002 | Vertical significance In any Cb layer, B 08 002 = 4 , else: in the first replication: if N = 9, then B 08 002 = 5, if N = /, then B 08 002 = missing, else B 08 002 = 1; in the other replications B 08 002 = 2, 3, 4. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount Ns In the first replication: If N = /, then B 20 011 = missing, else B 20 011 = Ns; in the other replications B 20 011 = Ns. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type C if N = 9 or /, then B 20 012 = missing, else B 20 012 = C. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud hshs | m, -1, 4 |
| D 07 094 |  |  | “Period” parameters (shortened) |  |
|  |  |  | Present and past weather |  |
|  | B 20 003 |  | Present weather ww | Code table, 0, 3 |
|  | B 04 024 |  | Time period At 00, 06, 12, 18 UTC = - 6. At 03, 09,15, 21 UTC = - 3. | Hour, 0, 4 |
|  | B 20 004 |  | Past weather (1) W1 | Code table, 0, 2 |
|  | B 20 005 |  | Past weather (2) W2 | Code table, 0, 2 |
|  |  |  | Precipitation |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours tR | Hour, 0, 4 |
|  | B 13 011 |  | Total precipitation RRR , R24 R24 R24 R24 no precipitation = 0 trace = - 0.1 | kg m-2, 1, 5 Encoded as: -00001 |
|  |  |  | Extreme temperatures |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 111 |  | Maximum temperature at height and over period specified snTxTxTx | °C, 2, 4 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 112 |  | Minimum temperature at height and over period specified snTnTnTn | °C, 2, 4 |
|  |  |  | Wind data |  |
|  | B 07 032 |  | Height of sensor above local ground (for wind measurement) | m, 2, 5 |
|  | B 02 002 |  | Type for instrumentation for wind measurement iw | Flag table, 0, 2 |
|  | B 08 021 |  | Time significance = 2 (time averaged) | Code table, 0, 2 |
|  | B 04 025 |  | Time period = - 10 (or number of minutes after a significant change of wind, if any) | Minute, 0, 4 |
|  | B 11 001 |  | Wind direction dd If dd = 00 (calm) or dd = 99 (variable), B 11 001 = 0. | Degree true, 0, 3 |
|  | B 11 002 |  | Wind speed ff | m s-1, 1, 4 |
|  | B 08 021 |  | Time significance (set to missing to cancel the previous value) | Code table, 0, 2 |

Note:	CREX Edition 1 is recommended for manual encoding of data.

Example

CREX++

T000103 A000 D07095++

61 677 1 2006 02 22 06 00 -1444 01730 00552 00564 10062 10122 //// // 0000 ///// ///// 00125 2900 2320 071 ///// 2500 038 07 03 0073 31 20 10 0001 01 03 08 0073 005 -0006 00 00 -0024 00000 //// ///// 00125 //// //// -0012 2210 01000 14 02 -0010 060 0025 //++
7777

Example with optional check digits:

CREX++

T000103 A000 D07095 E++

061 1677 21 32006 402 522 606 700 8-1444 901730 000552 100564 210062 310122 4//// 5// 60000 7///// 8///// 900125 02900 12320 2071 3///// 42500 5038 607 703 80073 931 020 110 20001 301 403 508 60073 7005 8-0006 900 000 1-0024 200000 3//// 4///// 500125 6//// 7////  8-0012 92210 001000 114 202 3-0010 4060 50025 6//++
7777