| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.3.3(1) ITEM: 3.3.3 (16.7. 2008) ENGLISH ONLY |
| --- | --- | --- |

# SMOS in BUFR

(Submitted by M. Dragosavac, ECMWF)

### Summary and Purpose of Document

This document summarizes SMOS definition in BUFR, and it presents a proposal for approval by the ET/DR+C.

________________________________________________________________

# ACTION PROPOSED

The ET/DR+C is invited to review the document and approve the contents for pre-operational implementation.

# BACKGROUND

# Scheduled for launch in 2008, SMOS (Soil Moisture and Ocean Salinity) is the second Earth Explorer Opportunity mission to be developed as part of ESA's (European Space Agency) Living Planet Programme. As well as demonstrating the use of the new radiometer, the data acquired from this mission will contribute to furthering our knowledge of the Earth's water cycle. The data acquired from the SMOS mission will lead to better weather and extreme-event forecasting, and contribute to seasonal-climate forecasting. As a secondary objective, SMOS will also provide observations over regions of snow and ice, contributing to studies of the cryosphere:

# (http://www.esa.int/esaLP/LPsmos.html).

# An important aspect of this mission is that it will demonstrate a new measuring technique by adopting a completely different approach in the field of observing the Earth from space. A novel instrument has been developed that is capable of observing both soil moisture and ocean salinity by capturing images of emitted microwave radiation around the frequency of 1.4 GHz (L-band). SMOS will carry the first-ever, polar-orbiting, space-

# borne, 2-D interferometric radiometer.

# Proposed  new Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 01 144 | Snapshop idenfier | Numeric | 0 | 0 | 31 | Numeric | 0 | 10 |
| 0 15 012 | Total electron count | 1/M**2 | -16 | 0 | 6 | 1/M**2 | -16 | 2 |
| 0 12 165 | Direct sun brightness temperature | K | 0 | 0 | 23 | K | 0 | 7 |
| 0 12 166 | Snapshot accuracy | K | 1 | -4000 | 13 | K | 1 | 4 |
| 0 12 167 | Radiomentric accuracy ( pure polarisation) | K | 1 | 0 | 9 | K | 1 | 3 |
| 012168 | Radiometric accuracy ( cross polarisation) | K | 1 | 0 | 9 | K | 1 | 3 |
| 030010 | Number of grid points | Numeric | 0 | 0 | 13 | Numeric | 0 | 4 |
| 001024 | Grid point identifier | Numeric | 0 | 0 | 24 | Numeric | 0 | 8 |
| 007011 | Grid point altitude | M | 2 | -10000 | 20 | M | 2 | 7 |
| 013048 | Water fraction | % | 1 | 0 | 10 | % | 1 | 4 |
| 012080 | Brightness temperature real part | K | 2 | 0 | 16 | K | 2 | 5 |
| 012081 | Brightness temperature imaginary part | K | 2 | 0 | 16 | K | 2 | 5 |
| 012082 | Pixel radiometric accuracy | K | 2 | 0 | 12 | K | 2 | 4 |
| 025081 | Incidence angle | Degree | 3 | 0 | 17 | Degree | 3 | 6 |
| 025082 | Azimuth angle | Degree | 3 | 0 | 19 | Degree | 3 | 6 |
| 025083 | Faraday rotational angle | Degree | 3 | 0 | 19 | Degree | 3 | 6 |
| 025084 | Geometric rotational angle | Degree | 5 | 0 | 26 | Degree | 5 | 8 |
| 027010 | Footprint axis 1 | M | -1 | 0 | 14 | M | -1 | 5 |
| 028010 | Footprint axis 2 | M | -1 | 0 | 14 | M | -1 | 5 |
| 025144 | SMOS information flag | Flag table | 0 | 0 | 14 | Flag table | 0 | 5 |
| 002098 | Polarisation | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 001007 | Satellite identifer | Code table | 0 | 0 | 10 |  |  |  |
| 004001 | Year | Year | 0 | 0 | 12 |  |  |  |
| 004002 | Month | Month | 0 | 0 | 4 |  |  |  |
| 004003 | Day | Day | 0 | 0 | 6 |  |  |  |
| 004004 | Hour | Hour | 0 | 0 | 5 |  |  |  |
| 004005 | Minute | Minute | 0 | 0 | 6 |  |  |  |
| 004006 | Second | Second | 0 | 0 | 6 |  |  |  |
| 005001 | Latitude | Degrees | 5 | -9000000 | 25 |  |  |  |
| 006001 | Longitude | Degrees | 5 | -18000000 | 26 |  |  |  |
| 033xxx | Snapshot overall quality | Code table | 0 | 0 | 3 |  |  |  |

# Proposed  new BUFR Table D sequence for SMOS data

312070    001007

002019

001144

001024

030010

301011

301013

301021

007011

015012

012165

012166

012167

012168

027010

028010

002098

013048

025081

025082

025083

025084

012080

012081

012082

025144

033028

# Add new code table 033028 Snapshot overall quality

# 0 33 028 Snapshot overall quality

# Code           Meaning

# 1                Nominal

# 2               Degraded by SW error; any error reported by the algorithms

# 3                Degraded by instrument error

# 4               Degraded by corrupted /missing ADF

# 5-6             Reserved

# 7               Missing value

Add  new code table  002098 Polarisation:

0 02 098  Polarisation

Code         Meaning

0		HH polarisation

1		VV polarisation

2	            HV polarisation real valued component

3		HV polarisation imaginary valued component

4-6		Reserved

7                Missing value

Add  new Flag table  025144  SMOS information flag:

0 25 144

Bit number     Meaning

1               Pixel is affected by RFI effects

2               Pixel is located in the hexagonal Alias direction centred on Sun alias

3               Pixel is close to the border delimiting the extended Alias free zone

4               Pixel is inside the extended Alias free zone

5               Pixel is inside the exclusive of Alias free zone

6               Pixel is located in a zone where a Moon Alias was reconstructed

7               Pixel is located in a zone where Sun reflection has been detected

8               Pixel is located in a zone where Sun Alias was reconstructed

9               Flat target transformation has been performed during image reconstruction                                         			of this pixel

10               Scene has been combined with an adjustment scene in opposite

polarisation during image reconstruction to account for cross-polarisation

leakage

11                Direct Moon correction has been performed during image reconstruction

of this pixel

12                Reflected Sun correction has been performed during image reconstruction

of this pixel

13                Direct Sun correction has been performed during image reconstruction of

this image

All 14           Missing valu

# Add the following new Sub category on Common Code Table C-13

Data category			International sub-category

12  Surface data (satellite)            007     SMOS data

An example of expanded sequence

DATA DESCRIPTORS (UNEXPANDED)

1  312070

DATA DESCRIPTORS (EXPANDED)

ELEMENT NAME                                                                 			 UNIT

1  001007  SATELLITE IDENTIFIER						CODE TABLE 1007

2  002019 SATELLITE INSTRUMENT USED                                                               CODE TABLE 2019

3  001144  SNAPSHOT IDENTIFIER (VAL)					NUMERIC

4  001024  GRID POINT IDENTIFIER  (VAL)					NUMERIC

5  030010  NUMBER OF GRID POINTS (VAL)                                       		NUMERIC

6  004001  YEAR                                                                                         		YEAR

7  004002  MONTH                                                                                      		MONTH

8  004003  DAY                                                                                            		DAY

9  004004  HOUR                                                                                        	 	HOUR

10  004005  MINUTE                                                                                     		MINUTE

11  004006  SECOND                                                                                    		SECOND

12  005001  LATITUDE (HIGH ACCURACY)                                             		DEGREE

13  006001  LONGITUDE (HIGH ACCURACY)                                           		DEGREE

14  007011  GRID POINT ALTITUDE (VAL)                                              		M

15  015012  TOTAL ELECTRON COUNT (VAL)                                        		1/M**2

16  012165  DIRECT SUN BRIGHTNESS TEMPERATURE (VAL)  		K

17  012166  SNAPSHOT ACCURACY (VAL)                                             		K

18  012167  RADIOMETRIC ACCURACY (PURE POLARISATION)  (VAL)	K

19  012168  RADIOMETRIC ACCURACY (CROSS POLARISATION) (VAL)	K

20  027010  FOOTPRINT AXIS 1 (VAL)                                           		 	M

21  028010  FOOTPRINT AXIS 2 (VAL)                                            		M

22  002098  POLARISATION  (VAL)                                              		 	CODE TABLE

23  013048  WATER FRACTION                                                    			%

24  025081  INCIDENCE ANGLE (VAL)                                             		DEGREE

25  025082  AZIMUTH ANGLE (VAL)                                               		DEGREE

26  025083  FARADAY ROTATIONAL ANGLE (VAL)                                    	DEGREE

27  025084  GEOMETRIC ROTATIONAL ANGLE (VAL)                                	DEGREE

28  012080  BRIGHTNESS TEMPERATURE REAL PART (VAL)                   	K

29  012081  BRIGHTNESS TEMPERATURE IMAGINARY PART (VAL)      	K

30  012082  PIXEL RADIOMETRIC ACCURACY (VAL)                                  	K

31  025144  SMOS INFORMATION FLAG  (VAL)                                     	 	FLAG TABLE

32  033028  SNAPSHOT OVERALL QUALITY                                                             CODE TABLE

Data size estimation:

One bufr message will contain 4800 subsets  which is equivalent to one snapshot with 4800 pixels. One file can contain one or more bufr messages.

The data size of  one subset = 405 bits ~ 50 bytes

Number of subsets                = 4800

Expected bufr compression rate= 5

Total size of one snapshot= 50*4800/5=48000 bytes

Number of snapshots/ day = 72000

Total size per day =   72000*48000  =   3.456 GB