| WORLD METEOROLOGICAL ORGANIZATION ________________ JOINT MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES and COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C Doc. 3.3.4(1) _______ (25.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for GOME data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new BUFR descriptors to be used in the reporting of GOME (Global Ozone Monitoring Experiment) data.

_________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve

the contents for preoperational implementation.

BACKGROUND AND DISCUSSION

A proposal was circulated via email to the WMO codes group in November 2007 concerning the plans of U.S. NESDIS to begin creating and disseminating ozone data from the GOME (Global Ozone Monitoring Experiment) in BUFR.  The proposed new sequence and two new descriptors were reviewed, and helpful comments were received from several members of the codes group.  After taking these into account, the sequence was revised as shown below.  NESDIS recently began disseminating these products to numerous customers, so preoperational status for the below proposal is now requested.

PROPOSAL

Color codes:

- New descriptor proposed as pre-operational within this document

3–10–018     Ozone data

001007 – Satellite identifier

005040 – Orbit number

004001 – Year

004043 – Day of year

004004 – Hour

004005 – Minute

004006 – Second

207002 – Increase scale, reference value and data width

026030 – Integration time

207000 – Cancel increase scale, reference value and data width

005002 – Latitude

006002 – Longitude

033072 – Ozone error flag

007025 – Solar zenith angle

005022 – Solar azimuth angle

207002 – Increase scale, reference value and data width

015001 – Total ozone

207000 – Cancel increase scale, reference value and data width

008003 - Vertical significance (“0” = surface)

207001 – Increase scale, reference value and data width

010004 – Pressure (terrain)

207000 - Cancel increase scale, reference value and data width

008003 - Vertical significance (“Missing” = Cancel)

008003 - Vertical significance (“2” = Cloud top)

033042 - Type of limit represented by following value (“0” = Exclusive lower limit)

207001 - Increase scale, reference value and data width

007004 – Pressure

207000 – Cancel increase scale, reference value and data width

207002 – Increase scale, reference value and data width

015001 – Total ozone (below cloud top pressure)

207000 – Cancel increase scale, reference value and data width

008003 – Vertical significance (“Missing” = Cancel)

207002 – Increase scale, reference value and data width

020081 – Cloud amount in segment (cloud fraction)

207000 – Cancel increase scale, reference value and data width

020065 – Snow cover

008029 – Remotely-sensed surface type

207004 – Increase scale, reference value and data width

015030 – Aerosol contamination index

207000 – Cancel increase scale, reference value and data width

008075 – Ascending/descending orbit qualifier

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 26 030 | Integration time | Second | 2 | 0 | 8 | Second | 2 | 8 |
| 0 33 072 | Ozone error flag | Code table | 0 | 0 | 5 | Code table | 0 | 5 |

0-33-072   Ozone error flag

| 0 | Good retrieval |
| --- | --- |
| 1 | Reflectivity out of range |
| 2 | Larger Pixels (Number of cross-track pixels less than 32) or backward scans Error |
| 3 | Solar zenith angle greater than 88 |
| 4 | Latitude/longitude out of range |
| 5 | Viewing zenith angle or solar zenith angle out of range |
| 6 | Step-one process failed in general |
| 7 | First guess ozone out of range |
| 8 | Too many iterations (exceed 8) |
| 9 | Step-one residue calculation failed |
| 10 | Step-two process failed in general |
| 11 | First guess ozone profile out of range |
| 12 | Step-two ozone value out of range |
| 13 | Step-two residue calculation failed |
| 14 | Step-three process failed in general |
| 15 | Polarization Correction Accuracy Alert |
| 16 | Radiance or irradiance less or equal to zero |
| 17-30 | Reserved |
| 31 | Missing |