| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.3.5(1) (25.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

# BUFR Table B and Table D entries for encoding of IASI principal component scores

# Submitted by EUMETSAT

________________________________________________________________

# Summary and Purpose of Document

This document contains a proposal for addition of new entries in BUFR Tables B and D.

________________________________________________________________

# ACTION PROPOSED

# The meeting is invited to discuss the content of this document and approve the contents for validation status.

# References:

[1] Manual on Codes, WMO-No. 306, Volume I.2

1. Background

In order to make effective use of the available band width for the dissemination of hyper-spectral data from the IASI instrument on its METOP spacecraft, EUMETSAT will perform a principal component analysis of the data, and disseminate a subset of principal component scores to its users.

In order to improve the efficiency of the method, each spectrum is split up in to three distinct bands, corresponding to the bands on the instrument itself.  The principal component analysis is performed separately for each band, and the resulting scores are encoded using three distinct blocks of delayed replication within the BUFR descriptor sequence.

Three new BUFR Table B descriptors have been used.  These are described in Section 3 of this document.  It is also proposed to introduce a new BUFR Table D sequence descriptor for these data.

# 2. Expanded descriptor sequence

It is proposed to use the following sequence of entries for the encoding of the principal component scores resulting from the compression of hyper-spectral data from IAIS data (new entries are in italicised and underlined):

| F X Y | Description | Unit | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
|  | Satellilte processing information |  |  |  |  |
| 0 01 007 | Satellite identifier |  |  |  |  |
| 0 01 031 | Identification of originating/generating centre |  |  |  |  |
| 0 02 019 | Satellite instruments |  |  |  |  |
| 0 02 020 | Satellite classification |  |  |  |  |
|  | Date and time |  |  |  |  |
| 0 04 001 | Year |  |  |  |  |
| 0 04 002 | Month |  |  |  |  |
| 0 04 003 | Day |  |  |  |  |
| 0 04 004 | Hour |  |  |  |  |
| 0 04 005 | Minute |  |  |  |  |
| 2 02 131 | Add 3 to the scale |  |  |  |  |
| 2 01 138 | Add 10 to the width |  |  |  |  |
| 0 04 006 | Seconds |  |  |  |  |
| 2 01 000 | Reset width to default |  |  |  |  |
| 2 02 000 | Reset scale to default |  |  |  |  |
| 0 05 001 | Latitude (high accuracy) |  |  |  |  |
|  | Location information |  |  |  |  |
| 0 06 001 | Longitude (high accuracy) |  |  |  |  |
| 0 07 024 | Satellite zenith angle |  |  |  |  |
| 0 05 021 | Bearing or azimuth |  |  |  |  |
| 0 07 025 | Solar zenith angle |  |  |  |  |
| 0 05 022 | Solar azimuth |  |  |  |  |
| 0 05 043 | Field of view number |  |  |  |  |
| 0 05 040 | Orbit number |  |  |  |  |
| 2 01 133 | Add 5 to the width |  |  |  |  |
| 0 05 041 | Scan line number |  |  |  |  |
| 2 01 000 | Reset width to default |  |  |  |  |
| 2 01 132 | Add 4 to the width |  |  |  |  |
| 0 25 070 | Major frame count |  |  |  |  |
| 2 01 000 | Reset width to default |  |  |  |  |
| 2 02 126 | Subtract 2 from the scale |  |  |  |  |
| 0 07 001 | Height of station |  |  |  |  |
| 2 02 000 | Reset scale to default |  |  |  |  |
|  | Quality information |  |  |  |  |
| 0 33 060 | Gqisflagqual - individual IASI-System quality flag |  |  |  |  |
| 0 33 061 | Gqisqualindex - indicator for instrument noise performance (contributions from spectral and radiometric) |  |  |  |  |
| 0 33 062 | Gqisqualindexloc - indicator for geometric quality index |  |  |  |  |
| 0 33 063 | Gqisqualindexrad - indicator for instrument noise performance (contributions from radiometric calibration) |  |  |  |  |
| 0 33 064 | Gqisqualindexspect - indicator for instrument noise performance (contributions from spectral calibration) |  |  |  |  |
| 0 33 065 | Gqissystecsondqual - output of system TEC (Technical Expertise Centre) quality function |  |  |  |  |
|  | AVHRR scene analysis |  |  |  |  |
| 0 02 019 | Satellite instruments |  |  |  |  |
| 0 25 051 | AVHRR channel combination |  |  |  |  |
| 1 01 007 | Repeat next one descriptor 7 times |  |  |  |  |
| 3 40 004 | IASI Level 1c AVHRR single scene |  |  |  |  |
| 0 20 081 | Cloud amount in segment |  |  |  |  |
| 0 08 029 | Remotely sensed surface type |  |  |  |  |
| 0 20 083 | Amount of segment covered by scene |  |  |  |  |
| 0 08 029 | Remotely sensed surface type |  |  |  |  |
| 0 33 007 | Per cent confidence |  |  |  |  |
|  | Instrument band definition |  |  |  |  |
| 1 04 003 | Repeat next 4 descriptors 3 times |  |  |  |  |
| 0 25 140 | Start channel |  |  |  |  |
| 0 25 141 | End channel |  |  |  |  |
| 0 40 015 | Quantization factor | Numeric | 2 | 0 | 16 |
| 0 40 016 | Residual RMS in band | Numeric | 0 | 0 | 16 |
|  | Principal component scores for band 1 |  |  |  |  |
| 1 01 000 | Delayed replication of one descriptor |  |  |  |  |
| 0 31 002 | Extended delayed replication factor |  |  |  |  |
| 0 40 017 | Non-normalised principal component score | Numeric | 0 | -1073741824 | 31 |
|  | Principal component scores for band 2 |  |  |  |  |
| 1 01 000 | Delayed replication of one descriptor |  |  |  |  |
| 0 31 002 | Extended delayed replication factor |  |  |  |  |
| 0 40 017 | Non-normalised principal component score | Numeric | 0 | -1073741824 | 31 |
|  | Principal component scores for band 3 |  |  |  |  |
| 1 01 000 | Delayed replication of one descriptor |  |  |  |  |
| 0 31 002 | Extended delayed replication factor |  |  |  |  |
| 0 40 017 | Non-normalised principal component score | Numeric | 0 | -1073741824 | 31 |

It is proposed to allocate the Table D entry 3 40 006 for the above sequence.

3. Explanation of proposed new descriptors

3.1 Quantization factor, 0 40 015

Principal component scores are divided by this number, before they are rounded to the nearest integer.

3.2 Residual RMS in band, 0 40 016

The noise normalised residual RMS for each band is a quality indicator which is computed based on noise normalised reconstruction residuals before quantisation.

3.3 Non-normalised principal component score, 0 40 017

The principal component scores within each field are ordered by rank (scores corresponding to eigenvectors with higher eigenvalues first). The total number of scores for a particular band is given by the associated extended delayed replication factor.

4. Summary

The Meeting is invited to consider the proposed Table B and Table D entries, and to reserve these for validation.

Appendix A: Acronyms

AVHRR	Advanced Very High Resolution Radiometer

EUMETSAT	European Organisation for the Exploitation of Meteorological Satellites

IASI		Infrared Atmospheric Sounding Interferometer

Metop		The Metop satellites carry on board a set of state-of-the-art sounding and imaging instruments that offer improved remote sensing capabilities to both meteorologists and climatologists. The Metop series is part of the Initial Joint Polar-Orbiting Operational Satellite System (IJPS) constellation, along with the NOAA-N and -N' satellites.

NOAA		U.S. National Oceanic and Atmospheric Administration

RMS		Root Mean Square

U.S.		United States of America