| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.3.5(2) (25.VIII.2008) ENGLISH ONLY |
| --- | --- | --- |

# BUFR Table B and Table D entries for encoding of enhanced data from IASI

# Submitted by EUMETSAT

________________________________________________________________

# Summary and Purpose of Document

This document contains proposals for additional BUFR element descriptors, sequence descriptors, and code table entries required for the representation of enhanced IASI data from the Metop spacecraft.

________________________________________________________________

# ACTION PROPOSED

# The meeting is invited to discuss the content of this document and approve the contents for validation status.

# References:

[1] Final Report of ET/DR&C Meeting, Muscat, Oman, 5-8 December, 2005

[2] Final Report of Joint ET/DR&C and ET/MTDCF Meeting, Montreal, Canada, 8-12 May, 2006

[3] Manual on Codes, WMO-No. 306, Volume I.2

1. Background

1.1 History of BUFR Table D descriptor, 3 40 001

The IASI instrument is a hyperspectral sounder, which flies on the METOP spacecraft operated by EUMETSAT.  The level 1c data from IASI are being exchanged operationally in BUFR via the GTS and via EUMETSAT’s DVB satellite multicast service, EUMETCast.

Additions to BUFR Tables B and D and the Code and Flag Tables were proposed for validation in 2005 (see reference document [1], paragraph 3.10.7).  These proposals were refined in 2006 and were proposed fro pre-operational status (see reference document [2], paragraph 3.4.2).  The additions to the Manual on Codes came into force in November 2007.

1.2 Data set with reduced number of channels

The Table D sequence descriptor (3-40-001) was designed for the encoding of 8,700 channels in each spectrum.  The associated data sets are too big for some users and require a large dissemination bandwidth.  As such, a subset of channels are compiled into a reduced product which is disseminated in parallel the users.  The encoding of this reduced data set uses a BUFR sequence very similar to 3-40-001, but with delayed rather than fixed replication of the channels.

1.3 Encoding of supplementary information

During the early operational life of IASI on METOP-A, it has become clear that some additional parameters are required as part of the level 1c data set in order to make more effective use of the data.  These parameters require minor modification to the existing BUFR Tables.

# 2. Proposed descriptor sequences

# 2.1 Full IASI level 1c data set (all channels)

It is proposed to use the following sequence of entries for the encoding of the full (8700 channel) IASI level 1c data (new entries are in italicised and underlined, changes from 3-40-001 are highlighted in grey):

New Sequence Descriptor (3-40-007): "IASI Level 1c data (all channels)"

| 0-01-007 | Satellite identifier |
| --- | --- |
| 0-01-031 | Identification of originating/generating centre |
| 0-02-019 | Satellite instruments |
| 0-02-020 | Satellite classification |
| 0-04-001 | Year |
| 0-04-002 | Month |
| 0-04-003 | Day |
| 0-04-004 | Hour |
| 0-04-005 | Minute |
| 2-02-131 | Add 3 to scale |
| 2-01-138 | Add 10 to width |
| 0-04-006 | Second |
| 2-01-000 | Reset width |
| 2-02-000 | Reset scale |
| 0-05-001 | Latitude (high accuracy) |
| 0-06-001 | Longitude (high accuracy) |
| 0-07-024 | Satellite zenith angle |
| 0-05-021 | Bearing or azimuth |
| 0-07-025 | Solar zenith angle |
| 0-05-022 | Solar azimuth |
| 0-05-043 | Field of view number |
| 0-05-040 | Orbit number |
| 2-01-133 | Add 5 to width |
| 0-05-041 | Scan line number |
| 2-01-000 | Reset width |
| 2-01-132 | Add 4 to width |
| 0-25-070 | Major frame count |
| 2-01-000 | Reset width |
| 2-02-126 | Subtract 2 from scale |
| 0-07-001 | Height of station |
| 2-02-000 | Reset scale |
| 1-03-003 | Repeat next 3 descriptor 3 times |
| 0-25-140 | Start channel |
| 0-25-141 | End channel |
| 0-33-060 | GQisFlagQual |
| 0-33-061 | QGisQualIndex |
| 0-33-062 | QGisQualIndexLoc |
| 0-33-063 | QGisQualIndexRad |
| 0-33-064 | QGisQualIndexSpect |
| 0-33-065 | GQisSysTecSondQual |
| 0-40-020 | GQisFlagQualDetailed - Quality flag for the system |
| 1-01-010 | Repeat next 1 descriptor 10 times |
| 3-40-002 | IASI Level 1c band description |
| 1-01-087 | Repeat next 1 descriptor 87 times |
| 3-40-003 | IASI Level 1c 100 channel sequence |
| 0-02-019 | Satellite instruments |
| 0-25-051 | AVHRR channel combination |
| 1-01-007 | Repeat next 1 descriptor 7 times |
| 3-40-004 | IASI Level 1c AVHRR single scene sequence |
| 0-20-081 | Cloud amount in segment |
| 0-08-029 | Remotely sensed surface type |
| 0-20-083 | Amount of segment covered by scene |
| 0-08-029 | Remotely sensed surface type |
| 0-40-018 | Average of imager measurements |
| 0-40-019 | Variance of imager measurements |
| 0-40-021 | Fraction of weighted AVHRR pixel in IASI FOV covered with snow/ice |
| 0-40-022 | Number of missing, bad or failed AVHRR pixels |

# 2.2 Reduced IASI level 1c data set (subset of channels)

It is proposed to use the following sequence of entries for the encoding of the full (8700 channel) IASI level 1c data (new entries are in italicised and underlined, changes from 3-40-001 are highlighted in grey):

New Sequence Descriptor (3-40-008): "IASI Level 1c data (subset of channels)"

| 0-01-007 | Satellite identifier |
| --- | --- |
| 0-01-031 | Identification of originating/generating centre |
| 0-02-019 | Satellite instruments |
| 0-02-020 | Satellite classification |
| 0-04-001 | Year |
| 0-04-002 | Month |
| 0-04-003 | Day |
| 0-04-004 | Hour |
| 0-04-005 | Minute |
| 2-02-131 | Add 3 to scale |
| 2-01-138 | Add 10 to width |
| 0-04-006 | Second |
| 2-01-000 | Reset width |
| 2-02-000 | Reset scale |
| 0-05-001 | Latitude (high accuracy) |
| 0-06-001 | Longitude (high accuracy) |
| 0-07-024 | Satellite zenith angle |
| 0-05-021 | Bearing or azimuth |
| 0-07-025 | Solar zenith angle |
| 0-05-022 | Solar azimuth |
| 0-05-043 | Field of view number |
| 0-05-040 | Orbit number |
| 2-01-133 | Add 5 to width |
| 0-05-041 | Scan line number |
| 2-01-000 | Reset width |
| 2-01-132 | Add 4 to width |
| 0-25-070 | Major frame count |
| 2-01-000 | Reset width |
| 2-02-126 | Subtract 2 from scale |
| 0-07-001 | Height of station |
| 2-02-000 | Reset scale |
| 1-03-003 | Repeat next 3 descriptor 3 times |
| 0-25-140 | Start channel |
| 0-25-141 | End channel |
| 0-33-060 | GQisFlagQual |
| 0-33-061 | QGisQualIndex |
| 0-33-062 | QGisQualIndexLoc |
| 0-33-063 | QGisQualIndexRad |
| 0-33-064 | QGisQualIndexSpect |
| 0-33-065 | GQisSysTecSondQual |
| 0-40-020 | GQisFlagQualDetailed - Quality flag for the system |
| 1-01-010 | Repeat next 1 descriptor 10 times |
| 3-40-002 | IASI Level 1c band description |
| 1-04-000 | Delayed replication of next 4 descriptors |
| 0-31-002 | Extended delayed replication factor |
| 2-01-136 | Add 8 to width |
| 0-05-042 | Channel number |
| 2-01-000 | Reset width |
| 0-14-046 | Scaled IASI radiance |
| 0-02-019 | Satellite instruments |
| 0-25-051 | AVHRR channel combination |
| 1-01-007 | Repeat next 1 descriptor 7 times |
| 3-40-004 | IASI Level 1c AVHRR single scene sequence |
| 0-20-081 | Cloud amount in segment |
| 0-08-029 | Remotely sensed surface type |
| 0-20-083 | Amount of segment covered by scene |
| 0-08-029 | Remotely sensed surface type |
| 0-40-018 | Average of imager measurements |
| 0-40-019 | Variance of imager measurements |
| 0-40-021 | Fraction of weighted AVHRR pixel in IASI FOV covered with snow/ice |
| 0-40-022 | Number of missing, bad or failed AVHRR pixels |

3. Explanation of proposed new descriptors

New Element Descriptors:

| Descriptor | Name | Units | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
| (0-40-018) | GIacAvgImagIIS - Average of imager measurements | W/(m² sr m-1) | -3 | 0 | 16 |
| (0-40-019) | GIacVarImagIIS - Variance of imager measurements | W/(m² sr m-1) | -3 | 0 | 16 |
| (0-40-020) | GQisFlagQualDetailed - Quality flag for the system | Flag Table | 0 | 0 | 17 |
| (0-40-021) | Fraction of weighted AVHRR pixel in IASI FOV covered with snow/ice | % | 0 | 0 | 7 |
| (0-40-022) | Number of missing, bad or failed AVHRR pixels | Numeric | 0 | 0 | 7 |

New Flag Table (0-40-020) " GQisFlagQualDetailed - Quality flag for the system "

Bit number		Meaning

1 			NZPD and Complex calibration error

2 			Band 3 affected by spike

3 			Band 3 affected by saturation

4 			Band 2 affected by spike

5 			Band 1 affected by spike

6 			Overflow/Under Flow

7 			On-board processing error

8 			Spectral calibration error

9 			Radiometric calibration error

10 			Missing AVHRR data

11 			Missing IIS data

12			Missing Sounder data

13			GQisFlagQual summary flag for all bands

14			On-Ground processing error

15			Inter-calibration error IASI/AVHRR

16			Spare

All 17			Missing

4. Summary

The Meeting is invited to consider the proposed Table B and Table D entries, and to reserve these for validation.

Appendix A: Acronyms

AVHRR	Advanced Very High Resolution Radiometer

DVB		Digital Video Broadcast

EUMETSAT	European Organisation for the Exploitation of Meteorological Satellites

FOV		Field of View

GTS		Global Telecommunications System

IASI		Infrared Atmospheric Sounding Interferometer

Metop		The Metop satellites carry on board a set of state-of-the-art sounding and imaging instruments that offer improved remote sensing capabilities to both meteorologists and climatologists. The Metop series is part of the Initial Joint Polar-Orbiting Operational Satellite System (IJPS) constellation, along with the NOAA-N and -N' satellites.

NOAA		U.S. National Oceanic and Atmospheric Administration

NZPD		Number of Zero Path Difference

U.S.		United States of America