| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.4(1) ITEM: 3.4 (19.8.2008) ENGLISH ONLY |
| --- | --- | --- |

Proposal for updated Master Table for oceanographic data

Submitted by Hester Viola for JCOMM and IOC

________________________________________________________________

Summary and Purpose of Document

The document contains the proposed new version of Master Table 10 for Oceanographic Data including Table B and updated Code Tables.

JCOMM and IOC wish to pose several questions to the ET DR&C before validation begins.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and

as far as possible provide advice on the questions asked. The process for validation of the new version should be discussed.

#### No. of Appendices (2)

#### References:

[1]  CT-MTDCF/ET-DR&C  Document 3.1.7 Templates for Oceanographic and Marine Meteorology, modifications to template for BATHY and requests for additions and modifications to common codes.

#### 1. Background

a) The first version of Master Table 10 was developed and finalised in 1998. Since then there has been minimal application of the table. Recently, the UK Metoffice has been using the master table in support of the GHRSST Project, but there has been little other use.

b) However JCOMM is keen to ensure that the Master Table is useful to data providers and users alike and was requested by GHRSST to update it and ensure it adhered to WMO regulations. Also, with the development of BUFR templates for various kinds of data collected by JCOMM, the need for this second Master Table has grown. In particular coastal ocean observations are expected soon to be ready for exchange in JCOMM and many of these new variables will be biogeochemical ones that require greater detail on instrumentation and methods, something that MT10 provides.

#### 2. Proposals

The proposed new version of Master Table 10 (in Appendix I) and its accompanying Code and Flag tables (Appendix II) is a modification of the original Master Table definition, which involved minor changes to the Table B classes 1-9 to make it conform to current regulations covering BUFR Master Tables.

a) Class Definitions - The proposed changes made to the 1998 MT10 Class definitions are as follows:

- Class “0 03: Methods” to be moved to a new class “0 25: Methods”

- Class “0 05: Time and Frequency” to be moved to a new class “0 27: Time and Frequency” unless the answer to Question A (see below) is affirmative

- Class “0 06: Location (horizontal)” split into Classes “0 05: Location (horizontal -1)” and “0 06: Location (horizontal -2)”

- Class “0 08: Location (relative)” moved to Class “0 10: Observation Qualifiers”

- Class “0 09: Instrument Metadata” moved to a new Class “0 26: Instrument Metadata”

- Class “0 10:Observation qualifiers” previously had no comment to explain its purpose, so the following comment has been added “Observation characteristics, quality and location qualifiers”

- Class “0 28: Significance qualifiers” was moved to Class “0 08: Significance Qualifiers”

- Within Class “0 01: Identification” the element entitled IGOSS message identifier (0 01 009) was renamed JCOMM GTS identifier. The alternative is to deprecate 009 and insert a new descriptor.

## BUFR MASTER 10 TABLE B — CLASSIFICATION OF ELEMENTS

| F | X | Class | Comments |
| --- | --- | --- | --- |
| 0 | 00 | BUFR table entries |  |
| 0 | 01 | Identification | Identifies origin and type of data |
| 0 | 02 | Instrumentation | Defines instrument types used |
| 0 | 03 | Reserved |  |
| 0 | 04 | Location (time) | Defines time and time derivatives |
| 0 | 05 | Location (horizontal – 1) | Defines geographical position, including horizontal derivatives, in association with class 06 (first dimension of horizontal space) |
| 0 | 06 | Location (horizontal – 2) | Defines geographical position, including horizontal derivatives, in association with class 05 (second dimension of horizontal space) |
| 0 | 07 | Location (vertical) | Defines height, altitude, pressure level, including vertical derivatives of position |
| 0 | 08 | Significance qualifiers | Defines special character of data |
| 0 | 09 | Reserved |  |
| 0 | 10 | Observation qualifiers | Observation characteristics, quality and location qualifiers |
| 0 | 11 | Meteorological elements | Observations of meteorological variables |
| 0 | 20 | Physical oceanographic elements | Observations of the physical oceanographic variables |
| 0 | 21 | Chemical elements | Observations of physical chemical variables |
| 0 | 22 | Geophysics | Observations of geophysical variables |
| 0 | 23 | Waves | Observations of surface gravity wave variables |
| 0 | 24 | Biological elements | Observations of biological variables |
| 0 | 25 | Methods | Defines methods used to make the observation |
| 0 | 26 | Instrument Metadata | Defines instrument characteristics |
| 0 | 27 | Time and Frequency |  |
| 0 | 29 | Processing information | Processing history of the data. |
| 0 | 31 | Data desc. operator qualifiers | Elements used in conjunction with data description operators. |

Names in bold have been added or changed in 2008

b) Code and Flag table definitions - The proposed additions and modifications to code tables are summarized as follows. More detail is included in document 3.1.7

- Element 0 01 006 Type of data buoy:  Various additions to code table 0 02 149 Type of data buoy

- Element  0 01 009 JCOMM GTS message identifier: Addition of one entry

- Element 0 02 007 Location System: Various additions to code table 0 02 148 Data Collection and Location System

- Element 0 02 008 to refer to code table 0 02 034

- Code figures added to Elements  0 01 007, 0 02 028, 0 02 007 (therefore 0 02 148),  for “Missing” value

#### 3. Questions

- Could the entries in “Class 0 27 Time and Frequency” fit within the definition of “Class 0 04 Location (Time)” ?

- Is it acceptable to have the contents of Class “0 08” as they are (the old contents of Class “0 28”)

- Do all non-SI units have to be specified with an additional comment?

- What is the process for validation and ongoing management of this Master Table? Noting that JCOMM would like the Master Table to be validated as soon as possible.

#### 4. Conclusions

The proposed changes to the Master Table should bring the definitions within the regulations of WMO.

The JCOMM Data Management Programme Area is forming a Task Team On Table Driven Code Forms with membership from other Programme Areas of JCOMM. It will be the responsibility of this team to coordinate the development and extension of BUFR templates for variables measured within JCOMM programmes. An additional responsibility will be the maintenance of MT10. It is expected that the Task Team will bring recommendations on new requirements and updates to ET DR&C for approval..

## APPENDIX I

Last update: Thursday, August 21, 2008

## BUFR MASTER 10 TABLE B — CLASSIFICATION OF ELEMENTS

| F | X | Class | Comments |
| --- | --- | --- | --- |
| 0 | 00 | BUFR table entries |  |
| 0 | 01 | Identification | Identifies origin and type of data |
| 0 | 02 | Instrumentation | Defines instrument types used |
| 0 | 03 | Reserved |  |
| 0 | 04 | Location (time) | Defines time and time derivatives |
| 0 | 05 | Location (horizontal – 1) | Defines geographical position, including horizontal derivatives, in association with class 06 (first dimension of horizontal space) |
| 0 | 06 | Location (horizontal – 2) | Defines geographical position, including horizontal derivatives, in association with class 05 (second dimension of horizontal space) |
| 0 | 07 | Location (vertical) | Defines height, altitude, pressure level, including vertical derivatives of position |
| 0 | 08 | Significance qualifiers | Defines special character of data |
| 0 | 09 | Reserved |  |
| 0 | 10 | Observation qualifiers | Observation characteristics, quality and location qualifiers |
| 0 | 11 | Meteorological elements | Observations of meteorological variables |
| 0 | 20 | Physical oceanographic elements | Observations of the physical oceanographic variables |
| 0 | 21 | Chemical elements | Observations of physical chemical variables |
| 0 | 22 | Geophysics | Observations of geophysical variables |
| 0 | 23 | Waves | Observations of surface gravity wave variables |
| 0 | 24 | Biological elements | Observations of biological variables |
| 0 | 25 | Methods | Defines methods used to make the observation |
| 0 | 26 | Instrument Metadata | Defines instrument characteristics |
| 0 | 27 | Time and Frequency |  |
| 0 | 29 | Processing information | Processing history of the data. |
| 0 | 31 | Data desc. operator qualifiers | Elements used in conjunction with data description operators. |

Names in bold have been added or changed in 2008

### Table of Contents

BUFR MASTER 10 TABLE B — CLASSIFICATION OF ELEMENTS	4

Table of Contents	5

Class 01: Identification	5

Class 02: Instrumentation	5

Class 03: Reserved	5

Class 04: Location (Time)	5

Class 05: Location (horizontal – 1)	5

Class 06: Location (horizontal-2)	5

Class 07: Location (vertical)	5

Class 08: Significance Qualifiers	5

Class 09:  Reserved	5

Class 10: Observation qualifiers	5

Class 11: Meteorological elements	5

Class 20: Physical oceanography elements	5

Class 21: Chemistry elements	5

Class 22: Geophysics elements	5

Class 23: Wave elements	5

Class 25 – Methods	5

Class 26 Instrument Metadata	5

Class 27: Time and Frequency (could go to Class 4?)	5

Class 29: Processing information	5

Class 31: Data descriptor operator qualifiers	5

Non-SI units used in the above tables	5

### Class 01: Identification

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 1 | Platform identifier | CCITT IA5 | 0 | 0 | 64 |
| 0 | 1 | 2 | GTS bulletin originating centre (CCCC) | CCITT IA5 | 0 | 0 | 32 |
| 0 | 1 | 3 | GTS bulletin type (TTAAII) | CCITT IA5 | 0 | 0 | 48 |
| 0 | 1 | 5 | Profile type | code | 0 | 0 | 7 |
| 0 | 1 | 6 | Type of data buoy (BUFR 0 02149) | code | 0 | 0 | 6 |
| 0 | 1 | 7 | Data originator | code | 0 | 0 | 10 |
| 0 | 1 | 8 | Data collection identifier | CCITT IA5 | 0 | 0 | 80 |
| 0 | 1 | 9 | JCOMM GTS message identifier | code | 0 | 0 | 4 |

### Class 02: Instrumentation

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 2 | 1 | Dissolved oxygen instrument | code | 0 | 0 | 3 |
| 0 | 2 | 2 | Cast type | code | 0 | 0 | 5 |
| 0 | 2 | 3 | Current instrument | code | 0 | 0 | 4 |
| 0 | 2 | 4 | Wave instrument | code | 0 | 0 | 5 |
| 0 | 2 | 5 | Salinity instrument | code | 0 | 0 | 4 |
| 0 | 2 | 6 | Water temperature instrument | code | 0 | 0 | 4 |
| 0 | 2 | 7 | Location system (BUFR 0 02 148) | code | 0 | 0 | 5 |
| 0 | 2 | 8 | Drogue type (BUFR 0 02 034) | code | 0 | 0 | 5 |

### Class 03: Reserved

### Class 04: Location (Time)

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 4 | 1 | Year | year | 0 | 0 | 12 |
| 0 | 4 | 2 | Month of the year | month | 0 | 0 | 4 |
| 0 | 4 | 3 | Day of the year (Jan 1st=1) | day | 0 | 0 | 9 |
| 0 | 4 | 4 | Hour | hour | 0 | 0 | 5 |
| 0 | 4 | 5 | Minute | minute | 0 | 0 | 6 |
| 0 | 4 | 6 | Second | second | 0 | 0 | 6 |
| 0 | 4 | 7 | Day of the month | day | 0 | 0 | 6 |
| 0 | 4 | 8 | Time period or displacement | year | 0 | -1024 | 11 |
| 0 | 4 | 9 | Time period or displacement | month | 0 | -1024 | 11 |
| 0 | 4 | 10 | Time period or displacement | day | 0 | -1024 | 11 |
| 0 | 4 | 11 | Time period or displacement | hour | 0 | -2048 | 12 |
| 0 | 4 | 12 | Time period or displacement | minute | 0 | -2048 | 12 |
| 0 | 4 | 13 | Time period or displacement | second | 0 | -4096 | 13 |

### Class 05: Location (horizontal – 1)

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 5 | 1 | Latitude (high accuracy) | degrees | 5 | -9000000 | 25 |
| 0 | 5 | 2 | Latitude (coarse accuracy) | degrees | 2 | -9000 | 15 |

### Class 06: Location (horizontal-2)

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 6 | 1 | Longitude (high accuracy) | degrees | 5 | -18000000 | 26 |
| 0 | 6 | 2 | Longitude (coarse accuracy) | degrees | 2 | -18000 | 16 |

### Class 07: Location (vertical)

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 7 | 1 | Height/altitude above ground level | metres | -1 | -40 | 16 |
| 0 | 7 | 2 | Height above sea floor | metres | 0 | -10000 | 15 |
| 0 | 7 | 3 | Bathymetric depth | metres | 1 | 0 | 17 |
| 0 | 7 | 4 | Depth below sea surface | metres | 1 | 0 | 17 |
| 0 | 7 | 5 | Height/altitude above mean sea level | metres | 1 | 0 | 17 |
| 0 | 7 | 6 | Height/altitude above sea surface | metres | 1 | 0 | 17 |
| 0 | 7 | 7 | Sea pressure (sea surface = o) | decibars | 3 | 0 | 24 |
| 0 | 7 | 8 | Relative total pressure | decibars | 3 | 0 | 24 |
| 0 | 7 | 9 | Observed sea level | metres | 3 | -30000 | 16 |
| 0 | 7 | 10 | Total pressure (atmosphere + sea pressure) | decibars | 3 | 0 | 24 |

### Class 08: Significance Qualifiers

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 8 | 1 | Time significance | code | 0 | 0 | 4 |
| 0 | 8 | 2 | Coordinate | code | 0 | 0 | 2 |
| 0 | 8 | 3 | Vertical significance (surface observations) (BUFR 0 08 002) | code | 0 | 0 | 6 |

### Class 09:  Reserved

### Class 10: Observation qualifiers

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 10 | 1 | Selection of depth levels | code | 0 | 0 | 4 |
| 0 | 10 | 2 | Depth of drogue | metres | 1 | 0 | 12 |
| 0 | 10 | 3 | Chemical component | code | 0 | 0 | 4 |
| 0 | 10 | 4 | Chemical content qualifier code | code | 0 | 0 | 4 |
| 0 | 10 | 5 | Salinity units | code | 0 | 0 | 3 |
| 0 | 10 | 10 | Direction reference | code | 0 | 0 | 3 |
| 0 | 10 | 11 | First order statistics code | code | 0 | 0 | 6 |
| 0 | 10 | 12 | Specific time of observation | code | 0 | 0 | 3 |
| 0 | 10 | 20 | GTSPP quality control code (BUFR 10-020) | code | 0 | 0 | 3 |
| 0 | 10 | 21 | JCOMM quality control code | code | 0 | 0 | 4 |
| 0 | 10 | 22 | Quality control test(s) performed | flag table | 0 | 0 | 64 |
| 0 | 10 | 23 | Quality control test(s) failed | flag table | 0 | 0 | 64 |
| 0 | 10 | 24 | Quality of location (WMO 3311) | code | 0 | 0 | 3 |
| 0 | 10 | 25 | Quality of buoy satellite transmission (WMO 3313) | code | 0 | 0 | 2 |
| 0 | 10 | 30 | Precision/accuracy indicator | code | 0 | 0 | 4 |
| 0 | 10 | 31 | Confidence interval | code | 0 | 0 | 3 |
| 0 | 10 | 32 | Data availability | code | 0 | 0 | 3 |
| 0 | 10 | 33 | Platform identifier type | code | 0 | 0 | 4 |
| 0 | 10 | 36 | Trace direction | code | 0 | 0 | 3 |
| 0 | 10 | 37 | Probe hit bottom indicator | code | 0 | 0 | 1 |
| 0 | 10 | 38 | Duplicate indicator | code | 0 | 0 | 1 |
| 0 | 10 | 39 | Wind speed indicator (WMO 1853) | code | 0 | 0 | 3 |
| 0 | 10 | 40 | Indicator for method of current measurement (WMO 2266) | code | 0 | 0 | 3 |
| 0 | 10 | 75 | Zenith angle of object from reference point | degrees | 2 | 0 | 14 |
| 0 | 10 | 76 | Across track displacement (starboard +ve) | metres | 0 | -30000 | 16 |
| 0 | 10 | 77 | Along track displacement | metres | 0 | 0 | 16 |
| 0 | 10 | 78 | Bearing of object from reference point | degrees | 1 | 0 | 12 |
| 0 | 10 | 79 | Distance of object in direction from reference point | metres | 0 | -50000 | 17 |
| 0 | 10 | 80 | Horizontal distance of object from reference point | metres | 0 | 0 | 16 |
| 0 | 10 | 81 | Direct distance of object from reference point | metres | 0 | 0 | 16 |
| 0 | 10 | 82 | Elevation angle of object from reference point | degrees | 2 | -9000 | 15 |
| 0 | 10 | 83 | Vertical distance of object above reference point | metres | 0 | -10000 | 15 |
| 0 | 10 | 84 | Pitch angle | degrees | 2 | 0 | 14 |
| 0 | 10 | 85 | Roll angle | degrees | 2 | -9000 | 15 |

### Class 11: Meteorological elements

|  | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 11 | 1 | Cloud cover (total) | percent | 0 | 0 | 7 |
| 0 | 11 | 2 | Total cloud amount (oktas, BUFR 20-011) | code | 0 | 0 | 4 |
| 0 | 11 | 3 | Height of base of cloud | meters | -1 | -40 | 11 |
| 0 | 11 | 4 | Cloud type (BUFR 20-012) | code | 0 | 0 | 6 |
| 0 | 11 | 7 | Present weather (BUFR 20-003) | code | 0 | 0 | 9 |
| 0 | 11 | 8 | Past weather(1) (BUFR 20-004) | code | 0 | 0 | 5 |
| 0 | 11 | 9 | Past weather(2) (BUFR 20-005) | code | 0 | 0 | 5 |
| 0 | 11 | 12 | Horizontal visibility | metres | -1 | 0 | 13 |
| 0 | 11 | 13 | Total precipitation/ total water equivalent | kg/m^2 | 1 | -1 | 14 |
| 0 | 11 | 14 | Rainfall/water equivalent of snow (averaged rate) | kg/m^2/s | 4 | 0 | 12 |
| 0 | 11 | 20 | Pressure reduced to mean sea level | pa | -1 | 0 | 14 |
| 0 | 11 | 21 | Pressure | pa | -1 | 0 | 14 |
| 0 | 11 | 22 | Pressure change | pa | -1 | -1024 | 11 |
| 0 | 11 | 23 | Vapour pressure | pa | -1 | 0 | 10 |
| 0 | 11 | 24 | Specific humidity | kg/kg | 5 | 0 | 14 |
| 0 | 11 | 25 | Relative humidity | percent | 0 | 0 | 7 |
| 0 | 11 | 26 | Humidity mixing ratio | kg/kg | 5 | 0 | 14 |
| 0 | 11 | 40 | Horizontal wind speed | m/s | 1 | 0 | 12 |
| 0 | 11 | 41 | Direction from which wind is blowing | degrees (true) | 0 | 0 | 9 |
| 0 | 11 | 42 | Maximum wind speed (gusts) | m/s | 1 | 0 | 12 |
| 0 | 11 | 43 | Maximum wind gust direction from which gust is blowing | degrees (true) | 0 | 0 | 9 |
| 0 | 11 | 44 | U component of wind speed (+ve east) | m/s | 1 | -4096 | 13 |
| 0 | 11 | 45 | V component of wind speed (+ve north) | m/s | 1 | -4096 | 13 |
| 0 | 11 | 46 | Absolute wind shear in 1 km layer below | m/s | 1 | 0 | 12 |
| 0 | 11 | 47 | Absolute wind shear in 1 km layer above | m/s | 1 | 0 | 12 |
| 0 | 11 | 48 | W component of wind speed | m/s | 2 | -4096 | 13 |
| 0 | 11 | 50 | Temperature/dry bulb temperature | degrees C | 1 | -1024 | 12 |
| 0 | 11 | 51 | Wet bulb temperature | degrees C | 1 | -1024 | 12 |
| 0 | 11 | 52 | Dew point temperature | degrees C | 1 | -1024 | 12 |
| 0 | 11 | 53 | Virtual air temperature | degrees C | 1 | -1024 | 12 |
| 0 | 11 | 60 | Brightness temperature | degrees C | 1 | -1024 | 12 |
| 0 | 11 | 61 | Short-wave direct radiation | w/m^2 | -3 | -2048 | 12 |
| 0 | 11 | 62 | Short-wave diffuse radiation | w/m^2 | -3 | -2048 | 12 |
| 0 | 11 | 63 | Short-wave incoming radiation | w/m^2 | -3 | -2048 | 12 |
| 0 | 11 | 64 | Short-wave outgoing radiation | w/m^2 | -3 | -2048 | 12 |
| 0 | 11 | 65 | Long-wave incoming radiation | w/m^2 | -3 | -2048 | 12 |
| 0 | 11 | 66 | Long-wave outgoing radiation | w/m^2 | -3 | -2048 | 12 |
| 0 | 11 | 67 | Net radiation | w/m^2 | -4 | -16348 | 15 |

### Class 20: Physical oceanography elements

|  | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 20 | 1 | Potential temperature | degrees C | 3 | -2000 | 16 |
| 0 | 20 | 2 | Salinity | psu (practical salinity units) | 3 | 0 | 14 |
| 0 | 20 | 3 | Electrical conductivity | mhos/m | 4 | 0 | 16 |
| 0 | 20 | 4 | Chlorinity (parts/thousand) | kg/kg | 3 | 0 | 16 |
| 0 | 20 | 5 | Chlorosity | kg/m^3 | 3 | 0 | 16 |
| 0 | 20 | 6 | Sea temperature | degrees C | 3 | -2000 | 16 |
| 0 | 20 | 7 | Sea density | kg/m^3 | 6 | 0 | 23 |
| 0 | 20 | 8 | Sound velocity | m/s | 3 | 0 | 21 |
| 0 | 20 | 9 | Horizontal current speed | m/s | 3 | 0 | 14 |
| 0 | 20 | 10 | Direction to which horizontal current is flowing | degrees (true) | 1 | 0 | 12 |
| 0 | 20 | 11 | East component of current | m/s | 3 | -10000 | 15 |
| 0 | 20 | 12 | North component of current | m/s | 3 | -10000 | 15 |
| 0 | 20 | 15 | Secchi disc depth | metres | 1 | 0 | 13 |
| 0 | 20 | 25 | Water colour (Forel-Ule scale) | code | 0 | 0 | 4 |
| 0 | 20 | 26 | Code for ice in vicinity of hydrographic observation | code | 0 | 0 | 4 |

### Class 21: Chemistry elements

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 21 | 1 | Hydrogen ion concentration (pH) | numeric | 3 | 0 | 14 |
| 0 | 21 | 2 | Total alkalinity | mmol/m^3 | 1 | 10000 | 14 |
| 0 | 21 | 3 | Carbonate alkalinity | mmol/m^3 | 1 | 10000 | 14 |
| 0 | 21 | 4 | Chlorophyll-a content | mg/m^3 | 3 | 0 | 16 |
| 0 | 21 | 5 | Dissolved oxygen | mmol/m^3 | 3 | 0 | 22 |
| 0 | 21 | 6 | Phosphate (PO4-P) content | mmol/m^3 | 2 | 0 | 10 |
| 0 | 21 | 7 | Total phosphorous (P) content | mmol/m^3 | 2 | 0 | 10 |
| 0 | 21 | 8 | Nitrate (N03-N) content | mmol/m^3 | 3 | 0 | 16 |
| 0 | 21 | 9 | Nitrite (NO2-N) content | mmol/m^3 | 3 | 0 | 12 |
| 0 | 21 | 10 | Nitrate + nitrite content | mmol/m^3 | 3 | 0 | 16 |
| 0 | 21 | 11 | Total nitrogen (N) content | mmol/m^3 | 3 | 0 | 16 |
| 0 | 21 | 12 | Organic nitrogen content | mmol/m^3 | 3 | 0 | 17 |
| 0 | 21 | 13 | Ammonium (NH4-N) content | mmol/m^3 | 3 | 0 | 12 |
| 0 | 21 | 14 | Silicate (SiO4-Si) content | mmol/m^3 | 2 | 0 | 15 |
| 0 | 21 | 15 | Total carbon (C) content | mmol/m^3 | 3 | 0 | 20 |
| 0 | 21 | 16 | Organic carbon content | mmol/m^3 | 3 | 0 | 17 |
| 0 | 21 | 17 | Hydrogen sulphide (H2S-S) content | mmol/m^3 | 3 | 0 | 16 |

### Class 22: Geophysics elements

|  | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 22 | 1 | Bathymetric two way travel time | seconds | 2 | 0 | 16 |
| 0 | 22 | 2 | Total magnetic field | nanoteslas | 0 | 0 | 16 |
| 0 | 22 | 3 | Residual magnetic field | nanoteslas | 0 | -60000 | 17 |
| 0 | 22 | 4 | Magnetic field correction | nanoteslas | 0 | -60000 | 17 |
| 0 | 22 | 5 | Observed gravity | milligals | 0 | 0 | 20 |
| 0 | 22 | 6 | Free air gravity anomaly | milligals | 0 | -500 | 10 |
| 0 | 22 | 7 | Bouger gravity anomaly | milligals | 0 | -500 | 10 |
| 0 | 22 | 8 | Gravity eotvos correction | milligals | 0 | -500 | 10 |
| 0 | 22 | 9 | Bathymetric datum indicator | code | 0 | 0 | 5 |

### Class 23: Wave elements

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 23 | 1 | Sea state (WMO code 3700) | code | 0 | 0 | 4 |
| 0 | 23 | 2 | Visual average wave height | metres | 2 | 0 | 13 |
| 0 | 23 | 3 | Visual estimate of wave period | seconds | 2 | 0 | 12 |
| 0 | 23 | 4 | Visual estimate of direction from which waves come | degrees | 0 | 0 | 9 |
| 0 | 23 | 5 | Direction from which swell is coming | degrees | 0 | 0 | 9 |
| 0 | 23 | 6 | Swell height | metres | 1 | 0 | 9 |
| 0 | 23 | 7 | Swell period | seconds | 0 | 0 | 6 |
| 0 | 23 | 10 | Total water depth | metres | 0 | 0 | 14 |
| 0 | 23 | 11 | Still water depth | metres | 0 | 0 | 14 |
| 0 | 23 | 12 | Mean record water depth | metres | 0 | 0 | 14 |
| 0 | 23 | 13 | Maximum wave level | metres | 2 | 0 | 13 |
| 0 | 23 | 14 | Minimum wave level | metres | 2 | 0 | 13 |
| 0 | 23 | 15 | Second highest wave crest | metres | 2 | 0 | 13 |
| 0 | 23 | 16 | Second lowest wave trough | metres | 2 | 0 | 13 |
| 0 | 23 | 17 | Maximum crest to trough wave height | metres | 2 | 0 | 13 |
| 0 | 23 | 18 | Maximum zero crossing wave height | metres | 2 | 0 | 13 |
| 0 | 23 | 19 | Average height highest one third | metres | 2 | 0 | 13 |
| 0 | 23 | 20 | Tucker Draper significant wave height | metres | 2 | 0 | 13 |
| 0 | 23 | 21 | RMS wave displacement | metres | 2 | 0 | 13 |
| 0 | 23 | 22 | Characteristic wave height (4*RMS) | metres | 2 | 0 | 13 |
| 0 | 23 | 30 | Period of maximum zero crossing wave | seconds | 2 | 0 | 13 |
| 0 | 23 | 31 | Average zero crossing wave period | seconds | 2 | 0 | 13 |
| 0 | 23 | 32 | Average wave crest period | seconds | 2 | 0 | 13 |
| 0 | 23 | 33 | Spectral width (broadness) | numeric | 2 | 0 | 10 |
| 0 | 23 | 40 | Instantaneous water surface elevation | metres | 2 | -10000 | 15 |
| 0 | 23 | 41 | Instantaneous heave acceleration | m/s^2 | 3 | -10000 | 15 |
| 0 | 23 | 42 | Water surface east-west tilt angle (+ve to east) | degrees | 2 | -9000 | 15 |
| 0 | 23 | 43 | Water surface north-south tilt angle (+ve to north) | degrees | 2 | -9000 | 15 |
| 0 | 23 | 50 | Wave variance spectral density: S(f) | m^2/hz | 6 | 0 | 27 |
| 0 | 23 | 51 | Wave spectrum peak period | seconds | 2 | 0 | 12 |
| 0 | 23 | 52 | Zeroeth moment of wave spectrum | m^2 | 6 | 0 | 27 |
| 0 | 23 | 53 | First moment of wave spectrum | m^2.hz | 6 | 0 | 27 |
| 0 | 23 | 54 | Second moment of wave spectrum | (m.hz)^2 | 6 | 0 | 27 |
| 0 | 23 | 55 | Third moment of wave spectrum | m^2.hz^3 | 6 | 0 | 27 |
| 0 | 23 | 56 | Fourth moment of wave spectrum | m^2.hz^4 | 6 | 0 | 27 |
| 0 | 23 | 57 | First negative moment of wave spectrum | m^2/hz | 6 | 0 | 27 |
| 0 | 23 | 58 | Second negative moment of wave spectrum | (m/hz)^2 | 6 | 0 | 27 |
| 0 | 23 | 59 | Waves spectral width from moments | numeric | 2 | 0 | 13 |
| 0 | 23 | 60 | Spectral moments (-1,0) wave period | seconds | 2 | 0 | 13 |
| 0 | 23 | 61 | Spectral moments (0,1) wave period | seconds | 2 | 0 | 13 |
| 0 | 23 | 62 | Spectral moments (0,2) wave period | seconds | 2 | 0 | 13 |
| 0 | 23 | 63 | Spectral moments (2,4) wave period | seconds | 2 | 0 | 13 |
| 0 | 23 | 70 | Auto-spectrum of north-south tilt | deg^2/hz | 6 | 0 | 27 |
| 0 | 23 | 71 | Auto-spectrum of east-west tilt | deg^2/hz | 6 | 0 | 27 |
| 0 | 23 | 72 | Quad-spectrum of heave and n-s tilt | m.deg/hz | 6 | -50000000 | 27 |
| 0 | 23 | 73 | Quad-spectrum of heave and e-w tilt | m.deg/hz | 6 | -50000000 | 27 |
| 0 | 23 | 74 | Quad-spectrum of n-s and e-w tilts | deg^2/hz | 6 | -50000000 | 27 |
| 0 | 23 | 75 | Co-spectrum of heave and n-s tilt | m.deg/hz | 6 | -50000000 | 27 |
| 0 | 23 | 76 | Co-spectrum of heave and east-west tilt | m.deg/hz | 6 | -50000000 | 27 |
| 0 | 23 | 77 | Co-spectrum of n-s and e-w tilts | deg^2/hz | 6 | -50000000 | 27 |
| 0 | 23 | 78 | Wave number from cross spectra | degrees/m | 6 | 0 | 27 |
| 0 | 23 | 79 | Mean wave direction from cross spectra | degrees | 2 | 0 | 16 |
| 0 | 23 | 80 | Wave dir spread from cross spectra | degrees | 2 | 0 | 15 |
| 0 | 23 | 81 | Directional wave spectrum density | m^2/hz | 6 | 0 | 27 |
| 0 | 23 | 82 | Specified direction of wave energy propagation | degrees | 0 | 0 | 9 |
| 0 | 23 | 84 | Wave spectrum peak energy direction | degrees | 2 | 0 | 16 |
| 0 | 23 | 85 | Wave spectrum mean energy direction | degrees | 0 | 0 | 9 |

### Class 25 – Methods

|  | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 25 | 1 | Free air gravity anomaly ref system | code | 0 | 0 | 4 |
| 0 | 25 | 2 | Reference residual magnetic field | code | 0 | 0 | 4 |
| 0 | 25 | 3 | Bathymetry sound velocity correct area | code | 0 | 0 | 5 |
| 0 | 25 | 4 | Prime navigation aid fix code | code | 0 | 0 | 3 |
| 0 | 25 | 5 | Free air gravity anomaly formula | code | 0 | 0 | 3 |
| 0 | 25 | 12 | Duration of application | code | 0 | 0 | 3 |
| 0 | 25 | 13 | Frequency sampling technique | code | 0 | 0 | 3 |
| 0 | 25 | 14 | Interval sampling code | code | 0 | 0 | 3 |
| 0 | 25 | 15 | Digitization method | code | 0 | 0 | 4 |
| 0 | 25 | 16 | Filter type | code | 0 | 0 | 3 |
| 0 | 25 | 20 | Correction procedure for depth from sound speed | code | 0 | 0 | 4 |
| 0 | 25 | 21 | Method of depth correction for sound speed | code | 0 | 0 | 4 |
| 0 | 25 | 22 | Method of sound velocity measurement | code | 0 | 0 | 3 |
| 0 | 25 | 23 | Density calculation | code | 0 | 0 | 4 |
| 0 | 25 | 28 | Method of current averaging | code | 0 | 0 | 4 |
| 0 | 25 | 29 | Duration and time of eulerian current measure (WMO 2264) | code | 0 | 0 | 4 |
| 0 | 25 | 30 | Period of current measurement (drift) (WMO 2265) | code | 0 | 0 | 4 |
| 0 | 25 | 35 | Method of temperature measurement | code | 0 | 0 | 5 |
| 0 | 25 | 36 | Method of salinity/depth measurement (WMO 2263) | code | 0 | 0 | 3 |
| 0 | 25 | 37 | Method of depth measurement | code | 0 | 0 | 4 |
| 0 | 25 | 38 | Pressure measurement method | code | 0 | 0 | 3 |
| 0 | 25 | 45 | Method code for position fixing | code | 0 | 0 | 5 |
| 0 | 25 | 46 | Method of wave calculation | code | 0 | 0 | 4 |

### Class 26 Instrument Metadata

|  | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 26 | 11 | Platform heading | degrees | 0 | 0 | 9 |
| 0 | 26 | 12 | True platform speed across the ground | m/s | 2 | 0 | 16 |
| 0 | 26 | 13 | Azimuth of major axis of navigation error ellipse | degrees | 0 | 0 | 9 |
| 0 | 26 | 14 | Length of semimajor axis of navigation error ellipse | metres | 0 | 0 | 13 |
| 0 | 26 | 15 | Length of semiminor axis of navigation error ellipse | metres | 0 | 0 | 13 |
| 0 | 26 | 16 | Magnetic variation from true north (+ve clockwise) | degrees | 1 | 0 | 12 |
| 0 | 26 | 17 | Bearing of object from reference point (+ve clockwise) | degrees | 0 | 0 | 9 |
| 0 | 26 | 18 | Angle of attack (aircraft) | degrees | 0 | 0 | 9 |
| 0 | 26 | 19 | Indicated platform speed (aircraft) | m/s | 2 | 0 | 16 |
| 0 | 26 | 20 | Relative platform speed through the air/water | m/s | 2 | 0 | 16 |
| 0 | 26 | 21 | Vertical platform speed | m/s | 2 | 0 | 16 |
| 0 | 26 | 22 | Angle of sideslip (aircraft) | degrees | 0 | 0 | 9 |

### Class 27: Time and Frequency (could go to Class 4?)

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 27 | 1 | Frequency | hertz | 5 | 0 | 17 |
| 0 | 27 | 2 | Frequency of spectral component | hertz | 5 | 0 | 17 |
| 0 | 27 | 3 | Bandwidth of spectral analysis | hertz | 5 | 0 | 17 |
| 0 | 27 | 4 | Bandwidth of spectral component | hertz | 5 | 0 | 17 |
| 0 | 27 | 5 | High frequency cutoff for integration under spectrum | hertz | 5 | 0 | 17 |
| 0 | 27 | 6 | Low frequency cutoff for integration under spectrum | hertz | 5 | 0 | 17 |
| 0 | 27 | 7 | Bandwidth of directional analysis | degrees | 0 | 0 | 9 |

### Class 29: Processing information

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 29 | 1 | Processing centre | code | 0 | 0 | 5 |
| 0 | 29 | 2 | Processing function identifier | code | 0 | 0 | 7 |
| 0 | 29 | 3 | Version of processing function | numeric | 2 | 0 | 10 |
| 0 | 29 | 4 | Processing action taken | code | 0 | 0 | 6 |
| 0 | 29 | 5 | Parameter acted upon | code | 0 | 0 | 8 |
| 0 | 29 | 6 | Qualifier of parameter acted upon | numeric | 3 | 0 | 25 |
| 0 | 29 | 7 | Value of parameter before action taken | numeric | 3 | 0 | 25 |

### Class 31: Data descriptor operator qualifiers

| F | X | Y | Element Name | Unit | Scale | Ref Value | Data Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 31 | 1 | Delayed descriptor replication factor | numeric | 0 | 0 | 8 |
| 0 | 31 | 2 | Extended delayed descriptor replication factor | numeric | 0 | 0 | 16 |
| 0 | 31 | 11 | delayed descriptor and data repetition factor | numeric | 0 | 0 | 8 |
| 0 | 31 | 12 | Extended delayed descriptor repetition factor | numeric | 0 | 0 | 16 |
| 0 | 31 | 21 | Associated field significance | code | 0 | 0 | 6 |
| 0 | 31 | 31 | Data present indicator | flag table | 0 | 0 | 1 |

### Non-SI units used in the above tables

1. 0-20-002 Salinity in psu (practical salinity units). This is now the basic measure of salinity based on a ratio of conductivity of a sample compared to a reference conductivity. Functionally it is almost equivalent in value to the previous standard which had units of Kg/Kg (parts per thousand).

2. 0-22-005 to 008 gravity measurements in milligals. A gal = 1 cm/sec/sec. It is a cgs unit and as such while not SI, conversion is trivial.

## APPENDIX II

Code Tables and Flag Tables Associated with BUFR Master Table 10, Table B

Notes: In developing code tables associated with BUFR Table B to specify units of elements, the following principles should be applied:

- Code tables specifying the units for an element which is defined, in the Manual on Codes, by a single symbolic letter shall be compatible with the relevant existing WMO code tables;

- Code tables combining two or more existing WMO code tables to specify the units for an element which is defined, in the Manual on Codes, by a group of symbolic letters shall be compatible with the combined Code

- figures of the relevant group of symbolic letters;

- Code tables combining two or more existing WMO code tables to specify the units for an element which is defined, in the Manual on Codes, by different symbolic letters shall be compatible with the Code

- figures of the relevant symbolic letters, with successive tens or hundreds values added, as appropriate;

- Code tables and flag tables should only be used for reporting qualitative information. Quantitative information should be reported as observed using entries in Table 13. "Data description operators" from Table C should be applied when a "scale change" or "data width change" is required;

- Reference to existing specification(s) and code table(s) in the Manual on Codes, with explanation of possible deviations, shall be given in an additional table annexed to the code tables associated with BUFR Table B.

Additional Note: Letters and symbols enclosed by [ ] indicate codes used in the originating GF3 code scheme.

Last update: August 19, 2008

0 01 005: Profile Type

| Code figure | Meaning |
| --- | --- |
| 0 | Temperature |
| 1 | Salinity |
| 2 | East component of current |
| 3 | North component of current |
| 4 | Sound velocity |
| 5 | Transmissivity |
| 6 | pH |
| 7 | CFC-11 |
| 8 | CFC-12 |
| 9-19 | Reserved |
| 20 | Carbonate alkalinity |
| 21 | Chlorinity |
| 22 | Chlorosity |
| 23 | Alkalinity |
| 24-29 | Reserved |
| 30 | Ammonia |
| 31 | Organic Carbon |
| 32 | Chlorophyll-A |
| 33 | Dissolved oxygen |
| 34 | Nitrate |
| 35 | Nitrite |
| 36 | Phosphate |
| 37 | Inorganic phosphate |
| 38 | Silicate |
| 39-49 | Reserved |
| 50 | Fluoride |
| 51 | Fluorescence |
| 52 | Sulphate |
| 53 | Vitamin B12 |
| 54-127 | Reserved |

0 01 006: Type of Data Buoy BUFR Table 02 149 **** additions proposed September 2008

0 01 007: Data originator

| Code figure | Meaning |
| --- | --- |
| 0 | Bedford Institute of Oceanography (Canada) |
| 1 | Institute of Ocean Sciences (Canada) |
| 2 | Institut Maurice Lamontagne (Canada) |
| 3 | Wood's Hole Oceanographic Institute (USA) |
| 4 | Scripps Insititution of Oceanography (USA) |
| 5 | Missing |
| 6-1023 | Reserved |

0 01 009: JCOMM GTS message identifier ****  addition proposed September 2008

| Code figure | Meaning |
| --- | --- |
| 0 | AAXX SYNOP message |
| 1 | BBXX SHIP message |
| 2 | JJXX message |
| 3 | KKXX TESAC message |
| 4 | ZZXX DRIFTER message |
| 5 | JJYY BATHY message |
| 6 | ZZYY BUOY message |
| 7 | NNXX TRACKOB message |
| 8 | JJVV BATHY message |
| 9 | KKYY TESAC message |
| 10 | UUAA TEMP SHIP |
| 11-14 | Reserved |
| 15 | Missing |

0 02 001: Dissolved oxygen instrument

| Code figure | Meaning |
| --- | --- |
| 0 | In-situ oxygen probe [PR] |
| 1 | Titration [TI] |
| 2-5 | Reserved |
| 6 | Unspecified [XX] |
| 7 | Missing |

0 02 002 Cast type

| Code figure | Meaning |
| --- | --- |
| 0 | Classical hydrographic station [WBR] |
| 1 | Rosette sampler with CTD [ROS] |
| 2 | CTD/STD cast |
| 3 | Mechanical BT [MBT] |
| 4 | Expendable BT [XBT] |
| 5 | Unspecified BT [UBT] |
| 6 | BATHY message [BTH] |
| 7 | TESAC message [TSC] |
| 8 | DRIFTER message [DRB] |
| 9 | Other [OTH] |
| 10 | Bucket measurement |
| 11 | Ship intake measurement |
| 12 | Infra-red scanner |
| 13 | Microwave scanner |
| 14 | Hull mounted sensor |
| 15 | Reversing thermometer |
| 16 | Thermosalinograph |
| 17-29 | Reserved |
| 30 | Unspecified [XXX] |
| 31 | Missing |

0 02 003: Current instrument

| Code figure | Meaning |
| --- | --- |
| 0 | Mechanical measure type of sensor [M] |
| 1 | Acoustic measure type of sensor [A] |
| 2 | Electronic measure type of sensor [E] |
| 3 | Eulerian measure, method unspecified [EL] |
| 4 | Lagrangian measure, method unspecified [LG] |
| 5 | Buoy drift |
| 6 | GEK [geomagnetic electrokinetograph] |
| 7 | Ship set and drift |
| 8-13 | Reserved |
| 14 | Unspecified type of sensor [X] |
| 15 | Missing |

0 02 004: Wave instrument

| Code figure | Meaning |
| --- | --- |
| 0 | Accelerometer (gimbled) |
| 1 | Accelerometer (strapped down) |
| 2 | Shipbourne wave records [B] |
| 3 | Inverted Echo Sounder [E] |
| 4 | Laser altimeter [L] |
| 5 | Bottom mounted pressure device [P] |
| 6 | Satellite altimeter [R] |
| 7 | Staff gauge [S] |
| 8 | Visual [V] |
| 9 | Synthetic aperture radar |
| 10-28 | Reserved |
| 29 | Unspecified instrumented sensor [X] |
| 30 | Unspecified sensor [U] |
| 31 | Missing |

0 02 005: Salinity instrument

| Code figure | Meaning |
| --- | --- |
| 0 | Bench salinometer [BS] |
| 1 | In-situ conductivity probe [PR] |
| 2 | Titration [TI] |
| 3 | In-situ salinity sensor [SL] |
| 4-13 | Reserved |
| 14 | Unspecified [XX] |
| 15 | Missing |

0 02 006: Water temperature instrument

| Code figure | Meaning |
| --- | --- |
| 0 | Reversing thermometer |
| 1 | Thermistor |
| 2 | Mechanical BT (MBT) |
| 3 | Infra-red scanner |
| 4 | Microwave scanner |
| 5 | Missing |
| 6-15 | Reserved |

0 02 007: Location system

BUFR Table 0 02 148 Data Collection or Location System **** – additions requested September 2008

0 02 008 Drogue type BUFR Table 02 034

0-08-001: Time significance

| Code figure | Meaning |
| --- | --- |
| 0 | GTS bulletin |
| 1 | Receipt time |
| 2 | Update time |
| 3 | Elapsed time |
| 4 | Duration |
| 5 | Interval |
| 6 | Processing time |
| 7-15 | Reserved |

0-08-002: Coordinate

| Code figure | Meaning |
| --- | --- |
| 0 | This is not a coordinate |
| 1 | This is a coordinate |
| 2-3 | Reserved |

0-08-003: Vertical significance (surface observations) (BUFR table 08-002)

0-10-001: Selection of depth levels

| Code figure | Meaning |
| --- | --- |
| 0 | Data selected at constant depth intervals from continuous profile [DI] |
| 1 | Data selected at inflexion points from continuous profile [IF] |
| 2 | Data selected at predefined fixed levels [FX] |
| 3 | Data selected from continuous profile using combination of above criteria [CB] |
| 4 | Observed levels only [OB] |
| 5 | Data interpolated to standard depth levels [ST] |
| 6 | Observed levels plus depth interpolations to standard levels MX] |
| 7-13 | Reserved |
| 14 | Unspecified [XX] |
| 15 | Missing |

0-10-003: Chemical component

| Code figure | Meaning |
| --- | --- |
| 0 | Dissolved component only [DX] |
| 1 | Particulate component only [PX] |
| 2 | Dissolved + particulate components [TX] |
| 3 | Total |
| 4-13 | Reserved |
| 14 | Component unspecified or unknown [XX] |
| 15 | Missing |

0-10-004: Chemical content qualifier

| Code figure | Meaning |
| --- | --- |
| 0 | Concentration is less than recorded value [L] |
| 1 | Concentration is greater than recorded value [G] |
| 2 | Trace concentration [T] |
| 3-14 | Reserved |
| 15 | Missing |

0-10-005: Salinity units

| Code figure | Meaning |
| --- | --- |
| 0 | Practical Salinity [P] |
| 1 | Salinity (pre 1978 definition) in parts/thousand |
| 2 | Unknown |
| 3-6 | Reserved |
| 7 | Missing |

0-10-010: Direction reference

| Code figure | Meaning |
| --- | --- |
| 0 | Direction relative to true north |
| 1 | Direction relative to magnetic north |
| 2 | Direction relative to true east |
| 3 | Direction relative to magnetic east |
| 4-6 | Reserved |
| 7 | Missing |

0-10-011: First order statistics

| Code figure | Meaning |
| --- | --- |
| 0-1 | Reserved |
| 2 | Maximum value |
| 3 | Minimum value |
| 4 | Mean value |
| 5 | Median value |
| 6 | Modal value |
| 7 | Mean absolute error |
| 8-9 | Reserved |
| 10 | Standard deviation |
| 11 | Harmonic mean |
| 12 | Variance |
| 13-31 | Reserved |
| 32-62 | Reserved for local use |
| 63 | Missing |

0-10-012: Specific time of observation

| Code figure | Meaning |
| --- | --- |
| 0 | Time of observation (UTC) |
| 1 | Time of observation start (UTC) |
| 2 | Time of observation end (UTC) |
| 3-6 | Reserved |
| 7 | Missing |

0-10-020: GTSPP quality control flags  BUFR Table   33 050 Global GTSPP quality flag

0-10-021:GTSPP quality control code

| Code figure | Meaning |
| --- | --- |
| 0 | No quality control has been performed |
| 1 | Quality control performed, value appears correct. |
| 2 | Quality control performed, value appears inconsistent |
| 3 | Quality control performed, value appears suspect |
| 4 | Quality control performed, value appears wrong. |
| 5 | Quality control performed, value has been changed |
| 6-8 | Reserved |
| 9 | Value of the parameter is missing |
| 10-15 | Reserved |

0-10-022: Quality control tests performed

0-10-023: Quality control tests failed

| Bit number | Meaning |
| --- | --- |
| 1 | Platform Identification |
| 2 | Impossible Date/Time |
| 3 | Impossible Location |
| 4 | Position on Land |
| 5 | Impossible Speed |
| 6 | Impossible Sounding |
| 7 | Global Impossible Parameter Values |
| 8 | Regional Impossible Parameter Values |
| 9 | Increasing Depth |
| 10 | Profile Envelop |
| 11 | Constant Profile |
| 12 | Freezing Point |
| 13 | Spike |
| 14 | Top and Bottom Spike |
| 15 | Gradient |
| 16 | Density Inversion |
| 17 | Bottom |
| 18 | Temperature Inversion |
| 19 | Levitus Seasonal Statistics |
| 20 | Emery and Dewar Climatology |
| 21 | Asheville Climatology |
| 22 | Levitus Monthly Climatology |
| 23 | Waterfall |
| 24 | Visual Inspection of Cruise Track |
| 25 | Visual Inspection of Profiles |
| 26-63 | Reserved (set to 0) |

0-10-024: Quality of location (WMO table 3311)

| Code figure | Meaning |
| --- | --- |
| 0 | The value transmitted at the beginning of the report is a reliable value (location made over two satellite passes) |
| 1 | The values at the beginning of the report are the latest known values (no location over the corresponding pass) |
| 2 | Dubious quality. The location was made over one pass only; second solution is possible in 5% of the cases |
| 3-6 | Reserved |
| 7 | Missing |

0-10-025: Quality of the buoy satellite transmission (WMO table 3311)

| Code figure | Meaning |
| --- | --- |
| 0 | Good quality (several identical reports have been received) |
| 1 | Dubious quality (no identical reports) |
| 2 | Reserved |
| 3 | Missing |

0-10-030: Precision/accuracy indicator

| Code figure | Meaning |
| --- | --- |
| 0-3 | Reserved |
| 4 | Thousands of units |
| 5 | Hundreds of units |
| 6 | Tens of units |
| 7 | Units |
| 8 | Tenths of units |
| 9 | Hundredths of units |
| 10 | Thousandths of units |
| 11-12 | Reserved |
| 13 | Trace |
| 14 | Undetected |
| 15 | Missing |

0-10-031: Confidence interval

| Code figure | Meaning |
| --- | --- |
| 0 | 95% |
| 1 | 66% |
| 2-6 | Reserved |
| 7 | Unknown |

0-10-032: Data availability

| Code figure | Meaning |
| --- | --- |
| 0 | Originator only |
| 1 | Holding agency and originator only |
| 2 | Project participants |
| 3 | Public |
| 4-6 | Reserved |
| 7 | Missing |

0-10-033: Platform identifier type

| Code figure | Meaning |
| --- | --- |
| 0 | ITU call sign |
| 1 | WMO platform identifier |
| 2 | WMO station identifier (IIiii) |
| 3 | CLS ARGOS identifier |
| 4-14 | Reserved |
| 15 | Unknown |

0-10-036: Trace direction

| Code figure | Meaning |
| --- | --- |
| 0 | Data collected serially during descent of probe [D] |
| 1 | Data collected serially during ascent of probe [A] |
| 2-5 | Reserved |
| 6 | Not applicable or unspecified [X] |
| 7 | Missing |

0-10-037: Probe hit bottom indicator

| Code figure | Meaning |
| --- | --- |
| 0 | Probe hit sea floor [1] |
| 1 | Unspecified/missing [0] |

0-10-038: Duplicates indicator

| Code figure | Meaning |
| --- | --- |
| 0 | Not a duplicate |
| 1 | Duplicates another record |

0-10-039: Wind speed units indicator (WMO code 1853)

| Code figure | Meaning |
| --- | --- |
| 0 | In m/s from land stations and ships with certified instruments |
| 1 | In knots m/s from land stations and ships with certified instruments |
| 2 | In m/s from ships with uncertified instruments |
| 3 | In knots from ships with uncertified instruments |
| 4-7 | Reserved |
| 7 | Missing |

0-10-040: Indicator for method of current measurement (WMO code 2266)

| Code figure | Meaning |
| --- | --- |
| 0 | GEK (Geomagnetic ElectroKinetograph) |
| 1 | Ship's set and drift determined by fixes 3-6 hours apart |
| 2 | Ship's set and drift determined by fixes more than 6 hours but than 12 hours apart |
| 3-6 | Reserved |
| 7 | Missing |

0-11-002: Total cloud amount (BUFR table 20-011)

0-11-004: Cloud type  (BUFR table 20-012)

0-11-007: Present weather code (BUFR table 20-003)

0-11-008: Past weather(1) (BUFR table 20-004)

0-11-009: Past weather(2) (BUFR table 20-005)

0-20-025: Water colour (forel-ule scale)

| Code figure | Meaning |
| --- | --- |
| 0 | Deep Blue |
| 1 | Blue |
| 2 | Greenish Blue |
| 3 | Green |
| 4 | Light Green |
| 5 | Yellowish Green |
| 6 | Yellow Green |
| 7 | Green Yellow |
| 8 | Greenish Yellow |
| 9 | Yellow |
| 10-14 | Reserved |
| 15 | Missing |

0-20-026: Ice in vicinity of oceanographic observations

| Code figure | Meaning |
| --- | --- |
| 0 | No ice |
| 1 | Ice present in vicinity but not identified as to type or amount |
| 2 | Few bergs (10 or less) |
| 3 | Many bergs (more than 10) |
| 4 | Pack ice more than 1 nautical mile from station: coverage 6/10 or less |
| 5 | Pack ice more than 1 nautical mile from station: coverage more than 6/10 |
| 6 | Pack ice less than 1 nautical mile from station: coverage 6/10 or less |
| 7 | Pack ice less than 1 nautical mile from station: coverage more than 6/10 |
| 8 | Station within heavy concentration of ice e.g. observations from islands, drifting pack, beset vessels, fast ice |
| 9 | No observations of ice made |
| 10-14 | Reserved |
| 15 | Missing |

0-22-009: Bathymetric Datum indicator

| Code figure | Meaning |
| --- | --- |
| 0 | Lowest normal low water [01] |
| 1 | Mean lower low water [02] |
| 2 | Lowest low water [03] |
| 3 | Mean lower low water spring [04] |
| 4 | Indian spring low water [05] |
| 5 | Mean low water spring [06] |
| 6 | Mean sea level [07] |
| 7 | Mean low water [08] |
| 8 | Equatorial spring low water [09] |
| 9 | Tropic lower low water [10] |
| 10 | Lowest astronomical tide [11] |
| 11-28 | Reserved |
| 29 | Other [88] |
| 30 | No correction applied [sea level] [00] |
| 31 | Missing |

0-23-001: Sea state (WMO code 3700)

| Code figure | Meaning |
| --- | --- |
| 0 | Calm (glassy): 0 height (m) |
| 1 | Calm (rippled): 0-0.1 height (m) |
| 2 | Smooth (wavelets): 0.1-0.5 height (m) |
| 3 | Slight: 0.5-1.25 height (m) |
| 4 | Moderate: 1.25-2.5 height (m) |
| 5 | Rough: 2.5-4 height (m) |
| 6 | Very rough: 4-6 height (m) |
| 7 | High: 6-9 height (m) |
| 8 | Very high: 9-14 height (m) |
| 9 | Phenomenal: Over 14 height (m) |
| 10-14 | Reserved |
| 15 | Missing |

0-25-001: Free air gravity anomaly reference system

| Code figure | Meaning |
| --- | --- |
| 0 | IGSN 1971 reference system [-A] |
| 1 | Potsdam reference system [-P] |
| 2 | Local reference system [-L] |
| 3-12 | Reserved |
| 13 | Other reference system [-Z] |
| 14 | Unknown |
| 15 | Missing |

0-25-002: Reference residual magnetic field

| Code figure | Meaning |
| --- | --- |
| 0 | IGFR 1965 [AA] |
| 1 | IGFR 1975 [AB] |
| 2 | IGFR 1980 [AC] |
| 3 | DGFR 1965 [DA] |
| 4 | DGFR 1970 [DB] |
| 5 | DGFR 1975 [DC] |
| 6 | PGFR 1975 [PA] |
| 7-13 | Reserved |
| 14 | Other reference field [XX] |
| 15 | Missing |

0-25-003: Bathymetry sound velocity correction area

| Code figure | Meaning |
| --- | --- |
|  | See "Echo Sounding Correction Tables", 3rd. edition N.P.139 (UK) |

0-25-004: Prime navigation aid fix

| Code figure | Meaning |
| --- | --- |
| 0 | Position is not primary navaid |
| 1 | Position is primary navaid [F] |
| 2-6 | Reserved |
| 7 | Missing |

0-25-005: Free air gravity anomaly formula

| Code figure | Meaning |
| --- | --- |
| 0 | Heiskanen 1924 formula [A-] |
| 1 | International 1930 formula [B-] |
| 2 | IAG system 1967 formula [C-] |
| 3-5 | Reserved |
| 6 | Other formula [Z-] |
| 7 | Missing |

0-25-012: Duration application

| Code figure | Meaning |
| --- | --- |
| 0 | Duration of processed observation [PR] |
| 1 | Duration of individual sample [SS] |
| 2-6 | Reserved |
| 7 | Missing |

0-25-013: Frequency sampling technique

| Code figure | Meaning |
| --- | --- |
| 0 | Frequency of processed observations [PR] |
| 1 | Original sampling/digitization interval [SS] |
| 2-6 | Reserved |
| 7 | Missing |

0-25-014: Interval sampling code

| Code figure | Meaning |
| --- | --- |
| 0 | Interval of processed observations – usually the same as the sampling of the data |
| 1 | Original sampling/digitization interval – used mainly in cases where the processed observation may be derived/extracted from higher resolution data. [SS] |
| 2-6 | Reserved |
| 7 | Missing |

0-25-015: Digitization method

| Code figure | Meaning |
| --- | --- |
| 0 | Hand digitized |
| 1 | Analog reading by one operator |
| 2 | Analog reading by 2 or more operators |
| 3 | Digital data logger, unreduced values |
| 4 | Digital data logger, resolution reduced to less than instrument limits |
| 5 | Digital data logger, resolution reduced to instrument limits |
| 6 | Digitized from analog record |
| 7-13 | Reserved |
| 14 | Unknown |
| 15 | Missing |

0-25-016: Filter type

| Code figure | Meaning |
| --- | --- |
| 0 | Digital filter has been used [F] |
| 1 | Analogue filter has been used [A] |
| 2 | Unspecified [X] |
| 3-6 | Reserved |
| 7 | Missing |

0-25-020: Correction procedure for depth from sound speed

| Code figure | Meaning |
| --- | --- |
| 0 | Corrected depth [C-] |
| 1 | Uncorrected depth [U-] |
| 2 | Corrected depth including refraction effects [R-] |
| 3 | Uncorrected depth, assumed sound velocity = 1500m/s [UA] |
| 4 | Uncorrected depth, assumed sound velocity = 800 fathoms/s [UF] |
| 5 | Uncorrected depth, assumed sound velocity other than above [UZ] |
| 6-14 | Reserved |
| 15 | Missing |

0-25-021: Method of depth correction for sound speed

| Code figure | Meaning |
| --- | --- |
| 0 | Used echo sounding correction tables [-T] |
| 1 | Used Mathews tables [-M] |
| 2 | Used velocimeter dips [-V] |
| 3 | Used W.D. Wilson formula on T-S data [-W] |
| 4 | Used Kuwahara formula on T-S data [-K] |
| 5 | Used Del Grosso formula on T-S data [-G] |
| 6-13 | Reserved |
| 14 | Used another technique [-Z] |
| 15 | Missing |

0-25-022: Method of sound velocity measurement

| Code figure | Meaning |
| --- | --- |
| 0 | In-situ sound velocity probe [PR] |
| 1 | Computed from other parameters [CV] |
| 2-5 | Reserved |
| 6 | Unspecified [XX] |
| 7 | Missing |

0-25-023: Density calculation

| Code figure | Meaning |
| --- | --- |
| 0 | International equation [1980] [EQ] |
| 1 | In-situ density probe [PR] |
| 2-13 | Reserved |
| 14 | Unspecified [XX] |
| 15 | Missing |

0-25-028: Method of current averaging

| Code figure | Meaning |
| --- | --- |
| 0 | Scalar averaged method of averaging [S] |
| 1 | Vector averaged method of averaging [C] |
| 2 | Discrete value method of averaging [D] |
| 3-13 | Reserved |
| 14 | Unspecified method of averaging [X] |
| 15 | Missing |

0-25-029: Duration and time of eulerian current measurement (WMO code 2264)

| Code figure | Meaning |
| --- | --- |
| 1 | Instantaneous (between H-1 and H) |
| 2 | Averaged over 3 minutes or less (between H-1 and H) |
| 3 | Averaged over more than 3 minutes, but 6 at the most (between H-1 and H) |
| 4 | Averaged over more than 6 minutes, but 12 at the most (between H-1 and H) |
| 5 | Instantaneous |
| 6 | Averaged over 3 minutes or less (between H-2 and H-1) |
| 7 | Averaged over more than 3 minutes, but 6 at the most (between H-2 and H-1) |
| 8 | Averaged over more than 6 minutes, but 12 at the most (between H-2 and H-1) |
| 9 | Vector or Doppler current profiling method not used |
| 10-14 | Reserved |
| 15 | Missing |

Note: H = time of observation

0-25-030: Period of current measurement (WMO code 2265)

| Code figure | Meaning |
| --- | --- |
| 1 | 1 hour or less |
| 2 | More than 1 hour but 2 at the most |
| 3 | More than 2 hours but 4 at the most |
| 4 | More than 4 hours but 8 at the most |
| 5 | More than 8 hours but 12 at the most |
| 6 | More than 12 hours but 18 at the most |
| 7 | More than 18 hours but 23 at the most |
| 8 | Reserved |
| 9 | Drift method not used |
| 10-14 | Reserved |
| 15 | Missing |

0-25-035: Method of temperature measurement

| Code figure | Meaning |
| --- | --- |
| 0 | Bucket |
| 1 | Ship intake [BK] |
| 2 | In-situ probe [PR] |
| 3 | Infra-red scanner [RS] |
| 4 | Microwave scanner [MW] |
| 5 | Hull mounted sensor |
| 6-9 | Reserved |
| 10 | Reversing Thermometer [RT] |
| 11 | STD/CTD sensor [ST] |
| 12 | Mechanical BT [MT] |
| 13 | Expendible BT [ET] |
| 14 | Unspecified BT [BT] |
| 15 | Thermosalinograph |
| 16-29 | Reserved |
| 30 | Unspecified [XX] |
| 31 | Missing |

0-25-036: Method of salinity/depth measurement

| Code figure | Meaning |
| --- | --- |
| 0 | No salinity measured |
| 1 | In situ sensor, accuracy better than 0.02 psu |
| 2 | In situ sensor, accuracy less than 0.02 psu |
| 3 | Sample analysis |
| 4-6 | Reserved |
| 7 | Missing |

0-25-037: Method of depth measurement

| Code figure | Meaning |
| --- | --- |
| 0 | Pressure measurement [PR] |
| 1 | Reversing thermometer [RT] |
| 2 | Echo sounding [ES] |
| 3 | Wire length [WL] |
| 4 | Fixed [eg. attached to tower or ship hull] [FX] |
| 5 | Standard depth for interpolated data [ID] |
| 6 | Determined by fall rate [BT] |
| 7-13 | Reserved |
| 14 | Unspecified [XX] |
| 15 | Missing |

0-25-038: Pressure measurement method

| Code figure | Meaning |
| --- | --- |
| 0 | Reversing thermometer [RT] |
| 1 | In-situ pressure probe [PR] |
| 2-5 | Reserved |
| 6 | Unspecified [XX] |
| 7 | Missing |

0-25-045: Method code for position fixing

| Code figure | Meaning |
| --- | --- |
| 0 | Celestial [star fix, sun line] [CL] |
| 1 | Satellite navigation [NS] |
| 2 | Omega [OM] |
| 3 | Loran A [LA] |
| 4 | Loran C [RC] |
| 5 | Decca [EE] |
| 6 | Mid range navigational net (200-500 km) [MD] |
| 7 | Short range navigational net (<200 km) [SH] |
| 8 | Acoustic (SOFAR, SONAR, etc.) [AU] |
| 9 | RADAR [BB] |
| 10 | Dead reckoning [DR] |
| 11 | GPS |
| 12 | Digital GPS |
| 13-29 | Reserved |
| 30 | Unspecified [XX] |
| 31 | Missing |

0-25-046: Method of wave calculation

| Code figure | Meaning |
| --- | --- |
| 0 | Fourier transform calculation [F] |
| 1 | Lag correlation calculation [L] |
| 2 | Simple computer analysis calculation [C] |
| 4 | Manual analysis of chart [M] |
| 5 | Visual estimation |
| 5-13 | Reserved |
| 14 | Unspecified method of calculation |
| 15 | Missing |

0-29-001: Processing centre

| Code figure | Meaning |
| --- | --- |
| 0 | Australian Oceanographic Data Centre |
| 1 | Atlantic Oceanographic & Meteorological Laboratory (U.S.) |
| 2 | Commonwealth Scientific & Industrial Research Organization (Australia) |
| 3 | Fleet Numerical Oceanography Center (U.S.) |
| 4 | Bundesamt fur Seeschiffahrt und Hydrographie (Germany) |
| 5 | Japan Meteorological Agency |
| 6 | Integrated Science Data Management (formerly Marine Environmental Data Service) (Canada) |
| 7 | National Oceanographic Data Center (U.S.) |
| 8 | National Weather Service (U.S.) |
| 9 | Scripps Institution of Oceanography (U.S.) |
| 10 | TOGA Subsurface Data Centre (France) |
| 11-31 | Reserved |

0-29-002: Processing function identifier

| Code figure | Meaning |
| --- | --- |
| 0 | MEDS software that reads IGOSS data in BUFR and convert to the ocean processing format |
| 1 | NODC converter of NODC UBT format to MEDS format |
| 2 | NODC converter of NODC IBT format to MEDS format |
| 3 | NODC converter of Navy Declassified IBT format to MEDS format |
| 4 | NODC duplicates software |
| 5 | NODC GTSPP Quality Control Cruise Track Software |
| 6 | NODC GTSPP software to remove duplicate stations found in an input file or in the database |
| 7 | NODC converter of SEAS III XBT format to GTSPP format |
| 8 | NODC converter of TSDC1 XBT format to GTSPP format |
| 9 | NODC converter of SEAS II XBT format to GTSPP format |
| 10 | NODC converter of CEADO XBT format to GTSPP format |
| 11 | NODC converter of TSDC2 XBT format to GTSPP format |
| 12 | NODC converter of CSIRO TOGA XBT format to GTSPP format |
| 13 | NODC converter of NODC UBT format to GTSPP format |
| 14 | NODC converter of TAMU XBT (1-labelled fields) format to GTSPP format |
| 15 | NODC converter of TAMU XBT (2-columnar fields) format to GTSPP format |
| 16 | NODC converter of JODC XBT format to GTSPP format |
| 17 | NODC converter of AODC XBT format to GTSPP format |
| 18 | NODC converter of AODC XBT (2-RV Franklin) format to GTSPP format |
| 19 | NODC converter of NODC CTD/STD (F022) format to GTSPP format |
| 20 | NODC converter of TAMU CTD (1-labelled fields) format to GTSPP format |
| 21 | NODC converter of NODC Station (SD1) format to GTSPP format |
| 22 | NODC converter of CSIRO meds format to GTSPP format |
| 23 | MEDS software to convert real-time IGOSS data to ocean processing structure |
| 24 | MEDS duplicates checking software. |
| 25 | MEDS duplicates review software |
| 26 | MEDS quality control software which checks ocean profiles |
| 27 | NODC program re-set QC temp flags from "2" to "1" if failed Levitus Climatology |
| 28 | MEDS convert Japanese JHD data to MEDS format |
| 29 | Update the MEDS archive |
| 30 | NODC converter of Bundesamtes fur Seeschiffahrt und Hydrographie (BSH) to GTSPP format |
| 31 | NODC Duplicates software |
| 32 | Convert NODC OPDB format to GTSPP format |
| 33 | NODC Delayed mode version of QCA1 |
| 34 | MEDS quality control software which checks that the space and time location as well as the identification of a station is sensible |
| 35 | NODC GTSPP QC Profiles software |
| 36 | AOML XBT QC Software |
| 37 | SCRIPPS |
| 38 | NODC |
| 39 | AOML XBT Edit software |
| 40-127 | Reserved |

0-29-004: Processing action taken

| Code figure | Meaning |
| --- | --- |
| 0 | Change a quality flag |
| 1 | Create record |
| 2 | Constant temperature, hit bottom. The temperature profile exhibits constant temperature which is considered to be erroneous when compared to neighbouring profiles and/or climatology and/or known characteristics of the region. The constant temperatures could occur over all of the profile or part of it. (The reasons could be sensor failure, depth calculation error, nose falling off the XBT, XBT sitting on the bottom, etc.) |
| 3 | Change value |
| 4 | Station was checked by duplicate checking software |
| 5 | Edit a parameter value |
| 6 | Fine structure error: leakage, PET fault, cusping, sticking bit. The temperature profile exhibits erroneous fine structure when compared to neighbouring profiles and/or climatology and/or known characteristics of the region. (The reasons could be signal leakage, XBT recording system failures (sticking bit, cusping, PET Fault, etc), complete instrument failure, etc.) |
| 7 | This history group operates on the complete input record |
| 8 | Mixed layer error: bowing. The temperature profile exhibits erroneous features (such as false inversions) in the mixed layer when compared to neighbouring profiles and/or climatology and/or known characteristics of the region. (The reasons could be XBT bowing problem, instrument drift, etc.) |
| 9 | No good trace |
| 10 | Position error. Profile position has been erroneously encoded. Corrected if possible |
| 11 | Quality Control |
| 12 | Surface feature error: surface anomaly, chopped surface value. The temperature exhibits erroneous features at the surface when compared to neighbouring profiles and known characteristics of the region. (The reasons could be XBT start-up transients, general instrument equilibration problems, sensors recording prematurely before entering water, etc.) |
| 13 | Set a value |
| 14 | Time error. Profile date/time has been erroneously encoded. Corrected if possible |
| 15 | Temperature gradient error: insulation penetration, spikes, high frequency noise, wire break, modulo 10 spikes. The temperature profile exhibits erroneous temperature gradients when compared to neighbouring profiles and/or climatology and/or known characteristics of the region. (The reasons could be spiking, interference, XBT wire break, modulo 10 problem, XBT wire insulation penetration, etc.) |
| 16 | Temperature inversion error: wire stretch. The temperature profile exhibits erroneous temperature inversions when compared to neighbouring profiles and/or climatology and/or known characteristics of the region. (The reasons could be XBT wire stretch, sensor drift, encoding error, etc.) |
| 17 | Temperature/depth offset. The temperature profile exhibits erroneous temperature/depth offsets compared to neighbouring profiles and/or climatology and/or known characteristics of the region. The offsets can occur.at depth, or over sections of the profile, or over the complete profile (The reason could be instrument drift/sensor failure, encoding error, XBT fall rate error, XBT start-of-descent timing error, etc.) |
| 18 | Station passed through the update program |
| 19 | Under resolved. Temperature data is encoded at standard depths/levels and can't be used to reconstitute a profile accurately |
| 20-63 | Reserved |

0-29-005: Parameter acted upon

| Code figure | Meaning |
| --- | --- |
| 0 | Temperature |
| 1 | Salinity |
| 2 | East component of current |
| 3 | North component of current |
| 4 | Sound velocity |
| 5 | Transmissivity |
| 6 | pH |
| 7 | CFC-11 |
| 8 | CFC-12 |
| 9-19 | Reserved |
| 20 | Carbonate alkalinity |
| 21 | Chlorinity |
| 22 | Chlorosity |
| 23 | Alkalinity |
| 24-29 | Reserved |
| 30 | Ammonia |
| 31 | Organic Carbon |
| 32 | Chlorophyll-A |
| 33 | Dissolved oxygen |
| 34 | Nitrate |
| 35 | Nitrite |
| 36 | Phosphate |
| 37 | Inorganic phosphate |
| 38 | Silicate |
| 39-49 | Reserved |
| 50 | Fluoride |
| 51 | Fluorescence |
| 52 | Sulphate |
| 53 | Vitamin B12 |
| 54-255 | Reserved |

0-31-021: Associated Field Significance

| Code figure | Meaning |
| --- | --- |
| 0 | Reserved |
| 1 | 1-bit indicator of quality 0 = good, 1 = suspect or bad |
| 2 | 2-bit indicator of quality 0 = good, 1 = slightly suspect, 2 = highly suspect, 3 = bad |
| 3-6 |  |
| 7 | Percentage confidence |
| 8-20 | Reserved |
| 21 | 1-bit indicator of correction 0 = original value, 1 = substituted/corrected value |
| 22-62 | Reserved for local use |
| 63 | Missing value |

0-31-031: Data Present Indicator

| Code figure | Meaning |
| --- | --- |
| 0 | Data present |
| 1 | Data not present |