| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 1-5 SEPTEMBER 2008 |  | CT-MTDCF/ET-DR&C/Doc. 3.5(3) ITEM: 3.3 (16.7.2008) ENGLISH ONLY |
| --- | --- | --- |

Proposal for new descriptors

for representation of UV radiation data

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for new descriptors for representation

of detailed information on UV radiation.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and recommend the proposed descriptors for validation.

Reference:

[1]  Manual on Codes, WMO-No. 306, Volume I.2.

[2]  http://www.wmo.ch/pages/prog/www/WMOCodes/OperationalCodes.html

[3]  Guide to Meteorological Instruments and Methods of Observation, WMO-No 8, Chapter 7.

[4]  Solar Energy, 21, 65-68 (1978)

1. Background

In March 2008, Mr. Michel Leroy indicated the intention of Météo-France to transmit UV-B radiation data in BUFR messages and requested advice on their data representation as the existing descriptors for short-wave radiation are too general for this purpose.

UV radiation data are expected to be exchanged through GTS/WIS. According to Dr Karel Vaníček of the Czech Hydrometeorological Institute, the following information will be required in GAW/IGACO  projects:

- Global UV spectral irradiance  (UV flux density for individual wavelengths of the spectral band specified). Range: 0.000000 - 1.000000 W m-2 nm-1;

- Global UV irradiation (UV energy integrated over period specified for different spectral bands).

Range:  0 - ~2 MJ m-2, daily integral for the spectral band 290-400nm;

- Global erythemal irradiation (UV energy weighted by the CIE Action Spectrum integrated over period specified).  Range:   0 -  ~10 kJ m-2, daily integral for the spectral band 290-400nm.

Note:

According to recommendation of CIMO [3] and ISES [4], the terms  “irradiance” and “irradiation” should be used for the UV density flux and the UV energy doses on the horizontal surface, respectively.

A draft version of this document was examined by the DWD experts Ms Sibylle Krebber, Mr. Klaus Behrens and  Dr Uwe Feister and they expressed agreement with the included proposal.

2. Proposal

It is proposed to introduced the following new descriptors for UV radiation and Notes under Class 14:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 071 | Global UV spectral irradiance | W. m-2 nm-1 | 6 | –1048576 | 21 | W m-2 nm-1 | 6 | 7 |
| 0 14 072 | Global UV irradiation | J m-2 | –3 | –8192 | 14 | J m-2 | –3 | 4 |
| 0 14 073 | Global erythemal irradiation | J m-2 | –3 | –32 | 6 | J m-2 | –3 | 2 |

The proposed descriptors allow representation of values of irradiance and irradiation:

| Range of values | kJ m-2 | J cm-2 | W. m-2 nm-1 |
| --- | --- | --- | --- |
|  |  | max upward | max downward | max upward | max downward | max upward | max downward |
| 0 14 071 | Global UV spectral irradiance |  |  |  |  | –1.048576 | 1.048574 |
| 0 14 072 | Global UV irradiation | –8192 | 8190 | –819.2 | –819.0 |  |  |
| 0 14 073 | Global erythemal irradiation | –32 | 30 | –3.2 | 3.0 |  |  |

Notes:

- Global UV spectral irradiance (0 14 071) is UV flux density for individual wavelengths specified.     0 14 071 shall be preceded by 0 02 071 (Spectrographic wavelength).

- Global UV irradiation (0 14 072)  is UV energy integrated over period specified for spectral band specified. 0 14 072 shall be preceded by a time period descriptor, 0 02 071 (Spectrographic wavelength) and 0 02 072 (Spectrographic width). E.g. If 0 14 072 is used for Global UV-B irradiation, 0 02 071 and 0 02 072  shall specify spectral band 280 to 315 nm.

- Global erythemal irradiation (0 14 073) is UV energy weighted by the CIE Action Spectrum integrated over period specified. 0 14 073 shall be preceded by a time period descriptor, 0 02 071 (Spectrographic wavelength) and 0 02 072 (Spectrographic width).