| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MONTREAL, 8-12 MAY 2006 |  | ET/DR&C/Doc. 3.1(1) _______ ENGLISH ONLY |
| --- | --- | --- |

# REVIEW OF ENTRIES AWAITING VALIDATION FOR BECOMING PRE-OPERATIONAL

(Submitted by the Secretariat)

### Summary and Purpose of Document

This document shows the list known by the Secretariat of entries, which still need to be validated.

________________________________________________________________

# ACTION PROPOSED

The Team is invited to review and check the list to consider any additional or remaining for validation entries or approval as pre-operational use with a view to their subsequent endorsement by CBS Ext.2006.

NEW ALLOCATED BUFR/CREX ENTRIES (AWAITING VALIDATION)

#### ADDITIONS FOR REPORTING BOTH NOMINAL AND INSTRUMENT VALUES IN BUFR TEMPLATES FOR SURFACE OBSERVATION DATA

A new descriptor in the Class 8 is proposed as a nominal value indicator (for Level II data):

0 08 083   Nominal value indicator, Flag table, 0, 0, 15

| Bit No. |  |
| --- | --- |
| 1 | Adjusted with respect to representative height of sensor above local ground (or deck of marine platform) |
| 2 | Adjusted with respect to representative height of sensor above water surface |
| 3 | Adjusted with respect to standard surface roughness |
| 4 | Adjusted with respect to wind speed |
| 5 | Adjusted with respect to temperature |
| 6 | Adjusted with respect to pressure |
| 7 | Adjusted with respect to humidity |
| 8 | Adjusted with respect to evaporation |
| 9 | Adjusted with respect to wetting losses |
| 10 -14 | Reserved |
| All 15 | Missing value |

Two new descriptors in Class 7 are proposed

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 07 065 | Representative height of sensor above local ground (or deck of marine platform) | m | 2 | 0 | 16 | m | 2 | 5 |

Note:	Representative height of sensor above local ground (or deck of marine platform) is the standard height of a sensor required by WMO documentation. Value of the following meteorological element should be adjusted using a formula (or a recommended procedure for obtaining nominal values). For example, standard height recommended in WMO documentation for surface wind sensors is 10 m. If the sensor is placed at different height, the wind speed should be adjusted using a formula.

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 07 066 | Representative height of sensor above water surface | m | 1 | 0 | 12 | m | 1 | 4 |

Note:	Representative height of sensor above water surface is the standard height of a sensor required by WMO documentation. Value of the following meteorological element should be adjusted using a formula (or a recommended procedure for obtaining nominal values).

ADDITIONS FOR REPORTING CORRECTLY INSTANTANEOUS RADIATION

| Table reference | Element name | Unit | Scale | Reference value | Data width |
| --- | --- | --- | --- | --- | --- |
| 0 14 061 | Instantaneous long-wave radiation | W m-2 | 0 | -512 | 10 |
| 0 14 062 | Instantaneous short-wave radiation | W m-2 | 0 | -2048 | 12 |

The Class 14 element descriptors 0 14 017 and 0 14 018 should be deprecated by a note.

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM SEA STATIONS SUITABLE FOR SHIP OBSERVATION DATA FROM VOS STATIONS

Sequence descriptor numbers written in blue in this template, have not yet been included in Manual on Codes, WMO-No. 306, I.2 (November 2005).

3 08 008  =  3 01 093  +  3 02 062   +  3 02 063

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 062 |  |  | SHIP “instantaneous” data from VOS |  |
|  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  | 0 08 002 |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 055 | 0 20 031 | Ice deposit (thickness) EsEs | m, 2 |
|  |  | 0 20 032 | Rate of ice accretion Rs | Code table, 0 |
|  |  | 0 20 033 | Cause of ice accretion Is | Flag table, 0 |
|  |  | 0 20 034 | Sea ice concentration ci | Code table, 0 |
|  |  | 0 20 035 | Amount and type of ice bi | Code table, 0 |
|  |  | 0 20 036 | Ice situation zi | Code table, 0 |
|  |  | 0 20 037 | Ice development Si | Code table, 0 |
|  |  | 0 20 038 | Bearing of ice edge Di | Degree true, 0 |

|  |  |  | Sea/water temperature |  |
| --- | --- | --- | --- | --- |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 063 |  |  | SHIP“period” data from VOS |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 064 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  |  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1) Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2) Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3) 0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4) 0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5) If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

ADDITIONS FOR COVERING REGIONAL PRACTICES

3. Proposal for new descriptors, code tables and additions to existing tables

3.1 Proposed new descriptors:

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 12 121 | Ground minimum temperature | K | 2 | 0 | 16 | oC | 2 | 4 |
| 0 12 122 | Ground minimum temperature of the preceding night | K | 2 | 0 | 16 | oC | 2 | 4 |
| 0 13 056 | Character and intensity of precipitation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 13 057 | Time of beginning or end of precipitation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 028 | Evolution of drift of snow | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 055 | State of sky in tropics | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 066 | Maximum diameter of hailstones | m | 3 | 0 | 8 | m | 3 | 3 |
| 0 20 067 | Diameter of deposit | m | 3 | 0 | 9 | m | 3 | 3 |
| 0 20 101 | Locust (acridian) name | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 102 | Locust (maturity) color | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 103 | Stage of development of locusts | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 104 | Organization state of swarm or band of locusts | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 105 | Size of swarm or band of locusts and duration of passage of swarm | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 106 | Locust population density | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 107 | Direction of movements of locust swarm | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 20 108 | Extent of vegetation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Moreover, it is proposed to rename descriptor 0 20 054 “True direction from which clouds are moving” to read “True direction from which a phenomenon or clouds are moving” to allow its usage for data representation of groups 919MWDa (type of water spout, tornado, whirlwind, dustdevils and direction from which they approach the station) and 918sqDp (type of squall and direction from which it approaches the station).

3.2 Proposed new Code tables:

|  |  | Manual on Codes, WMO-No.306, Vol. II |
| --- | --- | --- |
| 0 13 056 - | Character and intensity of precipitation | Code table 167 |
| 0 13 057 - | Time of beginning or end of precipitation | Code table 168 |
| 0 20 055 - | State of sky in tropics | Code table 430 |
| 0 20 101 - | Locust (acridian) name | Code table 162 |
| 0 20 102 - | Locust (maturity) color | Code table 159 |
| 0 20 103 - | Stage of development of locusts | Code table 160 |
| 0 20 104 - | Organization state of swarm or band of locusts | Code table 161 |
| 0 20 105 - | Size of swarm or band of locusts and duration of passage of swarm | Code table 173 |
| 0 20 106 - | Locust population density | Code table 139 |
| 0 20 107 - | Direction of movements of locust swarm | Code table 140 |
| 0 20 108 - | Extent of vegetation | Code table 182 |

The existing extent of the above listed Code tables from Manual on Codes, WMO-No. 306, Volume II, is to be supplemented by code figures 10-14 Reserved and by code figure15 Missing value.

Code Table 0 20 028 is proposed to express code figures for S’8  (Code table 3776, Manual on Codes, WMO-No. 306, Volume I.1).

|  | 0 20 028 Evolution of drift of snow |
| --- | --- |
| Code figure |  |
| 0 | Drift snow ended before the hour of observation |
| 1 | Intensity diminishing |
| 2 | No change |
| 3 | Intensity increasing |
| 4 | Continues, apart from interruption lasting less than 30 minutes |
| 5 | General drift snow has become drift snow near the ground |
| 6 | Drift snow near the ground has become general drift snow |
| 7 | Drift snow has started again after an interruption of more than 30 minutes |
| 8 -14 | Reserved |
| 15 | Missing value |

3.3 Proposed additions to the existing Flag tables:

| Bit No. | 0 20 023 Other weather phenomena |
| --- | --- |
| 12 | Water-spout |
| Bit No. | 0 20 027 Phenomenon occurrence |
| 6 | Below station level |
| Bit No. | 0 08 042 Extended vertical sounding significance |
| 15 | Level determined by regional decision |

4. Proposal for regional templates for SYNOP data

The global BUFR template for SYNOP data, shown in document ET DR&C/Doc. 5.4(1), may be expressed concisely as follows:

| 3 07 080 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data |
| --- | --- | --- |
| 3 01 090 |  | Fixed surface station identification, time, horizontal and vertical coordinates |
| 3 02 031 |  | Pressure data |
| 3 02 035 |  | Basic synoptic “instantaneous” data |
| 3 02 036 |  | Clouds with bases below station level |
| 3 02 047 |  | Direction of cloud drift |
| 0 08 002 |  | Vertical significance (= missing to cancel the previous value) |
| 3 02 048 |  | Direction and elevation of cloud |
| 3 02 037 |  | State of ground, snow depth, ground minimum temperature |
| 3 02 043 |  | Basic synoptic “period” data |
| 3 02 044 |  | Evaporation data |
| 1 01 002 |  | Replicate next descriptor 2 times |
| 3 02 045 |  | Radiation data (from 1 hour and/or 24 hour period) |
| 3 02 046 |  | Temperature change |

BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA I

It is proposed to represent this template by a descriptor 3 07 081.

3 07 081:

| 3 01 090 |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- |
| 3 02 031 |  | Pressure data |  |
| 3 02 035 |  | Basic synoptic “instantaneous” data |  |
| 3 02 036 |  | Clouds with bases below station level |  |
| 3 02 047 |  | Direction of cloud drift |  |
| 0 08 002 |  | Vertical significance (= missing to cancel the previous value) | Code table, 0 |
| 3 02 048 |  | Direction and elevation of cloud |  |
| 3 02 037 |  | State of ground, snow depth, ground minimum temperature (past 12 hours) |  |
| 0 12 122 |  | Ground minimum temperature of the preceding night snTgTg | K, 2 |
| 0 13 056 |  | Character and intensity of precipitation Rc | Code table, 0 |
| 0 13 057 |  | Time of beginning or end of precipitation Rt | Code table, 0 |
| 0 20 101 |  | Locust (acridian) name Ln | Code table, 0 |
| 0 20 102 |  | Locust (maturity) color Lc | Code table, 0 |
| 0 20 103 |  | Stage of development of locusts Ld | Code table, 0 |
| 0 20 104 |  | Organization state of swarm or band of locusts Lg | Code table, 0 |
| 0 20 105 |  | Size of swarm or band of locusts and duration of passage of swarm sL | Code table, 0 |
| 0 20 106 |  | Locust population density dL | Code table, 0 |
| 0 20 107 |  | Direction of movements of locust swarm DL | Code table, 0 |
| 0 20 108 |  | Extent of vegetation ve | Code table, 0 |
| 3 02 043 |  | Basic synoptic “period” data |  |
| 3 02 044 |  | Evaporation data |  |
| 1 01 002 |  | Replicate next descriptor 2 times |  |
| 3 02 045 |  | Radiation data (from 1 hour and/or 24 hour period) |  |
| 3 02 046 |  | Temperature change |  |

BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA II

It is proposed to represent this template by a descriptor 3 07 082.

3 07 082:

| 3 01 090 |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- |
| 3 02 031 |  | Pressure data |  |
| 3 02 035 |  | Basic synoptic “instantaneous” data |  |
| 3 02 036 |  | Clouds with bases below station level |  |
| 3 02 047 |  | Direction of cloud drift |  |
| 0 08 002 |  | Vertical significance (= missing to cancel the previous value) | Code table, 0 |
| 3 02 048 |  | Direction and elevation of cloud |  |
| 3 02 037 |  | State of ground, snow depth, ground minimum temperature (past 12 hours) |  |
| 0 12 121 |  | Ground minimum temperature (at the time of observation) snT’gT’g | K, 2 |
| 0 12 122 |  | Ground minimum temperature of the preceding night snTgTg | K, 2 |
| 3 02 043 |  | Basic synoptic “period” data |  |
| 3 02 044 |  | Evaporation data |  |
| 1 01 002 |  | Replicate next descriptor 2 times |  |
| 3 02 045 |  | Radiation data (from 1 hour and/or 24 hour period) |  |
| 3 02 046 |  | Temperature change |  |

BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA III

It is proposed to represent this template by a descriptor 3 07 083.

3 07 083:

| 3 01 090 |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- |
| 3 02 031 |  | Pressure data |  |
| 3 02 035 |  | Basic synoptic “instantaneous” data |  |
| 3 02 036 |  | Clouds with bases below station level |  |
| 3 02 047 |  | Direction of cloud drift |  |
| 0 08 002 |  | Vertical significance (= missing to cancel the previous value) | Code table, 0 |
| 3 02 048 |  | Direction and elevation of cloud |  |
| 3 02 037 |  | State of ground, snow depth, ground minimum temperature (past 12 hours) |  |
| 0 12 122 |  | Ground minimum temperature of the preceding night snTgTg | K, 2 |
| 3 02 043 |  | Basic synoptic “period” data |  |
| 3 02 044 |  | Evaporation data |  |
| 1 01 002 |  | Replicate next descriptor 2 times |  |
| 3 02 045 |  | Radiation data (from 1 hour and/or 24 hour period) |  |
| 3 02 046 |  | Temperature change |  |

BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA IV

It is proposed to represent this template by a descriptor 3 07 084.

3 07 084:

| 3 01 090 |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- |
| 3 02 031 |  | Pressure data |  |
| 3 02 035 |  | Basic synoptic “instantaneous” data |  |
| 3 02 036 |  | Clouds with bases below station level |  |
| 0 20 055 |  | State of sky in tropics CS | Code table, 0 |
| 3 02 047 |  | Direction of cloud drift |  |
| 0 08 002 |  | Vertical significance (= missing to cancel the previous value) | Code table, 0 |
| 3 02 048 |  | Direction and elevation of cloud |  |
| 3 02 037 |  | State of ground, snow depth, ground minimum temperature (past 12 hours) |  |
| 2 05 YYY |  | Additional information of YYY characters | CCITT IA5, 0 |
| 3 02 043 |  | Basic synoptic “period” data |  |
| 3 02 044 |  | Evaporation data |  |
| 1 01 002 |  | Replicate next descriptor 2 times |  |
| 3 02 045 |  | Radiation data (from 1 hour and/or 24 hour period) |  |
| 3 02 046 |  | Temperature change |  |

BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA V

No regional practices are indicated in Manual on Codes, WMO-No. 306, Volume II. Thus the RA V template is identical with the global BUFR template for SYNOP data (see ET DR&C/Doc. 5.4(1)). Nevertheless, a sequence descriptor number (3 07 085) is proposed to be reserved for a BUFR sequence for representation of SYNOP data in compliance with reporting practices in RA V, should they be developed in the future.

BUFR template for synoptic reports from fixed land stations suitable for SYNOP data in compliance with reporting practices in RA VI

It is proposed to represent this template by a descriptor 3 07 086.

3 07 086:

| 3 01 090 |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- |
| 3 02 031 |  | Pressure data |  |
| 3 02 035 |  | Basic synoptic “instantaneous” data |  |
| 3 02 036 |  | Clouds with bases below station level |  |
| 0 08 002 |  | Vertical significance (= missing to cancel the previous value) |  |
| 3 02 037 |  | State of ground, snow depth, ground minimum temperature |  |
| 3 02 066 |  | Dangerous weather phenomena |  |
|  |  | Groups 919MWDa and 96119 in SYNOP |  |
|  | 0 20 023 | Other weather phenomena MW (1= Dust/sand whirl, 9= Funnel clouds not touching surface, 10 = Funnel clouds touching surface, 12 = Water-spout) | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent) | Code table, 0 |
|  | 0 20 027 | Phenomenon occurrence (1=At time of observation, 3=In time period for past weather) | Flag table, 0 |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving Da | Degree true, 0 |
|  |  | Group 918sqDp in SYNOP |  |
|  | 0 20 023 | Other weather phenomena (2 = Squalls) sq | Flag table, 0 |
|  | 0 20 027 | Phenomenon occurrence (1=At time of observation, 3=In time period for past weather) | Flag table, 0 |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving Dp | Degree true, 0 |
|  |  | Group 929S8S’8 in SYNOP |  |
|  | 0 20 025 | Obscuration (13 = Snow) | Flag table, 0 |
|  | 0 20 026 | Character of obscuration (5= Low drifting, 6= Blowing) S8 | Code table, 0 |
|  | 0 20 027 | Phenomenon occurrence (1=At time of observation, 3=In time period for past weather) | Flag table, 0 |
|  | 0 20 028 | Evolution of drift of snow S’8 | Code table, 0 |
|  |  | Group 932RR |  |
|  | 0 20 066 | Maximum diameter of hailstones RR | m, 3 |
|  | 0 20 027 | Phenomenon occurrence (1=At time of observation, 3=In time period for past weather) | Flag table, 0 |
|  |  | Groups 934RR- 937RR in SYNOP |  |
|  | 0 20 021 | Type of precipitation (15=Glaze, 16=Rime, 20=Wet snow) | Flag table, 0 |
|  | 0 20 027 | Phenomenon occurrence (1=At time of observation, 3=In time period for past weather) | Flag table, 0 |
|  | 0 20 067 | Diameter of deposit RR | m, 3 |
| 3 02 043 |  | Basic synoptic “period” data |  |
| 3 02 044 |  | Evaporation data |  |
| 1 01 002 |  | Replicate next descriptor 2 times |  |
| 3 02 045 |  | Radiation data (from 1 hour and/or 24 hour period) |  |

Note:

Groups 56DLDMDH,  57CDaeC and 54g0sndT are not used in RA VI and therefore the corresponding sequence descriptors 3 02 047, 3 02 048 and 3 02 046 are not included in the RA VI regional template for SYNOP data.

Coverage of regional coding procedures in BUFR template for TEMP and TEMP SHIP data

If reporting of P,T,U or wind data at additional levels is required by Regional coding procedures for TEMP and TEMP SHIP data, the current BUFR template for TEMP, TEMP SHIP and TEMP MOBIL data (see ET DR&C/Doc. 5.4(1)) can be used without any modification.

Regional coding procedures in RA IV

The RA IV Regional coding procedures, however, require data representation of additional information that is specified in Manual on Codes, WMO-No. 306, Volume II, by supplementary groups 101AdfAdf (code table 421 for AdfAdf – Form of additional data reported).

BUFR template for TEMP and TEMP SHIP data:

Sequence for representation of TEMP, TEMP SHIP and TEMP MOBIL observation type data on global scale is defined by 3 09 052. It is proposed to add the following entries to allow representation of data in the groups 101AdfAdf. Some further additions will be needed, e.g. for stability index.

| 3 09 052 |  | Sequence for representation of TEMP, TEMP SHIP and TEMP MOBIL observation type data |  |
| --- | --- | --- | --- |
|  |  | to be supplemented by: |  |
|  |  | Reason for no report or incomplete report |  |
| 0 35 035 |  | Reason for termination | Code table, 0 |
|  |  | Doubtful data |  |
| 1 09 000 |  | Delayed replication of 9 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 0 04 086 |  | Long time period or displacement (since launch time) | Second |
| 0 08 042 |  | Extended vertical sounding significance | Flag table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 05 015 |  | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 0 06 015 |  | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 2 04 001 |  | Add associated field of 1 bit in length |  |
| 0 31 021 |  | Associated field significance = 1 (indicator of quality) | Code table, 0 |
|  |  | Associated field set to 1 (suspect or bad) |  |
| 0 10 009 |  | Geopotential height | gpm |
| 2 04 000 |  | Cancel Add associated field |  |
| 1 09 000 |  | Delayed replication of 9 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 0 04 086 |  | Long time period or displacement (since launch time) | Second |
| 0 08 042 |  | Extended vertical sounding significance | Flag table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 05 015 |  | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 0 06 015 |  | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 2 04 001 |  | Add associated field of 1 bit in length |  |
| 0 31 021 |  | Associated field significance = 1 (indicator of quality) | Code table, 0 |
|  |  | Associated field set to 1 (suspect or bad) |  |
| 0 12 101 |  | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
| 2 04 000 |  | Cancel Add associated field |  |
|  |  | Corrected data |  |
| 1 04 000 |  | Delayed replication of 4 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 2 04 001 |  | Add associated field of 1 bit in length |  |
| 0 31 021 |  | Associated field significance = 21 (indicator of correction) | Code table, 0 |
| 3 03 054 |  | Temperature, dew-point, wind at a pressure level with radiosonde position |  |
| 2 04 000 |  | Cancel Add associated field |  |