| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MONTREAL, 8-12 MAY 2006 |  | ET/DR&C/Doc. 3.2(1) _______ ENGLISH ONLY |
| --- | --- | --- |

# ELEMENTS FOR AIR CHEMISTRY

(Submitted by the Secretariat)

### Summary and  Purpose of Document

This document lists the conclusion of the discussion of the ET/DR&C on this subject last year in OMAN and list the proposed additions submitted for validation.

________________________________________________________________

# ACTION PROPOSED

The Team is invited to review the proposed descriptors in APPENDIX approved last year for validation to consider their approval as pre-operational use with a view to their subsequent endorsement by CBS Ext.2006.

APPENDIX:	NEW ADDITIONS TO BUFR/CREX FOR AIR CHEMISTRY, GEMS AND PARTICULATE MATTER

BACKGROUND

AIR CHEMISTRY

In Oman the ET/DR&C considered a proposal submitted by Yves Pelletier and Yves Rochon from Canada.  The proposed additions to the BUFR table B were intended to provide a framework suitable for the reporting and forecasting of atmospheric constituents in disciplines related to Air Chemistry.

## Scope of this proposal

There was a lot of ground to cover in order to produce a comprehensive depiction of atmospheric chemistry concepts in BUFR.  It seemed prudent, then, not to try to do it all at once.  A firm base should be established and validated before building toward more complex themes.  This was a process with at least two phases.  The first phase would cover:

- The cataloging of chemical species

- Descriptors for basic quantities or physical attributes in the discipline of Air Chemistry

- Basic descriptor sequences

The second and subsequent phases might cover:

- Instrumentation

- Representation of more complex species, such as particulate matter

- Descriptor sequences suitable for Table D

The Team agreed to deal with questions arising from items on Air chemistry, GEMS project and reporting of particulate matter at the same time, as the three items were closely related.  To facilitate future discussion, the Team agreed that the proposal of GEMS would be merged into the proposal of Canada.  The merged version should be revisited in this meeting.

##### PARAMETERS FOR GEMS

The GEMS project will develop and implement at ECMWF a comprehensive global data assimilation/forecast system for atmospheric dynamics and composition.  The model will use all available data to achieve global monitoring.  The monitoring will include atmospheric constituents with:

a) greenhouse gases

b) reactive gases

c) aerosols

It was planned to use BUFR format for the representation and exchange of the observational data.  In general, there was a need to represent chemicals in the BUFR form.  The Team agreed that these requirements, expressed by Martin Suttle from ECMWF, will be merged with the proposal from Canada.

#### NEW ENTRIES FOR REPORTING OF PARTICULATE MATTER

At a previous ET/DR+C meeting in Kuala Lumpur (June 2004), formal pre-operational approval was given to several descriptors that had previously been allocated (and subsequently validated) for use by the U.S. Environmental Protection Agency (EPA) in reporting ozone concentrations in BUFR/CREX.  The USA representative, Jeff Ator indicated that EPA would now like to begin developing similar products for the reporting of concentrations of fine particulate matter, which consisted of random particles of dust, dirt and other atmospheric contaminants trapped within a monitoring filter from a given volume of air and then measured by mass.  The Team combined these requirements with those expressed for Air chemistry.

APPENDIX

NEW ADDITIONS TO BUFR/CREX FOR AIR CHEMISTRY, GEMS AND

PARTICULATE MATTER

## AIR CHEMISTRY

## Example descriptor sequence

Full templates for specific instances of Air Quality observations are not provided; however, the general structure of a descriptor sequence is envisioned as follows (where indentation indicates repeatable sub-sequences of descriptors):

- Identification of measurement site and instrumentation

- Date/time of start of measurement

- Horizontal and vertical coordinates of measurement site

- Time displacement from start of measurement (high precision)

- Lat/long displacement from start of measurement (high precision)

- Vertical coordinate value (using high-precision descriptor when required)

- Atmospheric constituent type (new descriptor 0 08 043 or 0 08 044)

- Measured or physical quantities  (one or more measurement or forecast)

This structure was based on the WMO BUFR template for TEMP data (aerological sounding).  It would likely suit measurements taken by balloon or aircraft.  Appropriate templates would have to be designed for ground-based and satellite measurements.

## Design issues

Catalogue of chemical species:

Atmospheric chemistry potentially deals with thousands of molecules.  While an initial list may have "only" contained a few dozen species, we perceive that it is important to formulate an approach that scales well as the number of measured chemicals grows.  Unless well planned from the outset, this could become a significant maintenance issue and involve us in an area (the cataloguing of chemicals) that we may not want to get into.

We propose to address the issue as follows:

In chemistry, unambiguous identification of a chemical is commonly accomplished through the use of so-called CAS Registry Numbers. CAS (Chemical Abstracts Service, http://www.cas.org/EO/regsys.html ) is a division of the American Chemical Society.   A CAS number is composed of 11 characters at most: 9 digits or less, and 2 hyphens.  

We propose the creation of a BUFR table B descriptor that would allow the use of CAS numbers inside a BUFR message.  This would have at least three advantages:

  - allowing the use of CAS numbers would alleviate the need to create and maintain tables of atmospheric chemicals within the BUFR framework (but not quite eliminate it).   However, those tables that we would have to create, could then be short and generic.

  - CAS would provide a more robust catalogue than what we could come up with on our own

  - It would connect the BUFR representation of atmospheric chemistry with a tool that is well known and routinely used by chemists.

The downside of this, is that a chemical designated by its CAS Registry Number must then be looked up in the CAS database or some other source, such as could be found in the scientific literature.  We believe this is easily manageable by users in the field of Atmospheric Chemistry.  Thus, for completely unambiguous specification of chemical species in BUFR, the use of CAS registry numbers would be recommended.

A small WMO-maintained catalogue would still be required, but only for general and generic species without a CAS number, such as volcanic ash, smoke, and generic aerosols.  Very fundamental species such as water vapour, ozone and the other main greenhouse gases would also be included.  The catalogue would take the form of a code table corresponding to proposed element descriptor 0 08 043 (see below).  To prevent undue growth of the WMO maintained catalogue, the addition, to this table, of constituents endowed with a CAS number should be given careful consideration and occur only for especially common or important species.

A short discussion of the main chemicals of interest is included in ANNEX B.

Precision requirements and bit length of descriptors:

The absolute values and precision required for some measurement types (i.e. concentration) span across at least 16 decimal orders of magnitude.  Individual chemical species may have narrower requirements, but to accommodate a whole catalogue of species with a single concentration descriptor, that is what we need.   This means that a concentration descriptor meant for general use for any chemical would need to be at least 54 bits wide.   For individual species, the required width could in some cases exceed 32 bits.

Within the existing BUFR framework, the chosen solution was to give the concentration (and similar) descriptors default scales and bit width that work for the greater number of species, and to leave specialist users to choose appropriate scaling and bit width on a case by case basis, by using BUFR Data Description Operators.

As a means of providing additional flexibility, we also propose to create a new Data Description Operator that would make it possible to express values in IEEE floating-point format.  In many cases this would allow data representation with the fewest possible intermediate steps while maintaining sufficient precision.  It would, however, require the adaptation of existing decoders.  We believe this would be worth the work, since the added flexibility could have benefits in other areas that demand the depiction of extremely large value ranges.

## Proposed new descriptors for atmospheric constituents

- Measured or physical quantities

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 15 007 | Molecular mass | u (unified atomic mass unit) | 2 | 0 | 15 | U (unified atomic mass unit) | 2 | 5 |
| 0 15 008 | Volumetric mixing ratio | numeric | 16 | 0 | 31 | numeric | 16 | 10 |
| 0 15 009 | Integrated number density | m-2 | -12 | 0 | 31 | m-2 | -12 | 10 |
| 0 15 010 | Partial pressure | Pa | 12 | 0 | 31 | Pa | 12 | 10 |
| 0 15 021 | Integrated mass density | kg/m2 | 14 | 0 | 31 | Kg/m2 | 14 | 10 |
| 0 15 022 | Number density | m-3 | -8 | 0 | 31 | m-3 | -8 | 10 |
| 0 15 023 | Mass density | kg/m3 | 18 | 0 | 31 | kg/m3 | 18 | 10 |
| 0 15 024 | Optical depth | numeric | 4 | 0 | 24 | numeric | 4 | 8 |
| 0 15 029 | Extinction coefficient | m-1 | 9 | 0 | 30 | m-1 | 9 | 10 |
| 0 15 028 | Photo dissociation rate | s-1 | 14 | 0 | 31 | s-1 | 14 | 10 |

- Coordinates

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 07 011 | Pressure (high precision) | Pa | 4 | 0 | 31 | Pa | 4 | 10 |

- Processing information

| Table Reference | Element name | BUF | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 02 071 | Spectrographic wavelength | m | 13 | 0 | 30 | m | 13 | 10 |
| 0 02 072 | Spectrographic width | m | 13 | 0 | 30 | m | 13 | 10 |

- Significance qualifier

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 08 043 | Atmospheric chemical or physical constituent type | Code Table | 0 | 0 | 8 | Code table | 0 | 3 |
| 0 08 044 | CAS registry number | Numeric | 0 | 0 | 30 | Numeric | 0 | 10 |

Code table 0 08 043

See remarks in section “Design Issues”, sub-section 1, and in ANNEX B.

The last column in the table contains the associated registry number from the Chemical Abstracts Service (CAS) of the American Chemical Society.

| Code figure | Meaning |
| --- | --- |
|  | Name | Formula | CAS Number (if applicable) |
| 0 | Ozone | O3 | 10028-15-6 |
| 1 | Water vapour | H2O | 7732-18-5 |
| 2 | Methane | CH4 | 74-82-8 |
| 3 | Carbon dioxide | CO2 | 37210-16-5 |
| 04-24 | reserved |  |  |
| 25 | Particulate Matter < 1.0 microns |  |  |
| 26 | Particulate Matter < 2.5 microns |  |  |
| 27 | Particulate Matter < 10 microns |  |  |
| 28 | Aerosols (generic) |  |  |
| 29 | Smoke (generic) |  |  |
| 30 | Crustal Material (generic dust) |  |  |
| 31 | Volcanic Ash |  |  |
| 32-200 | reserved |  |  |
| 201-254 | reserved for local use |  |  |
| 255 | missing |  |  |

Data description operator

An already existing method of dealing with very large numerical ranges, used in satellite BUFR messages, will be incorporated in the proposal.  The method uses descriptors to specify explicitly the scale factor and data width.  It is still believed that adding the option of IEEE representation is desirable; but the existing method is tested and proven.

| Table Reference | Operator name | Operation Description |
| --- | --- | --- |
| F X Operand |  |  |
| 2 07 YYY | IEEE floating point representation | For elements in Table B other than CCITT IA5, code tables or flag tables, this operator shall indicate that values are represented in YYY bit IEEE floating point, where YYY can be set to 032, 064 or any valid IEEE floating point width. This operator shall override the scaling and bit width from Table B. The reference value from Table B may be used for bound-checking if applicable. An operand of YYY=000 shall reinstate the Table B scaling and bit width. |

## ANNEX A - Range correspondence

Determination and identification of the minimum and maximum values corresponding to the definitions of the descriptor elements in tables 1 to 3 are presented here.  Two maxima are provided when the range of possible expected values cannot be expressed with at most 31 bits; a maximum of at most 2x109 larger than the minimum value can be obtained from 31 bits. In such instances, both the magnitude corresponding to a limit of 31 bits, in consideration of the minimum value in the table, and the magnitude of the largest expected value are provided.

The range of values for concentrations of constituent observations is based on a minimum set according to a minimum OH mixing ratio of ~10-14 with a precision of 1% and the largest expected maximum set according to the upper limit for tropospheric H2O mixing ratio at ~0.04.  The next largest mixing ratios would be attributed to CO2 at a level just under 0.001.  For conversion to other units, which involve pressure and/or temperature, pressures of 105 Pa and 104 Pa for the calculation of the maxima and minima and a temperature of 300 were applied.  Use of 104 Pa with the OH mixing ratio is reasonable for determination of the minimum considering the increase in OH mixing ratio with decreasing pressure as well as the larger mixing ratios in the stratosphere and mesosphere for other constituents.  Here are the conversions applied to the volumetric mixing ratios followed by the resulting ranges:

| Parameter | Unit | Conversion factor from mixing ratio |
| --- | --- | --- |
| Pressure | Pascal | Pair |
| Number density | m-3 | PairNa /(R*T) |
| Mass density | kg/m3 | PairM /(R*T) x10-3 kg/g |
| Integrated number density | m-2 | HPairNa /(R*T) |
| Integrated mass density | kg/m2 | HPairM /(R*T) x10-3 kg/g |

where Pair is the atmospheric pressure in Pa, Na is the Avogradro constant (6.022x1023 /mol), R* is the gas constant (8.314 J K-1 mol-1), T is temperature in Kelvin, H is the scale height of the atmosphere set to 7x103 m, and M is the molecular mass in unified mass units u (i.e., g mol-1), hence the additional conversion factor of 10-3 kg/g.

| Table Reference | Element name | Unit | Minimum value | Maxima |
| --- | --- | --- | --- | --- |
|  |  |  |  | Based on a limit of 31 bits | Largest expected value |
| F X Y |  |  |  |  |  |
| 0 15 007 | Molecular mass | u (unified mass unit) | 0.01 | - | 327.67 |
| 0 15 008 | Mixing ratio in volume | numeric | 10-16 | 2x10-7 | 0.04 |
| 0 15 009 | Integrated number density | m-2 | 1012 | 2x1021 | 1028 |
| 0 15 010 | Partial pressure | Pa | 10-12 | 2x10-3 | 104 |
| 0 15 021 | Integrated mass density | kg/m2 | 10-14 | 2x10-5 | 102 |
| 0 15 022 | Number density | m-3 | 108 | 2x1017 | 1024 |
| 0 15 023 | Mass density | kg/m3 | 10-18 | 2x10-9 | 10-2 |
| 0 15 024 | Optical depth | numeric | 0.0001 | - | 1000 (clouds) |
| 0 15 029 | Extinction coefficient | m-1 | 10-9 | - | 1.0 (clouds) |
| 0 15 028 | Photo dissociation rate | s-1 | 10-14 | 2x10-5 | 0.1 |
| 0 07 011 | Pressure (high precision | Pa | 10-4 [0.1 Pa (~95 km) with 4 significant digits] | - | 2x105 |
| 0 25 103 | Spectral width (line widths to band models) | m | 10-13 | - | 10-4 |
| 0 25 102 | Wavelength | m | 10-13 (102 nm with 7 significant digits) | - | 10-4 (102 m) |

## ANNEX B  - Chemicals of Interest

We provide below a list of chemicals of interest not present in Code Table 0 08 043, with their CAS registry numbers.  In BUFR code, these chemicals would be identified by their CAS numbers, using element descriptor 0 08 044.  Maintenance of this list is not viewed as being within the scope of the Expert Team on Data Representation and Codes; it is only provided here for illustration purposes.

A first iteration of the list was based on Tables 4.1-4.3 and the text of the IGACO theme report of September 2004 (WMO TD No. 1235)).

Three halon compounds were included based on the table of class I ozone-depleting substances (Group II) of the U.S. Environmental Protection Agency

(http://www.epa.gov/docs/ozone/ods.html).

CFC-11 was added to complement CFC-12 and HCFC-22 of the IGACO report.

The list of measured volatile organic compounds (VOC) would be quite extensive and is not explicitly identified here.  A list of VOC and related families can be consulted in Makar et al. (JGR, 108, 2003).

Other species such as OH, HNO4, CCl4, NH3, CF4, H2O2, N2O5, HF, H2SO4, OCS, HOCl, PAN, O (1D) and mercury-related compounds could also be considered.

| Name | Formula | CAS registry number |
| --- | --- | --- |
| Carbon monoxide | CO | 630-08-0 |
| Nitrogen dioxide | NO2 | 10102-44-0 |
| Nitrous oxide | N2O | 10024-97-2 |
| Bromine oxide | BrO | 15656-19-6 |
| Chlorine monoxide | ClO | 7791-21-1 |
| Hydrogen chloride | HCl | 7647-01-0 |
| Chlorine dioxide | OClO | 10049-04-4 |
| Trichlorofluoromethane | CFC-11 (CCl3F) | 75-69-4 |
| Dichlorodifluoromethane | CFC-12 (CCl2F2) | 75-71-8 |
| Nitric Oxide | NO | 10102-43-9 |
| Nitric acid | HNO3 | 52583-42-3 |
| Acetylene | C2H2 | 74-86-2 |
| Ethane | C2H6 | 74-84-0 |
| Methyl bromide | CH3Br | 74-83-9 |
| Bromotrifluoro-methane | CF3Br (halon 1301) | 75-63-8 |
| Bromochloro- difluoromethane | CF2ClBr (halon 1211) | 353-59-3 |
| Dibromotetra-fluoroethane | C2F4Br2 (halon 2402) | 25497-30-7 |
| Chlorodifluoro-methane | HCFC-22 (CHClF2) | 75-45-6 |
| Chlorine nitrate | ClONO2 | 14545-72-3 |
| Formaldehyde | HCHO | 50-00-0 |
| Sulfur dioxide | SO2 | 7446-09-5 |

GEMS

Proposal by Martin Suttle (ECMWF)

Comments on the proposal by the Team:

  - Spectrographic wavelength descriptor from the proposal above is to be used to qualify optical depth, instead of carrying physical measurement and wavelength in same descriptor (remove 0 15 040 and rename 0 15 041)

  - Similarly, “error” descriptors are to use first order statistics from class 08

  - Meaning of “small mode” to be clarified (0 15 041).  If necessary, a new entry in First Order Statistics Code Table will be proposed.

  - It may be a little premature yet to create averaging kernel descriptors (linked to statistics).  We need the research community to reach consensus and then to express representation requirements. (0 15 044)

  - The version of Code Table 0 08 043 contained in this proposal should be used,; however, the proposed table elements “Maritime”, “Continental”, and “Sulfate” were refused as they are qualifiers and not physical or chemical constituents.

Key:	xxxx element from proposal of Pelletier and Rochon

yyyy new element needed

Aerosol

| Table Reference | Parameter | Units |
| --- | --- | --- |
| 0 01 007 | Satellite identifier |  |
| 0 02 019 | Satellite instrument |  |
| 0 01 033 | Identification of originating/generating centre |  |
| 0 02 172 | Product type for retrieved atmospheric gases |  |
| 0 04 001 | Year | year |
| 0 04 002 | Month | month |
| 0 04 003 | Day | day |
| 0 04 004 | Hour | hour |
| 0 04 005 | Minute | minute |
| 0 04 006 | Second | second |
| 0 05 001 | Latitude (high accuracy) | degree |
| 0 06 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 07 025 | Solar zenith angle | degree |
| 0 07 024 | Satellite zenith angle | degree |
|  | Solar azimuth angle | degree |
|  | Satellite azimuth angle | degree |
|  | Cloud mask and snow/ice indicator | Flag Table |
|  | Cloud amount percentage interval | Code Table |
| 0 08 013 | Day/night qualifier | Code Table |
| 0 08 065 | Sun-glint indicator | Code Table |
| 0 05 043 | Field of view number | numeric |
| 0 20 010 | Cloud cover (total) | % |
| 0 20 016 | Pressure at top of cloud | Pa |
| 0 13 040 | Surface flag (with proposed addition - see below) | Code Table |
| 0 33 003 | Quality information |  |
| 0 08 043 | Atmospheric chemical or physical constituent type | Code Table |
|  | Aerosol optical depth at 0.55 micron | numeric |
|  | Error in aerosol optical depth at 0.55 micron (see Note 2) | numeric |
|  | Ratio of small mode aerosol optical depth at 0.55 micron | numeric |
|  | Error in ratio of small mode aerosol optical depth at 0.55 micron (see Note 2) | numeric |
| 0 22 094 | Number of wavelength bands | numeric |
|  | Per wavelength band |  |
| 0 25 102 | Spectrographic wavelength | m |
|  | Reflectance | numeric |
|  | Error reflectance (see Note 2) | numeric |
| 0 10 040 | Number of retrieved layers (for optical depth) | numeric |
|  | Per optical depth layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
| 0 15 024 | Optical depth | numeric |
|  | Error optical depth (see Note 2) | numeric |
| 0 10 040 | Number of retrieved layers (for extinction) | numeric |
|  | Per extinction layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
| 0 15 029 | Extinction coefficient | m-1 |
|  | Error extinction coefficient (see Note 2) | m-1 |

Chemical species

Initial GEMS chemical species are:

- O3 (ozone)

- NO2 (nitrogen dioxide)

- SO2 (sulphur dioxide)

- HCHO (formaldehyde)

- CO2 (carbon dioxide)

- N2O (nitrous oxide)

- CO (carbon monoxide)

- CH4 (methane)

| Table Reference | Parameter | Units |
| --- | --- | --- |
| 0 01 007 | Satellite identifier |  |
| 0 02 019 | Satellite instrument |  |
| 0 01 033 | Identification of originating/generating centre |  |
| 0 02 172 | Product type for retrieved atmospheric gases |  |
| 0 04 001 | Year | year |
| 0 04 002 | Month | month |
| 0 04 003 | Day | day |
| 0 04 004 | Hour | hour |
| 0 04 005 | Minute | minute |
| 0 04 006 | Second | second |
| 0 05 001 | Latitude (high accuracy) | degree |
| 0 06 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 07 022 | Solar elevation | degree |
| 0 05 043 | Field of view number | numeric |
| 0 20 010 | Cloud cover (total) | % |
| 0 20 016 | Pressure at top of cloud | Pa |
| 0 08 012 | Land/sea mask | numeric |
| 0 33 003 | Quality information |  |
| 0 08 043 | Atmospheric chemical or physical constituent type (see Note 1) | Code Table |
| 0 10 040 | Number of retrieved layers | numeric |
|  | Per retrieved layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
| 0 15 021 | Integrated mass density | kg/m2 |
|  | Error integrated mass density (see Note 2) | kg/m2 |
|  | No. of averaging kernel layers | numeric |
|  | Per averaging kernel layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
|  | Averaging kernel value | numeric |

Notes:

1. Need CO, NO2, N2O, HCHO and SO2 include in proposed Code Table 0 08 043.

2. We will have to be clear on what “error” means, i.e. could be 1-σ, 3- σ, rms, etc.

New BUFR descriptors for GEMS observational data

| Table Reference | Element Name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data Width (Chars) |
| 015040 | Aerosol optical depth at 0.55 micron (see Note A) | numeric | 4 | 0 | 24 | numeric | 4 | 8 |
| 015041 | Ratio of small mode aerosol optical depth at 0.55 micron (see Note B) | numeric | 6 (4) | 0 | 20 (14) | numeric | 6 (4) | 7 (5) |
| 015042 | Reflectance (see Note C) | numeric | 6 (4) | 0 | 20 (14) | numeric | 6 (4) | 7 (5) |
| 015043 | No. of averaging kernel layers (see Note D) | numeric | 0 | 0 | 10 | numeric | 0 | 4 |
| 015044 | Averaging kernel value (see Note E) | numeric | 6 (4) | -5x106 (-5x104) | 24 (17) | numeric | 6 (4) | 8 (6) |
| 015045 | Snow/ice indicator | Flag table | 0 | 0 | 2 | Flag table | 0 | 1 |
| 015046 | Cloud amount percentage interval | Code Table | 0 | 0 | 3 | Code Table | 0 | 1 |

Notes:

A. Assumed same range and precision as for Optical Depth (0 15 024) proposed by Pelletier and Rochon.

B. Minimum value = 0.0, maximum value = 1.0, precision = 0.000001 (0.0001)

C. Minimum value = 0.0, maximum value = 1.0, precision = 0.000001 (0.0001)

D. Allow up to 1024 averaging kernel layers (as with Number of retrieved layers (0 10 040))

E. Minimum = -5.0, maximum = 5.0, precision = 0.000001 (0.0001)

New Flag Tables   015045

Cloud mask and snow/ice indicator

| Bit No. |  |
| --- | --- |
| 1 | Snow/ice present |
| All 2 | Missing value |

New Code Tables 015046

Cloud amount percentage interval

| Code figure |  |
| --- | --- |
| 0 | 0-25% cloudy pixels |
| 1 | 25-50% cloudy pixels |
| 2 | 50-75% cloudy pixels |
| 3 | 75-100% cloudy pixels |
| 5-6 | Reserved |
| 7 | Missing value |

Additions to existing Code Tables

0 13 040 Surface flag

| Code figure |  |
| --- | --- |
| 0 | Land |
| 1 | Reserved |
| 2 | Near coast |
| 3 | Ice |
| 4 | Possible ice |
| 5 | Ocean |
| 6 | Coast |
| 7 | Desert |
| 8-14 | Reserved |
| 15 | Missing value |

Additions to proposed Code Tables

0 08 043 Atmospheric chemical or physical constituent type

| Code figure |  |
| --- | --- |
| 0 | Ozone (O3) |
| 1 | Water vapour (H2O) |
| 2 | Methane (CH4) |
| 3 | Carbon dioxide (CO2) |
| 4 | Carbon monoxide (CO) |
| 5 | Nitrogen dioxide (NO2) |
| 6 | Nitrous oxide (N2O) |
| 7 | Formaldehyde (HCHO) |
| 8 | Sulphur dioxide (SO2) |
| 9-24 | Reserved |
| 25 | Particulate matter < 1.0 microns |
| 26 | Particulate matter < 2.5 microns |
| 27 | Particulate matter < 10 microns |
| 28 | Aerosols (generic) |
| 29 | Smoke (generic) |
| 30 | Crustal material (generic dust) |
| 31 | Volcanic ash |
| 32 | Continental (generic) |
| 33 | Maritime (generic) |
| 34 | Sulfate |
| 35-200 | Reserved |
| 201-254 | Reserved for local use |
| 255 | Missing value |

PARTICULATE MATTER

At the previous ET/DR+C meeting in Kuala Lumpur (June 2004), formal pre-operational approval was given to several descriptors that had previously been allocated (and subsequently validated) for use by the U.S. Environmental Protection Agency (EPA) in reporting ozone concentrations in BUFR/CREX.  The EPA would now like to begin developing similar products for the reporting of concentrations of fine particulate matter, which consists of random particles of dust, dirt and other atmospheric contaminants trapped within a monitoring filter from a given volume of air and then measured by mass.  Since the particles are of a mixed and varying chemical composition, there is no way to convert such mass measurements to moles, which precludes the use of the existing BUFR/CREX descriptor 0-15-026/B-15-026.  Therefore a new descriptor is required for reporting the concentration of such particles as a density (mass per unit volume).  The mass amounts are directly measured in units of micrograms (per cubic meter), so an appropriate scale factor was selected in order to convert such values to the SI unit of kilograms.

Since proposed Code Table 0 08 043 remains to be validated, and there is an ongoing operational requirement at the US Environmental Protection Agency, the Team proposed to keep using Code Table 0 15 025 for now and maintained the proposal to add new entries 11 and 12 in pre-operational mode.

Add the following new entries to existing BUFR/CREX code table 0-15-025/B-15-025 (i.e. “type of pollutant”):

- Fine particulate matter (diameter < 2.5 microns)

- Fine particulate matter (diameter < 10 microns)

A provision will be added to the merged proposal, suggesting that once the descriptors have been accepted for pre-operational use, the following note should be added to Class 15 in the Manual on Codes: “For reporting of the identity of an atmospheric pollutant or constituent, the use of 0 08 043 is preferred to the use of 0 15 025”.

Add the following new entry to BUFR/CREX Class 15:

| TABLE REFERENCE | TABLE ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
|  |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| F | X | Y |  |  |  |  |  |  |  |  |
| 0 | 15 | 027 | Concentration of pollutant | Kg m-3 | 9 | 0 | 10 | Kg m-3 | 9 | 4 |

In addition, and on a related note, we would like to point out the following typographical errors in the English translation of the current WMO Manual 306, Part B for BUFR/CREX Class 15:

- For both 0-15-025 and 0-15-026, the “ELEMENT NAME” contains the word “pollutant” misspelled as “polluant”.

The units of 0-15-026 should be “mol mol-1” (i.e. one included space) rather than “molmol-1”, which seems to imply the reciprocal of some heretofore unknown unit of measure!