| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES MONTREAL, 8-12 MAY 2006 |  | CT-MTDCF/ET-DR&C/Doc. 5.2(1) ITEM: 5.2 (16.IV.2006) ENGLISH ONLY |
| --- | --- | --- |

Proposal for coverage of regional reporting practices

in BUFR templates for TEMP and TEMP SHIP data

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for coverage of regional reporting practices in BUFR templates for TEMP and TEMP SHIP data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] Manual on Codes, WMO-No. 306, Volume II.

[3] Final Report, ET DR&C, Muscat, 5 - 8  December 2005

1. Background

Document ET DR&C/Doc. 5.2(1) submitted to the ET DR&C meeting in Muscat (5 - 8  December 2005) contained a proposal for coverage of regional reporting practices in BUFR templates for TAC data. No corrective comments or alternative suggestions have been obtained.

Coverage of regional reporting practices in BUFR templates for TEMP data was discussed in paragraph 6 of the above mentioned document.  It was mentioned, however, that the proposed additions did not fully covered representation of data in the groups 101AdfAdf, required for representation of RA IV reporting practices for TEMP and TEMP SHIP data, i.e. that some further additions were  needed.  Therefore, three new descriptors are proposed below.  Besides that, representation of doubtful temperature and geopotential data has been rewritten using significance qualifier 0 08 040.

The author wishes to thank Mr. Jeff Ator (USA) for providing her with the definition of stability index used in regional reporting procedures in RA IV.

2. Proposal for new descriptors and a Note under the Class 13

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 11 054 | Mean wind direction for 1500 m – 3000 m | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| 0 11 055 | Mean wind speed for 1500 m – 3000 m | m s-1 | 1 | 0 | 12 | m s-1 | 1 | 4 |
| 0 13 047 | Stability index | K | 0 | -20 | 6 | ºC | 0 | 2 |

It is proposed to add a Note under Class 13:

The “Stability index” is defined as the temperature difference between the ambient 500 hPa temperature and the temperature a parcel of air, initially at a selected base level, would have if brought from its condensation level to the 500 hPa surface by a moist adiabatic process.  Positive values denote stable conditions, while negative values denote unstable conditions.  The base level is 850 hPa, 800hPa or 750 hPa  if the station elevation is less than 1000, 1000 to 1400 or 1401 to 2000 m above mean sea level, respectively.

3. Coverage of regional coding procedures in BUFR template for TEMP and TEMP SHIP data

If reporting of P,T,U or wind data at additional levels is required by Regional coding procedures for TEMP and TEMP SHIP data, the current BUFR template for TEMP, TEMP SHIP and TEMP MOBIL data can be used without any modification.

Regional coding procedures in RA IV

The RA IV Regional coding procedures, however, require data representation of additional information that is specified in Manual on Codes, WMO-No. 306, Volume II, by supplementary groups 101AdfAdf (code table 421 for AdfAdf – Form of additional data reported).

RA IV BUFR template for TEMP and TEMP SHIP data:

Sequence for representation of TEMP, TEMP SHIP and TEMP MOBIL observation type data on global scale is defined by 3 09 052. It is proposed to add the following entries to allow representation of data in the groups 101AdfAdf.

| 3 09 052 |  | Sequence for representation of TEMP, TEMP SHIP and TEMP MOBIL observation type data |  |
| --- | --- | --- | --- |
|  |  | may be supplemented by: |  |
|  |  | Reason for no report or incomplete report |  |
| 0 35 035 |  | Reason for termination | Code table |
|  |  | Corrected data |  |
| 1 04 000 |  | Delayed replication of 4 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 2 04 001 |  | Add associated field of 1 bit in length |  |
| 0 31 021 |  | Associated field significance = 21 (indicator of correction) | Code table |
|  |  | Associated field set to 1 (corrected value) |  |
| 3 03 054 |  | Temperature, dew-point, wind at a pressure level with radiosonde position |  |
| 2 04 000 |  | Cancel Add associated field |  |
| 0 08 042 |  | Extended vertical sounding significance = missing (to cancel the previous value) | Flag table |
|  |  | Stability index and mean wind data |  |
| 0 13 047 |  | Stability index | K |
| 0 11 044 |  | Mean wind direction for surface – 1500 m | Degree true |
| 0 11 045 |  | Mean wind speed for surface – 1500 m | m s-1, scale 1 |
| 0 11 054 |  | Mean wind direction for 1500 m – 3000 m | Degree true |
| 0 11 055 |  | Mean wind speed for 1500 m – 3000 m | m s-1, scale 1 |
|  |  | Doubtful data |  |
| 1 12 000 |  | Delayed replication of 12 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 1 11 002 |  | Replicate next 11 descriptors 2 times |  |
| 0 04 086 |  | Long time period or displacement (since launch time) | Second |
| 0 08 040 |  | Flight level significance In the 1st replication = 4 (Begin doubtful temperature, height data), in the 2nd replication = 9 (End doubtful temperature, height data). | Code table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 05 015 |  | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 0 06 015 |  | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric |
| 0 10 009 |  | Geopotential height | gpm |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric |
| 0 12 101 |  | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  |  | Extrapolated geopotential data |  |
| 1 08 000 |  | Delayed replication of 8 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 0 04 086 |  | Long time period or displacement (since launch time) | Second |
| 0 08 040 |  | Flight level significance = 31 (Incremented height level (generated)) | Code table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 05 015 |  | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 0 06 015 |  | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
| 0 10 009 |  | Geopotential height | gpm |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |