| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF COORDINATION TEAM ON MIGRATION TO TABLE DRIVEN CODE FORMS AND EXPERT TEAM ON DATA REPRESENTATION AND CODES ICAO, MONTREAL, 8-12 MAY 2006 |  | CT-MTDCF/ET-DR&C/Doc. 5.4(2) ITEM: 5.4 (27.IV.2006) ENGLISH ONLY |
| --- | --- | --- |

Proposal for modification to BUFR template

for CLIMAT TEMP and CLIMAT TEMP SHIP data

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a revised version of BUFR template TM 309054 for CLIMAT TEMP and CLIMAT TEMP SHIP data

________________________________________________________________

ACTION PROPOSED

The meeting is kindly invited to consider the proposed modification

to BUFR template TM 309054 and the possibility to recommend them for implementation.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2

[2] Final Report, ET DR&C, Muscat, 5 – 8  December 2005

1. Background

Document ET DR&C/Doc. 5.4(1) submitted to the ET DR&C meeting in Muscat (5-8  December 2005) contained review of BUFR templates for reporting TAC data and a proposal for new common sequences, among others also for the sequence descriptor 3 09 054 for BUFR template for CLIMAT TEMP and CLIMAT TEMP SHIP data. During the process of writing the Regulations, however, two points were identified in this template that would need improvement.

The regulatory material B/C35 (Regulations for reporting CLIMAT TEMP and CLIMAT TEMP SHIP data in TDCF) already contains the revised version of the BUFR template TM 309054 as shown below. If its implementation were not acceptable for the Teams or if a new sequence descriptor were required to represent this common sequence, the text of B/C35 would have to be modified accordingly.

2. Proposed modifications

- Location of a land station is required to be reported with precision at least in thousandths of a degree. 0 05 002 (Latitude) and 0 06 002 (Longitude) cannot oblige this requirement. Consequently, 3 01 023 has been replaced by 3 01 021.

- Description of the level data should start with 0 08 001 (Vertical sounding significance) that applies to all the following 14 entries. Therefore, the first 3 entries under the delayed replication were reordered

| from | 0 08 023 | First order statistics (= 4; mean value) | to | 0 08 001 | Vertical sounding significance |
| --- | --- | --- | --- | --- | --- |
|  | 0 07 004 | Pressure |  | 0 08 023 | First order statistics (= 4; mean value) |
|  | 0 08 001 | Vertical sounding significance |  | 0 07 004 | Pressure |

3. Minor editorial corrections

- Note (1) under the template TM 309054 should explicitly be written as “(1)”.

- Within the template TM 309054, (1) as an upper index should be added also to Year and Month within 3 01 011; the beginning of the one month-period is specified not only by Day, Hour and Minute, but also by Year and Month within 3 01 011.

- The amendment suggested in 3(b) should be done also in the template TM 307073 (for CLIMAT data) and in the template TM 308013 (for CLIMAT SHIP data), for the same reasons as in the template TM 309054.

TM 309054 - BUFR template for reports of monthly aerological means

suitable for CLIMAT TEMP and CLIMAT TEMP SHIP data

| 3 09 054 |  | Sequence for representation CLIMAT TEMP and CLIMAT TEMP SHIP data |
| --- | --- | --- |

Sequence BUFR descriptor <3 09 054> expands as it is shown in the leftmost column below:

|  |  | Identification of launch site | Unit, scale |
| --- | --- | --- | --- |
| 3 01 001 | 0 01 001 | WMO block number | Numeric, 0 |
|  | 0 01 002 | WMO station number | Numeric, 0 |
| 0 01 011 |  | Ship's call sign | CCITT IA5, 0 |
|  |  | Date/time(1) |  |
| 3 01 011 | 0 04 001 | Year(1) | Year, 0 |
|  | 0 04 002 | Month(1) | Month, 0 |
|  | 0 04 003 | Day (= 1) (1) | Day, 0 |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour, 0 |
|  | 0 04 005 | Minute (= 0) (1) | Minute, 0 |
|  |  | Horizontal and vertical coordinates |  |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 0 07 007 |  | Height release of sonde above mean sea level | m, 0 |
|  |  | Monthly mean data |  |
| 0 04 023 |  | Time period (= number of days in the month) | Day, 0 |
| 0 04 059 |  | Times of observations used to compute the reported mean values | Flag table, 0 |
| 1 15 000 |  | Delayed replication of 15 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
| 0 08 001 |  | Vertical sounding significance | Flag table, 0 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table, 0 |
| 0 07 004 |  | Pressure | Pa, –1 |
| 0 10 009 |  | Geopotential height | gpm, 0 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, 2 |
| 0 12 103 |  | Dew-point temperature | K, 2 |
| 0 08 023 |  | First order statistics (= 32; vector mean) | Code table, 0 |
| 0 11 001 |  | Wind direction | Degree true, 0 |
| 0 11 002 |  | Wind speed | m s-1, 1 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table, 0 |
| 0 11 019 |  | Steadiness of wind | %, 0 |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 2; temperature) | Code table, 0 |
| 0 08 020 |  | Total number of missing entities (days) | Numeric, 0 |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 9; wind) | Code table, 0 |
| 0 08 020 |  | Total number of missing entities (days) | Numeric, 0 |

Note:

(1)  The time identification refers to the beginning of the one-month period.