| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MONTREAL, 8-12 MAY 2006 |  | ET/DR&C/Doc. 5.4(3) _______ ENGLISH ONLY |
| --- | --- | --- |

PROPOSED BUFR TEMPLATE FOR BUOY WAVE DATA

(Submitted by the Secretariat)

### Summary and Purpose of Document

This document lists the conclusion of the discussion of the ET/DR&C on this subject last year in OMAN and list the proposed template including additions submitted for validation.

________________________________________________________________

# ACTION PROPOSED

The Team is invited to review the proposed descriptors and accept the new attributed sequence number, but in view of the fact that usage has not started, to keep them in “ for validation status”.

Sequence number required for all existing BUOY template 3 08 005 (see Annex to 5.4(1)REV 1

Proposed BUFR Template for buoy and wave data

(draft)

Proposed template is listed in the table 1 below. Descriptors number 1 to 84 in the table correspond to the existing BUFR template for buoy data (i.e. the “Arusha” template).

Descriptors used are from BUFR Master table 0, version 11. No local table is being used.

- Are indicated in red descriptors that are presently being used for BUFR encoding of PDE buoy data

- Are indicated in blue descriptors that are similar to those being used for BUFR encoding of PDE buoy data (i.e. another way to code the same information is proposed)

- Are indicated in green, information which will have to be encoded for PDE buoys if the information is available (i.e. will be useful or required by users)

- New proposed descriptors for BUFR template for buoy data are indicated in bold and italic. They correspond to descriptors 85 and after.

Implication for PDE (Puertos Del Estado, Spain) buoys:

- Buoy WMO identification number to be coded and divided in 3 descriptors instead of 1 (i.e. 001003, 001020, and 001005).

- Buoy position to be coded in high accuracy instead of coarse accuracy.

- Air pressure reduced to sea level (MSLP) must be computed and encoded.

- Sensor height with regard to platform deck and average sea level will have to be encoded for air temperature and wind; wind is assumed to be corrected to 10m so this will have to be indicated in the reports (i.e. 008082 coded 1, and 007033 coded for 10m).

- Fields for which information is not available will be coded with “missing”.

- Section 1 of existing PDE BUFR reports was not encoded according to existing regulations:

  - Local table version should be coded 0 (not 1) as all descriptors being used are formal WMO descriptors (i.e. no PDE local descriptors are being used).

  - Current B§UFR table version is 11 (not 1)

  - Year should be coded as following: YYYY coded (YYYY-100*(Century-1)), e.g. 2005 coded 05.

Table 1: Proposed new template for buoy data, including directional and non-directional wave data

| # | Descriptor | Name | Expanded descriptors | Comment, encoding |
| --- | --- | --- | --- | --- |
| 1 | 001003 | WMO region | 001003 | First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO region sub-area | 001020 | Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 002001 | Type of station | 002001 | 1=Manned station |
| 5 | 002036 | Buoy type | 002036 | 1=Fixed buoy |
| 6 | 002149 | Type of data buoy | 002149 | 16=unspecified moored buoy 24=Omnidirectional waverider 25=Directional waverider |
| 7 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | Date of observation |
| 8 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | Time of observation |
| 9 | 008021 | Time significance | 008021 | Value = 26 (time of last known position) |
| 10 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | Date of last known position coded here; coded missing for fixed station |
| 11 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | Time of last known position coded here; coded missing for fixed station |
| 12 | 008021 | Time significance | 008021 | Value = “missing” |
| 13 | 301021 | Latitude and longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Coarse accuracy descriptors (005002 and 006002 respectively) were used with PDE buoys |
| 14 | 027004 | Alternate latitude (high accuracy) | 027004 | Coded if Argos is used for location; otherwise coded missing |
| 15 | 028004 | Alternate longitude (high accuracy) | 028004 | Coded if Argos is used for location; otherwise coded missing |
| 16 | 007030 | Height of station above MSL | 007030 |  |
| 17 | 001051 | Platform Transmitter ID | 001051 | If Argos is used, Argos ID number; |
| 18 | 002148 | Data collection and/or Location system | 002148 | 1=Argos 2=GPS Coded missing if none |
| 19 | 001012 | Platform drift direction | 001012 | Coded missing for moored buoys |
| 20 | 001014 | Platform drift speed | 001014 | Coded missing for moored buoys |
| 21 | 002040 | Method of removing platform direction and speed from current | 002040 | Coded missing for moored buoys |
| 22 | 033022 | Quality of buoy satellite transmission | 033022 | 0=Good 1=Dubious 3=missing |
| 23 | 033023 | Quality of buoy location | 033023 | 0=Reliable 1=Last known position 2=Dubious 3=missinh |
| 24 | 033027 | Location quality class (range of radius of 66% confidence) | 033027 | 0: >= 1500m 1: 500m to 1500m |
| 25 | 022063 | Total water depth | 022063 | Mooring depth; otherwise coded missing |
| 26 | 302021 | Waves | 022001 (direction of waves) 022011 (period of waves) 022021 (height of waves) |  |
| 27 | 302022 | Wind waves | 022002 (direction wind wv) 022012 (period wind wv) 022022 (height wind wv) |  |
| 28 | 302023 | Swell waves | 022003 (direction swell wv) 022013 (period swell wv) 022023 (height swell wv) |  |
| 29 | 008081 | Type of equipment (observing platform) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=3: Equipment = “platform” |
| 30 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Platform battery voltage |
| 31 | 008081 | Type of equipment (transmitter) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=1: Equipment = “transmitter” |
| 32 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Transmitter battery voltage |
| 33 | 008081 | Type of equipment (receiver) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=2: Equipment = “receiver” |
| 34 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Receiver battery voltage |
| 35 | 008081 | Type of equipment – value Missing = cancel | 008081 | 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value = “missing” |
| 36 | 002034 | Drogue type | 002034 | Coded missing for moored buoys |
| 37 | 022060 | Lagrangian drifter drogue status | 022060 | (New descriptor, scale=0, ref=0, bits=3) 0=detached 1=attached 3=missing Coded missing for moored buoys |
| 38 | 007070 | Drogue depth | 007070 | Coded missing for moored buoys |
| 39 | 002190 | Lagrangian drifter submergence | 002190 | Coded missing for moored buoys |
| 40 | 025086 | Depth correction indicator for sub-surface measurements along cable | 025086 | 0=depths are not corrected 1=depths are corrected 3=missing |
| 41 | 002035 | Cable length | 002035 | Depth of hydrostatic pressure sensor at bottom of cable |
| 42 | 002168 | Hydrostatic pressure of lower end of cable | 002168 |  |
| 43 | 020031 | Ice deposit (thickness) | 020031 | Ice thickness |
| 44 | 002038 | Method of temperature and/or velocity measurement | 002038 | e.g. 2=hull contact sensor 8=thermistor chain |
| 45 | 306004 | Digitization, depth/salinity method, depths/salinities/temperatures | 002032 (indicator for digit) 002033 (method sal/depth) 103000 (delayed repl 3 desc) 031001 (replication factor) 007062 (depth) 022043 (sea temperature) 022062 (salinity) | Replication factor indicates number of (depth, temp., salinity) data points that are encoded |
| 46 | 002030 | Method of current measurement | 002030 |  |
| 47 | 306005 | Time/duration of current measurement, depths/directions/speeds | 002031 (method current) 103000 (delayed repl 3 desc) 031001 (replicationfactor) 007062 (depth) 022004 (direction current) 022031 (speed current) | Replication factor indicates number of (pepth, dir, speed) data points that are encoded |
| 48 | 007031 | Height of barometer above MSL | 007031 |  |
| 49 | 008081 | Type of equipment (sensor) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=0: Equipment = “sensor” |
| 50 | 012064 | Instrument temperature | 012064 | Temperature of air pressure sensor |
| 51 | 302001 | Pressure and pressure change | 010004 (pressure at station) 010051 (MSLP) 010061 (3-hour tendency) 010063 (tend. Characteristic) | Mean Seal Level Pressure to be computed based upon pressure at station level and sensor height |
| 52 | 008081 | Type of equipment – value missing = cancel | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value = “missing” |
| 53 | 007032 | Height of sensor above marine deck platform (for temp.&hum. measurement) | 007032 | Height of thermometer above marine desck |
| 54 | 007033 | Height of sensor above water surface (for temp.&hum. measurement) | 007033 | Height of thermometer (assumed should be coded with value = 2 metres for PDE buoys) |
| 55 | 012101 | Dry-bulb temperature (scale 2) | 012101 | Dry-bulb temperature at 2m (012004) was used for PDE buoys |
| 56 | 012103 | Dew-point temperature (scale 2) | 012103 |  |
| 57 | 013003 | Relative humidity | 013003 |  |
| 58 | 007032 | Height of sensor above marine deck platform (for wind measurement) | 007032 | Real height of anemometer above marine deck |
| 59 | 007033 | Height of sensor above water surface (for wind measurement) | 007033 | Real height of anemometer above average water surface |
| 60 | 008082 | Artificial correction of sensor height to another value | 008082 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor height is not corrected 1=sensor height is artificially corrected 7=missing Assumed should be coded to value 1 for PDE buoys |
| 61 | 007033 | Height of sensor above water surface (here height of anemometer to which it is artificially corrected) | 007033 | Here height of anemometer to which it is artificially corrected Assumed should be coded with value = 10 metres for PDE buoys |
| 62 | 002169 | Anemometer type | 002169 | e.g. 0=rotor 1=propeller rotor |
| 63 | 002002 | Type of instrumentation for wind measurement | 002002 |  |
| 64 | 008021 | Time significance | 008021 | Value = 2 (time averaged) |
| 65 | 004025 | Time period in minutes | 004025 | Value for averaging period (e.g. 10 minutes) |
| 66 | 011001 | Wind direction | 011001 | Wind direction at 10m (011011) was used with PDE buoys |
| 67 | 011002 | Wind speed | 011002 | Wind speed at 10m (011012) was used with PDE buoys |
| 68 | 008021 | Time significance | 008021 | Value = 23 (monitoring period) |
| 69 | 004025 | Time period in minutes | 004025 | Period during which gust is being monitored prior to observation time |
| 70 | 011043 | Maximum wind gust direction | 011043 |  |
| 71 | 011041 | Maximum wind gust speed | 011041 |  |
| 72 | 008082 | Artificial correction of sensor height to another value (set to missing to reset previous value) | 008082 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor height is not corrected 1=sensor height is artificially corrected 7=missing Here coded with value = “missing” |
| 73 | 007033 | Height of sensor above water surface (set to missing to cancel previous value) | 007033 | Value=”missing”: Redefine height to previous level |
| 74 | 007032 | Height of sensor above marine deck platform (for precipitation measurement) | 007032 | Here height of precipitations |
| 75 | 004024 | Time period in hours | 004024 | Period during which precipitation is being monitored prior to observation time |
| 76 | 013011 | Total precipitation | 013011 | Total precipitation during monitoring period |
| 77 | 007032 | Height of sensor above marine deck platform (set to missing to cancel the previous value) | 007032 | Value = “missing” |
| 78 | 008021 | Time significance | 008021 | Value = 3 (accumulated) |
| 79 | 004024 | Time period in hours | 004024 | Period during which global radiation is being accumulated prior to observation time |
| 80 | 014021 | Global radiation, integrated over period specified | 014021 |  |
| 81 | 008021 | Time significance | 008021 | Value = “missing” |
| 82 | 025028 | Operator or manufacturer defined parameter (#1) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 1 |
| 83 | 025028 | Operator or manufacturer defined parameter (#2) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 2 |
| 84 | 025028 | Operator or manufacturer defined parameter (#3) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 3 |
| 85 | 022073 | Maximum wave height | 022073 |  |
| 86 | 022070 | Significant wave height | 022070 | HsHsHsHs in WAVEOB section 0 |
| 87 | 022074 | Average wave period | 022074 | PaPaPaPa in WAVEOB section 0 |
| 88 | 022076 | Direction from which dominant waves are coming | 022076 | dddd in WAVEOB section 0 |
| 89 | 022077 | Directional spread of dominant waves | 022077 | dsds in WAVEOB section 0 |
| 90 | 022071 | Spectral peak wave period | 022071 | PpPpPpPp in WAVEOB section 0 |
| 91 | 022078 | Duration of wave record | 022078 | D’D’D’D’ in WAVEOB section 1 |
| 92 | 022082 | Maximum non-directional spectral wave density | 022082 | CmCmCm in WAVEOB section 2 |
| 93 | 022084 | Band containing maximum non-directional spectral wave density | 022084 | nmnm in WAVEOB section 2 |
| 94 | 025043 | Wave sampling interval (time) | 025043 | SSSS in WAVEOB (Ia=0) |
| 95 | 025044 | Wave sampling interval (space) | 025044 | SSSS in WAVEOB (Ia=1) |
| 96 | 112000 | Delayed replication of 12 descriptors | 112000 | Replication for frequency bands. PDE buoys did not used delayed replication |
| 97 | 031001 | Replication factor | 031001 | Delayed replication therefore added. Replication factor = Number of frequency bands |
| 98 | 022080 | Waveband central frequency | 022080 | fnfnfn in WAVEOB section 1 |
| 99 | 201134 | Add 6 bits to data width | 201134 |  |
| 100 | 022096 | Spectral band width | 022096 | Here coded with 10 bits as descriptor requires 4 bits and we have 6 bits added due to previous operation descriptor |
| 101 | 201000 | Reset data width to normal | 201000 |  |
| 102 | 022090 | Non-directional spectral estimate by wave frequency | 022090 | AnAnAn in WAVEOB (Ib=0) section 5 |
| 103 | 022086 | Mean direction from which waves are coming | 022086 | da1da1 in WAVEOB section 4 |
| 104 | 022087 | Principal direction from which waves are coming | 022087 | da2da2 in WAVEOB section 4 |
| 105 | 022095 | Directional spread of individual waves | 022095 |  |
| 106 | 022085 | Spectral wave density ratio | 022085 | cncn in WAVEOB section 2 |
| 107 | 022088 | First normalized polar coordinate from Fourier coefficients | 022088 | r1r1 in WAVEOB section 4 |
| 108 | 022089 | Second normalized polar coordinate from Fourier coefficients | 022089 | r2r2 in WAVEOB section 4 |
| 109 | 022092 | Directional spectral estimate by wave frequency | 022092 | AnAnAn in WAVEOB (Ib=1) section 5 |