| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MONTREAL, 8-12 MAY 2006 |  | ET/DR&C/Doc. 5.4(4) _______ ENGLISH ONLY |
| --- | --- | --- |

Proposed BUFR template for Radiosonde data

Submitted by the Secretariat following information from Upper-air systems intercomparison Team

________________________________________________________________

Summary and Purpose of Document

The document contains a template wished for representation of radiosonde data.

________________________________________________________________

ACTION PROPOSED

CBS ET/DRC is invited to discuss the proposed template, possibly suggest changes, and make an adjusted recommendation for radiosonde templates.

This template is wished by manufacturers for production of BUFR information at the observation platform system.

High Resolution Radiosonde BUFR (Land, Ship or Mobile)

| Table Reference | Element Name | Type & Byte Size (Bits) | Comments |
| --- | --- | --- | --- |
|  | Identification of launch site and instrumentation. |  |  |
| 0 | 01 | 001 | WMO Block Number | Numeric | 7 |  |
| 0 | 01 | 002 | WMO Station Number | Numeric | 10 |  |
| 0 | 01 | 011 | Ship or mobile land station identifier | CCITT IA5 | 72 |  |
| 0 | 02 | 011 | Radiosonde Type | Code table | 8 | Code table might need updating |
| 0 | 02 | 013 | Solar and Infrared radiation correction | Code table | 4 | Code table might need updating |
| 0 | 02 | 014 | Tracking technique/status of system used | Code table | 7 | Code table might need updating |
| 0 | 02 | 003 | Type of measuring equipment used | Code table | 4 | Code table might need updating |
| 0 | 25 | 061 | Software identification number | CCITT IA5 | 96 | Text descriptor |
| 0 | 01 | 082 | Radiosonde ascension number | Numeric | 14 |  |
| 0 | 01 | 081 | Radiosonde serial number | CCITT IA5 | 160 |  |
| 0 | 02 | 067 | Radiosonde operating frequency | Hz, Scale-5 | 15 | Frequency at Launch |
| 0 | 02 | 095 | Type of pressure sensor | Code table | 5 |  |
| 0 | 02 | 096 | Type of temperature sensor | Code table | 5 |  |
| 0 | 02 | 097 | Type of humidity sensor | Code table | 5 |  |
| 0 | 02 | 081 | Type of balloon | Code table | 5 |  |
| 0 | 02 | 082 | Weight of balloon | Kg, scale 3 | 12 |  |
| 0 | 02 | 084 | Type of gas used in balloon | Code table | 4 |  |
| ? | ?? | ??? | Geopotential height calculation | Code table | 4 | 1 – from pressure 2 – from GPS Height |
|  |  |  | Date/time of launch |  |  |  |
| 0 | 08 | 021 | Time significance | Code table | 5 | Nominal hour? |
| 0 | 04 | 001 | Year | Year | 12 |  |
| 0 | 04 | 002 | Month 3 01 011 | Month | 4 |  |
| 0 | 04 | 003 | Day | Day | 6 |  |
| 0 | 04 | 004 | Hour | Hour | 5 |  |
| 0 | 04 | 005 | Minute 3 01 013 | Minute | 6 |  |
| 0 | 04 | 006 | Second | Second | 6 |  |
|  |  |  | Horizontal and vertical coordinates of launch site. |  |  |  |
| 0 | 05 | 001 | Latitude (High Accuracy) | Degree | 25 |  |
| 0 | 06 | 001 | Longitude (High Accuracy) | Degree | 26 |  |
| 0 | 07 | 030 | Height of station above MSL | M, scale 1 | 17 |  |
| 0 | 07 | 031 | Height of barometer above MSL | M, scale 1 | 17 |  |
| 0 | 07 | 007 | Height of radiosonde release above MSL | M | 15 |  |
|  |  |  | Surface information reported with vertical sounding |  |  |  |
| 0 | 08 | 002 | Vertical significance (surface obs) | Flag | 6 |  |
| 0 | 10 | 004 | Pressure | Pa, scale -1 | 14 | Need to change scale? |
| 0 | 12 | 101 | Temperature (dry bulb) | K, scale 2 | 16 |  |
| 0 | 13 | 003 | Relative humidity | %, scale 0 | 7 |  |
| 0 | 11 | 001 | Wind Direction | Deg,scale 0 | 9 |  |
| 0 | 11 | 002 | Wind Speed | m/s, scale 1 | 12 |  |
| 0 | 08 | 002 | Vertical significance | Flag | 6 | Cloud Ob |
| 0 | 20 | 011 | Cloud amount ( low or middle Nh) | Code table | 4 |  |
| 0 | 20 | 013 | Height of base of cloud (h) | m, scale -1 | 11 |  |
| 0 | 20 | 012 | Cloud Type (Low) | Code table | 6 |  |
| 0 | 20 | 012 | Cloud Type (Medium) | Code table | 6 |  |
| 0 | 20 | 012 | Cloud Type (High) | Code table | 6 |  |
| 0 | 08 | 002 | Vertical significance (missing values) | Flag | 6 |  |
|  |  |  | Present weather? |  |  |  |
| 0 | 22 | 043 | Sea/water temp (ship stations) | K, scale 2 | 15 |  |
|  |  |  | Vertical sounding data |  |  | *Repeated section* |
| 1 | 01 | 000 | Delayed replication of 1 descriptor |  |  |  |
| 0 | 31 | 002 | Extended delayed descriptor replication factor | Numeric | 16 |  |
| 0 | 04 | 086 | Long time period or displacement (since launch time) | Second | 15 |  |
| 0 | 08 | 042 | Extended vertical sounding significance | Flag table | 18 |  |
| 0 | 10 | 009 | Geopotential height | gpm, scale0 | 17 |  |
| 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) | Degree, Scale 5 | 25 | Displacement or actual? Is resolution too much 5 decimal places? |
| 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) | Degree, Scale 5 | 26 |  |
| 0 | 12 | 101 | Temperature/dry bulb | K, scale 2 | 12 |  |
| 0 | 13 | 003 | Relative Humidity | %, scale 0 | 7 |  |
| 0 | 11 | 001 | Wind direction | Degree true | 9 |  |
| 0 | 11 | 002 | Wind Speed | m/s, scale 1 | 12 |  |