| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS JOINT MEETING OF CT-MTDCF / ET-DRC MONTREAL, 8 - 12 MAY 2006 |  | ET /DRC 6.5(1) ITEM: (2.V.2006) ENGLISH ONLY |
| --- | --- | --- |

## Use of CREX

(Submitted by the Secretariat)

________________________________________________________________

Summary and Purpose of Document

Some information available at the WMO Secretariat is shown.

________________________________________________________________

ACTION PROPOSED

The meeting is asked to take into account this information and make appropriate recommendations.

- CODING OF SQUALL LINES IN WEST AFRICA IN CREX

West African Track and Trajectory CREX Code (WATTCC)

For squall lines observations and forecasted trajectory and evolution:

KTL01 GOOY 231830

# CREX++

T00020412// A007001 P00012000 U00 S001 Y20050823 H1830 D16051++

2005 08 23 17 50 1500 –01000 070 00010 1900 –00840 1100 –01220 02 0038 0300++

7777

T00020412// =	00 = Master table for meteorology

02 = CREX edition number

04 = BUFR edition number

12 = version table of BUFR/CREX

// = No local table

A007001 = 	007 = Synoptic features

001 = Squall Lines

P00012000 =	00012 = Originating Centre = Dakar

###### 000 = No sub-centre

U00 =	00 = Sequence number of message, = 0 = first

S001 =	001 = number of sub-sets in the report = 1

Y20050823 =	Date of the message = year, month, day

H1830 =	Hour of the message = hour, minute

D16050	Common sequence defining Squall line

### Time of observation:

### D01011 Date:

### 2005 	= Year

### 08	= Month

23	= Day

### D01012 Hour:

### 17		= Hour

#### 50	= Minute

Position of Centre:

### B05002 Latitude:

### 1500 =	15 deg. North

B06002 Longitude:

-01000 =	10 deg. West

B19005 Direction of moving feature:

070 =	070 degrees

B19006 Speed of moving feature:

00010 =	10 m/s

Amplitude of feature, from most external point to centre point:

North side:

B05002 Latitude:

1900 =	19 deg. North

B06002 Longitude:

-00840 =	8 deg. 40 West

South side:

## B05002 Latitude:

## 1100 =	11 deg. North

## B06002 Longitude:

## -01220 =	12 deg. 20 West

### B20028 Evolution of feature:

### 02 =	Intensification

### B11041 maximum burst expected:

### 0038 =	38 m/s

B13055 intensity of rain expected:

0300 =	300 mm/h

0 20 028

Expected change in intensity

| Code figure |  |
| --- | --- |
| 0 | Stability |
| 1 | Diminution |
| 2 | Intensification |
| 3 | Unknown |
| 4-14 | Reserved |
| 15 | Missing value |

West African Track and Trajectory CREX Code (WATTCC) type 2

For squall lines (defined with more than 3 points) observations and forecasted trajectory and evolution:

KTL02 GOOY 231830

# CREX++

T00020412// A007001 P00012000 U00 S001 Y20050823 H1830 D16051++

2005 08 23 17 50 1500 –01000 070 00010 0002 1900 –00840 1700 –00940 0001 1100 –01220 02 0038 0300++

7777

T00020412// =	00 = Master table for meteorology

02 = CREX edition number

04 = BUFR edition number

12 = version table of BUFR/CREX

// = No local table

A007001 = 	007 = Synoptic features

001 = Squall Lines

P00012000 =	00012 = Originating Centre = Dakar

###### 000 = No sub-centre

U00 =	00 = Sequence number of message, = 0 = first

S001 =	001 = number of sub-sets in the report = 1

Y20050823 =	Date of the message = year, month, day

H1830 =	Hour of the message = hour, minute

D16051	Common sequence defining Squall line (type 2)

### Time of observation:

### D01011 Date:

### 2005 	= Year

### 08	= Month

23	= Day

### D01012 Hour:

### 17		= Hour

#### 50	= Minute

Position of Centre:

### B05002 Latitude:

### 1500 =	15 deg. North

B06002 Longitude:

-01000 =	10 deg. West

B19005 Direction of moving feature:

070 =	070 degrees

B19006 Speed of moving feature:

00010 =	10 m/s

Amplitude of feature, from most external point to centre point:

North side:

##### R02000 define replication of next 2 descriptors:

##### 0002 =	twice (for 2 points)

First point:

B05002 Latitude:

1900 =	19 deg. North

B06002 Longitude:

-00840 =	8 deg. 40 West

Second point:

B05002 Latitude:

1700 =	17 deg. North

B06002 Longitude:

##### -00940 =	9 deg. 40 West

South side:

##### R02000 define replication of next 2 descriptors:

##### 0001 =	no replication (1 point only)

## B05002 Latitude:

## 1100 =	11 deg. North

## B06002 Longitude:

## -01220 =	12 deg. 20 West

### B20028 Evolution of feature:

### 02 =	Intensification

### B11041 maximum burst expected:

### 0038 =	38 m/s

B13055 intensity of rain expected:

0300 =	300 mm/h

- CODING OF SYNOP IN CREX AT EAMAC (NIAMEY)

Remarks made by Mr Sékou Sienta et Gilles Perret:

Miss examples of coding in CREX.

Questions:

Do not know what code tables are for CREX (not clear?)

Present and Past Weather: why coded with 3 and 2 figures?

Rain coded with //// or 0000?  How to indicate traces?

What about CAVOK, SKC, NSC and NSW of METAR, AND TAF in CREX?  If coded still, how?

Nebulosity: how to convert in %?

See example of attempted coded CREX in the Excel file.

- Use of CREX in RA I

      - In a Region where for a long-time half the countries have still no automated data processing, and where the majority have still manual observations and operators for national concentration:

        - Leased lines

        - SSB

        - Telephone lines

        - Internet

        - Cellular ( Primcel-SMS)

CREX might be the needed intermediate solution if one wants to transmit more accurate parameters and extra and correct meta-data.  Perhaps more explanation for CREX coding is needed in some of the new regulations for TDCF.

(radio,