| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on WIS-GTS Communication Techniques and Structure Toulouse, France, 26-30 May 2008 |  | ET-CTS/Doc. 6.1 (19.V.2008) ____________ ITEM 6 ENGLISH only |
| --- | --- | --- |

STATUS OF IMPLEMENTATION OF THE IMPROVED MTN (IMTN)

(Submitted by the Secretariat)

Summary and purpose of document This document includes current status of the IMTN Project.

ACTION PROPOSED:

The meeting is invited to review the status and to discuss the further development of IMTN.

1.  IMTN project

Most (17 of 25) of the MTN point-to-point circuits have migrated to managed data communication network services.  Two networks were established for the Improved MTN (IMTN), designated as IMTN Network I [Cloud I] and IMTN Network II [Cloud II], and operated by two different providers. However, some legacy links still exist attached to both networks.  Currently, 17 of 25 MTN circuits are operated on these networks (Networks I and II in Figure 1) while 8 are still operated on traditional point-to-point links.  Twelve of 18 MTN centres have joined the two networks.  RTHs Exeter, Tokyo and Moscow are designated gateways for both networks.

2.  Network I

The IMTN Network I (Cloud I) was established in 2003, interconnecting MTN links between Exeter, Melbourne, Tokyo and Washington.  The network has been operating very reliably via the FR network provided by BT Ignite.  Each centre has a contract with each local office of BT Ignite and are billed individually for the local access circuit and incoming CIRs. The backup circuits (PVCs) are paid by the Australian Government (BoM).

The objective of the backup circuits established by the Australian Bureau of Meteorology (BoM) was to connect its Disaster Recovery Site (DRS) located in Brisbane with other centres and create a powerful backup to WMC Melbourne.  Other resilience measures were introduced, including the implementation by Washington, Melbourne and Tokyo of automatic re-routing capabilities, which enabled the redirection of traffic between two centres via the router of the third centre.  Configuration of the IMTN Network I as of September 2007 is shown in Figure 2.

3.  Network II

The IMTN Network II was implemented operationally in 2004 as an extension of the RA VI-RMDCN, the regional telecommunication network for Region VI, initially based on the FR network provided by OBS (Orange Business Service, former EQUANT).  Centres from other Regions were allowed to join RMDCN, including MTN centres Beijing, Jeddah, New Delhi and Tokyo.  In June 2007 the Frame Relay network was replaced by an IP VPN MPLS based network also operated by OBS.  ECMWF continues to play a key role in both the management and operation of the network.  Figure 3 shows the current configuration of the IMTN Network II.

The use of MPLS technology has brought significant flexibility to the exchange of information in Network II and in RA VI RMDCN as a whole since MPLS allows any-to-any connectivity.  While this is a very positive aspect, some precautions should be taken to ensure proper functioning of the GTS at technical and operational levels. The new network shall maintain the agreed level of traffic priorities to fulfil the GTS timeliness requirements and respect, as much as possible, the current GTS hierarchy of centres to avoid disruption of a well established and globally agreed flow of information exchange.

Due to its own nature, MPLS cannot provide the same level of end-to-end traffic control as the point-to-point circuits and the Permanent Virtual Circuits of the Frame Relay networks, so good coordination and efficient network management are extremely important elements of success of GTS MPLS-based networks.

4.  MTN circuits outside IMTN Networks I and II

RTHs Brasilia, Buenos Aires and Moscow were originally planned to join IMTN Network I while RTHs Algiers, Cairo, Dakar and Nairobi would join Network II.  Brasilia, Buenos Aires and Moscow have indicated their willingness to join while Dakar and Nairobi have indicated their preference for other solutions.  No further decision from Algiers is available at this time. The current connections to MTN centres outside the IMTN Networks I and II are as follows:

Algiers - Toulouse:	64 kbps

Dakar - Toulouse:	34.8 kbps

Cairo - Moscow:	64 kbps

Cairo - Nairobi:	9.6 kbps

Cairo - New Delhi	100 bps

Nairobi - Offenbach:	64 kbps

Brasilia - Washington:	64 kbps, IP socket

Buenos Aires - Washington:	64 kbps, IP socket

5.  Additional circuits linking MTN centres

Several additional circuits connect to MTN centres but are not considered MTN circuits.  They are usually included in regional telecommunication networks to improve traffic flow between MTN centres.  The following circuits are functional at present:

Algiers - Cairo:	4.8 kbps

Algiers - Dakar:	50 bps

Algiers - Jeddah:	50 bps

Beijing - Melbourne:	Internet

Beijing - Moscow:	RMDCN IP VPN MPLS

Beijing - New Delhi:	RMDCN IP VPN MPLS

Brasilia - Buenos Aires:	64 kbps

Exeter - Offenbach:	RMDCN IP VPN MPLS

Jeddah - Washington:	Internet

Prague - Toulouse:	RMDCN IP VPN MPLS

Sofia - Toulouse:	RMDCN IP VPN MPLS

Melbourne - Moscow:	Internet (planned, to gain MTN status)

Moscow - Washington:	IP VPN via Internet (planned for 2007, to gain MTN status)

Nairobi - Toulouse:	64 kbps

New Delhi - Melbourne:	Internet

# Text boxes

Figure 1   Main Telecommunication Network (MTN)

Exeter

Sofia

Melbourne

Buenos Aires

Tokyo

Beijing

Nairobi

Washington

Network I

Jeddah

Prague

Toulouse

Dakar

Algiers

Offenbach

Brasilia

Cairo

Managed

data communication network

New Delhi

Moscow

Network II

1.5Mbps

256kbps

256kbps

Primary PVC

BoM Backup PVC

Figure 2   Configuration of IMTN Network I (Frame Relay)

Access line

1.5Mbps

Network  I

256kbps

Exeter

Melbourne

DRS Brisbane

Tokyo

Washington

768k

32k

32k

16k

64k

64k

32k

32k

32k

CIR in kbps

32k,16k

32k

16k

16k

16k

16k

4k

4k

Figure 3   Configuration of IMTN Network II (MPLS)

Network II

(RMDCN IP VPN MPLS)

Moscow

New Delhi

Jeddah

Sofia

Prague

Exeter

Toulouse

Tokyo

Offenbach

Beijing

128 K

128 K

1 M

1 M

2 M

2 M

512

512 K

512 K

512 K

2 M

2 M

2 M

2 M

4 M

2 M

2 M

2 M

128 K

512 K

Access

speed

IP VPN

Port

speed