| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on WIS-GTS Communication Techniques and Structure Toulouse, France, 26-30 May 2008 |  | ISS/ET-CTS 2008/Doc. 2 (1) (8.V.2008) Agenda Item 2&6.3 ENGLISH only |
| --- | --- | --- |

# Status of Implementation at RTH Beijing

(Submitted by Li Xiang, China)

Summary and Purpose of Document This document introduces the current status of implementation of TCP/IP procedures and applications at RTH Beijing.

- Current status of migration to TCP/IP

The current status for the GTS links at RTH Beijing is listed in the table below. The recent changes include a new connection between Beijing and EUMETSAT set up over MPLS VPN and 6 links upgraded in 2007. And, the migration of the only non-IP link, Beijing-Hanoi circuit, is under discussion.

| Link to | Connection type | Speed | Routing protocol | Transmission procedures | Exchanged data | File naming conventions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Offenbach | MPLS VPN (OBS service) | 2Mbps | BGP | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) | Upgraded from FR to MPLS VPN in July, 2007 |
| Tokyo |  |  | BGP | TCP sockets | GTS messages |  |  |
|  |  |  |  | FTP (put) | CMA satellite data (Beijing->Tokyo) | WMO general file naming conventions (pflag=A) |  |
|  |  |  |  | FTP (get) | NESDIS ATOVS data (Tokyo->Beijing) | NESDIS ATOVS data filename convention |  |
| Moscow |  |  | BGP | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) |  |
|  |  |  |  |  | CMA Satellite data (Beijing->Moscow) | WMO general file naming conventions (pflag=A) |  |
| New Delhi |  |  | BGP | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) |  |
| EUMETSAT |  |  | BGP | FTP (put) | Satellite data | Filename conventions used for EUMETCast and FENGYUNCast | Established in July, 2007 |
| Bangkok | Leased line | 64Kbps | BGP | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) | Upgraded from X.25 to IP link in December, 2007 |
| Seoul | Frame Relay | 32/32kbps | BGP | TCP sockets | GTS messages |  |  |
|  |  |  |  | FTP (put) | Observations (Beijing->Seoul) | CMA filename conventions |  |
| Pyongyang | Leased line | 64Kbps | Static | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) | Upgraded from ASYNC to IP link in April, 2007 |

| Link to | Connection type | Speed | Routing protocol | Transmission procedures | Exchanged data | File naming conventions | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ulan Bator | Leased line | 14.4Kbps | Static | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) |  |
|  |  |  |  |  | CMA Satellite data (Beijing->UB) | WMO general file naming conventions (pflag=A) |  |
| Hanoi | Leased line | 75 Baud |  | ASYNC | GTS messages |  |  |
| Melbourne | Internet |  |  | FTP (put) | GTS messages | WMO file naming conventions (for messages existing AHL) |  |
| Almaty | Internet |  |  | Email | GTS messages |  |  |

- GTS Infrastructure

- Use of Internet

3.1 Internet connection

CMA had a dedicated internet connection for exchanging the operational data and TIGGE data. It connects to the local ISP – CSTnet (China Science and Technology Network) through two access lines for redundancy, and with 1Gbps access rate and130Mbps protocol rate.

3.2 Usage of Internet

The operational use of Internet is listed as follows.

|  | Usage | Remarks |
| --- | --- | --- |
| 1 | GTS main | Exchanging GTS messages with RTH Melbourne via ftp Collecting GTS messages from NMC Almaty via Email |
| 2 | GTS backup | Backup the GTS traffic between RTH Beijing and RTH Offenbach |
| 3 | Data collection | Collecting NCEP GFS products from RTH Washington via ftp |
| 4 | TIGGE project | Exchanging TIGGE data with ECMWF and NCAR via LDM |

- Future plan

- Establish backup connection to the MTN links through Internet VPN.

- Upgrade the Beijing-Hanoi GTS connection from the current ASYNC circuit to an IP link.