| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEM & SERVICES Expert Team on WIS-GTS Communication Techniques and Structure (TOULOUSE, France, 26-30 MAY 2008) |  | ET-CTS 2008/Doc. 2(2) (21.V.2008) _____________ ITEM 2(2) ENGLISH only |
| --- | --- | --- |

STATUS OF RTH TOKYO

(Submitted by Tatsuya NOYORI (Japan))

Summary and purpose of document This document includes the report on the status of implementation of telecommunication systems and circuits at RTH Tokyo.

1.  GTS facilities

The Japan Meteorological Agency (JMA) integrated and replaced its Message Switching System (MSS) and the FAX exchange system in 2005 in consideration of expansion and improvement of information exchange with the recent ICT trends, such as TCP/IP, on the GTS.  The new MSS consists of two sub-systems: one is operational and the other is standby.  Each sub-system is a cluster server so as to assure stable operation.

2.  Current status of implementation of the GTS circuits

Current status of GTS circuits connected with the RTH Tokyo is shown in Table 1 and configuration on connectivity is shown in Figure 2.

Table 1   Implementation status of GTS circuits connected with RTH Tokyo (As of 27 April 2007)

| Circuit | Speed | Protocol | Exchange data type |
| --- | --- | --- | --- |
| Washington Tokyo | MTN | FR (IMTN cloud I) Port: WT=1.5 Mbps, TK=1.5 Mbps | TCP/IP Socket FTP (only from WT to TK) | Message (A/N, binary, fax) File (Satellite data) |
|  |  | CIR: WT to TK 768 kbps TK to WT 32 kbps |  |  |
| Melbourne Tokyo | MTN | FR (IMTN cloud I) Port: MB=256 kbps, TK=1.5 Mbps | TCP/IP Socket FTP | Message (A/N, binary, fax) File (Satellite data) |
|  |  | CIR: MB to TK 32 kbps TK to MB 16 kbps |  |  |
| Beijing Tokyo | MTN | MPLS (IMTN cloud II) Port: BJ=2 Mbps, TK=1 Mbps | TCP/IP Socket FTP | Message (A/N, binary, fax) File (Satellite data) |
| New Delhi Tokyo | MTN | MPLS (IMTN cloud II) Port: ND=128 kbps, TK=1 Mbps | TCP/IP Socket | Message (A/N, binary) |
| Bangkok Tokyo | RMTN | FR (NNI basis) Port: BK=128 kbps, TK=192 kbps | TCP/IP Socket | Message (A/N, binary) |
|  |  | CIR: BK to TK 16 kbps TK to BK 16 kbps |  |  |
| Khabarovsk Tokyo | RMTN | Dedicated line 64kbps | TCP/IP Socket | Message (A/N, binary, fax) |
| Seoul Tokyo | RMTN | FR (NNI basis) Port: SL=64 kbps,TK=192 kbps | TCP/IP Socket FTP | Message (A/N, binary, fax) File (Satellite data) |
|  |  | CIR: SL to TK 16 kbps TK to SL 16 kbps |  |  |
| Hong Kong Tokyo | RMTN | FR (NNI basis) Port: HK=64 kbps, TK=192 kbps | TCP/IP Socket FTP (only from TK to HK) | Message (A/N, binary) File (Satellite and one week ensemble data) |
|  |  | CIR: HK to TK 16 kbps TK to HK 16 kbps |  |  |
| Manila Tokyo | Inter-regional | FR (NNI basis) Port: MN=64 kbps, TK=192 kbps | TCP/IP Socket | Message (A/N, binary) |
|  |  | CIR: MN to TK 16 kbps TK ( MN 16 kbps |  |  |

CIR:	Committed Information Rate

FR:	Frame Relay

MPLS:	Multi-Protocol Label Switching

NNI:	Network-to-Network Interconnection

3.   Implementation status of TCP/IP protocol and applications

3.1  TCP/IP

TCP/IP protocol is used on all the GTS circuits connected to the RTH Tokyo.  Simple FTP is used to receive satellite data from Washington, Melbourne and Beijing and to relay subset of them to Melbourne, Beijing, Seoul and Hong Kong.  Products of JMA's one week ensemble forecast model are also distributed to Hong Kong by simple FTP.  Currently, data and products are exchanged in the following manner.

From

Washington:	GET by Tokyo

Melbourne:	PUT by Melbourne with file renaming

Beijing:	PUT by Beijing with file renaming

To

Melbourne:	PUT by Tokyo with file renaming

Beijing:	GET by Beijing

Hong Kong:	PUT by Tokyo with file renaming

Seoul:	PUT by Tokyo with file renaming

GTS file naming convention is used in these file exchange.

The new MSS is also able to receive meteorological messages via e-mail, which is under testing.

The MSS of the RTH Tokyo is applied to batched FTP procedure, which is already used for internal massage switching between servers.

3.2  Routing protocols

Border gateway protocol version 4 (BGP 4) is applied to almost all the TCP/IP circuits connected with the RTH Tokyo except for Khabarovsk-Tokyo and Manila-Tokyo where static routing is applied.  In principal Tokyo advertises all available routing information to BGP neighbours without filtering, while exchange of BGP routes with the Orange Business Service (OBS) router, which interconnects both Tokyo - Beijing and Tokyo - New Delhi as well as RA VI－RMDCN, is limited to a minimum that is necessary for establishing IP connectivity among these two centres and Seoul where re-routing operation is applied.

With growing IP connectivity among GTS centres, there would be a bypass route(s) through a third centre in addition to the direct one.  For making practical use of this feature, Tokyo, Washington and Melbourne started re-routing via the bypass route in case of a failure of the direct link on a triangle of circuits interconnecting these three centers established within IMTN could I in February 2003.  In September 2003 Brisbane joined to the triangle as a Disaster Recovery Site for Melbourne.  In addition, Tokyo, Beijing and Seoul also have a re-routing connection between them.

4.  Use of the Internet

4.1  Internet accessing systems and servers

There are two permanent connections to Internet Service Providers (ISPs), which provide more stable and reliable access to the Internet than the case of one ISP.

All the Internet servers such as JMA's DDB (Distributed Data Base), NEAR-GOOS (North East Asia Regional - Global Ocean Observing System) and WDCGG (World Data Centre for Greenhouse Gases) are placed in DMZ (Demilitarized Zone) for security reasons.  Firewalls are monitored and maintained appropriately with contractual vendor support.

4.2  RSMC Data Serving System

The RSMC Data Serving System (DSS) has been providing NWP products and global observation data to NMHSs mainly in the Asian region through the Internet since 1995.  To meet user requirements in expanding services, JMA replaced the DSS by the new one in October 2005.  The current DSS is a cluster system consists of three servers (Figure 4) in DMZ.  It has been confirmed that the server system based on clustering architecture has enough reliability and maintainability to keep around-the-clock operation, and also cost-effectiveness.

Users can access to the DSS by standard FTP commands with authentication procedures.  The DSS identifies accessing from an authenticated user by a user ID, a user password and an IP address of a client computer.  E-mails are used for communication between the administrator and users of DSS on operational information, such as password change, data to be newly available and so on.

5.  Traffic status of GTS links

Status of each GTS link connected to the RTH Tokyo is as follows.

(a) WMC Washington (MTN)

(b) WMC Melbourne (MTN)

(c)  RTH Beijing (MTN)

(d) RTH New Delhi (MTN)

(e) RTH Khabarovsk (RMTN)

(f)  RTH Bangkok (RMTN)

(g) NMC Hong Kong (RMTN)

(h) NMC Seoul (RMTN)

(i)  NMC Manila (Inter-regional)

# Text boxes

INTERNET

ISP

Domestic network

Private network in Headquarters

RSMC

Data

Serving

System

Servers for

Domestic data exchange

Firewall

Servers for

International data exchange

Router for GTS connections

NAT (Network Address Translation) Router

Management Server

Storage system

Storage system

Other

Data

Distribution

Servers

DMZ

Servers for

Application

Figure 1   GTS facilities and Internet accessing system

Internet

Public servers

(DDB, NEAR-GOOS…)

Load Balancer

20Mbps

20Mbps

Firewalls

Router Controllers

ISP #2 (C&W)

ISP #1 (IIJ)

Manila

Internet accessing system at JMA Headquarters

t

Main components of Operational Telecommunication System

in Kiyose, a satellite city of Tokyo

Pure IP circuits

circuits

Khabarovsk

Fiber-sw

Fiber-sw

Private IP address

Frame Relay Networks

s

202.245.39.0/24

Bangkok

Seoul

Hong Kong

Tokyo

Figure 4    RSMC Data Serving System

64 kbps

64 kbps

64 kbps

Frame Relay Networks

128 kbps

192 kbps

Load balancer

L2SW

L2SW

L2SW

L2SW

DMZ

User Ａ

User Ｂ

Internet

Network

L2SW

64 kbps

L2SW

256 kbps

2 Mbps

1.5 Mbps

1 Mbps

128 kbps

Beijing

OBS

MPLS Network

(IMTN Cloud II)

New Delhi

Washington

BT

FR Network

(IMTN Cloud I)

Melbourne

Storage system

Public Server

Super computer

system

GTS

MSS

Figure 3    Internet accessing systems and servers

Proxy Server

DMZ

RSMC

Data Serving System

JMA Office

Intranet

COSMETS

LAN

JMA Secure Zone

Real-time file

serving system

Satellite IP network system for information common-use

Local

Observatories

DNS, Web, FTP,

Mail servers

Figure 2    Configuration of the GTS circuit connected to the RTH Tokyo

1.5 Mbps