| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 3.1.10(1) _______ (8.III.2007) ENGLISH ONLY |
| --- | --- | --- |

Review of new METAR/SPECI/TAF templates and

related BUFR/CREX B and D descriptors

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for modifications/corrections of B and D descriptors in the new METAR/SPECI/TAF templates and clarification of usage of descriptors for wind speed and maximum wind speed (gusts) taking into account the required unambiguous conversion from TDCF data to TAC data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] Manual on Codes, WMO-No. 306, Volume II.

[3] Amendment 74 to Annex 3 to the Convention on International Civil Aviation

[4] Final Report, Joint Meeting of CT MTDCF and ET DR&C, Montreal, 8 - 12 May 2006

1. Background

Document CT-MTDCF/ET-DR&C/Doc. 5.5(1) submitted to the Joint Meeting CT MTDCF and ET DR&C (Montreal, 8 - 12 May 2006) contained a proposal for new METAR/SPECI/TAF templates and BUFR/CREX B and D descriptors. The Meeting recommended these new sequences and parameters for validation.

In January and February 2007, the correspondence with Mr. James Trew of NetSys International (Pty) Ltd. indicated that significant process of validation of METAR/SPECI/TAF templates had been done by this company, resulting into detection of some deficiencies in the B and D descriptors. During the following e-mail exchange, several points were discussed, among others the problem of unambiguous conversion from TDCF data to TAC data.

2. Proposal for modification of B-descriptors for representation of visibility

Two descriptors were proposed in Montreal for the representation of horizontal visibility [4]:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 060 | Prevailing horizontal visibility | m | 0 | 0 | 10 | m | 0 | 4 |
| 0 20 061 | Minimum horizontal visibility | m | 0 | 0 | 10 | m | 0 | 4 |

These descriptors were not able to express visibility 1100 m and higher, the precision (scale 0) was unnecessarily high and there was no provision for prevailing visibility “10 km and more”. The descriptor 0 20 061 has been already used for “Runway visual range (RVR)”, so 0 20 059 is used for Minimum horizontal visibility now. According to [3], this element cannot exceed 5000 m, and therefore data width of 9 bits and 3 characters is sufficient in BUFR and CREX, respectively.

Newly proposed B-descriptors for prevailing and minimum horizontal visibility with a Note to be added under Class 20:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 060 | Prevailing horizontal visibility (5) | m | -1 | 0 | 10 | m | -1 | 4 |
| 0 20 059 | Minimum horizontal visibility | m | -1 | 0 | 9 | m | -1 | 3 |

- A prevailing visibility value of 10000 m before scaling (after scaling 1000) shall be used to report prevailing visibility 10 km or more.

3. Unambiguous conversion from TDCF data to TAC data

Unambiguous conversion from TDCF data to TAC data is requested by ICAO as well as by many end users.

During the process of testing in the NetSys International, the following problem was identified: if wind speed is reported in m/s and in knots in a BUFR message using both 0 11 002 – Wind speed (m/s) and 0 11 084 Wind speed (knots), then it is not obvious in which unit the wind speed is to be expressed in the back converted TAC data. The same applies to maximum wind speed (gusts). Moreover, the value of wind speed might be expressed even in all three available wind speed units in a BUFR message. To guarantee that the back converted TAC data will be identical with the original TAC data, it is proposed to add two notes under the BUFR Table D, Category 7:

Notes:

- Within 3 07 045, 3 07 048 and 3 07 053, wind speed shall be reported in the same units as in the original TAC data  and:

0 11 083 shall be set to missing, if wind speed is reported in knots or m s-1 in TAC data,

0 11 084 shall be set to missing, if wind speed is reported in km h-1 or m s-1 in TAC data.

- Within 3 07 045, 3 07 048 and 3 07 053, maximum wind speed (gusts) shall be reported in the same units as in the original TAC data and:

0 11 085 shall be set to missing, if maximum wind speed is reported in knots or m s-1 in

TAC data,

0 11 086 shall be set to missing, if maximum wind speed is reported in km h-1 or m s-1 in

TAC data.

Following the Notes (x) an (y), the wind speed (and the maximum wind speed) will be reported only in meters per second in the BUFR message if these parameters are reported in meters per second in the original TAC data.

4. Additional modification of TAF template

Based on comments of Mr Milan Dragosavac (ECMWF), additional specifications of time entries have been introduced to describe precisely the character of the time period of forecast and the time period of the forecast change.

5. Conclusions

The Annex contains the METAR/SPECI/TAF templates and BUFR/CREX B and D descriptors with the proposed modifications, corrections and additions written in blue. If the proposals meet with approval of the meeting, the content of the Annex may replace the current file in the WMO Server.

ANNEX

NEW PROPOSED METAR/SPECI AND TAF TEMPLATES (NOT VALIDATED)

Proposed additions to BUFR Table D

| F X Y | Reference | Element/Sequence name | METAR/SPECI/TAF Code group(s) |
| --- | --- | --- | --- |
|  |  | (Main part of METAR/SPECI), replacing 3 07 011 |  |
| 3 07 045 | 0 01 063 | ICAO location indicator | CCCC |
|  | 0 08 079 | Aviation product status (routine, special) | METAR SPECI COR |
|  | 0 02 001 | Type of station | (AUTO) |
|  | 3 01 011 | Year, month, day | YY |
|  | 3 01 012 | Hour, minute | GGgg |
|  | 3 01 024 | Latitude-longitude (coarse accuracy), height of station |  |
|  | 0 07 032 | Height of sensor above local ground = 10m |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | dndndn |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | dxdxdx |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 083 | Wind speed (km/h) (see Note (x)) | ff |
|  | 0 11 084 | Wind speed (knots) (see Note (x)) | ff |
|  | 0 11 002 | Wind speed (m/s) (see Note (x)) | ff |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 085 | Maximum wind speed (gusts) (km/h) (see Note (y)) | fmfm |
|  | 0 11 086 | Maximum wind speed (gusts) (knots) (see Note (y)) | fmfm |
|  | 0 11 041 | Maximum wind speed (gusts) (m/s) (see Note (y)) | fmfm |
|  | 0 08 054 | Qualifier for wind speed or wind gusts = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = 2m |  |
|  | 0 12 023 | Temperature (Celsius) | T´T´ |
|  | 0 12 024 | Dew point (Celsius) | T´dT´d |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  | 0 10 052 | Altimeter setting (QNH) | PHPHPHPH |
|  | 0 20 009 | General Weather Indicator TAF/METAR | CAVOK |
|  |  | (METAR/SPECI visibility) |  |
| 3 07 046 | 0 20 060 | Prevailing visibility | VVVV or VVVVNDV |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replication (up to 2) |  |
|  | 0 05 021 | Bearing or azimuth (direction of minimum visibility observed) | Dv |
|  | 0 20 059 | Minimum visibility | VNVNVNVN |
|  |  | (METAR/SPECI/TAF clouds), replacing 3 07 015 |  |
| 3 07 047 | 1 05 000 | Delayed replication of 5 descriptor |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 08 002 | Vertical significance |  |
|  | 0 20 011 | Cloud amount | NsNsNs |
|  | 0 20 012 | Cloud type | CC |
|  | 0 20 013 | Height of base of cloud (m) | hshshs |
|  | 0 20 092 | Height of base of cloud (feet) | hshshs |
|  | 0 20 002 | Vertical visibility (m) | VVhshshs |
|  | 0 20 091 | Vertical visibility (feet) | VVhshshs |
|  |  | (Trend type forecast), replacing 3 07 018 |  |
| 3 07 048 | 0 08 016 | Change qualifier for trend type forecast | TTTTT NOSIG |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replications (0, 1 or 2) |  |
|  | 0 08 017 | Qualifier for time of forecast change | TT |
|  | 3 01 012 | Time of change | GGgg |
|  | 1 12 000 | Delayed replication of twelve descriptors |  |
|  | 0 31 000 | Short delayed replication count (0 or 1) |  |
|  | 0 07 032 | Height of sensor above local ground = 10m |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 083 | Wind speed (km/h) (see Note (x)) | ff |
|  | 0 11 084 | Wind speed (knots) (see Note (x)) | ff |
|  | 0 11 002 | Wind speed (m/s) (see Note (x)) | ff |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 085 | Maximum wind speed (gusts) (km/h) (see Note (y)) | fmfm |
|  | 0 11 086 | Maximum wind speed (gusts) (knots) (see Note (y)) | fmfm |
|  | 0 11 041 | Maximum wind speed (gusts) (m/s) (see Note (y)) | fmfm |
|  | 0 08 054 | Qualifier for wind speed or wind gusts = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  | 0 20 009 | General weather indicator | CAVOK NSW NSC SKC |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 000 | Short delayed replication count (0 or 1) |  |
|  | 0 20 060 | Prevailing visibility | VVVV |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 047 | METAR/SPECI/TAF clouds | NsNsNshshshs |
|  |  | (Sea conditions WTsTs/SS’) |  |
| 3 07 049 | 1 02 000 | Delayed replication of 2 descriptors |  |
|  | 0 31 000 | Short delayed replication factor (0 or 1) |  |
|  | 0 22 043 | Sea/water temperature | TsTs |
|  | 0 22 021 | Height of waves | S’ |
|  |  | (Runway state RRRRERERCReReRBRBR) |  |
| 3 07 050 | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 000 | Short delayed replication factor (0 or 1) |  |
|  | 0 20 085 | General condition of runway | SNOCLO |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 01 064 | Runway designator | RRRR |
|  | 0 20 085 | General condition of runway | CLRD// |
|  | 1 05 000 | Delayed replication of 5 descriptors |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 01 064 | Runway designator | RRRR |
|  | 0 20 086 | Runway deposits | ER |
|  | 0 20 087 | Runway contamination | CR |
|  | 0 20 088 | Depth of runway deposits | eReR |
|  | 0 20 089 | Runway friction coefficient | BRBR |
|  |  | (Full METAR/SPECI), replacing 3 07 021 |  |
| 3 07 059 | 3 07 045 | Main part of METAR/SPECI data |  |
|  | 3 07 046 | Visibility | VVVV or VVVVNDV VNVNVNVNDv |
|  | 3 07 013 | Runway visual range | RDRDRVRVRVRVR |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 047 | Clouds | NsNsNshshshs |
|  | 3 07 016 | Recent weather phenomena | REw’w’ |
|  | 3 07 017 | Runway shear | WS RWYDRDR |
|  | 3 07 049 | Sea conditions | WTsTs/SS’ |
|  | 3 07 050 | Runway state | RRRRERCReReRBRBR |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication count (0 to 3 normally) |  |
|  | 3 07 048 | Trend type forecast |  |
|  |  | (Aerodrome forecast identification and time interval) |  |
| 3 07 052 | 0 01 063 | ICAO location identifier | CCCC |
|  | 0 08 039 | Time significance = 0 (Issue time of forecast) |  |
|  | 3 01 011 | Year, Month, Day | YY |
|  | 3 01 012 | Hour, Minute | GGgg |
|  | 0 08 079 | Aviation product status | COR CNL AMD NIL |
|  | 0 08 039 | Time significance = 1 (Time of commencement of period of the forecast) |  |
|  | 3 01 011 | Year, Month, Day | Y1Y1 |
|  | 3 01 012 | Hour, Minute | G1G1 |
|  | 0 08 039 | Time significance = 2 (Time of ending of period of the forecast) |  |
|  | 3 01 011 | Year, Month, Day | Y2Y2 |
|  | 3 01 012 | Hour, Minute | G2G2 |
|  | 3 01 024 | Latitude, Longitude, Height of station |  |
|  |  | (Forecast weather at an aerodrome) |  |
| 3 07 053 | 0 07 032 | Height of sensor above local ground = 10m |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 083 | Wind speed (km/h) (see Note (x)) | ff |
|  | 0 11 084 | Wind speed (knots) (see Note (x)) | ff |
|  | 0 11 002 | Wind speed (m/s) (see Note (x)) | ff |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 085 | Maximum wind speed (gusts) (km/h) (see Note (y)) | fmfm |
|  | 0 11 086 | Maximum wind speed (gusts) (knots) (see Note (y)) | fmfm |
|  | 0 11 041 | Maximum wind speed (gusts) (m/s) (see Note (y)) | fmfm |
|  | 0 08 054 | Qualifier for wind speed or wind gusts = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  | 0 20 009 | General weather indicator | CAVOK NSW NSC SKC |
|  | 0 20 060 | Prevailing visibility | VVVV |
|  | 3 07 014 | Weather | w’w’ |
|  | 3 07 047 | Cloud layer(s) | NsNsNshshshs |
|  |  | (Forecast of extreme temperatures) |  |
| 3 07 054 | 0 07 032 | Height of sensor above local ground = 2m |  |
|  | 0 08 039 | Time significance = 3 (Forecast time of maximum temperature) |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 08 023 | First order statistics = 3 (Minimum) |  |
|  | 0 12 023 | Temperature (Celsius) | TFTF |
|  | 0 08 039 | Time significance = 4 (Forecast time of minimum temperature) |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 08 023 | First order statistics = 2 (Maximum) |  |
|  | 0 12 023 | Temperature (Celsius) | TFTF |
|  | 0 08 023 | First order statistics = missing (to cancel the previous value) |  |
|  | 0 08 039 | Time significance = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  |  | (Change indicator and forecast changes) |  |
| 3 07 055 | 0 33 045 | Probability of following event | C2C2 |
|  | 0 08 016 | Change qualifier for an aerodrome forecast | TTTTTT |
|  | 0 08 039 | Time significance = 5 (Time of beginning of the forecast change) |  |
|  | 0 04 003 | Day |  |
|  | 3 01 012 | Hour, Minute | GGgg |
|  | 0 08 039 | Time significance = 6 (Time of beginning of the forecast change) |  |
|  | 0 04 003 | Day |  |
|  | 3 01 012 | Hour, Minute | GeGe |
|  | 3 07 053 | Forecast conditions during or after change |  |
|  |  | (Aerodrome forecast – full TAF) |  |
| 3 07 056 | 3 07 052 | Identification and time interval |  |
|  | 3 07 053 | Forecast |  |
|  | 3 07 054 | Extreme temperatures forecast |  |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication factor |  |
|  | 3 07 055 | Forecast change |  |

The following notes are proposed to be included under BUFR Table D, Category 7.

Notes:

- Within 3 07 045, 3 07 048 and 3 07 053, wind speed shall be reported in the same units as in the original TAC data  and:

0 11 083 shall be set to missing, if wind speed is reported in knots or m s-1 in TAC data,

0 11 084 shall be set to missing, if wind speed is reported in km h-1 or m s-1 in TAC data.

- Within 3 07 045, 3 07 048 and 3 07 053, maximum wind speed (gusts) shall be reported in the same units as in the original TAC data  and:

0 11 085 shall be set to missing, if maximum wind speed is reported in knots or m s-1 in TAC data,

0 11 086 shall be set to missing, if maximum wind speed is reported in km h-1 or m s-1 in TAC data.

Proposed additions to BUFR/CREX table B.

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Reference | Width | Unit | Scale | Width |
| 0 08 039 | Time significance (Aviation forecast) | Code table | 0 | 0 | 6 | Code table | 0 | 2 |
| 0 08 054 | Qualifier for wind speed or wind gusts | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 11 083 | Wind speed | km h-1 | 0 | 0 | 9 | km h-1 | 0 | 3 |
| 0 11 084 | Wind speed | knot | 0 | 0 | 8 | knot | 0 | 3 |
| 0 11 085 | Maximum wind gust speed | km h-1 | 0 | 0 | 9 | km h-1 | 0 | 3 |
| 0 11 086 | Maximum wind gust speed | knot | 0 | 0 | 8 | knot | 0 | 3 |
| 0 12 023 | Temperature | Celsius | 0 | -99 | 8 | Celsius | 0 | 2 |
| 0 12 024 | Dew point temperature | Celsius | 0 | -99 | 8 | Celsius | 0 | 2 |
| 0 20 059 | Minimum horizontal visibility | m | -1 | 0 | 9 | m | -1 | 3 |
| 0 20 060 | Prevailing horizontal visibility (5) | m | -1 | 0 | 10 | m | -1 | 4 |
| 0 20 085 | General condition of runway | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 20 086 | Runway deposits | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 20 087 | Runway contamination | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 20 088 | Depth of runway deposits | m | 3 | 0 | 12 | m | 0 | 4 |
| 0 20 089 | Runway friction coefficient | Code table | 0 | 0 | 7 | Code table | 0 | 2 |
| 0 20 092 | Height of base of cloud | Feet | -2 | 0 | 10 | Feet | -2 | 3 |
| 0 20 091 | Vertical visibility | Feet | -2 | 0 | 10 | Feet | -2 | 3 |

The following Note (5) is proposed to be included under Class 20:

- A prevailing visibility value of 10000 m before scaling (after scaling 1000) shall be used to report prevailing visibility 10 km or more.

Proposed additions to BUFR Code/Flag tables

| 0 08 039 |
| --- |
| Time significance (Aviation forecast) |
| Code figure |  |
| 0 | Issue time of forecast |
| 1 | Time of commencement of period of the forecast |
| 2 | Time of ending of period of the forecast |
| 3 | Forecast time of maximum temperature |
| 4 | Forecast time of minimum temperature |
| 5 | Time of beginning of the forecast change |
| 6 | Time of ending of the forecast change |
| 7…62 | Reserved |
| 63 | Missing |
| 0 08 054 |
| Qualification of wind speed or wind gusts |
| 0 | Wind speed or gust is as reported |
| 1 | Wind speed is greater than that reported (P in METAR/TAF/SPECI) |
| 2…6 | Reserved |
| 7 | Missing |
| 0 20 086 |
| Runway deposits |
| Code figure |  |
| 0 | Clear and dry |
| 1 | Damp |
| 5 | Wet snow |
| 6 | Slush |
| 7 | Ice |
| 8 | Compacted or rolled snow |
| 9 | Frozen ruts or ridges |
| 10-14 | Reserved |
| 15 | Missing or not reported |

Proposed additions to BUFR Code table 0 08 079

| 0 08 079 |
| --- |
| Product status |
| Code figure |  |
| 6 | Special report (SPECI) |
| 7 | Corrected special report (SPECI COR) |
| 8…14 | Reserved |
| 15 | Missing or not applicable |