| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 3.1.5(1) _______ (10.IV.2007) ENGLISH ONLY |
| --- | --- | --- |

New Descriptors for GHRSST data

Submitted by Stan Kellett and John Stark (UK Met Office)

________________________________________________________________

Summary and Purpose of Document

New descriptors to be used for exchanging GHRSST data

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

# 1. Background

The Global Ocean Data Assimilation Experiment (GODAE) high-resolution sea surface temperature pilot project (GHRSST-PP) provides a new generation of global high-resolution (<10km) SST  data products to the operational oceanographic, meteorological, climate and general scientific community, in near real time and delayed mode. The project involves a wide range of international participants who have invested a great deal in delivering high quality SST products.

There is a requirement to exchange GHRSST data between operational centers in a WMO standard format. Although the GHRSST standard product is delivered in NetCDF, and is being converted to BUFR at the Met Office for operational use. This necessitates the use of suitable descriptors for the exchange of this data.

This document was submitted last year in Montreal and was rejected as the document needed to pick some descriptors and required some corrections. This is the document that was subsequently passed round the ETDRC group via email and accepted. These descriptors are now being used operationally at the UK Met Office.

# 2. Proposal

The proposal is for the group to agree on descriptors for the following to be used when exchanging GHRSST data:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 25 037 | SST bias | K | 2 | -127 | 8 | K | 2 | 3 |
| 0 14 035 | Solar Radiation Flux | W/M2 | 1 | 0 | 14 |  |  |  |
| 0 25 022 | GHRSST Rejection Flag | Flag table | 0 | 0 | 9 |  |  |  |
| 0 25 023 | GHRSST Confidence Flag | Flag table | 0 | 0 | 9 |  |  |  |
| 0 25 024 | GHRSST data quality. | Code table | 0 | 0 | 4 |  |  |  |
| 0 01 028 | Aerosol optical Depth (AOD) source | Code table | 0 | 0 | 5 |  |  |  |
| 0 01 024 | Wind Speed source | Code Table | 0 | 0 | 5 |  |  |  |
| 0 01 029 | SSI Source | Code Table | 0 | 0 | 5 |  |  |  |
| 0 01 038 | Source of Sea Ice Fraction | Code Table | 0 | 0 | 5 |  |  |  |
| 0 25 038 | Difference between SST and analysis | K | 1 | -127 | 8 | K | 1 | 3 |
| 0 22 046 | Sea Ice Fraction | Numeric | 2 | 0 | 7 |  |  |  |

Table 1. Proposed BUFR and CREX codes.

0 25 022 - GHRSST Rejection Flag

| Bit No. |  |
| --- | --- |
| 1 | Unprocessed |
| 2 | Land suspected. |
| 3 | Wind speed too large |
| 4 | Ice detected. |
| 5 | Rain detected (Microwave retrievals only) |
| 6 | Cloudy detected (Infra-red retrievals only) |
| 7 | Cosmetic value |
| 8 | SST out of range |
| All 9 | Missing value |

0 25 023 - GHRSST Confidence Flag

| Bit No. |  |
| --- | --- |
| 1 | Default confidence value has been used. |
| 2 | Default bias and standard deviation has been used. |
| 3 | Sun glint suspected |
| 4 | Sea ice retrieval for microwave data |
| 5 | High wind speed retrieval |
| 6 | Inaccurate SST due to low SST (< 285K). (Only applies to the TMI instrument). |
| 7 | Relaxed rain contamination suspected |
| 8 | Potential side lobe contamination |
| All 9 | Missing value |

0 25 024 – GHRSST proximity confidence.

| Code figure |  |
| --- | --- |
| 0 | Unprocessed infrared retrieval |
| 1 | Cloudy retrievals. |
| 2 | Bad: Data that are probably contaminated by cloud. |
| 3 | Suspect data. |
| 4 | Acceptable data. |
| 5 | Excellent data. |
| 6 | Cool skin suspected. |
| 7-9 | Reserved |
| 10 | Unprocessed microwave retrieval. |
| 11 | Questionable microwave retrieval that may be contaminated. |
| 12 | Acceptable microwave retrieval. |
| 13 | High probability of diurnal variability. |
| 14 | Reserved |
| 15 | Missing value |

0 01 028 - Aerosol optical Depth (AOD) source

| Code figure |  |
| --- | --- |
| 0 | No AOD data available |
| 1 | NESDIS |
| 2 | NAVOCEANO |
| 3 | NAAPS |
| 4 | MERIS |
| 5 | AATSR |
| 6-30 | Reserved for future use |
| 31 | Missing value |

0 01 024 - Wind Speed source

| Code figure |  |
| --- | --- |
| 0 | No wind speed data available |
| 1 | AMSR-E data |
| 2 | TMI data |
| 3 | NWP: ECMWF |
| 4 | NWP: UK Met Office |
| 5 | NWP: NCEP |
| 6 | Reference climatology |
| 7 | ERS_Scatterometer |
| 8-30 | Reserved for future use |
| 31 | Missing value |

0 01 029 - SSI Source

| Code figure |  |
| --- | --- |
| 0 | No SSI data available |
| 1 | MSG_SEVIRI |
| 2 | GOES East |
| 3 | GOES West |
| 4 | ECMWF |
| 5 | NCEP |
| 6 | UK Met Office |
| 7-30 | Reserved for future use |
| 31 | Missing value |

0 01 038 - Source of Sea Ice Fraction

| Code figure |  |
| --- | --- |
| 0 | No sea ice set |
| 1 | NSIDC SSM/I Cavalieri et al (1992) |
| 2 | AMSR-E |
| 3 | ECMWF |
| 4 | CMS (France) cloud mask used by Medspiration |
| 5 | EUMETSAT OSI-SAF |
| 6-30 | Reserved for future use |
| 31 | Missing value |

Table of Acronyms

| Acronym | Expansion |
| --- | --- |
| AATSR | Advanced Along-Track Scanning Radiometer. |
| AMSR-E | Advanced Microwave Scanning Radiometer. |
| AOD | Aerosol optical depth. |
| BUFR | Binary Universal Form for the Representation of meteorological data. |
| CMS | Centre de Meteorologie Spatiale (Lannion, France). |
| CREX | Character form for the Representation and Exchange of meteorological and other data. |
| ECMWF | European Centre for Medium-range Weather Forecasts. |
| ERS | European Remote-sensing Satellite. |
| EUMETSAT | European organization for the exploitation of meteorological satellites. |
| GHRSST-PP | GODAE High Resolution Sea Surface Temperature Pilot Project. |
| GODAE | Global Ocean Data Assimilation Experiment. |
| GOES | Geostationary Operational Environment Satellite. |
| IR | Infra-red. |
| MERIS | Medium Resolution Imaging Spectrometer. |
| MSG | Meteosat Second Generation. |
| MW | Microwave. |
| NAAPS | Navy Aerosol Analysis and Prediction System. |
| NAVOCEANO | Naval Oceanographic Office (United States of America). |
| NCEP | National Centers for Environmental Prediction. |
| NESDIS | National Environmental Satellite, Data, and Information Service. (United States of America). |
| NWP | Numerical weather prediction. |
| OSI-SAF | Ocean and Sea Ice Satellite Applications Facility. |
| RF | Radio frequency. |
| SEVIRI | Spinning Enhanced Visible and Infrared Imager |
| SSI | Surface Solar Irradiance. |
| TMI | Tropical Rainfall Measuring Mission (TRMM) Microwave Imager. |