| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 3.1.6(1) _______ (14.III.2007) ENGLISH ONLY |
| --- | --- | --- |

BUFR template for representation of SYNOP data

and surface observations from one-hour period

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a revised version of BUFR template suitable for reporting both SYNOP data and surface observations from one-hour period, in particular at the national level.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Final Report, ET DR&C and CT MTDCF, Montreal, 8 – 12 May 2006

[3] Final Report, Commission for Basic Systems, Extraordinary Session, Seoul, Republic of

Korea, 9 to 16 November 2006

1. Background

At the Joint meeting of ET DR&C and CT MTDCF (Montreal, 8 – 12 May 2006), a proposal for a BUFR template, blending the current AWS and SYNOP BUFR templates was submitted by Mr Michel Leroy, the representative of EUMETNET. As stated in [2]: “The Meeting considered that this template needed review and Dr Eva Červená accepted to contact the producers of this template to fix with them the points needing improvements.”

As requested, the combined AWS-SYNOP template was revised in June 2006 and sent to the authors of the submitted proposal with explanations of the modifications done (shown in the Annex). No objections with regard to the revised form of the template have been received, and therefore it may be supposed that the authors of the original template have accepted the introduced changes.

2. Usage of the proposed template and its consequences

The Joint meeting of ET DR&C and CT MTDCF recognized that there was a recommended set of templates to convert traditional observations into BUFR. The Meeting accepted the possibility of different templates, but warned that a proliferation of such templates should not be a good idea, although BUFR decoders will be able to extract fully the required parameters for the applications. The handling of the data is much slower and more complicated if the content of the BUFR Data Section is not described by a common sequence descriptor.

The proposed combined AWS-SYNOP template is suitable in particular for transmission of data from the observing stations to the National Meteorological Centre (NMC), because one BUFR message can contain both SYNOP data and the surface observations from one-hour period. These single-subset messages will have to be decoded in the NMC prior to producing the multi-subset BUFR messages for the international exchange.

Two approaches may be used in the NMC:

- The expanded data may be encoded into two BUFR messages, one of them containing the SYNOP data using the template TM 307080 (or any of the regional templates TM 307081 to TM 307086), the other containing the surface observations from one-hour period using the proposed template TM 307091 (after its validation). No further action is needed in this case.

- If the expanded data are to be encoded using this combined AWS-SYNOP template for the international exchange, a new data sub-categories will have to be defined for this type of data and, consequently also new telecommunication  headers for the BUFR messages. It might be also useful to appoint a common sequence descriptor for this template to ease the data handling. In this case, however, some additional modifications may be needed, e.g. to replace the “Extreme temperature” part that is marked yellow in the Annex, by 3 02 077 (the one-hour extreme temperatures) and 3 02 041 (SYNOP extreme temperatures), as suggested in the attached comments.

ANNEX

“MERGED” BUFR TEMPLATE FOR SURFACE OBSERVATIONS FROM ONE-HOUR PERIOD AND FOR REPORTING SYNOP DATA IN BUFR (REVISED, JUNE 2006)

This template is proposed to be used for representation of surface observation data from both automatic stations and manned stations.  This template is also suitable for SYNOP observation data, by including parameters covering periods longer than one hour.

Descriptors used by both templates are not marked.

Descriptors used from the SYNOP BUFR template TM 307080 are indicated by an asterisk *.

Descriptors used from the AWS BUFR template are indicated by an asterisk *.

| 3 01 090 |  |  | 3 07 080 | AWS | Surface station identification; time, horizontal and vertical co-ordinates |
| --- | --- | --- | --- | --- | --- |
|  | 3 01 004 |  |  |  | Surface station identification |  |
|  |  | 0 01 001 |  |  | WMO block number | Numeric |
|  |  | 0 01 002 |  |  | WMO station number | Numeric |
|  |  | 0 01 015 |  |  | Station or site name | CCITT IA5 |
|  |  | 0 02 001 |  |  | Type of station | Code table |
|  | 3 01 011 | 0 04 001 |  |  | Year | Year |
|  |  | 0 04 002 |  |  | Month | Month |
|  |  | 0 04 003 |  |  | Day | Day |
|  | 3 01 012 | 0 04 004 |  |  | Hour | Hour |
|  |  | 0 04 005 |  |  | Minute | Minute |
|  | 3 01 021 | 0 05 001 |  |  | Latitude (high accuracy) | Degree, scale 5 |
|  |  | 0 06 001 |  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 |  |  |  | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 |  |  |  | Height of barometer above mean sea level | m, scale 1 |
| 0 08 010 |  |  |  |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  |  |  | * | Surface station instrumentation |  |
|  | 0 02 180 |  |  | * | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 |  |  | * | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 |  |  | * | Visibility measurement system | Code table, 0 |
|  | 0 02 183 |  |  | * | Cloud detection system | Code table, 0 |
|  | 0 02 184 |  |  | * | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 |  |  | * | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 |  |  | * | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 |  |  | * | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 |  |  | * | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 |  |  | * | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 031 |  |  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 |  |  | Pressure | Pa, scale –1 |
|  |  | 0 10 051 |  |  | Pressure reduced to mean sea level | Pa, scale –1 |
|  |  | 0 10 061 |  |  | 3-hour pressure change | Pa, scale –1 |
|  |  | 0 10 063 |  |  | Characteristic of pressure tendency | Code table, 0 |
|  | 0 10 062 |  | * |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  |  |  | Pressure (standard level) | Pa, scale –1 |
|  | 0 10 009 |  |  |  | Geopotential height of the standard level | gpm, 0 |
| 3 02 072 |  |  |  |  | Temperature and humidity data |  |
|  | 0 07 032 |  |  |  | Height of sensor above local ground | m, scale 2 |
|  | 0 07 033 |  |  | * | Height of sensor above water surface | m, scale 1 |
|  | 0 12 101 |  |  |  | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 12 103 |  |  |  | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 13 003 |  |  |  | Relative humidity | %, 0 |
| 1 01 005 |  |  |  | * | Replicate one descriptor five times |  |
| 3 07 063 | 0 07 061 |  |  | * | Depth below land surface | m, scale 2 |
|  | 0 12 130 |  |  | * | Soil temperature (scale 2) | K, scale 2 |
| 3 02 069 |  |  |  |  | Visibility data |  |
|  | 0 07 032 |  |  |  | Height of sensor above local ground | m, scale 2 |
|  | 0 07 033 |  |  | * | Height of sensor above water surface | m, scale 1 |
|  | 0 33 041 |  |  | * | Attribute of following value | Code table |
|  | 0 20 001 |  |  |  | Horizontal visibility | m, scale –1 |
| 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
| 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, scale 1 |
| 0 20 031 |  |  |  | * | Ice deposit (thickness) | m, scale 2 |
| 0 20 032 |  |  |  | * | Rate of ice accretion | Code table, 0 |
| 0 02 038 |  |  |  | * | Method of sea surface temperature measurement | Code table, 0 |
| 0 22 043 |  |  |  | * | Sea/water temperature (scale 2) | K, scale 2 |
| 3 02 021 | 0 22 001 |  |  | * | Direction of waves | Degree true |
|  | 0 22 011 |  |  | * | Period of waves | s, scale 0 |
|  | 0 22 021 |  |  | * | Height of waves | m, scale 1 |
| 3 02 078 |  |  |  |  | State of ground and snow depth measurement |  |
|  | 0 02 176 |  |  | * | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 |  |  |  | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 |  |  | * | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 |  |  |  | Total snow depth | m, scale 2 |
| 0 12 113 |  |  | * |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, scale2 |
|  |  |  |  |  | Cloud data |  |
| 3 02 004 | 0 20 010 |  |  |  | Cloud cover (total) | %, scale 0 |
|  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | * |  | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  | 0 20 013 |  | * |  | Height of base of cloud h | m, –1 |
|  | 0 20 012 |  | * |  | Cloud type (low clouds CL) CL | Code table, 0 |
|  | 0 20 012 |  | * |  | Cloud type (middle clouds CM) CM | Code table, 0 |
|  | 0 20 012 |  | * |  | Cloud type (high clouds CH) CH | Code table, 0 |
| 1 05 004 |  |  |  | * | Replicate 5 descriptors four times |  |
| 0 08 002 |  |  |  |  | Vertical significance | Code table, 0 |
| 0 20 011 |  |  |  |  | Cloud amount | Code table, 0 |
| 0 20 012 |  |  |  |  | Cloud type | Code table, 0 |
| 0 33 041 |  |  |  | * | Attribute of following value | Code table, 0 |
| 0 20 013 |  |  |  |  | Height of base of cloud | m, scale -1 |
|  |  |  | * |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | * |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | * |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | * |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | * |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | * |  | Cloud top description Ct | Code table, 0 |
|  |  |  | * |  | Direction of cloud drift 6DLDMDH |  |
| 3 02 047 | 1 02 003 |  | * |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | * |  | Vertical significance (7= low cloud, 8= middle cloud, 9 = high cloud) | Code table, 0 |
|  | 0 20 054 |  | * |  | True direction from which clouds are moving DLDMDH | Degree true, 0 |
| 0 08 002 |  |  | * |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | * |  | Direction and elevation of cloud 57CDaeC |  |
| 3 02 048 | 0 05 021 |  | * |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | * |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | * |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | * |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | * |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  |  |  | Present and past weather |  |
| 0 20 003 |  |  |  |  | Present weather (See Note 3) | Code table, 0 |
| 1 03 002 |  |  |  |  | Replicate 3 descriptors 2 times |  |
| 0 04 025 |  |  |  |  | Time period (= - 60 minutes in the first replication, -x minutes in the second replication, corresponding to the duration of the period W1W2 in the SYNOP report) | Minute, 0 |
| 0 20 004 |  |  |  |  | Past weather (1) | Code table, 0 |
| 0 20 005 |  |  |  |  | Past weather (2) | Code table, 0 |
| 3 02 075 |  |  |  | * | Intensity of precipitation, size of precipitation element |  |
|  | 0 08 021 |  |  | * | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 055 |  |  | * | Intensity of precipitation | kg m-2s-1,scale 4 |
|  | 0 13 058 |  |  | * | Size of precipitation element | m, scale 4 |
|  | 0 08 021 |  |  | * | Time significance (= missing value) | Code table, 0 |
| 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
| 3 02 076 |  |  |  | * | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 |  |  | * | Type of precipitation | Flag table, 0 |
|  | 0 20 022 |  |  | * | Character of precipitation | Code table, 0 |
|  | 0 26 020 |  |  | * | Duration of precipitation (See Note 4) | Minute, 0 |
|  | 0 20 023 |  |  | * | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 |  |  | * | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 |  |  | * | Obscuration | Flag table, 0 |
|  | 0 20 026 |  |  | * | Character of obscuration | Code table, 0 |
| 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
| 0 13 059 |  |  |  | * | Number of flashes | Numeric, 0 |
|  |  |  |  |  | Wind data |  |
| 0 07 032 |  |  |  |  | Height of sensor above local ground | m, scale 2 |
| 0 07 033 |  |  |  |  | Height of sensor above water surface | m, scale 1 |
| 0 08 021 |  |  |  |  | Time significance (= 2 (time averaged)) | Code table, 0 |
| 0 04 025 |  |  |  |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind, if any) | Minute, 0 |
| 0 11 001 |  |  |  |  | Wind direction | Degree true, 0 |
| 0 11 002 |  |  |  |  | Wind speed | m s-1, scale 1 |
| 0 08 021 |  |  |  |  | Time significance (= missing value) | Code table, 0 |
| 1 03 003 |  |  |  |  | Replicate next 3 descriptors 3 times |  |
| 0 04 025 |  |  | * |  | Time period (= - 10 minutes in the first replication, = - 60 minutes in the second replication = - 60*3 or 60*6 minutes in the third replication) | Minute, 0 |
| 0 11 043 |  |  |  |  | Maximum wind gust direction | Degree true, 0 |
| 0 11 041 |  |  |  |  | Maximum wind gust speed | m s-1, scale 1 |
| 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
| 0 11 016 |  |  |  | * | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
| 0 11 017 |  |  |  | * | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
|  |  |  |  |  | Extreme temperature data |  |
| 0 07 032 |  |  |  |  | Height of sensor above local ground | m, scale 2 |
| 0 07 033 |  |  |  | * | Height of sensor above water surface | m, scale 1 |
| 1 06 002 |  |  |  |  | Replicate 6 descriptors 2 times |  |
| 0 04 024 |  |  | * |  | Time period or displacement (= - 1 hour in the first replication, = - 12 or - 24 or – x hours in the second replication) | Hour, 0 |
| 0 04 024 |  |  | * |  | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
| 0 12 111 |  |  |  |  | Maximum temperature (scale 2) at height and over period specified | K, scale 2 |
| 0 04 024 |  |  | * |  | Time period or displacement (= - 1 hour in the first replication, = - 12 or - 24 or – x hours in the second replication) | Hour, 0 |
| 0 04 024 |  |  | * |  | Time period or displacement (see Note 2) | Hour, 0 |
| 0 12 112 |  |  |  |  | Minimum temperature (scale 2) at height and over period specified | K, scale 2 |
| 0 07 032 |  |  |  | * | Height of sensor above local ground (for ground temperature) | m, scale 2 |
| 0 04 025 |  |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
| 0 12 112 |  |  |  | * | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, scale 2 |
| 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, scale 1 |
|  |  |  |  |  | Precipitation measurement |  |
| 0 07 032 |  |  |  |  | Height of sensor above local ground | m, scale 2 |
| 0 02 175 |  |  |  | * | Method of precipitation measurement | Code table, 0 |
| 0 02 178 |  |  |  | * | Method of liquid water content measurement of precipitation | Code table, 0 |
| 1 02 004 |  |  |  |  | Replicate 2 descriptors 4 times |  |
| 0 04 024 |  |  |  |  | Time period in hours tR (= - 1 hour in the first replication, = - 3, -6, -12 or - 24 hours in the next replications) | Hour, 0 |
| 0 13 011 |  |  |  |  | Total precipitation / total water equivalent of snow | kg m-2, scale 1 |
| 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
|  |  |  |  |  | Evaporation measurement |  |
| 0 02 185 |  |  |  | * | Method of evaporation measurement | Code table, 0 |
| 1 01 002 |  |  |  |  | Replicate 1 descriptor 2 times |  |
| 3 02 044 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in the first replication, = -24 hours in the second replication) | Hour, 0 |
|  | 0 02 004 |  | * |  | Type of instrument for evaporation measurement or type of crop | Code table, 0 |
|  | 0 13 033 |  |  |  | Evaporation /evapotranspiration | kg m-2, scale 1 |
|  |  |  |  |  | Total sunshine data |  |
| 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
| 3 02 039 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in the first replication, = -x hours in the second replication) | Hour, 0 |
|  | 0 14 031 |  |  |  | Total sunshine | Minute, 0 |
|  |  |  |  |  | Radiation data |  |
| 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
| 3 02 045 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in the first replication, = -24 hours in the second replication) | Hour, 0 |
|  | 0 14 002 |  |  |  | Long-wave radiation, integrated over period specified | J m-2, scale -3 |
|  | 0 14 004 |  |  |  | Short-wave radiation, integrated over period specified | J m-2, scale -3 |
|  | 0 14 016 |  |  |  | Net radiation, integrated over period specified | J m-2, scale -4 |
|  | 0 14 028 |  |  |  | Global solar radiation (high accuracy), integrated over period specified | J m-2, scale -2 |
|  | 0 14 029 |  |  |  | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, scale -2 |
|  | 0 14 030 |  |  |  | Direct solar radiation (high accuracy), integrated over period specified | J m-2, scale -2 |
| 3 02 046 |  |  | * |  | Temperature change gr. 54g0sndT |  |
|  | 0 04 024 |  | * |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | * |  | Time period or displacement (see Note 5) | Hour, 0 |
|  | 0 12 049 |  | * |  | Temperature change over period specified sndT | K, 0 |
| 3 02 083 |  |  |  | * | First order statistics of P, W, T, U data |  |
|  | 0 04 025 |  |  | * | Time period (= -10 minutes ) | Minute, 0 |
|  | 0 08 023 |  |  | * | First order statistics (= 9 (best estimate of standard deviation)) (see Note 6) | Code table, 0 |
|  | 0 10 004 |  |  | * | Pressure | Pa, scale –1 |
|  | 0 11 001 |  |  | * | Wind direction | Degree true, 0 |
|  | 0 11 002 |  |  | * | Wind speed | m s-1, scale 1 |
|  | 0 12 101 |  |  | * | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 13 003 |  |  | * | Relative humidity | %, 0 |
|  | 0 08 023 |  |  | * | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  |  |  | * | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  |  |  | * | Internal measurement status information (AWS) | Code table, 0 |

Notes:

1) Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2) Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3) Present weather shall be always represented by 0 20 003. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should be used, when applicable.

4) Duration of precipitation represents number of minutes in which precipitation was registered.

5) To construct the required time range, descriptor 004024 has to be included two times.

6) Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

Comments (written in June 2006 and the template modified accordingly):

- Reporting of SYNOP Section 3 cloud data is mandatory if the data are available. The meaning of the question “Useful considering the following Cloud layers?” is not quite clear.

- Present weather in the combined AWS-SYNOP template has to be always represented using code table 0 20 003.

- Past weather data in the combined AWS-SYNOP template have to be able to represent not only past weather from the previous 1 hour, but also past weather from period required by Regulations 12.2.6.6.1 and 12.2.6.7.1 (B/C 1.10.1.7.1 and B/C 1.10.1.8.1). Using time period in hour would be preferable.

- The time period for maximum and for minimum temperatures may differ, therefore the each of them has to be preceded by its own <0 04 024, 0 04 024>. Consequently, the proposed replication 1 04 002 should be 1 06 002.

- The part of the template, marked in yellow, might be better replaced by 3 02 077 (the one-hour extreme temperatures) and 3 02 041 (SYNOP extreme temperatures).

- Number of different required time periods, from which amount of precipitation is reported, shall never exceed 4, corresponding to tR in the group 6 in  Section 1,  tR in the group 6 in  Section 3, 24 hours (group 7 in  Section 3) and one hour from the AWS template. Therefore, 1 02 004 is sufficient.

- Type of instrument for evaporation measurement or type of crop 0 02 004 is required for reporting SYNOP data in BUFR.

- Radiation data are described by 1 descriptor 3 02 045. These data are required from one hour and 24 hour period. Therefore, 3 02 045 is to be replicated twice (not three times).

- Cloud bases below station level, ice deposit, sea/water temperature and waves are parameters of instantaneous character and they cannot be placed at the end of the template. Additional parameters required by regional or national reporting practices shall be accommodated as described in B/C1 - Regulations for reporting SYNOP data in TDCF.

- If this template is used only for transmission from the stations to the NMC, certain reduction is possible, e.g. 3 02 047 or 3 02 048 may be omitted from the template in not needed.

- It is to be considered that nominal values are required for some variables from the AWS template.