| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 3.1.7(1) _______ (2.III.2007) ENGLISH ONLY |
| --- | --- | --- |

AWS templates with

national and WMO station identification

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for representation of national AWS identification and reduction of the volume of AWS BUFR messages.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Final Report, Commission for Basic Systems, Extraordinary Session, Seoul, Republic of Korea,

9 to 16 November 2006

1. Background

The existing international system of station numbers is not sufficient for automatic weather stations and BUFR descriptors 0 01 001 (WMO block number) and 0 01 002 (WMO station number) merely reflect this fact. This international numbering system cannot be changed without the approval of the relevant WMO authorities.

Some WMO Member States are using national station numbers to identify their AWSs. To allow representation of these national station numbers, the introduction of a new numbering system is proposed. This system, represented by 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number), will allow each WMO Member State to accommodate up to 999999 stations. This system shall be fully independent of, completely separated from the WMO international numbering system represented by 0 01 001 (WMO block number) and 0 01 002 (WMO station number). It is proposed to introduce the national identification for all stations, including the stations that are identified by the WMO international numbers.

Extraordinary Session of the Commission for Basic Systems recommended “... with regard to AWS, minimizing the actual data transmission such as: (a) Variables measured; (b) Instruments used; (c) Data procedures used; and (d) Data QC procedures used;” [2].

The submitted proposal has been developed taking into consideration the outcome of the discussion with members of ET- AWS, ET- DR&C and CT- MTDCF, in particular Messrs M. Dragosavac (ECMWF), S. Kellett (UK), M. Leroy (France), J. W. Noteboom (Netherlands), J. M. Rezende (Brazil), M. Weis (IBL Software Engineering) and I. Zahumenský (Slovakia).

2. Proposed new descriptors

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 01 101 | WMO Member State identifier | Code table | 0 | 0 | 10 | Code table | 0 | 3 |
| 0 01 102 | National AWS number | Numeric | 0 | 0 | 20 | Numeric | 0 | 6 |

Proposal for the Code table 0 01 101 is included in the Annex to this document.

| Table reference | Table reference | Element name |
| --- | --- | --- |
| 3 01 089 |  | National station identification |
|  | 0 01 101 | WMO Member State identifier |
|  | 0 01 102 | National AWS number |

| Table reference | Table reference | Element name |
| --- | --- | --- |
| 3 07 091 | See paragraph 3 below | AWS BUFR template for surface observations from one-hour period with national and WMO station identification |
| 3 07 092 | See paragraph 4 below | AWS BUFR template for surface observations from n-minute period with national and WMO station identification |
| 3 07 093 | See paragraph 5 below | Nominal values |

3. AWS BUFR template for surface observations from one-hour period

Sequence descriptor 3 07 091 is proposed to be used for representation of AWS BUFR template for surface observations from one-hour period with national and WMO station identification.

This template shall be used for representation of surface observation data from automatic and manned stations using the national numbering system. The WMO international identification  0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station. The text written in blue corresponds to the proposal for the representation of national AWS numbers.

If the national numbering system has not yet been introduced by the WMO Member State, the existing AWS template for surface observations from one-hour period, available at:

http://www.wmo.int/web/www/WMOCodes/MigrationTDCF/ExamplesotherTemplates.htm

may be used until the national identification system is implemented.

Extensive usage of short delayed replications has been introduced to allow reduction of the message volume. The entries written in red would allow to reduce the volume of the BUFR message, especially in case of stations with limited instrumentation.

TM 307091

|  |  |  | Unit, scale |
| --- | --- | --- | --- |
| 3 01 089 |  | National station identification |  |
|  | 0 01 101 | WMO Member State identifier (1) | Code table, 0 |
|  | 0 01 102 | National AWS number (1) | Numeric, 0 |
| 3 01 090 |  | Fixed surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 | Surface station identification |  |
|  |  | WMO block number(1) | Numeric, 0 |
|  |  | WMO station number(1) | Numeric, 0 |
|  |  | Station or site name | CCITT IA5, 0 |
|  |  | Type of station | Code table, 0 |
|  | 3 01 011 | Year(2) | Year, 0 |
|  |  | Month(2) | Month, 0 |
|  |  | Day(2) | Day, 0 |
|  | 3 01 012 | Hour(2) | Hour, 0 |
|  |  | Minute(2) | Minute, 0 |
|  | 3 01 021 | Latitude (high accuracy) | Degree, 5 |
|  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, 1 |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  | Surface station instrumentation |  |
|  | 0 02 180 | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 | Visibility measurement system | Code table, 0 |
|  | 0 02 183 | Cloud detection system | Code table, 0 |
|  | 0 02 184 | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 001 | 0 10 004 | Pressure | Pa, –1 |
|  | 0 10 051 | Pressure reduced to mean sea level | Pa, –1 |
|  | 0 10 061 | 3-hour pressure change(3) | Pa, –1 |
|  | 0 10 063 | Characteristic of pressure tendency(3) | Code table, 0 |
| 0 07 004 |  | Pressure (standard level) | Pa, –1 |
| 0 10 009 |  | Geopotential height of the standard level | gpm, 0 |
| 3 02 072 |  | Temperature and humidity data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  | Replicate one descriptor five times |  |
| 3 07 063 | 0 07 061 | Depth below land surface | m, 2 |
|  | 0 12 130 | Soil temperature (scale 2) | K, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 |  | Visibility data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 001 | Horizontal visibility | m, –1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 05 000 |  | Delayed replication of 5 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  | Rate of ice accretion | Code table, 0 |
| 0 02 038 |  | Method of sea surface temperature measurement | Code table, 0 |
| 0 22 043 |  | Sea/water temperature (scale 2) | K, 2 |
| 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  | 0 22 011 | Period of waves | s, 0 |
|  | 0 22 021 | Height of waves | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 |  | State of ground and snow depth measurement |  |
|  | 0 02 176 | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 | Total snow depth | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 073 |  | Cloud data |  |
|  | 0 20 010 | Cloud cover (total) | %, 0 |
|  | 1 05 004 | Replicate 5 descriptors four times |  |
|  | 0 08 002 | Vertical significance | Code table, 0 |
|  | 0 20 011 | Cloud amount | Code table, 0 |
|  | 0 20 012 | Cloud type | Code table, 0 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 013 | Height of base of cloud | m, -1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 074 |  | Present and past weather |  |
|  | 0 20 003 | Present weather(4) | Code table, 0 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 20 004 | Past weather (1) (4) | Code table, 0 |
|  | 0 20 005 | Past weather (2) (4) | Code table, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 075 |  | Intensity of precipitation, size of precipitation element |  |
|  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 055 | Intensity of precipitation | Kg m-2 s-1, 4 |
|  | 0 13 058 | Size of precipitation element | m, 4 |
|  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute, 0 |
| 3 02 076 |  | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 | Type of precipitation | Flag table, 0 |
|  | 0 20 022 | Character of precipitation | Code table, 0 |
|  | 0 26 020 | Duration of precipitation (5) | Minute, 0 |
|  | 0 20 023 | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 | Obscuration | Flag table, 0 |
|  | 0 20 026 | Character of obscuration | Code table, 0 |
| 3 02 071 |  | Wind data from one-hour period |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind, if any) | Minute, 0 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  | 0 04 025 | Time period (= - 10 minutes in the first replication, = - 60 minutes in the second replication) | Minute, 0 |
|  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 | Maximum wind gust speed | m s-1, 1 |
|  | 0 04 025 | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
| 3 02 077 |  | Extreme temperature data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 07 032 | Height of sensor above local ground (for ground temperature) | m, 2 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 079 |  | Precipitation measurement |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 02 175 | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 | Method of liquid water content measurement of precipitation | Code table, 0 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 13 011 | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 080 |  | Evaporation measurement |  |
|  | 0 02 185 | Method of evaporation measurement | Code table, 0 |
|  | 0 04 025 | Time period ( = - 60 minutes) | Minute, 0 |
|  | 0 13 033 | Evaporation /evapotranspiration | kg m-2, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 081 |  | Total sunshine data |  |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 14 031 | Total sunshine | Minute, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 082 |  | Radiation data |  |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 14 002 | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute, 0 |
| 0 13 059 |  | Number of flashes | Numeric, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 |  | First order statistics of P, W, T, U data |  |
|  | 0 04 025 | Time period (= -10 minutes ) | Minute, 0 |
|  | 0 08 023 | First order statistics (= 9 (best estimate of standard deviation)) (6) | Code table, 0 |
|  | 0 10 004 | Pressure | Pa, –1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 08 023 | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) shall be used to identify a station within the national numbering system that is completely independent of  the WMO international numbering system. The WMO international identification  0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station.

- The time identification refers to the end of the one-hour period.

- 0 10 061 (3-hour pressure change) and 0 10 063 (Characteristic of pressure tendency) are included in this template, although they refer to 3-hour period preceding the time of observation.

- Present weather may be represented only by 0 20 003, especially if reported from a manned non-automated station. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should be used, if applicable.

- Duration of precipitation (in minutes) represents number of minutes in which any precipitation was registered.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

- If reporting nominal values is required, the template shall be supplemented with 3 07 093.

4. AWS BUFR template for surface observations from n-minute period

It is proposed to modify the existing AWS BUFR template for observations from n-minute period as follows: to add 3 01 089 (National station identification) at the beginning of it and to introduce the usage of short delayed replications in a similar way as it has been done in TM 3 07 091 in paragraph 3. After being validated, the AWS template for surface observations from n-minute period is proposed to be represented by the descriptor 3 07 092.

5. Representation  of nominal values

If reporting nominal values is required, the template TM 307091 or TM 307092 shall be supplemented with the following sequence:

| 3 07 093 |  | Nominal values |  |
| --- | --- | --- | --- |
|  | 2 23 000 | Substituted values operator |  |
|  | 2 36 000 | Backward reference bit map |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor = number of element descriptors | Numeric, 0 |
|  | 0 31 031 | Data present indicator | Numeric, 0 |
|  | 0 01 033 | Indication of originating/generating center | Code table, 0 |
|  | 0 01 032 | Generating application | Code table, 0 |
|  | 0 08 083 | Nominal value indicator | Flag table, 0 |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 255 | Substituted values |  |
|  | 1 08 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 000 | Substituted values operator |  |
|  | 2 37 000 | Use previously defined bit map |  |
|  | 0 01 033 | Indication of originating/generating center | Code table, 0 |
|  | 0 01 032 | Generating application | Code table, 0 |
|  | 0 08 083 | Nominal value indicator | Flag table, 0 |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 255 | Substituted values |  |

ANNEX

Code Table 0 01 101

WMO Member State identifier

| Code figure |  |
| --- | --- |
| 0-99 | Reserved |
| 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 122 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 -199 | Algeria Angola Benin Botswana Burkina Faso Burundi Cameroon Cape Verde Central African Republic Chad Comoros Congo Cote d'Ivoire Democratic Republic of the Congo Djibouti Egypt Eritrea Ethiopia France (RA I) Gabon Gambia Ghana Guinea Guinea-Bissau Kenya Lesotho Liberia Libyan Arab Jamahiriya Madagascar Malawi Mali Mauritania Mauritius Morocco Mozambique Namibia Niger Nigeria Portugal (RA I) Rwanda Sao Tom and Prince Senegal Seychelles Sierra Leone Somalia South Africa Spain Sudan Swaziland Togo Tunisia Uganda United Kingdom of Great Britain and Northern Ireland (RA I) United Republic of Tanzania Zambia Zimbabwe Reserved for Region I (Africa) |
| 200 201 202 203 204 205 206 207 208 209 210 211 212 213 214 215 216 217 218 219 220 221 222 223 224 225 226 227 228 229 230 231 232 233 234 235 -299 | Afghanistan Bahrain Bangladesh Bhutan Cambodia China Democratic People's Republic of Korea Hong Kong, China India Iran, Islamic Republic of Iraq Japan Kazakhstan Kuwait Kyrgyz Republic Lao People's Democratic Republic Macao, China Maldives Mongolia Myanmar Nepal Oman Pakistan Qatar Republic of Korea Republic of Yemen Russian Federation (RA II) Saudi Arabia Sri Lanka Tajikistan Thailand Turkmenistan United Arab Emirates Uzbekistan Viet Nam, Socialist Republic of Reserved for Region II (Asia) |
| 300 301 302 303 304 305 306 307 308 309 310 311 312 313 -399 | Argentina Bolivia Brazil Chile Colombia Ecuador France Guyana Paraguay Peru Suriname Uruguay Venezuela Reserved for Region III (South America) |
| 400 401 402 403 404 405 406 407 408 409 410 411 412 413 414 415 416 417 418 419 420 421 422 423 424 425 426 - 499 | Antigua and Barbuda Bahamas Barbados Belize British Caribbean Territories Canada Colombia Costa Rica Cuba Dominica Dominican Republic El Salvador France (RA IV) Guatemala Haiti Honduras Jamaica Mexico Netherlands Antilles and Aruba Nicaragua Panama Saint Lucia Trinidad and Tobago United Kingdom of Great Britain and Northern Ireland (RA IV) United States of America (RA IV) Venezuela Reserved for Region IV (North America, Central America and the Caribbean) |
| 500 501 502 503 504 505 506 507 508 509 510 511 512 513 514 515 516 517 518 519 520 521 – 599 | Australia Brunei Darussalam Cook Islands Fiji French Polynesia Indonesia Kiribati Malaysia Micronesia, Federated States of New Caledonia New Zealand Niue Papua New Guinea Philippines Samoa Singapore Solomon Islands Tonga United Kingdom of Great Britain and Northern Ireland (RA V) United States of America (RA V) Vanuatu Reserved for Region V (South-West Pacific) |
| 600 601 602 603 604 605 606 607 608 609 610 611 612 613 614 615 616 617 618 619 620 621 622 623 624 625 626 627 628 629 630 631 632 633 634 635 636 637 638 639 640 641 642 643 644 645 646 647 648 649 650 - 699 | Albania Armenia Austria Azerbaijan Belarus Belgium Bosnia and Herzegovina Bulgaria Croatia Cyprus Czech Republic Denmark Estonia Finland France (RA VI) Georgia Germany Greece Hungary Iceland Ireland Israel Italy Jordan Kazakhstan Latvia Lebanon Lithuania Luxembourg Malta Monaco Montenegro Netherlands Norway Poland Portugal (RA VI) Republic of Moldova Romania Russian Federation (RA VI) Serbia Slovakia Slovenia Spain Sweden Switzerland Syrian Arab Republic The Former Yugoslav Republic of Macedonia Turkey Ukraine United Kingdom of Great Britain and Northern Ireland (RA VI) Reserved for Region VI (Europe) |
| 700 – 999 1000 – 1022 1023 | Reserved Not used Missing value |