| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 3.1.9(1)Rev1 _______ (13.IV.2007) ENGLISH ONLY |
| --- | --- | --- |

EUCOS BUFR template for representation of radiosonde data

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a revised version of BUFR template  for radiosonde reporting that was submitted to Joint meeting of

ET DR&C and CT MTDCF in Montreal with a proposal for

possible recommendation of the  ET DR&C meeting.

A new EUCOS template has been introduced.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2

[2] Final Report, ET DR&C and CT MTDCF, Montreal, 8 – 12 May 2006

[3] Final Report, Commission for Basic Systems, Extraordinary Session, Seoul, Republic of

Korea, 9 to 16 November 2006

1. Background

The Joint meeting of ET DR&C and CT MTDCF (Montreal, 8 – 12 May 2006) reviewed a proposal for “HIGH RESOLUTION RADIOSONDE BUFR (LAND, SHIP OR MOBILE)” template which introduction had been coordinated by EUCOS, and suggested several changes to it. Moreover, a set of comments was formulated referring to the questions in the rightmost column of the proposed template. Somewhat later, further modifications to the template were suggested.

One of the most important finding of the Meeting in Montreal was: Sequence 3 09 052 has the same capability to handle high-resolution data as the proposed template [2]. To avoid any confusion, the proposed template is referred to as “EUCOS BUFR template for representation of radiosonde data” in this document or as “EUCOS template”.

The revised version of the EUCOS template and the comments are shown in the Annex I to this document.

On 12 April 2007, an e-mail with detailed explanations from Mr. Stuart Goldstraw, the former EUCOS Operations Manager, was received. Main points from his message have been incorporated in this revised version of the document and the template in ANNEX II.

2. Available templates for representation of radiosonde data

2.1 BURF template TM 309052

The Extraordinary Session of the Commission for Basic Systems (Seoul, Republic of Korea, 9 to 16 November 2006) recommended B/C25 Regulations for reporting TEMP, TEMP SHIP and TEMP MOBIL data in TDCF, based on the already operationally used common sequence descriptor 3 09 052 (template TM 309052). This template is suitable for P,T,U and wind vertical profiles, including the time and position of radiosonde at each level and allows to report the required wind shear data and the information on surface observations of clouds. Moreover, if additional information on sounding instrumentation is required, the sequence 3 09 052 may be supplemented by one or more additional parameters to allow data representation of this information.

After all corrections have been done to the proposed EUCOS template, the only difference between this template and template TM 309052 is that the former allows to report relative humidity, whereas the later dew point temperature (and wind shear data). Both templates have the same capability to accommodate high resolution data, limited by the length of a BUFR message (500 000 octets).

2.2 BURF templates 3 09 060, 3 09 061, 3 09 062, 3 09 063, 3 09 064, 3 09 065 and 3 09 066

There is a set of common sequence descriptors, suitable for representation of a single vertical profile data of high resolution:

3 09 060 (Radiosonde complete registration and surface observation), containing 0 13 003 (Relative humidity, %, scale 0),

3 09 061 (Raw PTU), containing 0 13 009 (Relative humidity, %, scale 1),

3 09 062 (RAW GPS unsmoothed wind),

3 09 063 (RAW GPS smoothed wind),

3 09 064 (Processed PTU), containing 0 13 003 (Relative humidity, %, scale 0),

3 09 065 (Processed GPS),

3 09 066 (Standard and significant levels), containing 0 13 003 (Relative humidity, %, scale 0).

These descriptors allow transmission of detailed information on radiosonde soundings. They represent data of one level, the vertical profile being created as a multi-subset BUFR message. If they are used for a single profile data, the BUFR compression is extremely effective, which may allow inclusion of high resolution data.

These descriptors, however, are not recommended for representation of TEMP, TEMP SHIP and TEMP MOBIL data as the entries for the required wind shear data are not available within them. If added, they would have to be reported at each level of the sounding. The same applies to the required surface observations otherwise this information would have to be transmitted in a separate BUFR message. Moreover, these descriptors are not suitable for a multi-report BUFR bulletin as the BUFR compression is not efficient in this case.

3. Extract from the e-mail of Mr. Stuart Goldstraw, the former EUCOS Operations Manager

- The template was not proposed for reporting of TEMP, TEMP SHIP and TEMP MOBIL data.

- Geopotential height (calculated from GPS height) is required to be used as the vertical coordinate.

- Inclusion of the information on sounding instrumentation within the template is preferred.

- Reporting of relative humidity as the measured element is required. Dew point temperature as the derived value may be influenced by an error of temperature. On the other hand, there are radiosondes that do not measure relative humidity, but have a dew point temperature sensor.

- Inclusion of instantaneous values of pressure, temperature, relative humidity, wind direction and speed from surface station instruments is required (measured at the time of launch).

- Addition of present weather would be useful to complete the information on launch conditions.

4. Proposal for possible recommendation of the ET DR&C

It might be proposed:

- To contact the current EUCOS Operations Manager and the authors of the original EUCOS template and to learn their opinion on the submitted new version of the EUCOS template (suitable for representation of high resolution radiosonde data with geopotential height as the vertical coordinate, the vertical resolution being limited by the length of BUFR message).

- If radiosonde data of very high resolution with pressure as the vertical coordinate is to be accomplished, usage of sequence descriptors 3 09 060 to 3 09 066 might be recommended.

- Producing TEMP, TEMP SHIP and TEMP MOBIL data in BUFR for the international exchange requires usage of the template TM 309052 that covers the complete extend of the TAC data. This is the main condition that has to be met during the migration process. Therefore, the alternatives in 4a) and 4b) could not be used for Migration to TDCF.

5. Proposal for a new Code table

Among the required instrumentation entries in the original proposal, there was a request for a new code table for “Geopotential height calculation”. If this parameter is validated and becomes preoperational, it should be included also in the ANNEX II to B/C25 Regulations for reporting TEMP, TEMP SHIP and TEMP MOBIL data in TDCF.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 02 191 | Geopotential height calculation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Code table 0 02 191

Geopotential height calculation

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | Geopotential height calculated from pressure |
| 2 | Geopotential height calculated from GPS Height |
| 3 - 14 | Reserved |
| 15 | Missing value |

ANNEX I

HIGH RESOLUTION RADIOSONDE BUFR (LAND, SHIP OR MOBILE)

| Table Reference | Element Name | Type & Byte Size (Bits) | Comments |
| --- | --- | --- | --- |
|  | Identification of launch site and instrumentation. |  |  |
| 0 | 01 | 001 | WMO Block Number | Numeric | 7 |  |
| 0 | 01 | 002 | WMO Station Number | Numeric | 10 |  |
| 0 | 01 | 011 | Ship or mobile land station identifier | CCITT IA5 | 72 |  |
| 0 | 02 | 011 | Radiosonde Type | Code table | 8 | Code table might need updating |
| 0 | 02 | 013 | Solar and Infrared radiation correction | Code table | 4 | Code table might need updating |
| 0 | 02 | 014 | Tracking technique/status of system used | Code table | 7 | Code table might need updating |
| 0 | 02 | 003 | Type of measuring equipment used | Code table | 4 | Code table might need updating |
| 0 | 25 | 061 | Software identification number | CCITT IA5 | 96 | Text descriptor |
| 0 | 01 | 082 | Radiosonde ascension number | Numeric | 14 |  |
| 0 | 01 | 081 | Radiosonde serial number | CCITT IA5 | 160 |  |
| 0 | 02 | 067 | Radiosonde operating frequency | Hz, Scale-5 | 15 | Frequency at Launch |
| 0 | 02 | 095 | Type of pressure sensor | Code table | 5 |  |
| 0 | 02 | 096 | Type of temperature sensor | Code table | 5 |  |
| 0 | 02 | 097 | Type of humidity sensor | Code table | 5 |  |
| 0 | 02 | 081 | Type of balloon | Code table | 5 |  |
| 0 | 02 | 082 | Weight of balloon | Kg, scale 3 | 12 |  |
| 0 | 02 | 084 | Type of gas used in balloon | Code table | 4 |  |
| ? | ?? | ??? | Geopotential height calculation | Code table | 4 | 1 – from pressure 2 – from GPS Height |
|  |  |  | Date/time of launch |  |  |  |
| 0 | 08 | 021 | Time significance (=18 Launch time) | Code table | 5 | Nominal hour? No |
| 0 | 04 | 001 | Year | Year | 12 |  |
| 0 | 04 | 002 | Month 3 01 011 | Month | 4 |  |
| 0 | 04 | 003 | Day | Day | 6 |  |
| 0 | 04 | 004 | Hour | Hour | 5 |  |
| 0 | 04 | 005 | Minute 3 01 013 | Minute | 6 |  |
| 0 | 04 | 006 | Second | Second | 6 |  |
|  |  |  | Horizontal and vertical coordinates of launch site |  |  |  |
| 0 | 05 | 001 | Latitude (High Accuracy) | Degree | 25 |  |
| 0 | 06 | 001 | Longitude (High Accuracy) | Degree | 26 |  |
| 0 | 07 | 030 | Height of station above MSL | M, scale 1 | 17 |  |
| 0 | 07 | 031 | Height of barometer above MSL | M, scale 1 | 17 |  |
| 0 | 07 | 007 | Height of radiosonde release above MSL | M | 15 |  |
| 0 | 33 | 024 | Station quality mark (for mobile stations) | Code table | 4 |  |
|  |  |  | Surface information reported with vertical sounding |  |  |  |
| 0 | 08 | 002 | Vertical significance (surface obs) | Flag | 6 | Vertical significance 008002 is not capable to identify “surface level”. |
| 0 | 10 | 004 | Pressure | Pa, scale -1 | 14 | Need to change scale? |
| 0 | 12 | 101 | Temperature (dry bulb) | K, scale 2 | 16 |  |
| 0 | 13 | 003 | Relative humidity | %, scale 0 | 7 |  |
| 0 | 11 | 001 | Wind Direction | Deg,scale 0 | 9 |  |
| 0 | 11 | 002 | Wind Speed | m/s, scale 1 | 12 |  |
| 0 | 08 | 002 | Vertical significance | Flag | 6 | Cloud Ob |
| 0 | 20 | 011 | Cloud amount ( low or middle Nh) | Code table | 4 |  |
| 0 | 20 | 013 | Height of base of cloud (h) | m, scale -1 | 11 |  |
| 0 | 20 | 012 | Cloud Type (Low) | Code table | 6 |  |
| 0 | 20 | 012 | Cloud Type (Medium) | Code table | 6 |  |
| 0 | 20 | 012 | Cloud Type (High) | Code table | 6 |  |
| 0 | 08 | 002 | Vertical significance (missing values) | Flag | 6 |  |
|  |  |  | Present weather? |  |  |  |
| 0 | 22 | 043 | Sea/water temp (ship stations) | K, scale 2 | 15 |  |
|  |  |  | Vertical sounding data |  |  | *Repeated section* |
| 1 | 10 | 000 | Delayed replication of 10 descriptors |  |  |  |
| 0 | 31 | 002 | Extended delayed descriptor replication factor | Numeric | 16 |  |
| 0 | 04 | 086 | Long time period or displacement (since launch time) | Second | 15 |  |
| 0 | 08 | 042 | Extended vertical sounding significance | Flag table | 18 |  |
| 0 | 07 | 004 | Pressure | Pa, scale -1 | 14 |  |
| 0 | 10 | 009 | Geopotential height | gpm, scale0 | 17 |  |
| 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) | Degree, Scale 5 | 25 | Displacement or actual? Is resolution too much 5 decimal places? |
| 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) | Degree, Scale 5 | 26 |  |
| 0 | 12 | 101 | Temperature/dry bulb | K, scale 2 | 12 |  |
| 0 | 13 | 003 | Relative Humidity | %, scale 0 | 7 |  |
| 0 | 11 | 001 | Wind direction | Degree true | 9 |  |
| 0 | 11 | 002 | Wind Speed | m/s, scale 1 | 12 |  |

COMMENTS:

The template could have one of two possible purposes, and the extent of the required changes depends on the intended purpose of the template.

If the template is intended to be used for local archival of data or for the transmission of minimally processed data from the observing site to a national centre for further processing then the changes included under A) below would be recommended.

On the other hand, if the template is intended for the international exchange of data, much more extensive changes would be necessary (see B) below).

A)  Changes recommended if the template is intended for local archive or for transmission to

a national centre, include:

- The nominal data time is reported in Section 1 of the BUFR message.  The first time included in the template, preceded by time significance descriptor 0 08 021 should be the launch time. The value associated with the 0 08 021 descriptor should be 18 (= Launch time).

- The surface pressure, temperature, relative humidity, and wind direction and speed should be represented as a surface level (bit 1 of the value associated with descriptor 0 08 042, extended vertical sounding significance) within the main data replication [Vertical sounding data *Repeated section*]. The vertical significance 0 08 002 specifies the type of clouds and is not capable to identify the character of the level, i.e. “surface level”. Therefore, it is proposed to delete the whole part of the template written in red.

- The pressure must be included in the main data replication.

- The number of descriptors to be repeated in the main data replication was incorrect.  It was given as one (1 01 000) and should be ten (1 10 000) when pressure is included, or eleven (1 11 000) if both pressure and dew point are included.

B)  If the template is intended to be used for the international exchange of data, then further major

changes would be required including

- The addition of dew point temperature within each level of the vertical sounding data.

- The addition of wind shear data is required by the current rules for the international exchange of upper air data.

The meeting would also comment that this proposed template has much in common with the existing template TM309052 and largely duplicates the functionality of table D sequence 3 09 052.  Sequence 3 09 052 has the same capability to handle high-resolution data as the proposed template.  The additional metadata descriptors (marked yellow in the template) may be prep ended to descriptor 3 09 052 in section 3 of the BUFR message.

Questions implied by the proposed template include also:

- The comment about changing scale against descriptor 0 10 004 implies some concern about the scale.  The scale of descriptor 0 10 004 is -1 (10 Pa, 0.1hPa) which seems to be sufficiently accurate.  If more accuracy is required, then either change scale and change data width descriptors should be used or a formal request for a new, higher resolution descriptor should be made to the ET-DR&C.

- There is a comment “Present Weather?”.  It is unclear what this comment is intended to convey.  If the purpose is to ask what descriptor can be used to describe the weather at the time of launch, then 0 20 003 can be used.

- There is a query “Displacement or actual” against descriptors 0 05 015 and 0 01 016 (Latitude and longitude displacement) as to the meaning.  These two descriptors are displacements from the launch point that is the difference between the current location and the launch point.

- There is a query against the resolution (5 decimal places, 0.00001 deg, approximately 1m) of descriptors 0 05 015 and 0 06 015.  This was requested, by data users in order to cope with constantly improving technology.

ANNEX II

EUCOS template for representation of radiosonde data with geopotential height as the vertical coordinate (to be validated)

This template is suitable for representation of high resolution radiosonde data with geopotential height as the vertical coordinate, the vertical resolution being limited by the length of BUFR message.

| 3 01 111 |  | Identification of launch site and instrumentation |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 0 25 061 |  | Software identification and version number | CCITT IA5 |
| 0 01 081 |  | Radiosonde serial number | CCITT IA5 |
| 0 01 082 |  | Radiosonde ascension number | Numeric |
| 0 02 067 |  | Radiosonde operating frequency | Hz, scale -5 |
| 0 02 095 |  | Type of pressure sensor | Code table |
| 0 02 096 |  | Type of temperature sensor | Code table |
| 0 02 097 |  | Type of humidity sensor | Code table |
| 0 02 081 |  | Type of balloon | Code table |
| 0 02 082 |  | Weight of balloon | kg, scale 3 |
| 0 02 084 |  | Type of gas used in balloon | Code table |
| 0 02 191 |  | Geopotential height calculation | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Surface station measurements |  |
| 0 10 004 |  | Pressure | Pa, scale –1 |
| 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, scale 2 |
|  | 0 12 101 | Temperature/dry-bulb temperature(scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 13 003 | Relative humidity | % |
| 0 07 032 |  | Height of sensor above local ground (for wind measurement) | m, scale 2 |
| 0 02 002 |  | Type of instrumentation for wind measurement | Flag table |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
| 0 20 003 |  | Present weather | Code table |
| 3 02 049 |  | Cloud information reported with vertical soundings |  |
|  | 0 08 002 | Vertical significance | Code table |
|  | 0 20 011 | Cloud amount (of low or middle clouds Nh) | Code table |
|  | 0 20 013 | Height of base of cloud (h) | m, scale –1 |
|  | 0 20 012 | Cloud type (low clouds CL) | Code table |
|  | 0 20 012 | Cloud type (middle clouds CM) | Code table |
|  | 0 20 012 | Cloud type (high clouds CH) | Code table |
|  | 0 08 002 | Vertical significance ( = missing value) | Code table |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Temperature, dew-point, relative humidity and wind data at height levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 yyy |  | Temperature, dew-point, relative humidity and wind data at a height level with radiosonde position |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 13 009 | Relative humidity (see Note 4) | %, scale 1 |
|  | 0 12 103 | Dew-point temperature (scale 2) (see Note 4) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |

Notes:	(1)	Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

- Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds).

- Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

- If the radiosonde is equipped with a relative humidity sensor, 0 13 009 shall be reported as mandatory and dew-point temperature may be included as a derived value. If the radiosonde is equipped with a dew-point temperature sensor, 0 12 103 shall be reported and 0 13 009 shall be set to a missing value.