| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C Doc. 3.6(2) _______ ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for SBUV/2 ozone data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new BUFR descriptors to be used in the reporting of SBUV/2 ozone data.

_________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve

the contents for preoperational implementation.

BACKGROUND AND DISCUSSION

The U.S. NESDIS was previously tasked to distribute ozone data from its SBUV/2 (Solar Backscatter Ultraviolet) instrument in BUFR.  Several new Table B and Table D entries were developed during this effort, and several atmospheric chemistry descriptors previously proposed to the ET/DR+C in Montreal (May 2005) were utilized as well.  Sample data resulting from this work was submitted to the ET/DR+C and others for validation in November 2006.  Since that time, NESDIS has begun real-time distribution of such data within the U.S. as well as to numerous external customers including Canada, India, UKMO and ECMWF.  Therefore, it is now requested that the attached proposal be formally approved for preoperational implementation.

PROPOSAL

New Table D sequence

|  |  | (Ozone data) |
| --- | --- | --- |
| 3 10 019 | 0 01 007 | Satellite identifier |
|  | 0 02 019 | Satellite instruments (“624” = SBUV/2) |
|  | 3 01 011 | Date |
|  | 3 01 013 | Time |
|  | 3 01 023 | Lat/Long |
|  | 0 07 025 | Solar zenith angle |
|  | 0 08 021 | Time significance (“28” = Start of scan) |
|  | 0 07 025 | Solar zenith angle |
|  | 0 08 021 | Time significance (“29” = End of scan) |
|  | 0 07 025 | Solar zenith angle |
|  | 0 08 021 | Time significance (“Missing” = Cancel) |
|  | 0 08 029 | Remotely-sensed surface type |
|  | 0 05 040 | Orbit number |
|  | 0 08 075 | Ascending/descending orbit qualifier |
|  | 0 08 003 | Vertical significance (“0” = Surface) |
|  | 0 10 004 | Pressure (terrain) |
|  | 0 08 003 | Vertical significance (“Missing” = Cancel) |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 15 001 | Total ozone |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 33 070 | Total ozone quality |
|  | 0 15 030 | Aerosol contamination index |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 20 081 | Cloud amount in segment (cloud fraction) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 003 | Vertical significance (“2” = Cloud top) |
|  | 0 33 042 | Type of limit represented by following value (“0” = Exclusive lower limit) |
|  | 0 07 004 | Pressure |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 15 001 | Total ozone (below cloud top pressure) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 003 | Vertical significance (“Missing” = Cancel) |
|  | 1 13 021 | Repeat next 13 descriptors 21 times |
|  | 0 07 004 | Pressure (at bottom of layer) |
|  | 0 07 004 | Pressure (at top of layer) |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 08 021 | Time significance (“27” = First guess) |
|  | 0 15 005 | Ozone p |
|  | 0 08 021 | Time significance (“Missing” = Cancel) |
|  | 0 15 005 | Ozone p |
|  | 0 33 007 | % confidence |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 026 | Matrix significance (“4” = Row of averaging kernel matrix) |
|  | 1 01 020 | Repeat next descriptor 20 times |
|  | 0 25 143 | Linear coefficient |
|  | 0 08 026 | Matrix significance (“Missing” = Cancel) |
|  | 0 08 043 | Atmospheric chemical type (“0” = Ozone) |
|  | 1 09 015 | Repeat next 9 descriptors 15 times |
|  | 0 07 004 | Pressure |
|  | 0 08 090 | Decimal scale of following Table B values |
|  | 2 07 006 | Increase scale, reference value and data width |
|  | 0 15 008 | Scaled mixing ratio (volumetric) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 090 | Decimal scale of following Table B values (“Missing” = Cancel) |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 33 007 | % confidence |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 043 | Atmospheric chemical type (“Missing” = Cancel) |
|  | 0 33 071 | Profile ozone quality |
|  | 1 08 008 | Repeat next 8 descriptors 8 times |
|  | 2 02 124 | Change scale |
|  | 2 01 107 | Change data width |
|  | 0 02 071 | Spectrographic wavelength |
|  | 2 01 000 | Cancel change data width |
|  | 2 02 000 | Cancel change scale |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 20 081 | Cloud amount in segment (cloud fraction) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |

New Table B descriptors

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 15 030 | Aerosol contamination index (see Note 6) | Numeric | 2 | -1000 | 12 | Numeric | 2 | 4 |
| 0 33 070 | Total ozone quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 33 071 | Profile ozone quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

0-33-070	Total ozone quality

| 0 | Low path length, good scan |
| --- | --- |
| 1 | High path length, good scan |
| 2 | Very high path, good scan |
| 3 | Reserved |
| 4 | Inconsistency between best ozone and the largest weighted ozone pair |
| 5 | Difference between best ozone and total zone for profile greater than three sigma |
| 6 | Reserved |
| 7 | Photometer reflectivity and monochrometer reflectivity differ by more than 0.15 |
| 8 | Best reflectivity out of range (less than 0.05 or greater than 1.05) |
| 9 | A-pair, B-pair or C-pair ozone exceeds the dynamic range of the tables. (See Note) |
| 10-14 | Reserved |
| 15 | Missing |

Note:  The dynamic ranges are: 
        	* Latitude < 15 deg - 180-350 DU 
         	* Latitude 15-45 deg - 180-600 DU 
        	* Latitude > 45 deg - 180-650 DU

0-33-071 	Profile ozone quality

| 0 | No error |
| --- | --- |
| 1 | Lower level anomaly |
| 2 | Inconsistency between best ozone and profile total ozone |
| 3 | Final residue greater than 3 sigma |
| 4 | Measured Q-value calculated with a priori profile and multiple-scattering/reflectivity correction |
| 5 | C greater than 3.0 DU or less than 0.5 DU |
| 6 | Sigma greater than 0.8 or less than 0.3 |
| 7 | Reflectivity is less than -0.05, greater than 1.05, or changes by more than 0.05 from wavelength to wavelength |
| 8 | Total ozone not available |
| 9 | Bad radiance or eclipse contamination |
| 10-14 | Reserved |
| 15 | Missing |

Add the following note to BUFR/CREX Class 15:

- For this descriptor, numbers less than -1 indicate a predominance of scattering aerosols, increasing in concentration as the number becomes more negative.  Numbers greater than +1 indicate a predominance of absorptive aerosols, increasing in concentration as the number becomes more positive.  Numbers between -1 and +1 indicate clouds or noise.

Add the following entries to the existing code table for

0-08-029 	Remotely-sensed surface type

| 4 | Low inland (below sea level) |
| --- | --- |
| 5 | Mix of land and water |
| 6 | Mix of land and low inland |
| 7-254 | Reserved |