| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C Doc. 3.6(4) _______ ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for GFA data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new BUFR descriptors to be used in the reporting of GFA  (Graphical Forecast AIRMET) data.

_________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve

the contents for preoperational implementation.

BACKGROUND AND DISCUSSION

The U.S. NCEP Aviation Weather Center (AWC) has been working to develop a graphical forecast application for the generation of AIRMET messages.  The resulting graphical output contains more detailed information than can be represented within the official ICAO AIRMET text format, and this information is of great interest to certain elements of the U.S. aviation community as well as other potential customers in Canada and elsewhere.  In order to easily disseminate such detailed information to these customers, new BUFR sequences were developed and tested.  During this process, an effort was made to utilize many of the same BUFR descriptors and sequences that were recently approved for use in the reporting of SIGMET messages.  Nevertheless, a few additional descriptors and sequences were also required as shown in the below proposal.  The new application will allow the AWC to provide the necessary level of detail to those customers who are able to receive and process BUFR messages, while at the same time continuing to provide backward-capable generation of the ICAO AIRMET text format for others.

A copy of the below proposal, along with several sample BUFR files and corresponding documentation, was provided to the ET/DR+C in October 2006, but no responses have been received to date.  Given the apparent lack of interest in this data by other centers, we respectfully request that the below proposal be accorded preoperational status.  In doing so, we would emphasize that this proposal is intended to represent a superset of the information available within the ICAO AIRMET text format, rather than just the information available within that format.

PROPOSAL

New Table B descriptors

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 01 038 | Graphical Forecast AIRMET (GFA) sequence identifier | CCITT IA5 | 0 | 0 | 40 | Character | 0 | 5 |
| 0 20 006 | Flight Rules | Code Table | 0 | 0 | 3 | Code Table | 0 | 1 |

| Code Figure | 0 20 006 Flight Rules |
| --- | --- |
| 0 | Low Instrument Flight Rules - Ceiling < 500 feet and/or Visibility < 1 mile |
| 1 | Instrument Flight Rules - Ceiling < 1000 feet and/or Visibility < 3 miles |
| 2 | Marginal Visual Flight Rules – 1000 feet <= Ceiling < 3000 feet and/or 3 miles <= Visibility < 5 miles |
| 3 | Visual Flight Rules - Ceiling >= 3000 feet and/or Visibility >= 5 miles |
| 4-6 | Reserved |
| 7 | Missing value |

Add new values to the existing code/flag tables for the following BUFR/CREX Table B descriptors:

0 08 040

34	Freezing level

0 08 041

8	IFR Ceiling and Visibility

9	Mountain obscuration

10	Strong surface wind

11	Freezing level

0 20 023

12	Wind shear

0 20 025

14	Cloud

15 	Precipitation

New Table D descriptors:

|  |  | (Graphical AIRMET Sierra) |
| --- | --- | --- |
| 3 16 051 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 055 | GFA IFR Ceiling and Visibility |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 056 | GFA Mountain Obscuration |
|  |  | (Graphical AIRMET Tango) |
| 3 16 052 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 057 | GFA Turbulence |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 058 | GFA Strong Surface Wind |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 059 | GFA Low-Level Wind Shear |
|  |  | (Graphical AIRMET Zulu) |
| 3 16 053 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 060 | GFA Icing |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 061 | GFA Freezing Level |

|  |  | (GFA Identifier and Observed/Forecast Location) |
| --- | --- | --- |
| 3 16 054 | 0 01 038 | GFA sequence identifier |
|  | 0 08 021 | Time significance, 4=Forecast, 16=Analysis |
|  | 3 01 014 | Time period (for which hazard is being observed/forecast) |
|  | 3 01 027 | Description of Feature |
|  | 0 08 021 | Time Significance, Missing=Cancel |

|  |  | (GFA IFR Ceiling and Visibility) |
| --- | --- | --- |
| 3 16 055 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 041 | Data significance, 8=IFR Ceiling and Visibility |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 006 | Flight rules, 1=IFR |
|  | 2 02 129 | Increase scale by 1 |
|  | 2 01 130 | Increase bit width by 2 |
|  | 0 33 042 | Type of limit represented by following (cloud base) value, 2=Exclusive upper limit, 7=Missing |
|  | 0 20 013 | Height of base of cloud |
|  | 0 33 042 | Type of limit represented by following (visibility) value, 2=Exclusive upper limit, 7=Missing |
|  | 0 20 001 | Horizontal visibility |
|  | 2 01 000 | Cancel increase bit width |
|  | 2 02 000 | Cancel increase scale |
|  | 0 20 025 | Obscuration |
|  | 0 20 026 | Character of obscuration, 6=Blowing, 15=Missing |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Mountain Obscuration) |
| 3 16 056 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 041 | Data significance, 9=Mountain obscuration |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 006 | Flight rules, 1=IFR |
|  | 0 20 025 | Obscuration |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Turbulence) |
| 3 16 057 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 011 | Meteorological feature, 13=Turbulence |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 11 031 | Degree of turbulence, 6=Moderate |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Strong Surface Wind) |
| 3 16 058 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 041 | Data significance, 10=Strong surface wind |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 33 042 | Type of limit represented by following (wind speed) value, 0=Exclusive lower limit |
|  | 0 11 012 | Wind speed at 10 m |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Low-Level Wind Shear) |
| 3 16 059 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 011 | Meteorological feature, 16=Phenomenon |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 023 | Other weather phenomena, bit 12=Wind shear |
|  | 0 20 024 | Intensity of phenomena |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |

|  |  | (GFA Icing) |
| --- | --- | --- |
| 3 16 060 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 011 | Meteorological feature, 15=Airframe Icing |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 041 | Airframe icing, 4=Moderate Icing |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Freezing Level) |
| 3 16 061 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD |
|  | 0 08 041 | Data significance, 11=Freezing level |
|  | 3 16 054 | GFA Identifier and Observed/Forecast Location |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |