| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 4.1(1) _______ (12.IV.2007) ENGLISH ONLY |
| --- | --- | --- |

Problem for assignment of Radiosonde numbers

Submitted by Secretariat

________________________________________________________________

Summary and Purpose of Document

The document presents some proposal by Dr Steve Schroeder from USA (Texas A&M University) to solve the saturation of Common Code Table C-2 for Radiosonde numbers.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to take the included information into consideration and make any necessary further recommendations.

Reference:

Manual on Code- Common Code Table C-2

Background

The Common Code Table C-2 is saturated.  Before all the radiosondes systems switched to BUFR, an interim solution imagined by Dr Steve Schroeder from USA (Texas A&M University) could solve the problem (see copy of emails).  One needs to record the assignment date in the Common Code Table of new sondes, which are then given the same 2 digits number of sondes no longer in use at the date of assignment.  An example of a new look Common Code Table C-2 is shown at the end.  The encoding/decoding software will have to take this into account, especially if one converts to or from BUFR.

I think my proposed solution would work because it does not go much beyond updating a code table, which is your standard procedure.  The table would need a note which says that the alphanumeric code format reports only the last 2 digits, and the correct first digit is identified from the date (the first digit is 0 if the observation is before the expiration date of the "old" 2-digit code, or 1 otherwise).

This is conceptually similar to space-saving procedures which WMO has always used, such as truncating certain heights because the "thousands" digit can be reconstructed.

The only software changes would be to programs which convert ASCII to BUFR (because they need to add the missing digit), or convert BUFR to ASCII (to include only the last 2 digits), or prepare the original transmitted observation in either ASCII or BUFR (to look up the correct code).

Tim,

I included you because I think this would make your next update of the radiosonde catalog easier, since quite a few stations are already reporting "unknown" instruments.  I notice you had to get special confirmations from France (because they picked an old code) and China (because they are not using the 31313 group since they only have one code.  It took me a while to figure out that "Shang/M" is the old GZZ-2 radiosonde with goldbeaters' skin hygrometer, and "Shang/E" is the new GTS-1 radiosonde with a carbon hygristor).  India is using their 31313 groups quite erratically (mainly, if they use a 31313 group, the instrument is IMD Mark IV instead of IMD Mark III), including 2 unknown instruments (but one code, 09002 at New Delhi in Dec 2005 and Jan 2006, is a brief test of Sippican Mark II based on personal contacts and an online document from a NOAA meeting at http://www.oco.noaa.gov/docs/GCOSUAWII/ pres_Bhatia_RC_Status_Indian_Radisonde.ppt).  Actually, I think most stations in India are still using mostly the old IMD MK III sondes and few or no MK IV sondes, so it would be very helpful for them to start using 31313 codes regularly, with a different code for each type.

Also, issue # 2 in the copied e-mail below is slightly relevant for you because those of us who use historical radiosonde data would like to know when a change actually occurred.

Finally, it would be good to add a table somewhere in the radiosonde catalog web page that describes each radiosonde type (Manufacturer, model number, frequency, sensor types, and a link to additional information if available).  You have little space in the Excel spreadsheet to put in much of an explanation, and the Code Table 3685 explanations are also abbreviated.  My list of atmospheric profiling equipment types is up to 2167 different codes (1144 for radiosondes that measure at least temperature), but some of them I know very little about (such as "MARL-A or Vektor-M-RZM-2") and some are probably wrong (such as "EEC Company type 23", which I think is a radar and not a radiosonde).  I could give you an ftp address to get a copy of the file containing my list.  I include references to documentation of each instrument type, with as much information as I have been able to locate.

Regards,

Steve Schroeder

Dept. of Atmospheric Sciences

Texas A&M University

steves@ariel.met.tamu.edu

Joel,

Please find below a proposal on how to handle the reporting of the RSO instrument type. I suggest that the coding group of CBS (ET-DR&C)pays an attention to this interesting proposal.  Please inform Mr Schroeder, CIMO and GCOS on action taken on this issue. Please let me know if there is a need to involve CIMO experts. If yes, Mr Oakley (UK) and Dr Zahumensky (Slovakia) could help.

Regards,

Miroslav

___________________________________________

Miroslav Ondras

Senior Scientific Officer

WWW/Observing System Division

World Meteorological Organization

7 bis, Avenue de la Paix

P.O.Box 2300

CH-1211 Geneva 2

Switzerland

Tel: +41 22 730 8409

Fax: +41 22 730 8021

E-mail: MOndras@wmo.int

http://www.wmo.int/web/www/IMOP/IMOP-home.html

Richard,

I saw your presentation at the AMS meeting in San Antonio, and wanted to ask you about certain WMO policies for reporting radiosonde instrument types and certain station changes, but needed to go to another session before I got a chance to talk to you.  If you don't deal with these issues, please pass this on to someone who is involved with decisions in this area.

- - - - - - -

(1)  Reporting instrument types in the 31313 group:

My first question is who makes decisions about the future assignment of instrument codes in the 31313 group.  Code Table 3685 is almost filled up, so the 31313 group is losing its usefulness to distinguish instrument types.  I would like to suggest a way to expand the code table in the short term without interfering with the eventual change to BUFR.

The suggestion is that, since BUFR now allows code numbers from 2 to 254 (excluding reserved values), if a code number has not been used for at least several years,  a code equal to that code number plus 100 can be assigned for a new instrument type (or eventually plus 200 if the number is reassigned a second time).  Observations in the current text format would report the last 2 digits.  To make this work, Code Table 3685 would need to state the beginning date for any reassigned code, and would note that the last 2 digits are reported in a text observation.  After the effective date of a code value of 100 or larger, an earlier code with the same last 2 digits cannot be used (although the old codes would stay in the table).  If a text report is converted to BUFR, it is simple to correctly restore the missing digit.  Usually, a reassigned code should be given to the same manufacturer as the old code, but codes from companies that no longer make radiosondes can be freely assigned.

To further "stretch" the codes, a manufacturer or country can rename any of their codes, as is done now, but I would recommend this only for codes that never were used after they were assigned, or where the instrument name in English is renamed without changing the instrument (as with the 5 Russian changes in Sep 2006).

An example:  Sippican (formerly VIZ, now Lockheed Martin-Sippican or LMS) has renamed Mark IIA sondes as LMS5 and introduced a new series called LMS6.  Also, some LMS5 radiosondes have a capacitive instead of a carbon humidity sensor, which is a major change.  I think all 3 permutations now use the same code numbers (85 without pressure or 87 with pressure).  Codes 85 and 87 should mean Mark IIA (LMS5) sondes with a carbon hygristor.  Codes 11, 14, 31, 38, 48, 65, 82, and 83 are assigned to VIZ, Sippican, or Canadian companies and were not used since 2002 or earlier (except for typographical errors), and codes 31, 48, 82, and 83 were never used.  The never-used codes might be enough to accommodate new models for a while, but if codes 11 and 14 are reassigned, they would be replaced by 111 and 114.  Weather observations in text format would use codes 11 and 14, but a processing center could figure out that after a specified date, codes 111 and 114 are implied.

Observations already in the archives would not change, so explicit metadata would be needed to tell users of historical data which instruments were used.  However, I know of one case where a retroactive change of a code is justified.  France has already "borrowed" code 34 from Czechoslovakia for the Vaisala RS92/Star, and an effective date of 2004 for code 134, assigned to Vaisala RS92/Star, would alert users of historical data that code 34 starting 2004 did not mean that France started using Czechoslovakian instruments from the 1980s.  Through November 2006, the codes (from 10 to 89) that have not been used since at least 2002 are as follows:  11 to 19, 23 to 25, 30 to 33, 35, 36, 38 to 44, 46, 48, 57 to 59, 64, 65, 68 to 70, 72, 73, 82, 83, and 89.  However, I think codes 32, 58, 59, 68, 69, and 88 represent real instruments so those codes should not be reassigned.

India should have at least 3 new codes (Mark IV, Mark IV with a silicon pressure sensor, Mark IV digital sonde, and possibly an undescribed intermediate version of Mark IV that is now reported as an "unknown instrument.").  China should have 2 codes (GZZ-2 and the new GTS-1) and should be encouraged to report the 31313 code because about 20 percent of stations still use the old GZZ-2 instrument.  Besides the new Sippican models I mention above, Graw and Modem have new models that they exhibited at the AMS meeting which should have new instrument codes.  They might just rename some of their old codes otherwise.  By the way, my list of upper air instruments is up to over 2100 models, so even BUFR will need to expand, but I read that it is expandable without arbitrary limits.

(2)  Stations should be encouraged to report the actual date of a change in location, elevation, or instrument.

The WMO Operational Newsletter has a form for stations to report changes in locations and other data.  There is space for remarks, and stations should be requested to state the effective date of a change, and whether the date is scheduled (reported in advance) or actual (reported after the change occurs).  (If a station schedules a change, and the change takes place at a different time, it would report the change twice.)  The reason is that, for climate purposes, it is difficult to reconstruct the history of station moves and other changes because changes are reported haphazardly with an unknown relationship between the date a catalog is updated and when the change occurred.

Even if this discussion is a little long, I cannot bring up all aspects of each issue, but the 31313 issue needs to be resolved soon since there are already more new instruments in use than there are codes to assign.

Regards,

Steve Schroeder

Dept. of Atmospheric Sciences

Texas A&M University

steves@ariel.met.tamu.edu

COMMON CODE TABLE C-2: RADIOSONDE/ SOUNDING SYSTEM USED

| Common Code Table: | (Code table 3685 -rara (Radiosonde/sounding system used) – for alphanumeric codes |
| --- | --- |
|  | (Code table 0 02 011 (Radiosonde type) in BUFR |

| Date of Assignment of number (if after 30/04/2007) | Code figure for rara (Code table 3685) | Code figure for BUFR (Code table 0 02 011) |  |
| --- | --- | --- | --- |
|  | 00–01 | 000–001 | Reserved |
|  | 02 | 002 | No radiosonde – passive target (e.g. reflector) |
|  | 03 | 003 | No radiosonde – active target (e.g. transponder) |
|  | 04 | 004 | No radiosonde – passive temperature-humidity profiler |
|  | 05 | 005 | No radiosonde – active temperature-humidity profiler |
|  | 06 | 006 | No radiosonde – radio-acoustic sounder |
|  | 07–08 | 007–008 | No radiosonde – . . . (reserved) |
|  | 09 | 009 | No radiosonde – system unknown or not specified |
|  | 10 | 010 | VIZ type A pressure-commutated (USA) |
|  | 11 | 011 | VIZ type B time-commutated (USA) |
|  | 12 | 012 | RS SDC (Space Data Corporation – USA) |
|  | 13 | 013 | Astor (no longer made — Australia) |
|  | 14 | 014 | VIZ Mark I MICROSONDE (USA) |
|  | 15 | 015 | EEC Company type 23 (USA) |
|  | 16 | 016 | Elin (Austria) |
|  | 17 | 017 | Graw G. (Germany) |
|  | 18 | 018 | Reserved for allocation of radiosonde |
|  | 19 | 019 | Graw M60 (Germany) |
|  | 20 | 020 | Indian Meteorological Service MK3 (India) |
|  | 21 | 021 | VIZ/Jin Yang Mark I MICROSONDE (South Korea) |
|  | 22 | 022 | Meisei RS2-80 (Japan) |
|  | 23 | 023 | Mesural FMO 1950A (France) |
|  | 24 | 024 | Mesural FMO 1945A (France) |
|  | 25 | 025 | Mesural MH73A (France) |
|  | 26 | 026 | Meteolabor Basora (Switzerland) |
|  | 27 | 027 | AVK-MRZ (Russian Federation) |
|  | 28 | 028 | Meteorit Marz2-1 (Russian Federation) |
|  | 29 | 029 | Meteorit Marz2-2 (Russian Federation) |
|  | 30 | 030 | Oki RS2-80 (Japan) |
|  | 31 | 031 | VIZ/Valcom type A pressure-commutated (Canada) |
|  | 32 | 032 | Shanghai Radio (China) |
|  | 33 | 033 | UK Met Office MK3 (UK) |
|  | 34 | 034 | Vinohrady (Czechoslovakia) |
|  | 35 | 035 | Vaisala RS18 (Finland) |
|  | 36 | 036 | Vaisala RS21 (Finland) |
|  | 37 | 037 | Vaisala RS80 (Finland) |
|  | 38 | 038 | VIZ LOCATE Loran-C (USA) |
|  | 39 | 039 | Sprenger E076 (Germany) |
|  | 40 | 040 | Sprenger E084 (Germany) |
|  | 41 | 041 | Sprenger E085 (Germany) |
|  | 42 | 042 | Sprenger E086 (Germany) |
|  | 43 | 043 | AIR IS - 4A - 1680 (USA) |
|  | 44 | 044 | AIR IS - 4A - 1680 X (USA) |
|  | 45 | 045 | RS MSS (USA) |
|  | 46 | 046 | Air IS - 4A - 403 (USA) |
|  | 47 | 047 | Meisei RS2-91 (Japan) |
|  | 48 | 048 | VALCOM (Canada) |
|  | 49 | 049 | VIZ MARK II (USA) |
|  | 50 | 050 | GRAW DFM-90 (Germany) |
|  | 51 | 051 | VIZ-B2 (USA) |
|  | 52 | 052 | Vaisala RS80-57H |
|  | 53 | 053 | AVK-RF95 (Russian Federation) |
|  | 54 | 054 | GRAW DFM-97 (Germany) |
|  | 55 | 055 | Meisei RS-016 (Japan) |
|  | 56 | 056 | M2K2 (France) |
|  | 57 | 057 | M2K2-DC Modem (France) |
|  | 58 | 058 | AVK-MRZ (Russian Federation) |
|  | 59 | 059 | Modem M2K2-R 1680 MHz RDF radiosonde with pressure sensor chip (France) |
|  | 60 | 060 | Vaisala RS80/MicroCora (Finland) |
|  | 61 | 061 | Vaisala RS80/Loran/Digicora I,II or Marwin (Finland) |
|  | 62 | 062 | Vaisala RS80/PCCora (Finland) |
|  | 63 | 063 | Vaisala RS80/Star (Finland) |
|  | 64 | 064 | Orbital Sciences Corporation, Space Data Division, transponder radiosonde, type 909-11-XX, where XX correspond to the model of the instrument (USA) |
|  | 65 | 065 | VIZ transponder radiosonde, model number 1499–520 (USA) |
|  | 66 | 066 | Vaisala RS80 /Autosonde (Finland) |
|  | 67 | 067 | Vaisala RS80/Digicora III (Finland) |
|  | 68 | 068 | AVK-RZM-2 (Russian Federation) |
|  | 69 | 069 | MARL-A or Vektor-M-RZM-2 (Russian Federation) |
|  | 70 | 070 | Vaisala RS92/Star (Finland) |
|  | 71 | 071 | Vaisala RS90/Digicora I,II or Marwin (Finland) |
|  | 72 | 072 | Vaisala RS90/PC-Cora (Finland) |
|  | 73 | 073 | Vaisala RS90/Autosonde (Finland) |
|  | 74 | 074 | Vaisala RS90/Star (Finland) |
|  | 75 | 075 | AVK-MRZ-ARMA (Russian Federation) |
|  | 76 | 076 | AVK-RF95-ARMA (Russian Federation) |
|  | 77 | 077 | GEOLINK GPSonde GL98 (France) |
|  | 78 | 078 | Vaisala RS90/Digicora III (Finland) |
|  | 79 | 079 | Vaisala RS92/Digicora I,II or Marwin (Finland) |
|  | 80 | 080 | Vaisala RS92/Digicora III (Finland) |
|  | 81 | 081 | Vaisala RS92/Autosonde (Finland) |
|  | 82 | 082 | Sippican MK2 GPS/STAR (USA) with rod thermistor, carbon element, and derived pressure |
|  | 83 | 083 | Sippican MK2 GPS/W9000 (USA) with rod thermistor, carbon element, and derived pressure |
|  | 84 | 084 | Sippican MARK II with chip thermistor, carbon element, and derived pressure from GPS height |
|  | 85 | 085 | Sippican MARK IIA with chip thermistor, carbon element, and derived pressure from GPS height |
|  | 86 | 086 | Sippican MARK II with chip thermistor, pressure, and carbon element |
|  | 87 | 087 | Sippican MARK IIA with chip thermistor, pressure, and carbon element |
|  | 88 | 088 | MARL-A or Vektor-M-MRZ (Russian Federation) |
|  | 89 | 089 | MARL-A or Vektor-M-MRZ (Russian Federation) |
|  | 90 | 090 | Radiosonde not specified or unknown |
|  | 91 | 091 | Pressure-only radiosonde |
|  | 92 | 092 | Pressure-only radiosonde plus transponder |
|  | 93 | 093 | Pressure-only radiosonde plus radar-reflector |
|  | 94 | 094 | No-pressure radiosonde plus transponder |
|  | 95 | 095 | No-pressure radiosonde plus radar-reflector |
|  | 96 | 096 | Descending radiosonde |
|  | 97–99 | 097–099 | Reserved for allocation of sounding systems with incomplete sondes |
|  | Not available | 100-109 | Reserved |
| 1/05/2007 | 10 | 110 | NNNNNNNNNN |
|  |  | 111–254 | Reserved |
|  |  | 255 | Missing value |

NOTES:

(1)	References to countries in brackets indicate the manufacturing location rather than the country using the instrument.

(2)	Some of the radiosondes listed are no longer in use but are retained for archiving purposes.

(3)	The alphanumeric code format reports only the last 2 digits, and the correct first digit is identified from the date (the first digit is 0 if the observation is before the expiration date of the "old" 2-digit code, or 1 otherwise).