| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES EUMETSAT, 23-27 April 2007 |  | ET/DR&C/Doc. 5.3(3) _______ (1.III.2007) ENGLISH ONLY |
| --- | --- | --- |

Development of a BUFR template for cross-border exchange

of Road Weather Information

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains information on development of a BUFR template

for road weather information as a part of the Regional TDCF Migration Plan.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to take the included information into consideration.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2

[2] SH70 – Road Weather Data Code, DWD-CHMI, 2003.

Background

The cross-boarder exchange of road weather information between the German Meteorological Service (DWD) and the Czech Hydrometeorological Institute (CHMI) has been realized using SH70 code (a modification of German national code SH10).

In compliance with the WMO policy to migrate from traditional alphanumeric codes to table driven code forms, a BUFR template for road weather data has been developed that will allow to transmit not only the parameters included in the SH70 code, but also additional useful parameters and details about road weather stations.

The template and local descriptors were developed by Eva Červená (CHMI) and Sibylle Krebber (DWD) in cooperation with Thomas Endrulat (DWD) and Jan Sulan (CHMI).

BUFR Template Road Weather Information

This template is proposed to be used for representation of road weather data corresponding to the data encoded in SH70 code.

|  |  | Identification |  |
| --- | --- | --- | --- |
| 0 01 018 |  | Short station or site name (for identification of the road weather monitoring site) Dddd | CCITT IA5 (up to 5 characters) |
| 0 01 015 |  | Station or site name | CCITT IA5 (up to 20 characters) |
| 0 01 241 |  | State / federal state identifier | CCITT IA5 (up to 4 characters) |
| 0 01 242 |  | Highway designator | CCITT IA5 (up to 5 characters) |
| 0 01 243 |  | Routes kilometer of highway | m, scale -2 |
| 0 02 243 |  | Extended type of station | Flag table |
| 0 02 244 |  | Type of road | Code table |
| 0 02 245 |  | Type of construction | Code table |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day DD | Day |
| 3 01 012 | 0 04 004 | Hour hh | Hour |
|  | 0 04 005 | Minute mm | Minute |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, scale 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, scale 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
|  |  | Temperature, humidity and visibility data |  |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature snTTT | K, scale 2 |
| 0 12 103 |  | Dew-point temperature snTdTdTd | K, scale 2 |
| 0 13 003 |  | Relative humidity | % |
| 0 07 032 |  | Height of sensor above local ground (= missing value) | m, scale 2 |
| 0 20 001 |  | Horizontal visibility VVVV | m, scale –1 |
|  |  | Road temperature and other data |  |
| 1 09 000 |  | Replicate nine descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | numeric |
| 0 02 242 |  | Position of road sensors | Code table |
| 0 12 241 |  | Road surface temperature snTsTsTs | K, scale 2 |
| 1 02 000 |  | Replicate two descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | numeric |
| 0 07 061 |  | Depth below land surface = 0.30 m in the first replication, = e.g. 0.15 or 0.07 m in the second replication | m, scale 2 |
| 0 12 242 |  | Road sub-surface temperature snTuTuTu | K, scale 2 |
| 0 07 061 |  | Depth below land surface (= missing value) | m, scale 2 |
| 0 13 241 |  | Water film thickness hwhw | m, scale 3 |
| 0 20 241 |  | Road surface condition Sz | Code table |
|  |  | Precipitation data |  |
| 0 04 025 |  | Time period (= - 15 minutes) | Minute |
| 0 20 024 |  | Intensity of phenomena (for intensity of precipitation) KR | Code table |
| 0 13 055 |  | Intensity of precipitation | kg m-2 s-1 , scale 4 |
| 0 20 021 |  | Type of precipitation W | Flag table |
| 0 13 011 |  | Total precipitation / total water equivalent of snow RR | kg m-2, scale 1 |
|  |  | Wind data |  |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 08 021 |  | Time significance (= 2 (time averaged)) | Code table |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute |
| 0 11 001 |  | Wind direction dd | Degree true |
| 0 11 002 |  | Wind speed ff | m s-1, scale 1 |
| 0 08 021 |  | Time significance (= missing value) | Code table |
|  |  | Maximum wind gust |  |
| 0 04 025 |  | Time period in minutes | Minute |
| 0 11 043 |  | maximum wind gust direction | Degree true |
| 0 11 041 |  | maximum wind gust speed | m s-1, scale 1 |
|  |  | State of functionality |  |
| 0 33 005 |  | Quality information (AWS data) F | Flag table |

Notes:

- Telecommunication header – ISXD70  CCCC YYGGgg.

- To represent Intensity of precipitation KR, Type of precipitation W and State of functionality F,   0 20 024 (Code table), 0 20 021(Flag table) and 0 33 005 (Flag table) are used, respectively. The conversion between the code figures for  W and F in the SH70 code and the flag table entries of the corresponding BUFR descriptors is not straightforward.

- To reduce the workload with respect to the station database, some more descriptors are required for e.g. identification of the federal state, identification of the highway and so on.

- Method or name of road sensor manufacturer (m in the SH70 code) ) is not represented in the BUFR template. The corresponding descriptor 0 02 241 is included, however, in ANNEX for potential use in the future if the data from a particular sensor were significantly influenced by its origin or for selective visualization of data measured with sensors of chosen producers only.

- Class of water film thickness (Kw in the SH70 code) is not represented in the BUFR template. It has been considered not to be very useful as there is no standard definition of the classes.

- Majority of stations has only one position on the road and one sub-surface temperature sensor. Delayed replications have been introduced to increase flexibility and volume efficiency.

- Each position of road sensors includes the measurements of

  - road surface temperature

  - road sub-surface temperatures

  - water film thickness

  - road surface condition

- Some type of stations do not have the ability to identify the accurate surface condition. They could only report conditions like "not dry" or "glazed". The code table for road surface conditions has been adjusted accordingly.

ANNEX

Proposal for local descriptors:

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 01 241 | State / federal state identifier | CCITT IA5 | 0 | 0 | 32 | CCITT IA5 | 0 | 4 |
| 0 01 242 | Highway designator | CCITT IA5 | 0 | 0 | 40 | CCITT IA5 | 0 | 5 |
| 0 01 243 | Routes kilometer of highway | m | -2 | 0 | 14 | m | -2 | 5 |
| 0 02 241 | Name of road sensor manufacturer | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 02 242 | Position of road sensors | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 02 243 | Extended type of station | Flag table | 0 | 0 | 6 | Flag table | 0 | 2 |
| 0 02 244 | Type of road | Code table | 0 | 0 | 5 | Code table | 0 | 2 |
| 0 02 245 | Type of construction | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 12 241 | Road surface temperature | K | 2 | 0 | 16 | C | 2 | 4 |
| 0 12 242 | Road sub-surface temperature | K | 2 | 0 | 16 | C | 2 | 4 |
| 0 13 241 | Water film thickness | m | 3 | 0 | 7 | m | 3 | 2 |
| 0 20 241 | Road surface condition | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Note:

0 02 241 (Name of road sensor manufacturer) does not appear in the current template, but it is left  for potential use in the future in case that data from a particular sensor would be significantly influenced by its manufacturer.

Code tables:

0 02 241   Name of road sensor manufacturer

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | ANT/Bosch |
| 2 | Boschung |
| 3 | SSI/Scan (MicKS) |
| 4 | Vaisala |
| 5 | Vibrometer |
| 6 | Malling |
| 7 -14 | Reserved |
| 15 | Missing value |

0 02 242   Position of road sensors

| Code figure |  |
| --- | --- |
| 0 | Fast lane between the wheel tracks |
| 1 | Fast lane between the wheel tracks in the opposite direction |
| 2 | Fast lane in the wheel tracks |
| 3 | Fast lane in the wheel tracks in the opposite direction |
| 4 | Slow lane between the wheel tracks |
| 5 | Slow lane between the wheel tracks in the opposite direction |
| 6 | Slow lane in the wheel tracks |
| 7 | Slow lane in the wheel tracks in the opposite direction |
| 8 - 14 | Reserved |
| 15 | Missing value |

0 02 243   Extended type of station

| Bit No. |  |
| --- | --- |
| 1 | Automatic |
| 2 | Manned |
| 3 | Event triggered |
| 4-5 | Reserved |
| all 6 | Missing value |

0 02 244   Type of road

| Code figure |  |
| --- | --- |
| 0 | Free track without further information |
| 1 | Free track, embankment |
| 2 | Free track, flat relative to surroundings |
| 3 | Free track, water basin(s) in vicinity |
| 4 | Free track, forest |
| 5 | Free track, cleft |
| 6 | Free track, on hilltop |
| 7 | Free track, on hilltop, forest |
| 8 | Free track, in valley |
| 9 | Free track, in valley, forest |
| 10 | Free track, north inclination |
| 11 | Free track, north inclination, forest |
| 12 | Free track, south inclination |
| 13 | Free track, south inclination, forest |
| 14-19 | Reserved |
| 20 | Bridge without further information |
| 21 | Bridge across a valley in a urban area |
| 22 | Bridge across a valley with forest/meadows/fields |
| 23 | Bridge across street/track |
| 24 | Bridge across big river/canal |
| 25 | Bridge across river/canal of medium size |
| 26 | Bridge across a small stream/loading canal |
| 27-30 | Reserved |
| 31 | Missing value |

0 02 245   Type of construction

| Code figure |  |
| --- | --- |
| 0 | Asphalt |
| 1 | Concrete |
| 2 | Concrete construction |
| 3 | Steel-girder construction |
| 4 | Box girder bridge |
| 5 | Orthotrope slab |
| 6 | Drain asphalt |
| 7-14 | Reserved |
| 15 | Missing value |

0 20 241   Road surface condition

| Code figure |  |
| --- | --- |
| 0 | Dry |
| 1 | Moist |
| 2 | Wet |
| 3 | Rime |
| 4 | Snow |
| 5 | Ice |
| 6 | Glaze |
| 7 | Not dry |
| 8-14 | Reserved |
| 15 | Missing value |