| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, OMAN, 5 - 8 DECEMBER 2005 |  | ET DR&C/Doc. 3.1(1) (30.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

## Review of Entries awaiting Validation for becoming Pre-Operational

Submitted by the Secretariat

________________________________________________________________

Summary and Purpose of Document

This document lists the entries awaiting Validation for becoming Pre-Operational, after removal of the entries for SIGMET likely to become pre-operatinal.

________________________________________________________________

ACTION PROPOSED

The ET DR&C meeting is kindly asked to review these entries and consider the status of their validation and possibly recommend some to become pre-operational.

NEW ALLOCATED BUFR/CREX ENTRIES (AWAITING VALIDATION)

(Updated 12/08/05)

#### ADDITIONS FOR REPORTING BOTH NOMINAL AND INSTRUMENT VALUES IN BUFR TEMPLATES FOR SURFACE OBSERVATION DATA

A new descriptor in the Class 8 is proposed as a nominal value indicator (for Level II data):

0 08 083   Nominal value indicator, Flag table, 0, 0, 15

| Bit No. |  |
| --- | --- |
| 1 | Adjusted with respect to representative height of sensor above local ground (or deck of marine platform) |
| 2 | Adjusted with respect to representative height of sensor above water surface |
| 3 | Adjusted with respect to standard surface roughness |
| 4 | Adjusted with respect to wind speed |
| 5 | Adjusted with respect to temperature |
| 6 | Adjusted with respect to pressure |
| 7 | Adjusted with respect to humidity |
| 8 | Adjusted with respect to evaporation |
| 9 | Adjusted with respect to wetting losses |
| 10 -14 | Reserved |
| All 15 | Missing value |

Two new descriptors in Class 7 are proposed

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 07 065 | Representative height of sensor above local ground (or deck of marine platform) | m | 2 | 0 | 16 | m | 2 | 5 |

Note:	Representative height of sensor above local ground (or deck of marine platform) is the standard height of a sensor required by WMO documentation. Value of the following meteorological element should be adjusted using a formula (or a recommended procedure for obtaining nominal values). For example, standard height recommended in WMO documentation for surface wind sensors is 10 m. If the sensor is placed at different height, the wind speed should be adjusted using a formula.

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 07 066 | Representative height of sensor above water surface | m | 1 | 0 | 12 | m | 1 | 4 |

Note:	Representative height of sensor above water surface is the standard height of a sensor required by WMO documentation. Value of the following meteorological element should be adjusted using a formula (or a recommended procedure for obtaining nominal values).

NEW DESCRIPTORS NEEDED FOR DATA REPRESENTATION OF SYNOP DATA

The current version of the template for SYNOP data does not provide facilities for reporting all groups of SYNOP Section 3 described in the international part of Manual on Codes (groups 54g0sndT, 56DLDMDH, 57CDaeC, 58p24p24p24 and 59p24p24p24). BUFR/CREX descriptors are available only for some of these elements. Therefore, the following entries are proposed (0 12 049 for data representation of sndT, 0 20 054 for DL, DM and DH):

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| 0 12 049 | Temperature change over specified period | K | 0 | -30 | 6 | oC | 0 | 2 |
| 0 20 054 | True direction from which clouds are moving | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |

ADD THE FOLLOWING TABLE B ENTRY FOR NUMERICAL MODEL IDENTIFIER :

0 01 030	Numerical model identifier, CCITTIA5, Scale=0, Reference=0,Data bit width=128

Note: The value of this feature could be a string of characters which contains the name of the model and other useful elements such as the model mesh.

#### ADDITIONS FOR REPORTING CORRECTLY INSTANTANEOUS RADIATION

| Table reference | Element name | Unit | Scale | Reference value | Data width |
| --- | --- | --- | --- | --- | --- |
| 0 14 061 | Instantaneous long-wave radiation | W m-2 | 0 | -512 | 10 |
| 0 14 062 | Instantaneous short-wave radiation | W m-2 | 0 | -2048 | 12 |

The Class 14 element descriptors 0 14 017 and 0 14 018 should be deprecated by a note.

#### SEQUENCE DESCRIPTORS FOR SYNOPTIC REPORTS FROM LAND AND SEA STATIONS (SUITABLE FOR SYNOP, SYNOP MOBIL, SHIP AND SHIP FROM VOS STATIONS OBSERVATION DATA)

1. List of sequence descriptors displayed in the templates

The following sequence descriptors for synoptic reports from land and ship (suitable for SYNOP, SYNOP MOBIL, SHIP and SHIP from VOS stations observations data) are listed below within the Templates in paragraph 3.

3 01 092, 3 01 093, 3 02 031, 3 02 032, 3 02 033, 3 02 034, 3 02 035, 3 02 036, 3 02 037, 3 02 038, 3 02 039, 3 02 040, 3 02 041, 3 02 042, 3 02 043, 3 02 044, 3 02 045, 3 02 046, 3 02 047, 3 02 048, 3 02 052, 3 02 053, 3 02 054, 3 02 055, 3 02 056, 3 02 057, 3 02 058, 3 02 059, 3 02 060, 3 02 062, 3 02 063 and 3 07 070.

2. Sequence descriptors 3 02 046, 3 02 047 and 3 02 048

3 02 046 is proposed to express the data of the SYNOP group 54g0sndT, where

g0  is “Period of time, in hours, between the time of observation and the temperature change”,

sn   is “Sign of the temperature change” – Code table 3845,

dT  is “ Amount of temperature change, the sign of the change given by sn “– Code table 0822.

|  |  |  |  |  |  | (Temperature change) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 046 | 0 | 04 | 024 | Time period or displacement |
|  |  |  | 0 | 04 | 024 | Time period or displacement |
|  |  |  | 0 | 12 | 049 | Temperature change over period specified |

3 02 047 is proposed to express data of SYNOP group 56DLDMDH, where

DL  is  “True direction from which CL clouds are moving” – Code table 0700,

DM  is  “True direction from which CM clouds are moving” – Code table 0700,

DH  is  “True direction from which CH clouds are moving”  – Code table 0700.

|  |  |  |  |  |  | (Direction of cloud drift) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 047 | 1 | 02 | 003 | Replicate 2 descriptors 3 times |
|  |  |  | 0 | 08 | 002 | Vertical significance |
|  |  |  | 0 | 20 | 054 | True direction from which clouds are moving |

3 02 048 is proposed to express data of SYNOP group 57CDaeC, where

C  is  “Genus of cloud” – Code table 0500,

Da  is  “True direction in which the phenomenon indicated is observed” – Code table 0700,

eC is  “Elevation angle of the top of the cloud indicated by C”  – Code table 1004.

|  |  |  |  |  |  | (Direction and elevation of cloud) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 048 | 0 | 05 | 021 | Bearing or azimuth |
|  |  |  | 0 | 07 | 021 | Elevation angle |
|  |  |  | 0 | 20 | 012 | Cloud type |
|  |  |  | 0 | 05 | 021 | Bearing or azimuth ( = missing to cancel the previous value) |
|  |  |  | 0 | 07 | 021 | Elevation angle ( = missing to cancel the previous value) |

3. Review of BUFR templates for synoptic reports from land and sea stations (suitable for SYNOP, SYNOP MOBIL, SHIP and SHIP from VOS stations observation data)

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM LAND STATIONS SUITABLE FOR SYNOP OBSERVATION DATA

| 3 01 090 |  |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 004 | 0 01 001 | WMO block number II | Numeric, 0 |
|  |  | 0 01 002 | WMO station number iii | Numeric, 0 |
|  |  | 0 01 015 | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 031 | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  | 0 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  | Pressure (standard level) a3 | Pa, –1 |
|  | 0 10 009 |  | Geopotential height of the standard level hhh | gpm, 0 |
| 3 02 035 |  |  | Basic synoptic “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 033 | 0 07 032 | Height of sensor above local ground (for visibility measurement) | m, 2 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  |  |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | Cloud top description Ct | Code table, 0 |
|  |  |  | Direction of cloud drift gr. 56DLDMDH |  |
| 3 02 047 | 1 02 003 |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | Vertical significance = 7 (low cloud) = 8 (middle cloud) = 9 (high cloud) | Code table, 0 |
|  | 0 20 054 |  | True direction from which clouds are moving DL, DM, DH | Degree true, 0 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Direction and elevation of cloud gr. 57CDaeC |  |
| 3 02 048 | 0 05 021 |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  | State of ground, snow depth, ground minimum temperature |  |
| 3 02 037 | 0 20 062 |  | State of ground (with or without snow) E or E’ | Code table, 0 |
|  | 0 13 013 |  | Total snow depth sss | m, 2 |
|  | 0 12 113 |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, 2 |
| 3 02 043 |  |  | Basic synoptic “period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Sunshine data |  |
|  | 1 02 002 |  | Replicate 2 descriptors 2 times |  |
|  | 3 02 039 | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 14 031 | Total sunshine SS and SSS | Minute, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 041 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 042 | 0 07 032 | Height of sensor above local ground (for wind measurement) | m, 2 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Evaporation data |  |
| 3 02 044 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 02 004 |  | Type of instrument for evaporation or crop type for evapotranspiration iE | Code table, 0 |
|  | 0 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1 |
|  |  |  | Radiation data (from 1 hour and 24 hour period) |  |
| 1 01 002 |  |  | Replicate next descriptor 2 times |  |
| 3 02 045 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified 553SS 4FFFF or 553SS 5FFFF, 55SSS 4F24F24F24F24 or 55SSS 5F24F24F24F24 | J m-2, -3 |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified 553SS 6FFFF, 55SSS 6F24F24F24F24 | J m-2, -3 |
|  | 0 14 016 |  | Net radiation, integrated over period specified 553SS 0FFFF or 553SS 1FFFF, 55SSS 0F24F24F24F24 or 55SSS 1F24F24F24F24 | J m-2, -4 |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified 553SS 2FFFF, 55SSS 2F24F24F24F24 | J m-2, -4 |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified 553SS 3FFFF, 55SSS 3F24F24F24F24 | J m-2, -4 |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified 55408 4FFFF, 55508 5F24F24F24F24 | J m-2, -4 |
| 3 02 046 |  |  | Temperature change group 54g0sndT |  |
|  | 0 04 024 |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | Time period or displacement (see Note 3) | Hour, 0 |
|  | 0 12 049 |  | Temperature change over period specified sndT | K, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)	To construct the required time range, descriptor 004024 has to be included two times.

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM LAND STATIONS SUITABLE FOR SYNOP MOBIL OBSERVATION DATA

BUFR template for SYNOP MOBIL is similar to the BUFR template for SYNOP.  The only difference between them is in the very first sequence descriptor; in case of representation of SYNOP MOBIL data, the station identification, time, horizontal and vertical coordinates is provided by a newly proposed sequence descriptor 3 01 092:

| 3 01 092 |  |  | Mobile surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 0 01 011 |  | Mobile land station identifier D….D | CCITT IA5, 0 |
|  | 0 01 003 |  | WMO Region number A1 | Code table, 0 |
|  | 0 02 001 |  | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) LaLaLa | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) LoLoLoLo | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  | 0 33 024 |  | Station elevation quality mark im | Code table, 0 |

The rest of the template is identical with the BUFR template for SYNOP data, including the Notes below the template for SYNOP data.

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM SEA STATIONS SUITABLE FOR SHIP OBSERVATION DATA

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 001 | 0 10 004 |  | Pressure P0P0P0P0 | Pa, –1 |
|  | 0 10 051 |  | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  | 0 10 061 |  | 3-hour pressure change ppp | Pa, –1 |
|  | 0 10 063 |  | Characteristic of pressure tendency a | Code table, 0 |
| 3 02 054 |  |  | SHIP “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
| 3 02 055 | 0 20 031 |  | Ice deposit (thickness) EsEs | m, 2 |
|  | 0 20 032 |  | Rate of ice accretion Rs | Code table, 0 |
|  | 0 20 033 |  | Cause of ice accretion Is | Flag table, 0 |
|  | 0 20 034 |  | Sea ice concentration ci | Code table, 0 |
|  | 0 20 035 |  | Amount and type of ice bi | Code table, 0 |
|  | 0 20 036 |  | Ice situation zi | Code table, 0 |
|  | 0 20 037 |  | Ice development Si | Code table, 0 |
|  | 0 20 038 |  | Bearing of ice edge Di | Degree true, 0 |
| 3 02 057 |  |  | SHIP marine data |  |
|  |  |  | Sea/water temperature |  |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 060 |  |  | SHIP“period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 059 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)	0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4)	0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5)	If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM SEA STATIONS SUITABLE FOR SHIP OBSERVATION DATA FROM VOS STATIONS

3 07 070  =  3 01 093  +  3 02 062   +  3 02 063

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 062 |  |  | SHIP “instantaneous” data from VOS |  |
|  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  | 0 08 002 |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 055 | 0 20 031 | Ice deposit (thickness) EsEs | m, 2 |
|  |  | 0 20 032 | Rate of ice accretion Rs | Code table, 0 |
|  |  | 0 20 033 | Cause of ice accretion Is | Flag table, 0 |
|  |  | 0 20 034 | Sea ice concentration ci | Code table, 0 |
|  |  | 0 20 035 | Amount and type of ice bi | Code table, 0 |
|  |  | 0 20 036 | Ice situation zi | Code table, 0 |
|  |  | 0 20 037 | Ice development Si | Code table, 0 |
|  |  | 0 20 038 | Bearing of ice edge Di | Degree true, 0 |
|  |  |  | Sea/water temperature |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 063 |  |  | SHIP“period” data from VOS |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 059 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  |  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)	0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4)	0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5)	If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

Descriptors and Code tables

for TRACKOB and  RADOB data

1. For TRACKOB template

Class 02 - Instrumentation

| 0 | 02 | 042 | Indicator for sea surface current speed | Code table | 0 | 0 | 2 | Code table | 0 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 04 - Location (time)

| 0 | 04 | 080 | Averaging period for following value | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 22 - Oceanographic elements

| 0 | 22 | 005 | Direction of sea surface current | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 22 | 032 | Speed of sea surface current | m s-1 | 2 | 0 | 13 | m s-1 | 2 | 4 |
| 0 | 22 | 049 | Sea surface temperature | K | 2 | 0 | 15 | K | 2 | 5 |
| 0 | 22 | 059 | Sea surface salinity | Part per thousand | 2 | 0 | 14 | Part per thousand | 2 | 5 |

0 02 042

Indicator for sea surface current speed

| Code figure |  |
| --- | --- |
| 0 | Value originally reported in m/s |
| 1 | Value originally reported in knots |
| 2 | No sea current data available |
| 3 | Missing |

0 04 080

Averaging period for following value

| Code figure |  |
| --- | --- |
| 0 | Spot values |
| 1 | Less than 15 minutes |
| 2 | From 15 to 45 minutes |
| 3 | More than 45 minutes |
| 4-8 | Reserved |
| 9 | Data not available |
| 10-14 | Not used |
| 15 | Missing |

2. For RADOB template

Class 02 - Instrumentation

| 0 | 02 | 160 | Wave length of the radar | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 19 - Synoptic features

| 0 | 19 | 100 | Time interval over which the movement of the centre or the eye of the tropical cyclone has been calculated | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 19 | 101 | Accuracy of the position of the centre or the eye of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 102 | Shape and definition of the eye of the tropical cyclone | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 103 | Diameter or length of major axis of the eye of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 104 | Change in character of the eye during the 30 minutes preceding the time of observation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 105 | Distance between the end of the observed outermost spiral band and the centre of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

New code tables:

0 02 160

Wave length of the radar

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | 10 to less than 20 mm |
| 2 | Reserved |
| 3 | 20 to less than 40 mm |
| 4 | Reserved |
| 5 | 40 to less than 60 mm |
| 6 | Reserved |
| 7 | 60 to less than 90 mm |
| 8 | 90 to less than 110 mm |
| 9 | 110 mm and greater |
| 10-14 | Not used |
| 15 | Missing value |

0 19 100

Time interval over which the movement of the centre or the eye of the tropical

cyclone has been calculated

| Code figure |  |
| --- | --- |
| 0-2 | Not used |
| 3 | During the preceding 15 minutes |
| 4 | During the preceding 30 minutes |
| 5 | During the preceding 1 hour |
| 6 | During the preceding 2 hours |
| 7 | During the preceding 3 hours |
| 8 | During the preceding 6 hours |
| 9 | During a period of more than 6 hours |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 101

Accuracy of the position of the centre or the eye of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | Eye visible on radar scope, accuracy good (within 10 km) |
| 2 | Eye visible on radar scope, accuracy fair (within 30 km) |
| 3 | Eye visible on radar scope, accuracy poor (within 50 km) |
| 4 | Position of the centre within the area covered by the radar scope, determination by means of the spiral-band overlay, accuracy good (within 10 km) |
| 5 | Position of the centre within the area covered by the radar scope, determination by means of the spiral-band overlay, accuracy fair (within 30 km) |
| 6 | Position of the centre within the area covered by the radar scope, determination by means of the spiral-band overlay, accuracy poor (within 50 km) |
| 7 | Position of the centre outside the area covered by the radar scope, extrapolation by means of the spiral-band overlay |
| 8-9 | Reserved |
| 10 | Accuracy undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 102

Shape and definition of the eye of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Circular |
| 1 | Elliptical — the minor axis is at least 3/4 the length of the major axis well defined |
| 2 | Elliptical — the minor axis is less than 3/4 the length of the major axis |
| 3 | Apparent double eye |
| 4 | Other shape |
| 5 | Ill defined |
| 6 | Undetermined |
| 7 | Missing |

0 19 103

Diameter or length of major axis of the eye of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Less than 5 km |
| 1 | 5 to less than 10 km |
| 2 | 10 to less than 15 km |
| 3 | 15 to less than 20 km |
| 4 | 20 to less than 25 km |
| 5 | 25 to less than 30 km |
| 6 | 30 to less than 35 km |
| 7 | 35 to less than 40 km |
| 8 | 40 to less than 50 km |
| 9 | 50 km and greater |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 104

Change in character of the eye during the 30 minutes

preceding the time of observation

| Code figure |  |
| --- | --- |
| 0 | Eye has first become visible during the past 30 minutes |
| 1 | No significant change in the characteristics or size of the eye |
| 2 | Eye has become smaller with no other significant change in characteristics |
| 3 | Eye has become larger with no other significant change in characteristics |
| 4 | Eye has become less distinct with no significant change in size |
| 5 | Eye has become less distinct and decreased in size |
| 6 | Eye has become less distinct and increased in size |
| 7 | Eye has become more distinct with no significant change in size |
| 8 | Eye has become more distinct and decreased in size |
| 9 | Eye has become more distinct and increased in size |
| 10 | Change in character and size of eye cannot be determined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 105

Distance between the end of the observed outermost spiral band

and the centre of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | 0 to less than 100 km |
| 1 | 100 to less than 200 km |
| 2 | 200 to less than 300 km |
| 3 | 300 to less than 400 km |
| 4 | 400 to less than 500 km |
| 5 | 500 to less than 600 km |
| 6 | 600 to less than 800 km |
| 7 | 800 km or more |
| 8-9 | Reserved |
| 10 | Doubtful or undetermined |
| 11-14 | Not used |
| 15 | Missing value |

Descriptors and Code tables for SAREP Template

Class 25 - Processing information

| 0 | 25 | 150 | Method of tropical cyclone intensity analysis using satellite data | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 19 - Synoptic features

| 0 | 19 | 106 | Identification number of tropical cyclone | Numeric | 0 | 0 | 7 | Numeric | 0 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 19 | 107 | Time interval over which the movement of the tropical cyclone has been calculated | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 108 | Accuracy of determination of the geographical position of the tropical cyclone | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 109 | Mean width or mean diameter of the feature specified by SfSf,or mean diameter of the overcast cloud of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 110 | Apparent 24-hour change in intensity of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 111 | Intensity of the tropical cyclone (Current Intensity (CI) number) | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 112 | Data tropical (DT) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 113 | Cloud pattern type of the DT-number | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 114 | Model Expected tropical (MET) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 115 | Trend of the past 24-hour intensity change of the tropical cyclone by comparing the cloud features (+: Developed, -: Weakened) | Numeric | 1 | -30 | 6 | Numeric | 1 | 2 |
| 0 | 19 | 116 | Pattern tropical (PT) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 117 | Cloud picture type of the PT-number | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 118 | Final tropical (T) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 119 | Type of the final T-number | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 150 | Typhoon International Common Number (Typhoon Committee) | CCITTIA5 | 0 | 0 | 32 | Character | 0 | 4 |

New Code Tables:

0 25 150

Method of tropical cyclone intensity analysis using satellite data

| Code figure | Method |
| --- | --- |
| 1 | The Dvorak intensity analysis using VIS (visual imagery) data |
| 2 | The Dvorak intensity analysis using EIR (Enhanced Infrared imagery) data |
| 3-14 | Reserved |
| 15 | Missing value |

0 19 107

Time interval over which the movement of the tropical cyclone

has been calculated

| Code figure |  |
| --- | --- |
| 0 | Less than 1 hour |
| 1 | 1 to less than 2 hours |
| 2 | 2 to less than 3 hours |
| 3 | 3 to less than 6 hours |
| 4 | 6 to less than 9 hours |
| 5 | 9 to less than 12 hours |
| 6 | 12 to less than 15 hours |
| 7 | 15 to less than 18 hours |
| 8 | 18 to less than 21 hours |
| 9 | 21 to less than 30 hours |
| 10-14 | Not used |
| 15 | Missing value |

0 19 108

Accuracy of determination of the geographical position of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Cyclone centre within 10 km of the transmitted position |
| 1 | Cyclone centre within 20 km of the transmitted position |
| 2 | Cyclone centre within 50 km of the transmitted position |
| 3 | Cyclone centre within 100 km of the transmitted position |
| 4 | Cyclone centre within 200 km of the transmitted position |
| 5 | Cyclone centre within 300 km of the transmitted position |
| 6 | Cyclone centre undetermined |
| 7 | Missing value |

0 19 109

Mean width or mean diameter of the feature specified by SfSf,

or mean diameter of the overcast cloud of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Less than 1° of latitude |
| 1 | 1° to less than 2° of latitude |
| 2 | 2° to less than 3° of latitude |
| 3 | 3° to less than 4° of latitude |
| 4 | 4° to less than 5° of latitude |
| 5 | 5° to less than 6° of latitude |
| 6 | 6° to less than 7° of latitude |
| 7 | 7° to less than 8° of latitude |
| 8 | 8° to less than 9° of latitude |
| 9 | 9° of latitude or more |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 110

Apparent 24-hour change in intensity of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Much weakening |
| 1 | Weakening |
| 2 | No change |
| 3 | Intensification |
| 4 | Strong Intensification |
| 5-8 | Reserved |
| 9 | Not observed previously |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 113

Cloud pattern type of the DT-number

| Code figure | Type |
| --- | --- |
| 1 | Curved Band |
| 2 | Shear |
| 3 | Eye |
| 4 | Banding Eye |
| ５ | Central Dense Overcast (CDO) |
| 6 | Embedded Center |
| 7 | Center Cold Cover (CCC) |
| 8-14 | Reserved |
| 15 | Missing value |

0 19 117

Cloud picture type of the PT-number

| Code figure | Type |
| --- | --- |
| 1 | A (Curved Band) |
| 2 | B (CDO) |
| 3 | C (Shear) |
| 4-6 | Reserved |
| 7 | Missing value |

0 19 119

Type of the final T-number

| Code figure | Type |
| --- | --- |
| 1 | DT-number |
| 2 | PT-number |
| 3 | MET-number |
| 4-6 | Reserved |
| 7 | Missing value |