| WORLD METEOROLOGICAL ORGANIZATION ________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, OMAN, 5 - 8 DECEMBER 2005 |  | ET/DR&C/Doc. 3.10(7) _______ (17.XI.2005) ENGLISH only |
| --- | --- | --- |

OTHER ADDITIONS TO BUFR/CREX

Additional entries for polar satellite data

Submitted by Simon Elliott (EUMETSAT)

________________________________________________________________

Summary and Purpose of Document

This document contains proposals for additional BUFR element descriptors, sequence descriptors, and code table entries required for the representation of data from the Metop and NOAA18 spacecraft.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the submitted proposals and to consider the possible allocation of the requested entries.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

#### Discussion

#### 1. Background

The successful launch of NOAA 18 marked the start of the Initial Joint Polar System (IJPS), being operated by NOAA and EUMETSAT.  On NOAA 18, the AMSU-B instrument previously in the ATOVS package has been replaced by MHS (the Mircowave Humidity Sounder), supplied by EUMETSAT.

Within the context of the IJPS, EUMETSAT plans to launch the first of its polar spacecraft, Metop 2, in June 2006.  In addition to EUMETSAT's instruments GRAS (a radio occultation sounder), GOME2 (a high resolution spectrometer), IASI (a hyperspectral sounder), ASCAT (a scatterometer), and MHS, the spacecraft will also have AVHRR, AMSU-A and HIRS instruments from the USA.

Data from AMSU-A, MHS, HIRS, IASI, GRAS and ASCAT will be exchanged in BUFR.  In order to represent data from the new instruments, new BUFR element descriptors, sequence descriptors, and code and flag table entries required.

2. Proposal for new code table entries

# 2.1 MHS

The MHS instrument replaces the AMSU-B instrument in the ATOVS package operated by EUMETSAT and NOAA.  The level 1b data from the MHS can be represented in BUFR using exactly the same sequence of descriptors, which was used for AMSU-B.

The following changes are required to standardize the representation of MHS data:

Code Table 0-02-048

Add: 		11, Parameter = MHS

Change: 	11 to 14, Parameter = Reserved

to:		12 to 14, Parameter = Reserved

Code Table 0-02-150

Add: 		54, Parameter = MHS 1

Add: 		55, Parameter = MHS 2

Add: 		56, Parameter = MHS 3

Add: 		57, Parameter = MHS 4

Add: 		58, Parameter = MHS 5

Change: 	54 to 62, Parameter = Reserved

to:		59 to 62, Parameter = Reserved

Code Table 0-02-151

Add: 		9, Parameter = MHS

Change: 	8 to 2046, Parameter = Reserved

to:		10 to 2046, Parameter = Reserved

Sequence Descriptor 3-10-010

Change:	Title = "ATOVS AMSU-B report"

to:		Title = "ATOVS AMSU-B / MHS report"

2.2 IASI

The IASI instrument is a hyperspectral sounder, which will fly on the Metop spacecraft operated by EUMETSAT.  The level 1c data from IASI will be exchanged in BUFR.  The details of the representation of the data have been discussed by many parties (ECMWF, UK Met Office, NOAA, MeteoFrance, DWD) in great detail and presented at several international meetings (including the 14th International TOVS Study Conference in Beijing).  Synthetic IASI data are being generated in near real time by NOAA using the descriptors proposed here.  These data have been successfully encoded and decoded by independent software.

The new element and sequence descriptors given here are from the range of local values and are shown in parentheses.   It is proposed to assign descriptors from Classes and Categories 40, 41 and 42 of BUFR Tables B and D within Master Tables 0, as per Section 3.5 of the Final Report of the 2004 meeting of the ET/DR&C.

The following changes are required to standardize the representation of IASI data:

New Sequence Descriptor (3-50-102): " IASI Level 1c data"

| 0-01-007 | Satellite identifier |
| --- | --- |
| 0-01-031 | Identification of originating/generating centre |
| 0-02-019 | Satellite instruments |
| 0-02-020 | Satellite classification |
| 0-04-001 | Year |
| 0-04-002 | Month |
| 0-04-003 | Day |
| 0-04-004 | Hour |
| 0-04-005 | Minute |
| 2-02-131 | Add 3 to scale |
| 2-01-138 | Add 10 to width |
| 0-04-006 | Second |
| 2-01-000 | Reset width |
| 2-02-000 | Reset scale |
| 0-07-024 | Satellite zenith angle |
| 0-05-021 | Bearing or azimuth |
| 0-07-025 | Solar zenith angle |
| 0-05-022 | Solar azimuth |
| 0-05-043 | Field of view number |
| 0-05-040 | Orbit number |
| 2-01-133 | Add 5 to width |
| 0-05-041 | Scan line number |
| 2-01-000 | Reset width |
| 2-01-132 | Add 4 to width |
| 0-25-070 | Major frame count |
| 2-01-000 | Reset width |
| 2-02-126 | Subtract 2 from scale |
| 0-07-001 | Height of station |
| 2-02-000 | Reset scale |
| (0-33-192) | GQisFlagQual |
| (0-33-193) | QGisQualIndex |
| (0-33-194) | QGisQualIndexLoc |
| (0-33-195) | QGisQualIndexRad |
| (0-33-196) | QGisQualIndexSpect |
| (0-33-197) | GQisSysTecSondQual |
| 1-01-010 | Repeat next 1 descriptor 10 times |
| (3-50-103) | IASI Level 1c band description |
| 1-01-087 | Repeat next 1 descriptor 87 times |
| (3-50-104) | IASI Level 1c 100 channel sequence |
| 0-02-019 | Satellite instruments |
| 0-25-051 | AVHRR channel combination |
| 1-01-007 | Repeat next 1 descriptor 7 times |
| (3-50-106) | IASI Level 1c AVHRR single scene sequence |

New Sequence Descriptor: (3-50-103) "IASI Level 1c band description"

| (0-25-192) | Start channel |
| --- | --- |
| (0-25-193) | End channel |
| (0-25-194) | Channel scale factor |

New Sequence Descriptor: (3-50-104) " IASI Level 1c 100 channel sequence"

| 1-04-100 | Repeat next 4 descriptor 100 times |
| --- | --- |
| 2-01-136 | Add 8 to width |
| 0-05-042 | Channel number |
| 2-01-000 | Reset width |
| (0-14-192) | Scaled IASI radiance |

New Sequence Descriptor: (3-50-106) " IASI Level 1c AVHRR single scene sequence"

| (0-05-192) | Y angular position from centre of gravity |
| --- | --- |
| (0-05-193) | Z angular position from centre of gravity |
| 0-25-085 | Fraction of clear pixels in HIRS FOV |
| 1-05-006 | Repeat next 5 descriptor 6 times |
| 0-05-042 | Channel number |
| (0-25-194) | Channel scale factor |
| (0-14-193) | Scaled mean AVHRR radiance |
| (0-25-194) | Channel scale factor |
| (0-14-194) | Scaled std dev AVHRR radiance |

New Element Descriptors:

| Descriptor | Name | Units | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
| (0-05-192) | Y angular position from centre of gravity | Degree | 6 | -8000000 | 24 |
| (0-05-193) | Z angular position from centre of gravity | Degree | 6 | -8000000 | 24 |
| (0-14-192) | Scaled IASI radiance | None | 0 | 0 | 16 |
| (0-14-193) | Scaled mean AVHRR radiance | None | 0 | 0 | 31 |
| (0-14-194) | Scaled std dev AVHRR radiance | None | 0 | 0 | 31 |
| (0-25-192) | Start channel | None | 0 | 0 | 14 |
| (0-25-193) | End channel | None | 0 | 0 | 14 |
| (0-25-194) | Channel scale factor | None | 0 | 0 | 6 |
| (0-33-192) | GQisFlagQual - individual IASI-System quality flag | Code Table | 0 | 0 | 2 |
| (0-33-193) | GQisQualIndex - indicator for instrument noise performance (contributions from spectral and radiometric) | % | 0 | 0 | 7 |
| (0-33-194) | GQisQualIndexLoc - indicator for geometric quality index | % | 0 | 0 | 7 |
| (0-33-195) | GQisQualIndexRad - indicator for instrument noise performance (contributions from radiometric calibration) | % | 0 | 0 | 7 |
| (0-33-196) | GQisQualIndexSpect - indicator for instrument noise performance (contributions from spectral calibration) | % | 0 | 0 | 7 |
| (0-33-197) | GQisSysTecSondQual - output of a function | Code Table | 0 | 0 | 24 |

New Code Table (0-33-192) "GQisFlagQual - individual IASI-System quality flag"

0, 			Parameter = Okay

1, 			Parameter = Bad

2, 			Parameter = Reserved

3, 			Parameter = Missing

New Code Table (0-33-197) " GQisSysTecSondQual - output of TEC function"

0 to 16777214, 	Parameter = Reserved

16777215, 		Parameter = Missing

#### 2.3 ASCAT

EUMETSAT will produce level 1b ASCAT products at its headquarters in Darmstadt, Germany.  These data will be encoded in BUFR and disseminated via EUMETCast (DVB satellite multicast service) and on the GTS.  EUMETSAT's Ocean and Sea Ice Satellite Application Facility (OSI-SAF), hosted by KNMI, will produce level 2 products from the level 1b data.  It is also foreseen to add soils moisture to the level 2 ASCAT product in the future.

The new element and sequence descriptors given here have been developed by close co-operation between EUMETSAT, the OSI-SAF and the ASCAT Science Advisory Group (SAG).  The proposed sequence will accommodate both the level 1b and the level 2 data simultaneously.  When the level 1b data leave EUMETSAT, the parts of the sequence relating to level 2 processing will be set to "missing".  This approach will allow users to ingest the same sequence, whether they are receiving level 1b data or level 2 data.

The new element and sequence descriptors are from the range of local values and are shown in parentheses.   It is proposed to assign descriptors from Classes and Categories 40, 41 and 42 of BUFR Tables B and D within Master Tables 0, as per Section 3.5 of the Final Report of the 2004 meeting of the ET/DR&C.

The following changes are required to standardize the representation of ASCAT data:

New Sequence Descriptor: (3-12-225) "ASCAT Level 1b and level 2 data sequence"

| (3-12-218) | ASCAT level 1b data |
| --- | --- |
| (3-12-220) | Scatterometer soil moisture data |
| (3-12-219) | Scatterometer wind data |

New Sequence Descriptor: (3-12-218) "ASCAT level 1b data sequence"

| (3-01-203) | ASCAT header information |
| --- | --- |
| 3-01-011 | Date information |
| 3-01-013 | Time information |
| 3-01-021 | Position information |
| (3-12-215) | ASCAT level 1b cell information |
| (0-21-192) | Beam co-location |
| 1-01-003 | Repeat next 1 descriptor 3 times |
| (3-21-192) | ASCAT sigma-0 information |

New Sequence Descriptor: (3-12-220) "Scatterometer soil moisture data sequence"

| 0-25-060 | Software identification |
| --- | --- |
| (0-25-192) | Database identification |
| (0-40-001) | Surface soil moisture (ms) |
| (0-40-002) | Estimated error in surface soil moisture |
| 0-21-062 | Extrapolated backscatter at 40deg incidence angle (sigma0_40) |
| (0-21-193) | Estimated error in sigma0 at 40deg incidence angle |
| (0-21-194) | Slope at 40deg incidence angle |
| (0-21-195) | Estimated error in slope at 40deg incidence angle |
| (0-21-196) | Soil moisture sensitivity |
| 0-21-062 | Dry backscatter |
| 0-21-062 | Wet backscatter |
| (0-40-003) | Mean surface soil moisture |
| (0-40-004) | Rain fall detection |
| (0-40-005) | Soil moisture correction flag |
| (0-40-006) | Soil moisture processing flag |
| (0-40-007) | Soil moisture quality |
| 0-20-065 | Snow cover |
| (0-40-008) | Frozen land surface fraction |
| (0-40-009) | Inundation and wetland fraction |
| (0-40-010) | Topographic complexity |

New Sequence Descriptor: (3-12-219) "Scatterometer wind data sequence"

| (3-12-216) | Scatterometer wind cell information |
| --- | --- |
| 1-01-000 | Delayed replication of next 1 descriptor |
| 0-31-001 | Delayed replication factor |
| (3-12-217) | Ambiguous wind data |

New Sequence Descriptor: (3-01-203) "ASCAT header information sequence"

| 0-01-033 | Identification of originating/generating centre |
| --- | --- |
| 0-01-034 | Identification of originating/generating sub-centre |
| 0-25-060 | Software identification |
| 0-01-007 | Satellite identifier |
| 0-02-019 | Satellite instruments |
| 0-01-012 | Direction of motion of moving observing platform |

New Sequence Descriptor: (3-12-215) " ASCAT level 1b cell information"

| 0-05-033 | Pixel size on horizontal-1 |
| --- | --- |
| 0-05-040 | Orbit number |
| 0-06-034 | Cross track cell number |
| (0-07-192) | Height of atmosphere used |
| (0-21-245) | Loss per unit length of atmosphere used |

New Sequence Descriptor: (3-21-192) "ASCAT sigma-0 information"

| (0-08-192) | Beam identifier |
| --- | --- |
| 2-02-129 | Increase scaling by 10^1 |
| 2-01-131 | Increase data width by 3 bits |
| 0-02-111 | Radar incidence angle |
| 2-01-000 | Cancel change data width |
| 2-01-132 | Increase data width by 4 bits |
| 0-02-134 | Antenna beam azimuth |
| 2-01-000 | Cancel change data width |
| 2-02-000 | Cancel change scaling |
| 0-21-062 | Backscatter |
| 0-21-063 | Radiometric resolution (noise value) |
| (0-21-246) | ASCAT kp estimate quality |
| (0-21-247) | ASCAT sigma-0 usability |
| (0-21-248) | ASCAT synthetic data quality |
| (0-21-249) | ASCAT synthetic data quantity |
| (0-21-250) | ASCAT satellite orbit and attitude quality |
| (0-21-251) | ASCAT solar array reflection contamination |
| (0-21-252) | ASCAT telemetry presence and quality |
| (0-21-253) | ASCAT extrapolated reference function |
| (0-21-254) | ASCAT land fraction |

New Sequence Descriptor: (3-12-216) "Scatterometer wind cell information sequence"

| 0-25-060 | Software identification |
| --- | --- |
| 0-01-032 | Generating application |
| 0-11-082 | Model wind speed at 10 m |
| 0-11-081 | Model wind direction at 10 m |
| (0-20-195) | Ice probability |
| (0-20-196) | Ice age (a-parameter) |
| (0-21-216) | Wind vector cell quality |
| 2-01-133 | Increase data width by 5 bits |
| 0-21-101 | Number of vector ambiguities |
| 0-21-102 | Index of selected wind vector |
| 2-01-000 | Cancel change data width |

New Sequence Descriptor: (3-12-217) "Ambiguous wind data"

| 2-01-130 | Increase data width by 2 bits |
| --- | --- |
| 2-02-129 | Increase scaling by 10^1 |
| 0-11-012 | Wind speed at 10 m |
| 2-02-000 | Cancel change scaling |
| 2-01-000 | Cancel change data width |
| 2-01-131 | Increase data width by 3 bits |
| 2-02-129 | Increase scaling by 10^1 |
| 0-11-011 | Wind direction at 10 m |
| 2-02-000 | Cancel change scaling |
| 2-01-000 | Cancel change data width |
| (0-21-226) | Backscatter distance |
| 0-21-104 | Likelihood computed for solution |

New Element Descriptors:

| Descriptor | Name | Units | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
| (0-07-192) | Height of atmosphere used | m | 0 | 0 | 16 |
| (0-08-192) | Beam identifier | Code table | 0 | 0 | 3 |
| (0-20-195) | Ice probability | Numeric | 3 | 0 | 10 |
| (0-20-196) | Ice age ("A" parameter) | dB | 2 | -4096 | 13 |
| (0-21-192) | Beam collocation | Code table | 0 | 0 | 2 |
| (0-21-193) | Estimated error in sigma0 at 40deg incidence angle | dB | 2 | 0 | 9 |
| (0-21-194) | Slope at 40deg incidence angle | dB/Deg | 2 | -80 | 7 |
| (0-21-195) | Estimated error in slope at 40deg incidence angle | dB/Deg | 2 | -40 | 6 |
| (0-21-196) | Soil moisture sensitivity | dB | 2 | 0 | 12 |
| (0-21-216) | Wind vector cell quality | Flag table | 0 | 0 | 24 |
| (0-21-226) | Backscatter distance | Numeric | 1 | -4096 | 13 |
| (0-21-245) | Loss per unit length of atmosphere used | dB m-1 | 10 | 0 | 22 |
| (0-21-246) | ASCAT kp estimate quality | Code table | 0 | 0 | 2 |
| (0-21-247) | ASCAT sigma-0 usability | Code table | 0 | 0 | 2 |
| (0-21-248) | ASCAT use of synthetic data | Numeric | 3 | 0 | 10 |
| (0-21-249) | ASCAT synthetic data quantity | Numeric | 3 | 0 | 10 |
| (0-21-250) | ASCAT satellite orbit and attitude quality | Numeric | 3 | 0 | 10 |
| (0-21-251) | ASCAT solar array reflection contamination | Numeric | 3 | 0 | 10 |
| (0-21-252) | ASCAT telemetry presence and quality | Numeric | 3 | 0 | 10 |
| (0-21-253) | ASCAT extrapolated reference function presence | Numeric | 3 | 0 | 10 |
| (0-21-254) | ASCAT land fraction | Numeric | 3 | 0 | 10 |
| (0-25-192) | Database identification | Numeric | 0 | 0 | 14 |
| (0-40-001) | Surface soil moisture (ms) | % | 1 | 0 | 10 |
| (0-40-002) | Estimated error in surface soil moisture | % | 1 | 0 | 10 |
| (0-40-003) | Mean surface soil moisture | Numeric | 3 | 0 | 10 |
| (0-40-004) | Rain fall detection | Numeric | 3 | 0 | 10 |
| (0-40-005) | Soil moisture correction flag | Flag table | 0 | 0 | 8 |
| (0-40-006) | Soil moisture processing flag | Flag table | 0 | 0 | 16 |
| (0-40-007) | Soil moisture quality | % | 1 | 0 | 10 |
| (0-40-008) | Frozen land surface fraction | % | 1 | 0 | 10 |
| (0-40-009) | Inundation and wetland fraction | % | 1 | 0 | 10 |
| (0-40-010) | Topographic complexity | % | 1 | 0 | 10 |

New Code Table (0-08-192) "Beam identified"

0, 			Parameter = Fore beam

1, 			Parameter = Mid beam

2, 			Parameter = Aft beam

3 to 6, 			Parameter = Reserved

7, 			Parameter = Missing

New Code Table (0-21-192) "Beam co-location"

0, 			Parameter = Data from single ground station (no co-location)

1, 			Parameter = Data from multiple ground station (co-located data)

2, 			Parameter = Reserved

3, 			Parameter = Missing

New Flag Table (0-21-216) "Wind vector cell quality"

Bit 1: 			Not enough good sigma-0 available for wind retrieval

Bit 2: 			Poor azimuth diversity among sigma-0 for wind retrieval

Bit 3: 			Any beam noise content above threshold

Bit 4: 			Product monitoring not used

Bit 5: 			Product monitoring flag

Bit 6: 			KNMI quality control fails

Bit 7: 			Variational quality control fails

Bit 8: 			Some portion of wind vector cell is over land

Bit 9: 			Some portion of wind vector cell is over ice

Bit 10: 			Wind retrieval not performed for wind vector cell

Bit 11: 			Reported wind speed is greater than 30 m/s

Bit 12: 			Reported wind speed is less than or equal to 3 m/s

Bit 13: 			Rain flag for the wind vector cell is not usable

Bit 14: 			Rain flag algorithm detects rain

Bit 15: 			No meteorological background used

Bit 16: 			Data are redundant

Bit 17-23: 		Reserved

All 24: 			Missing

New Code Table (0-21-246) "ASCAT KP quality estimate"

0, 			Parameter = Okay

1, 			Parameter = Not okay

2, 			Parameter = Reserved

3, 			Parameter = Missing

New Code Table (0-21-247) "ASCAT sigma-0 usability"

0, 			Parameter = Good

1, 			Parameter = Usable

2, 			Parameter = Bad

3, 			Parameter = Missing

New Flag Table (0-40-005) "Soil moisture correction flags"

Bit 1:			Soil moisture between -20% and 0%

Bit 2: 			Soil moisture between 100% and 120%

Bit 3: 			Correction of wet backscatter reference

Bit 4: 			Correction of dry backscatter reference

Bit 5: 			Correction of volume scattering in sand

Bits 6-7: 		Reserved

All 8: 			Missing

New Flag Table (0-40-006) "Soil moisture processing flags"

Bit 1: 			Not soil

Bit 2: 			Sensitivity to soil moisture below limit

Bit 3: 			Azimuthal noise above limit

Bit 4: 			Backscatter Fore-Aft beam out of range

Bit 5: 			Slope Mid-Fore beam out of range

Bit 6: 			Slope Mid-Aft beam out of range

Bit 7: 			Soil moisture below -20%

Bit 8: 			Soil moisture above 120%

Bits 9-16: 		Reserved

Code Table 0-02-048

Add: 		12, Parameter = ASCAT

Change: 	12 to 14, Parameter = Reserved

to:		13 to 14, Parameter = Reserved

#### Conclusion

The meeting is invited to consider the proposed new code table entries, and to endorse their addition to the existing table.