| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, 5-8 DECEMBER 2005 |  | ET/DR&C/Doc. 3.10 (8) _______ (21.XI.2006) ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

PRE-OPERATIONAL ENTRIES OF BUFR TABLES B AND D

FOR NEW TEMPLATES OF RADOB, TRACKOB AND SAREP

Submitted by the Japan Meteorological Agency

________________________________________________________________

Summary and Purpose of Document

This document contains Table B and D descriptors and code tables necessary for RADOB, TRACKOB and SAREP Templates to be pre-operational, and also Table D descriptors which correspond with whole these templates, respectively, for validation.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the descriptors of BUFR/CREX Table B and D and Code Tables as pre-operational with a view to submitting them to the next CBS with exception of proposed three Table D descriptors for validation.

Discussion

Exchange of TRACKOB data in BUFR

The Japan Meteorological Agency (JMA) is collecting reports of marine surface observations in FM62 TRACKOB from Voluntary Observing Ships through the INMARSAT and distributing them through the Global Telecommunication System (GTS).

In accordance with the migration plan, a BUFR template for TRACKOB data as well as necessary descriptors and code tables were drafted by JMA.  A validation test was carried out with the kind help from the European Centre for Medium-Range Weather Forecasts (ECMWF) and successfully completed.  The experimental exchange of TRACKOB data in BUFR started in November 2005.

Exchange of RADOB and SAREP data in BUFR

JMA has been producing tropical cyclone information in FM85 SAREP, which is derived from Japanese geostationary satellite.  Also, JMA and some members of the ESCAP/WMO Typhoon Committee (hereinafter referred to as TC) have been producing tropical cyclone information in FM20 RADOB, which is derived from radar observations.  These products are  being exchanged between the members of TC for disaster prevention and mitigation activities according to the Typhoon Committee Operational Manual, Meteorological Component (Report No. TCP-23).

In accordance with the approval at the 37th Session of TC (Shanghai, China, Nov. 2004), BUFR templates for SAREP and RADOB data were drafted by JMA with necessary descriptors and code tables.  Validation tests were carried out with the kind help of ECMWF and successfully completed.  Distribution of tropical cyclone information in BUFR from JMA started in November 2005.

Table D descriptors for RADOB, TRACKOB and SAREP

At the meeting of the Coordination Team on Migration to Table Driven Code Forms (CT/MTDCF) held in Geneva, November 2005, it was recommended to create one Table D descriptor for each whole sequence of RADOB, TRACKOB and SAREP.

PROPOSAL

1)	Descriptors and code tables for the templates of RADOB, TRACKOB and SAREP are listed in the Annex I to this document.  The meeting is invited to examine them with a view to giving recommendations to the next CBS session for operational implementation.

2)	In accordance with the recommendation from the meeting of CT/MTDCF, three Table D descriptors for RADOB, TRACKOB and SAREP Templates are proposed for validation (see Annex II).  The meeting is invited to endorse the Table D Descriptors for validation.

I.   Descriptors

I-1   For RADOB

Class 02 - Instrumentation

| 0 | 02 | 160 | Wave length of the radar | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 19 - Synoptic features

| 0 | 19 | 100 | Time interval to calculate the movement of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 19 | 101 | Accuracy of the position of the centre of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 102 | Shape and definition of the eye of the tropical cyclone | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 103 | Diameter of major axis of the eye of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 104 | Change in character of the eye during the 30 minutes | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 105 | Distance between the end of spiral band and the centre | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

I-2   For TRACKOB

Class 02 - Instrumentation

| 0 | 02 | 042 | Indicator for sea surface current speed | Code table | 0 | 0 | 2 | Code table | 0 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 04 - Location (time)

| 0 | 04 | 080 | Averaging period for following value | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Class 22 - Oceanographic elements

| 0 | 22 | 005 | Direction of sea surface current | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 22 | 032 | Speed of sea surface current | m s-1 | 2 | 0 | 13 | m s-1 | 2 | 4 |
| 0 | 22 | 049 | Sea surface temperature | K | 2 | 0 | 15 | K | 2 | 5 |
| 0 | 22 | 059 | Sea surface salinity | Part per thousand | 2 | 0 | 14 | Part per thousand | 2 | 5 |

I-3   For SAREP

Class 19 - Synoptic features

| 0 | 19 | 106 | Identification number of tropical cyclone | Numeric | 0 | 0 | 7 | Numeric | 0 | 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 19 | 107 | Time interval of the tropical cyclone analysis | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 108 | Accuracy of geographical position of the tropical cyclone | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 109 | Mean diameter of the overcast cloud of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 110 | Apparent 24-hour change in intensity of the tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 111 | Current Intensity (CI) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 112 | Data tropical (DT) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 113 | Cloud pattern type of the DT-number | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 19 | 114 | Model Expected tropical (MET) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 115 | Trend of past 24-hour change (+: Developed, -: Weakened) | Numeric | 1 | -30 | 6 | Numeric | 1 | 2 |
| 0 | 19 | 116 | Pattern tropical (PT) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 117 | Cloud picture type of the PT-number | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 118 | Final tropical (T) number of the tropical cyclone | Numeric | 1 | 0 | 7 | Numeric | 1 | 3 |
| 0 | 19 | 119 | Type of the final T-number | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 19 | 150 | Typhoon International Common Number (Typhoon Committee) | CCITTIA5 | 0 | 0 | 32 | Character | 0 | 4 |

Class 25 - Processing information

| 0 | 25 | 150 | Satellite intensity analysis method of tropical cyclone | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Category 01 - Location and identification sequence

| 3 | 01 | 005 | 0 01 035 0 01 034 | Originating centre Identification of originating/generating sub-centre |
| --- | --- | --- | --- | --- |

II.   Code Tables

II-1   For RADOB

0 02 160

Wave length of the radar

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | 10 to less than 20 mm |
| 2 | Reserved |
| 3 | 20 to less than 40 mm |
| 4 | Reserved |
| 5 | 40 to less than 60 mm |
| 6 | Reserved |
| 7 | 60 to less than 90 mm |
| 8 | 90 to less than 110 mm |
| 9 | 110 mm and greater |
| 10-14 | Not used |
| 15 | Missing value |

0 19 100

Time interval to calculate the movement of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0-2 | Not used |
| 3 | During the preceding 15 minutes |
| 4 | During the preceding 30 minutes |
| 5 | During the preceding 1 hour |
| 6 | During the preceding 2 hours |
| 7 | During the preceding 3 hours |
| 8 | During the preceding 6 hours |
| 9 | During a period of more than 6 hours |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 101

Accuracy of the position of the centre of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | Eye visible on radar scope, accuracy good (within 10 km) |
| 2 | Eye visible on radar scope, accuracy fair (within 30 km) |
| 3 | Eye visible on radar scope, accuracy poor (within 50 km) |
| 4 | Position of the centre within the area covered by the radar scope, determination by means of the spiral-band overlay, accuracy good (within 10 km) |
| 5 | Position of the centre within the area covered by the radar scope, determination by means of the spiral-band overlay, accuracy fair (within 30 km) |
| 6 | Position of the centre within the area covered by the radar scope, determination by means of the spiral-band overlay, accuracy poor (within 50 km) |
| 7 | Position of the centre outside the area covered by the radar scope, extrapolation by means of the spiral-band overlay |
| 8-9 | Reserved |
| 10 | Accuracy undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 102

Shape and definition of the eye of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Circular |
| 1 | Elliptical — the minor axis is at least 3/4 the length of the major axis |
| 2 | Elliptical — the minor axis is less than 3/4 the length well defined of the major axis |
| 3 | Apparent double eye |
| 4 | Other shape |
| 5 | Ill defined |
| 6 | Undetermined |
| 7 | Missing |

0 19 103

Diameter of major axis of the eye of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Less than 5 km |
| 1 | 5 to less than 10 km |
| 2 | 10 to less than 15 km |
| 3 | 15 to less than 20 km |
| 4 | 20 to less than 25 km |
| 5 | 25 to less than 30 km |
| 6 | 30 to less than 35 km |
| 7 | 35 to less than 40 km |
| 8 | 40 to less than 50 km |
| 9 | 50 km and greater |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 104

Change in character of the eye during the 30 minutes

| Code figure |  |
| --- | --- |
| 0 | Eye has first become visible during the past 30 minutes |
| 1 | No significant change in the characteristics or size of the eye |
| 2 | Eye has become smaller with no other significant change in characteristics |
| 3 | Eye has become larger with no other significant change in characteristics |
| 4 | Eye has become less distinct with no significant change in size |
| 5 | Eye has become less distinct and decreased in size |
| 6 | Eye has become less distinct and increased in size |
| 7 | Eye has become more distinct with no significant change in size |
| 8 | Eye has become more distinct and decreased in size |
| 9 | Eye has become more distinct and increased in size |
| 10 | Change in character and size of eye cannot be determined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 105

Distance between the end of spiral band and the centre

| Code figure |  |
| --- | --- |
| 0 | 0 to less than 100 km |
| 1 | 100 to less than 200 km |
| 2 | 200 to less than 300 km |
| 3 | 300 to less than 400 km |
| 4 | 400 to less than 500 km |
| 5 | 500 to less than 600 km |
| 6 | 600 to less than 800 km |
| 7 | 800 km or more |
| 8-9 | Reserved |
| 10 | Doubtful or undetermined |
| 11-14 | Not used |
| 15 | Missing value |

II-2   For TRACKOB

0 02 042

Indicator for sea surface current speed

| Code figure |  |
| --- | --- |
| 0 | Value originally reported in m/s |
| 1 | Value originally reported in knots |
| 2 | No sea current data available |
| 3 | Missing |

0 04 080

Averaging period for following value

| Code figure |  |
| --- | --- |
| 0 | Spot values |
| 1 | Less than 15 minutes |
| 2 | From 15 to 45 minutes |
| 3 | More than 45 minutes |
| 4-8 | Reserved |
| 9 | Data not available |
| 10-14 | Not used |
| 15 | Missing |

II-3   For SAREP

0 19 107

Time interval of the tropical cyclone analysis

| Code figure |  |
| --- | --- |
| 0 | Less than 1 hour |
| 1 | 1 to less than 2 hours |
| 2 | 2 to less than 3 hours |
| 3 | 3 to less than 6 hours |
| 4 | 6 to less than 9 hours |
| 5 | 9 to less than 12 hours |
| 6 | 12 to less than 15 hours |
| 7 | 15 to less than 18 hours |
| 8 | 18 to less than 21 hours |
| 9 | 21 to less than 30 hours |
| 10-14 | Not used |
| 15 | Missing value |

0 19 108

Accuracy of geographical position of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Cyclone centre within 10 km of the transmitted position |
| 1 | Cyclone centre within 20 km of the transmitted position |
| 2 | Cyclone centre within 50 km of the transmitted position |
| 3 | Cyclone centre within 100 km of the transmitted position |
| 4 | Cyclone centre within 200 km of the transmitted position |
| 5 | Cyclone centre within 300 km of the transmitted position |
| 6 | Cyclone centre undetermined |
| 7 | Missing value |

0 19 109

Mean diameter of the overcast cloud of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Less than 1° of latitude |
| 1 | 1° to less than 2° of latitude |
| 2 | 2° to less than 3° of latitude |
| 3 | 3° to less than 4° of latitude |
| 4 | 4° to less than 5° of latitude |
| 5 | 5° to less than 6° of latitude |
| 6 | 6° to less than 7° of latitude |
| 7 | 7° to less than 8° of latitude |
| 8 | 8° to less than 9° of latitude |
| 9 | 9° of latitude or more |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 110

Apparent 24-hour change in intensity of the tropical cyclone

| Code figure |  |
| --- | --- |
| 0 | Much weakening |
| 1 | Weakening |
| 2 | No change |
| 3 | Intensification |
| 4 | Strong Intensification |
| 5-8 | Reserved |
| 9 | Not observed previously |
| 10 | Undetermined |
| 11-14 | Not used |
| 15 | Missing value |

0 19 113

Cloud pattern type of the DT-number

| Code figure | Type |
| --- | --- |
| 1 | Curved Band |
| 2 | Shear |
| 3 | Eye |
| 4 | Banding Eye |
| ５ | Central Dense Overcast (CDO) |
| 6 | Embedded Center |
| 7 | Center Cold Cover (CCC) |
| 8-14 | Reserved |
| 15 | Missing value |

0 19 117

Cloud picture type of the PT-number

| Code figure | Type |
| --- | --- |
| 1 | A (Curved Band) |
| 2 | B (CDO) |
| 3 | C (Shear) |
| 4-6 | Reserved |
| 7 | Missing value |

0 19 119

Type of the final T-number

| Code figure | Type |
| --- | --- |
| 1 | DT-number |
| 2 | PT-number |
| 3 | MET-number |
| 4-6 | Reserved |
| 7 | Missing value |

0 25 150

Satellite intensity analysis method of tropical cyclone

| Code figure | Method |
| --- | --- |
| 1 | The Dvorak’s VIS (visual imagery) intensity analysis |
| 2 | The Dvorak’s EIR (Enhanced Infrared imagery) intensity analysis |
| 3-14 | Reserved |
| 15 | Missing value |

Proposed Table D descriptors which correspond with

whole sequences of RADOB, TRACKOB and SAREP

1.   RADOB Template (part A: Information on tropical cyclone)

Proposal:

[ 3 16 032 ] = 3 01 001 + 3 01 011 + 3 01 012 + 0 02 160 + 0 08 005 + 0 05 002

+ 0 06 002 + 0 08 005 + 0 19 100 + 0 19 005 + 0 19 006 + 0 19 101

+ 0 19 102 + 0 19 103 + 0 19 104 + 0 19 105

| Table reference | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
|  |  | Station identification and time |  |  |  |  |
| 3 01 001 | 0 01 001 | WMO block number | Numeric | 0 | 0 | 7 |
|  | 0 01 002 | WMO station number | Numeric | 0 | 0 | 10 |
| 3 01 011 | 0 04 001 | Year | Year | 0 | 0 | 12 |
|  | 0 04 002 | Month | Month | 0 | 0 | 4 |
|  | 0 04 003 | Day | Day | 0 | 0 | 6 |
| 3 01 012 | 0 04 004 | Hour | Hour | 0 | 0 | 5 |
|  | 0 04 005 | Minute | Minute | 0 | 0 | 6 |
|  |  | Radar information |  |  |  |  |
| 0 02 160 | NEW | Wave length of the radar | Code table | 0 | 0 | 4 |
|  |  | Tropical Cyclone |  |  |  |  |
| 0 08 005 |  | Meteorological attribute significance (=1) | Code table | 0 | 0 | 4 |
| 0 05 002 |  | Latitude (coarse accuracy) | Degree | 2 | –9000 | 15 |
| 0 06 002 |  | Longitude (coarse accuracy) | Degree | 2 | –18000 | 16 |
| 0 08 005 |  | Meteorological attribute significance (set to missing to cancel the previous value) | Code table | 0 | 0 | 4 |
| 0 19 100 | NEW | Time interval to calculate the movement of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 005 |  | Direction of motion of feature | Degree true | 0 | 0 | 9 |
| 0 19 006 |  | Speed of motion of feature | m s–1 | 2 | 0 | 14 |
| 0 19 101 | NEW | Accuracy of the position of the centre of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 102 | NEW | Shape and definition of the eye of the tropical cyclone | Code table | 0 | 0 | 3 |
| 0 19 103 | NEW | Diameter of major axis of the eye of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 104 | NEW | Change in character of the eye during the 30 minutes | Code table | 0 | 0 | 4 |
| 0 19 105 | NEW | Distance between the end of spiral band and the centre | Code table | 0 | 0 | 4 |

2.   TRACKOB Template

Proposal:

[ 3 08 010 ] = 0 01 011 + 1 13 000 + 0 31 001 + 3 01 011 + 3 01 012 + 3 01 021

+ 0 04 080 + 0 22 049 + 0 04 080 + 0 22 059 + 0 04 080 + 0 22 005

+ 0 02 042 + 0 22 032 + 0 02 042 + 0 04 080

| Table reference | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
| 0 01 011 |  | Ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 72 |
| 1 13 000 |  | Delayed replication of 13 descriptors |  |  |  |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |
| 3 01 011 | 0 04 001 | Year | Year | 0 | 0 | 12 |
|  | 0 04 002 | Month | Month | 0 | 0 | 4 |
|  | 0 04 003 | Day | Day | 0 | 0 | 6 |
| 3 01 012 | 0 04 004 | Hour | Hour | 0 | 0 | 5 |
|  | 0 04 005 | Minute | Minute | 0 | 0 | 6 |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree | 5 | –9000000 | 25 |
|  | 0 06 001 | Longitude (high accuracy) | Degree | 5 | –18000000 | 26 |
| 0 04 080 | NEW | Averaging period for following value | Code table | 0 | 0 | 4 |
| 0 22 049 | NEW | Sea surface temperature | K | 2 | 0 | 15 |
| 0 04 080 | NEW | Averaging period for following value | Code table | 0 | 0 | 4 |
| 0 22 059 | NEW | Sea surface salinity | Part per thousand | 2 | 0 | 14 |
| 0 04 080 | NEW | Averaging period for following value | Code table | 0 | 0 | 4 |
| 0 22 005 | NEW | Direction of sea surface current | Degree true | 0 | 0 | 9 |
| 0 02 042 | NEW | Indicator for sea surface current speed | Code table | 0 | 0 | 2 |
| 0 22 032 | NEW | Speed of sea surface current | ms-1 | 2 | 0 | 13 |
| 0 02 042 | NEW | Indicator for sea surface current speed (cancel) | Code table | 0 | 0 | 2 |
| 0 04 080 | NEW | Averaging period for following value (cancel) | Code table | 0 | 0 | 4 |

3.   SAREP Template (part A: Information on tropical cyclone)

Proposal:

[ 3 16 032 ] = 3 01 005 + 3 01 011 + 3 01 012 + 0 01 007 + 0 25 150 + 1 22 000

+0 31 001 + 0 01 027 + 0 19 150 + 0 19 106 + 0 08 005 + 0 05 002

+0 06 002 + 0 08 005 + 0 19 107 + 0 19 005 + 0 19 006 + 0 19 108

+0 19 109 + 0 19 110 + 0 19 111 + 0 19 112 + 0 19 113 + 0 19 114

+0 19 115 + 0 19 116 + 0 19 117 + 0 19 118 + 0 19 119

| Table reference | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
|  |  | (Station identification and time) |  |  |  |  |
| 3 01 005 NEW | 0 01 035 | Originating centre | Common code table C-11 | 0 | 0 | 16 |
|  | 0 01 034 | Identification of originating/generating sub-centre | Common code table C-12 | 0 | 0 | 8 |
| 3 01 011 | 0 04 001 | Year | Year | 0 | 0 | 12 |
|  | 0 04 002 | Month | Month | 0 | 0 | 4 |
|  | 0 04 003 | Day | Day | 0 | 0 | 6 |
| 3 01 012 | 0 04 004 | Hour | Hour | 0 | 0 | 5 |
|  | 0 04 005 | Minute | Minute | 0 | 0 | 6 |
|  |  | (Satellite information) |  |  |  |  |
| 0 01 007 |  | Satellite identifier | Code table | 0 | 0 | 10 |
| 0 25 150 | NEW | Satellite intensity analysis method of tropical cyclone | Code table | 0 | 0 | 4 |
|  |  | (Tropical cyclone information) |  |  |  |  |
| 1 22 000 |  | Delayed replication of 22 descriptors |  |  |  |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |
| 0 01 027 |  | WMO long storm name | CCITT IA5 | 0 | 0 | 80 |
| 0 19 150 | NEW | Typhoon International Common Number (Typhoon Committee) | CCITT IA5 | 0 | 0 | 32 |
| 0 19 106 | NEW | Identification number of tropical cyclone | Numeric | 0 | 0 | 7 |
| 0 08 005 |  | Meteorological attribute significance (=1) | Code table | 0 | 0 | 4 |
| 0 05 002 |  | Latitude (coarse accuracy) | Degree | 2 | –9000 | 15 |
| 0 06 002 |  | Longitude (coarse accuracy) | Degree | 2 | –18000 | 16 |
| 0 08 005 |  | Meteorological attribute significance (set to missing to cancel the previous value) | Code table | 0 | 0 | 4 |
| 0 19 107 | NEW | Time interval of the tropical cyclone analysis | Code table | 0 | 0 | 4 |
| 0 19 005 |  | Direction of motion of feature | Degree true | 0 | 0 | 9 |
| 0 19 006 |  | Speed of motion of feature | m s–1 | 2 | 0 | 14 |
| 0 19 108 | NEW | Accuracy of geographical position of the tropical cyclone | Code table | 0 | 0 | 3 |
| 0 19 109 | NEW | Mean diameter of the overcast cloud of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 110 | NEW | Apparent 24-hour change in intensity of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 111 | NEW | Current Intensity (CI) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 112 | NEW | Data tropical (DT) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 113 | NEW | Cloud pattern type of the DT-number | Code table | 0 | 0 | 4 |
| 0 19 114 | NEW | Model Expected tropical (MET) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 115 | NEW | Trend of the past 24-hour change (+: Developed, -: Weakened) | Numeric | 1 | -30 | 6 |
| 0 19 116 | NEW | Pattern tropical (PT) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 117 | NEW | Cloud picture type of the PT-number | Code table | 0 | 0 | 3 |
| 0 19 118 | NEW | Final tropical (T) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 119 | NEW | Type of the final T-number | Code table | 0 | 0 | 3 |

# Text boxes

Annex I

Annex II