| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, OMAN, 5 - 8 DECEMBER 2005 |  | ET DR&C/Doc. 3.2(1) (22.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

## New BUFR Descriptors for Atmospheric Chemistry

Submitted by Yves Pelletier and Yves Rochon (Canada)

________________________________________________________________

Summary and Purpose of Document

This document proposes several new BUFR descriptors and code tables for the representation of atmospheric chemistry observations and forecasts.

________________________________________________________________

ACTION PROPOSED

The ET DR&C meeting is kindly asked to consider the submitted proposals.

Even if generally acceptable, the proposed wording may need refinements.

DISCUSSION

## Introduction

The following proposed additions to the BUFR table B are intended to provide a framework suitable for the reporting and forecasting of atmospheric constituents in disciplines related to Air Chemistry.  This is in response to immediate requirements that were expressed in an observational context by the Canadian research community, and in anticipation of similar international needs as described in the 2004 IGACO theme team report.  We also foresee a need for the exchange of forecast data from an emerging international population of atmospheric chemistry prediction models.

In the spirit of BUFR, we aim to produce a set of new descriptors that is sufficiently general to meet current and most future needs, while leaving room for extension to meet future requirements that were not seen at the outset.

## Scope of this proposal

There is a lot of ground to cover in order to produce a comprehensive depiction of atmospheric chemistry concepts in BUFR.  It seems prudent, then, not to try to do it all at once. A firm base should be established and validated before we build toward more complex themes. We see this as a process with at least two phases.  The first phase will cover:

- The cataloging of chemical species

- Descriptors for basic quantities or physical attributes in the discipline of Air Chemistry

- Basic descriptor sequences

The second and subsequent phases might cover:

- Instrumentation

- Representation of more complex species, such as particulate matter

- Descriptor sequences suitable for Table D

Representation of averaging kernels and correlation matrices

## Example descriptor sequence

We do not provide here full templates for specific instances of Air Quality observations; having said this, the general structure of a descriptor sequence is envisioned as follows (where indentation indicates repeatable sub-sequences of descriptors):

- Identification of measurement site and instrumentation

- Date/time of start of measurement

- Horizontal and vertical coordinates of measurement site

- Time displacement from start of measurement (high precision)

- Lat/lon displacement from start of measurement (high precision)

- Vertical coordinate value (using high-precision descriptor when required)

- Atmospheric constituent type (new descriptor 0 08 043 or 0 08 044)

- Measured or physical quantities  (one or more measurement or forecast)

This structure was based on the WMO BUFR template for TEMP data (aerological sounding). It would likely suit measurements taken by balloon or aircraft.  Appropriate templates would have to be designed for ground-based and satellite measurements.

## Design issues

- Catalog of chemical species:   Atmospheric chemistry potentially deals with thousands of molecules.  While an initial list may have "only" contained a few dozen species, we perceive that it is important to formulate an approach that scales well as the number of measured chemicals grows. Unless well planned from the outset, this could become a significant maintenance issue and involve us in an area (the cataloging of chemicals) that we may not want to get into.

We propose to address the issue as follows:

In chemistry, unambiguous identification of a chemical is commonly accomplished through the use of so-called CAS Registry Numbers. CAS (Chemical Abstracts Service, http://www.cas.org/EO/regsys.html ) is a division of the American Chemical Society.  A CAS number is composed of 11 characters at most: 9 digits or less, and 2 hyphens.  

We propose the creation of a BUFR table B descriptor that would allow the use of CAS numbers inside a BUFR message. This would have at least three advantages:

  - allowing the use of CAS numbers would alleviate the need to create and maintain tables of atmospheric chemicals within the BUFR framework (but not quite eliminate it).  However, those tables that we would have to create, could then be short and generic.

  - CAS would provide a more robust catalog than what we could come up with on our own

  - It would connect the BUFR representation of atmospheric chemistry with a tool that is well known and routinely used by chemists.

The downside of this, is that a chemical designated by its CAS Registry Number must then be looked up in the CAS database or some other source, such as could be found in the scientific litterature. We believe this is easily manageable by users in the field of Atmospheric Chemistry.  Thus, for completely unambiguous specification of chemical species in BUFR, the use of CAS registry numbers would be recommended.

A small WMO-maintained catalog would still be required, but only for general and generic species without a CAS number, such as volcanic ash, smoke, and generic aerosols. Very fundamental species such as water vapour, ozone and the other main greenhouse gases would also be included.  The catalog would take the form of a code table corresponding to proposed element descriptor 0 08 043 (see below).  To prevent undue growth of the WMO maintained catalog, the addition, to this table, of constituents endowed with a CAS number should be given careful consideration and occur only for especially common or important species.

A short discussion of the main chemicals of interest is included in Annex B.

Precision requirements and bit length of descriptors: The absolute values and precision required for some measurement types (i.e. concentration) span across at least 16 decimal orders of magnitude. Individual chemical species may have narrower requirements, but to accomodate a whole catalog of species with a single concentration descriptor, that is what we need.  This means that a concentration descriptor meant for general use for any chemical would need to be at least 54 bits wide.  For individual species, the required width could in some cases exceed 32 bits.

Within the existing BUFR framework, the solution we settled on was to give the concentration (and similar) descriptors default scales and bit width that work for the greater number of species, and to leave specialist users to choose appropriate scaling and bit width on a case by case basis, by using BUFR Data Description Operators.

As a means of providing additional flexibility, we also propose to create a new Data Description Operator that would make it possible to express values in IEEE floating point format.  In many cases this would allow data representation with the fewest possible intermediate steps while maintaining sufficient precision.  It would, however, require the adaptation of existing decoders.  We believe this would be worth the work, since the added flexibility could have benefits in other areas that demand the depiction of extremely large value ranges. 

Another alternative, which we have not implemented here, would be to define the element descriptor, for such wide-spectrum data, as the logarithm of the actual value.  Precautions would have to be taken as the value neared zero, with the use of an appropriate threshold value to prevent accidental attempts to perform the logarithm of zero.  One problem with this method is that the appropriate value for the near-zero threshold varies widely from species to species, as would the optimum scaling and bit-width.  So the use of Data Description Operators would, again, be difficult to avoid.

## Proposed new descriptors for atmospheric constituents

- Measured or physical quantities

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 15 007 | Molecular mass | u (unified atomic mass unit) | 2 | 0 | 15 | U (unified atomic mass unit) | 2 | 5 |
| 0 15 008 | Volumetric mixing ratio | numeric | 16 | 0 | 31 | numeric | 16 | 10 |
| 0 15 009 | Integrated number density | m-2 | -12 | 0 | 31 | m-2 | -12 | 10 |
| 0 15 010 | Partial pressure | Pa | 12 | 0 | 31 | Pa | 12 | 10 |
| 0 15 021 | Integrated mass density | kg/m2 | 14 | 0 | 31 | Kg/m2 | 14 | 10 |
| 0 15 022 | Number density | m-3 | -8 | 0 | 31 | m-3 | -8 | 10 |
| 0 15 023 | Mass density | kg/m3 | 18 | 0 | 31 | kg/m3 | 18 | 10 |
| 0 15 024 | Optical depth | numeric | 4 | 0 | 24 | numeric | 4 | 8 |
| 0 15 027 | Extinction coefficient | m-1 | 9 | 0 | 30 | m-1 | 9 | 10 |
| 0 15 028 | Photo dissociation rate | s-1 | 14 | 0 | 31 | s-1 | 14 | 10 |

- Coordinates

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 07 011 | Pressure (high precision) | Pa | 4 | 0 | 31 | Pa | 4 | 10 |

- Processing information

| Table Reference | Element name | BUF | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 25 102 | Spectrographic wavelength | m | 13 | 0 | 30 | m | 13 | 10 |
| 0 25 103 | Spectral width | m | 13 | 0 | 30 | m | 13 | 10 |

- Significance qualifier

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 08 043 | Atmospheric chemical or physical constituent type | Code Table | 0 | 0 | 8 | Code table | 0 | 3 |
| 0 08 044 | CAS registry number | CCITT IA5 | 0 | 0 | 88 | CCITT IA5 | 9 | 11 |

Code table

Code table 0 08 043

See remarks in section “Design Issues”, sub-section 1, and in Appendix B.

The last column in the table contains the associated registry number from the Chemical Abstracts Service (CAS) of the American Chemical Society.

| Code figure | Meaning |
| --- | --- |
|  | Name | Formula | CAS Number (if applicable) |
| 0 | Ozone | O3 | 10028-15-6 |
| 1 | Water vapour | H2O | 7732-18-5 |
| 2 | Methane | CH4 | 74-82-8 |
| 3 | Carbon dioxide | CO2 | 37210-16-5 |
| 04-24 | reserved |  |  |
| 25 | Particulate Matter < 1.0 microns |  |  |
| 26 | Particulate Matter < 2.5 microns |  |  |
| 27 | Particulate Matter < 10 microns |  |  |
| 28 | Aerosols (generic) |  |  |
| 29 | Smoke (generic) |  |  |
| 30 | Crustal Material (generic dust) |  |  |
| 31 | Volcanic Ash |  |  |
| 32-200 | reserved |  |  |
| 201-254 | reserved for local use |  |  |
| 255 | missing |  |  |

- Data description operator

See remarks in Section “Design Issues”, sub-section 2.

| Table Reference | Operator name | Operation Description |
| --- | --- | --- |
| F X Operand |  |  |
| 2 07 YYY | IEEE floating point representation | For elements in Table B other than CCITT IA5, code tables or flag tables, this operator shall indicate that values are represented in YYY bit IEEE floating point, where YYY can be set to 032, 064 or any valid IEEE floating point width. This operator shall override the scaling and bit width from Table B. The reference value from Table B may be used for bound-checking if applicable. An operand of YYY=000 shall reinstate the Table B scaling and bit width. |

## Appendix A - Range correspondence

Determination and identification of the minimum and maximum values corresponding to the definitions of the descriptor elements in tables 1 to 3 are presented here. Two maxima are provided when the range of possible expected values cannot be expressed with at most 31 bits; a maximum of at most 2x109 larger than the minimum value can be obtained from 31 bits. In such instances, both the magnitude corresponding to a limit of 31 bits, in consideration of the minimum value in the table, and the magnitude of the largest expected value are provided.

The range of values for concentrations of constituent observations is based on a minimum set according to a minimum OH mixing ratio of ~10-14 with a precision of 1% and the largest expected maximum set according to the upper limit for tropospheric H2O mixing ratio at ~0.04. The next largest mixing ratios would be attributed to CO2 at a level just under 0.001. For conversion to other units which involve pressure and/or temperature, pressures of 105 Pa and 104 Pa for the calculation of the maxima and minima and a temperature of 300 were applied. Use of 104 Pa with the OH mixing ratio is reasonable for determination of the minimum considering the increase in OH mixing ratio with decreasing pressure as well as the larger mixing ratios in the stratosphere and mesosphere for other constituents. Here are the conversions applied to the volumetric mixing ratios followed by the resulting ranges:

| Parameter | Unit | Conversion factor from mixing ratio |
| --- | --- | --- |
| Pressure | Pascal | Pair |
| Number density | m-3 | PairNa /(R*T) |
| Mass density | kg/m3 | PairM /(R*T) x10-3 kg/g |
| Integrated number density | m-2 | HPairNa /(R*T) |
| Integrated mass density | kg/m2 | HPairM /(R*T) x10-3 kg/g |

where Pair is the atmospheric pressure in Pa, Na is the Avogradro constant (6.022x1023 /mol), R* is the gas constant (8.314 J K-1 mol-1), T is temperature in Kelvin, H is the scale height of the atmosphere set to 7x103 m, and M is the molecular mass in unified mass units u (i.e., g mol-1), hence the additional conversion factor of 10-3 kg/g.

| Table Reference | Element name | Unit | Minimum value | Maxima |
| --- | --- | --- | --- | --- |
|  |  |  |  | Based on a limit of 31 bits | Largest expected value |
| F X Y |  |  |  |  |  |
| 0 15 007 | Molecular mass | u (unified mass unit) | 0.01 | - | 327.67 |
| 0 15 008 | Mixing ratio in volume | numeric | 10-16 | 2x10-7 | 0.04 |
| 0 15 009 | Integrated number density | m-2 | 1012 | 2x1021 | 1028 |
| 0 15 010 | Partial pressure | Pa | 10-12 | 2x10-3 | 104 |
| 0 15 021 | Integrated mass density | kg/m2 | 10-14 | 2x10-5 | 102 |
| 0 15 022 | Number density | m-3 | 108 | 2x1017 | 1024 |
| 0 15 023 | Mass density | kg/m3 | 10-18 | 2x10-9 | 10-2 |
| 0 15 024 | Optical depth | numeric | 0.0001 | - | 1000 (clouds) |
| 0 15 027 | Extinction coefficient | m-1 | 10-9 | - | 1.0 (clouds) |
| 0 15 028 | Photo dissociation rate | s-1 | 10-14 | 2x10-5 | 0.1 |
| 0 07 011 | Pressure (high precision | Pa | 10-4 [0.1 Pa (~95 km) with 4 significant digits] | - | 2x105 |
| 0 25 103 | Spectral width (line widths to band models) | m | 10-13 | - | 10-4 |
| 0 25 102 | Wavelength | m | 10-13 (102 nm with 7 significant digits) | - | 10-4 (102 m) |

## Appendix B  - Chemicals of Interest

We provide below a list of chemicals of interest not present in Code Table 0 08 043, with their CAS registry numbers.  In BUFR code, these chemicals would be identified by their CAS numbers, using element descriptor 0 08 044.  Maintenance of this list is not viewed as being within the scope of the Expert Team on Data Representation and Codes; it is only provided here for illustration purposes.

A first iteration of the list was based on Tables 4.1-4.3 and the text of the IGACO theme report of September 2004 (WMO TD No. 1235)).

Three halon compounds were included based on the table of  class I ozone-depleting substances (Group II) of the U.S. Environmental Protection Agency (http://www.epa.gov/docs/ozone/ods.html).

CFC-11 was added to complement CFC-12 and HCFC-22 of the IGACO report.

The list of measured volatile organic compounds (VOC) would be quite extensive and is not explicitly identified here.  A list of VOC and related families can be consulted in Makar et al. (JGR, 108, 2003).

Other species such as OH, HNO4, CCl4, NH3, CF4, H2O2, N2O5, HF, H2SO4, OCS, HOCl, PAN, O (1D) and mercury-related compounds could also be considered.

| Name | Formula | CAS registry number |
| --- | --- | --- |
| Carbon monoxide | CO | 630-08-0 |
| Nitrogen dioxide | NO2 | 10102-44-0 |
| Nitrous oxide | N2O | 10024-97-2 |
| Bromine oxide | BrO | 15656-19-6 |
| Chlorine monoxide | ClO | 7791-21-1 |
| Hydrogen chloride | HCl | 7647-01-0 |
| Chlorine dioxide | OClO | 10049-04-4 |
| Trichlorofluoromethane | CFC-11 (CCl3F) | 75-69-4 |
| Dichlorodifluoromethane | CFC-12 (CCl2F2) | 75-71-8 |
| Nitric Oxide | NO | 10102-43-9 |
| Nitric acid | HNO3 | 52583-42-3 |
| Acetylene | C2H2 | 74-86-2 |
| Ethane | C2H6 | 74-84-0 |
| Methyl bromide | CH3Br | 74-83-9 |
| Bromotrifluoro-methane | CF3Br (halon 1301) | 75-63-8 |
| Bromochloro- difluoromethane | CF2ClBr (halon 1211) | 353-59-3 |
| Dibromotetra-fluoroethane | C2F4Br2 (halon 2402) | 25497-30-7 |
| Chlorodifluoro-methane | HCFC-22 (CHClF2) | 75-45-6 |
| Chlorine nitrate | ClONO2 | 14545-72-3 |
| Formaldehyde | HCHO | 50-00-0 |
| Sulfur dioxide | SO2 | 7446-09-5 |

## References

WMO Manual on Codes, Volume I.2, Part B (WMO publication No. 306) http://www.wmo.int/web/www/WMOCodes/ManualCodes/WMO306vol-I-2PartB.pdf

Report of the Integrated Global Atmospheric Chemistry Observation Theme Team, September 2004 http://ioc.unesco.org/igospartners/docs/theme_reports/IGACO-ThemeReport-Sep2004.pdf

Makar, P.A., M.D. Moran, M.T. Scholtz, and A. Taylor, Specification of volatile organic compound emissions for regional air quality  modeling of particulate matter and ozone, J. Geophys. Res., 108(D2), 4041, doi:10.1029/2001JD000797, 2003.