| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, OMAN, 5 - 8 DECEMBER 2005 |  | ET DR&C/Doc. 3.9(1) (15.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

## BUFR parameters for GEMS

Submitted by Martin Suttie (ECMWF)

________________________________________________________________

Summary and Purpose of Document

This document proposes a few new table B entries to represent aerosols and chemical species

________________________________________________________________

ACTION PROPOSED

The ET DR&C meeting is kindly asked to consider the proposed requirements.

1.  BUFR table B entries for GEMS observational data

The GEMS ( Global and regional Earth-system Monitoring using Satellite and in situ data) project will develop and implement at ECMWF a comprehensive global data assimilation/forecast system for atmospheric dynamics and composition. The model will use all available data to achieve global monitoring. The monitoring will include atmospheric constituents including:

a) greenhouse gases

b) reactive gases

c) aerosols

It is planned to use BUFR format for the representation and exchange of the observational data. In general, there is a need to represent chemicals in the BUFR form. The following table B entries are needed at this stage.

Key:	xxxx element from proposal of Pelletier and Rochon

yyyy new element needed

Aerosol

| Table Reference | Parameter | Units |
| --- | --- | --- |
| 0 01 007 | Satellite identifier |  |
| 0 02 019 | Satellite instrument |  |
| 0 01 033 | Identification of originating/generating centre |  |
| 0 02 172 | Product type for retrieved atmospheric gases |  |
| 0 04 001 | Year | year |
| 0 04 002 | Month | month |
| 0 04 003 | Day | day |
| 0 04 004 | Hour | hour |
| 0 04 005 | Minute | minute |
| 0 04 006 | Second | second |
| 0 05 001 | Latitude (high accuracy) | degree |
| 0 06 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 07 025 | Solar zenith angle | degree |
| 0 07 024 | Satellite zenith angle | degree |
|  | Solar azimuth angle | degree |
|  | Satellite azimuth angle | degree |
|  | Cloud mask and snow/ice indicator | Flag Table |
|  | Cloud amount percentage interval | Code Table |
| 0 08 013 | Day/night qualifier | Code Table |
| 0 08 065 | Sun-glint indicator | Code Table |
| 0 05 043 | Field of view number | numeric |
| 0 20 010 | Cloud cover (total) | % |
| 0 20 016 | Pressure at top of cloud | Pa |
| 0 13 040 | Surface flag (with proposed addition - see below) | Code Table |
| 0 33 003 | Quality information |  |
| 0 08 043 | Atmospheric chemical or physical constituent type | Code Table |
|  | Aerosol optical depth at 0.55 micron | numeric |
|  | Error in aerosol optical depth at 0.55 micron (see Note 2) | numeric |
|  | Ratio of small mode aerosol optical depth at 0.55 micron | numeric |
|  | Error in ratio of small mode aerosol optical depth at 0.55 micron (see Note 2) | numeric |
| 0 22 094 | Number of wavelength bands | numeric |
|  | Per wavelength band |  |
| 0 25 102 | Spectrographic wavelength | m |
|  | Reflectance | numeric |
|  | Error reflectance (see Note 2) | numeric |
| 0 10 040 | Number of retrieved layers (for optical depth) | numeric |
|  | Per optical depth layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
| 0 15 024 | Optical depth | numeric |
|  | Error optical depth (see Note 2) | numeric |
| 0 10 040 | Number of retrieved layers (for extinction) | numeric |
|  | Per extinction layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
| 0 15 027 | Extinction coefficient | m-1 |
|  | Error extinction coefficient (see Note 2) | m-1 |

Chemical species

Initial GEMS chemical species are:

- O3 (ozone)

- NO2 (nitrogen dioxide)

- SO2 (sulphur dioxide)

- HCHO (formaldehyde)

- CO2 (carbon dioxide)

- N2O (nitrous oxide)

- CO (carbon monoxide)

- CH4 (methane)

| Table Reference | Parameter | Units |
| --- | --- | --- |
| 0 01 007 | Satellite identifier |  |
| 0 02 019 | Satellite instrument |  |
| 0 01 033 | Identification of originating/generating centre |  |
| 0 02 172 | Product type for retrieved atmospheric gases |  |
| 0 04 001 | Year | year |
| 0 04 002 | Month | month |
| 0 04 003 | Day | day |
| 0 04 004 | Hour | hour |
| 0 04 005 | Minute | minute |
| 0 04 006 | Second | second |
| 0 05 001 | Latitude (high accuracy) | degree |
| 0 06 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 27 001 | Latitude (high accuracy) | degree |
| 0 28 001 | Longitude (high accuracy) | degree |
| 0 07 022 | Solar elevation | degree |
| 0 05 043 | Field of view number | numeric |
| 0 20 010 | Cloud cover (total) | % |
| 0 20 016 | Pressure at top of cloud | Pa |
| 0 08 012 | Land/sea mask | numeric |
| 0 33 003 | Quality information |  |
| 0 08 043 | Atmospheric chemical or physical constituent type (see Note 1) | Code Table |
| 0 10 040 | Number of retrieved layers | numeric |
|  | Per retrieved layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
| 0 15 021 | Integrated mass density | kg/m2 |
|  | Error integrated mass density (see Note 2) | kg/m2 |
|  | No. of averaging kernel layers | numeric |
|  | Per averaging kernel layer |  |
| 0 07 004 | Layer top pressure | Pa |
| 0 07 004 | Layer bottom pressure | Pa |
|  | Averaging kernel value | numeric |

Notes:

1. Need CO, NO2, N2O, HCHO and SO2 include in proposed Code Table 0 08 043.

2. We will have to be clear on what “error” means, i.e. could be 1-σ, 3- σ, rms, etc.

New BUFR descriptors for GEMS observational data

| Table Reference | Element Name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data Width (Chars) |
| 015040 | Aerosol optical depth at 0.55 micron (see Note A) | numeric | 4 | 0 | 24 | numeric | 4 | 8 |
| 015041 | Ratio of small mode aerosol optical depth at 0.55 micron (see Note B) | numeric | 6 (4) | 0 | 20 (14) | numeric | 6 (4) | 7 (5) |
| 015042 | Reflectance (see Note C) | numeric | 6 (4) | 0 | 20 (14) | numeric | 6 (4) | 7 (5) |
| 015043 | No. of averaging kernel layers (see Note D) | numeric | 0 | 0 | 10 | numeric | 0 | 4 |
| 015044 | Averaging kernel value (see Note E) | numeric | 6 (4) | -5x106 (-5x104) | 24 (17) | numeric | 6 (4) | 8 (6) |
| 015045 | Snow/ice indicator | Flag table | 0 | 0 | 2 | Flag table | 0 | 1 |
| 015046 | Cloud amount percentage interval | Code Table | 0 | 0 | 3 | Code Table | 0 | 1 |

Notes:

A. Assumed same range and precision as for Optical Depth (0 15 024) proposed by Pelletier and Rochon.

B. Minimum value = 0.0, maximum value = 1.0, precision = 0.000001 (0.0001)

C. Minimum value = 0.0, maximum value = 1.0, precision = 0.000001 (0.0001)

D. Allow up to 1024 averaging kernel layers (as with Number of retrieved layers (0 10 040))

E. Minimum = -5.0, maximum = 5.0, precision = 0.000001 (0.0001)

New Flag Tables   015045

Cloud mask and snow/ice indicator

| Bit No. |  |
| --- | --- |
| 1 | Snow/ice present |
| All 2 | Missing value |

New Code Tables 015046

Cloud amount percentage interval

| Code figure |  |
| --- | --- |
| 0 | 0-25% cloudy pixels |
| 1 | 25-50% cloudy pixels |
| 2 | 50-75% cloudy pixels |
| 3 | 75-100% cloudy pixels |
| 5-6 | Reserved |
| 7 | Missing value |

Additions to existing Code Tables

0 13 040 Surface flag

| Code figure |  |
| --- | --- |
| 0 | Land |
| 1 | Reserved |
| 2 | Near coast |
| 3 | Ice |
| 4 | Possible ice |
| 5 | Ocean |
| 6 | Coast |
| 7 | Desert |
| 8-14 | Reserved |
| 15 | Missing value |

Additions to proposed Code Tables

0 08 043 Atmospheric chemical or physical constituent type

| Code figure |  |
| --- | --- |
| 0 | Ozone (O3) |
| 1 | Water vapour (H2O) |
| 2 | Methane (CH4) |
| 3 | Carbon dioxide (CO2) |
| 4 | Carbon monoxide (CO) |
| 5 | Nitrogen dioxide (NO2) |
| 6 | Nitrous oxide (N2O) |
| 7 | Formaldehyde (HCHO) |
| 8 | Sulphur dioxide (SO2) |
| 9-24 | Reserved |
| 25 | Particulate matter < 1.0 microns |
| 26 | Particulate matter < 2.5 microns |
| 27 | Particulate matter < 10 microns |
| 28 | Aerosols (generic) |
| 29 | Smoke (generic) |
| 30 | Crustal material (generic dust) |
| 31 | Volcanic ash |
| 32 | Continental (generic) |
| 33 | Maritime (generic) |
| 34 | Sulfate |
| 35-200 | Reserved |
| 201-254 | Reserved for local use |
| 255 | Missing value |